## Slide 1: PowerPoint 13: Calculating for wall and floor tiling
PowerPoint presentation
Unit 116: Wall and floor tiling

## Slide 2: Aim: To give learners an understanding of calculating quantities used in wall and floor tiling. Outcomes: At the end of this session, the learner will be able to: Outcome 1: Identify a range of different methods of measurement, including areas, linear and how to allow for wastage. Outcome 2: Identify and relate measurement types to tiling work applications.
PowerPoint presentation

## Slide 3: Calculating for wall and floor tiling: planning Good planning can save on costs.
PowerPoint presentation
Being organised in advance with the correct labour, quantities of materials and resources means it will be less likely that problems occur. A disorganised workforce can be costly in the long run.
Risk assessments and method statements need to be produced before the work starts.
Materials and resources must be ordered in advance of the scheduled work to ensure deadlines are met.
Tiling materials need to be stored correctly to avoid damage.

## Slide 4: Types of measurement used
In wall and floor tiling, there are several methods of calculation used to work out quantities of materials and which are used when setting out prior to tiling.
We will look at:
measuring linear
measuring area
allowing for wastage.

## Slide 5: Calculating for wall and floor tiling
As a wall and floor tiler, you will be required to measure and calculate a range of tiling materials for a tiling installation.
This can include: tiles, cement board, plasterboard, decoupling membrane, stair nose trim, tile trim and many others.
When tendering for tiling contracts, it is important to calculate accurately and not underestimate the quantity of materials as this can be very costly.
Allowances must be made for waste when calculating quantities.

## Slide 6: Units of measurements
When calculating for quantities of tiling materials, the following units are used for measuring:
Units | Materials
Linear measurements | Tile trim
Square metres | Tiles
Litres | Primers and bonding agents
Kilograms | Adhesive and grout

## Slide 7: Calculations for wall and floor tiling
When calculating for plastering materials, we use the following basic operations:
addition +
subtraction -
multiplication x
division ÷

## Slide 8: Calculations for wall and floor tiling: percentages %
An easy way to calculate the percentage (%) of a number is to divide the number by 100 and multiply it by the percentage figure you require.
Note:
20% is the number added for VAT on materials (2021)
5% to 10% is a number used for adding waste when calculating quantities of materials for a contract.
See example on next slide

## Slide 9: Calculations for wall and floor tiling: percentages %
A room has a total floor area of 12.500m² which needs to be covered with porcelain tiles.
Calculate the total area needed, adding 6% for cutting and wastage.
12.500 ÷ 100 = 0.125
0.125 × 6 = 0.750m² (extra)
0.750 + 12.500 = 13.250m²
Total required 13.250m²

## Slide 10: Linear measurements
Linear measurements are how long an item measures.
Tile trims are measured by linear measurements.
When applying silicon sealant, we measure the length of the bead by linear measurement.
Movement joint trims are another tiling material measured by linear measurement.
When measuring the perimeter (four sides) of a room, for a tiled skirting, linear measurement is used.

## Slide 11: Area
To measure how many square metres of tile material is required to cover a surface area of a floor, you need to calculate the area.
To find the area you multiply the length by its width (L x W).
5.000m
3.000m
Length 5.000m x Width 3.000m =
Total =
(15.000 square metres)
Multiplying two linear measurements together gives a square measurement ()

## Slide 12: Area
Irregular shaped areas can be broken down into sections and then added together.
Side 6: 2.1m
Side 4
Side 2: 3.2m
Side 1
Side 5: 2.8m
Side 3: 2.5m
Step 1
Divide the area into two parts, and then calculate the area of each part. The easiest way to do this is to divide it into two smaller sections:
Section A Section B
Side 6: 2.1m
Side 5: 2.8m
Side 1
Side 4
Side 2: 3.2m
Side 3: 2.5m
Step 2
Work out the areas of section A and section B: section A = 2.1 × 2.8 = 5.88m²
section B = 2.5 × 3.2 = 8m²
Step 3
Add the areas of section A and section B together: section A + section B = total floor area
5.88 + 8 = 13.88m²
The total floor area is 13.88m².
Notes: Set Worksheet 38

## Slide 13
Any questions?