## Slide 1: PowerPoint 3: Types of materials used in wall and floor tiling
PowerPoint presentation
Unit 116: Wall and floor tiling

## Slide 2: Aim: To introduce learners to the different types of materials used in wall and floor tiling. Outcomes: At the end of this session, the learner will be able to: Outcome 1: Identify different types of materials associated with a variety of wall and floor tiling activities.
PowerPoint presentation

## Slide 3: Types of materials used for fixing wall and floor tiles
There are many different types of materials in construction that a tiler must know about while fixing wall and floor tiles.
The range of tiling materials looked at here are:
tiles (ceramic and porcelain)
trims (plastic)
adhesives (ready mixed and powder)
grout (ready mixed and powder)
primers and bonding agents
levelling and smoothing compounds
sealants
decoupling membranes.

## Slide 4: Tiles: ceramic
Glazed porous body ceramic tiles consist of a porous bisque body with a decorative glazed surface.
Ceramic tiles are made by dry pressing or extrusion method.
It is important to know that their higher water absorption and low breaking strength make some ceramic tiles not suitable for floors.
Information taken from British Standards.

## Slide 5: Tiles: porcelain
These are highly attractive and very hardwearing tiles that have extremely low water absorbency. Available as wall or floor tiles, sometimes glazed and often with good anti-slip properties, they can be used internally, and providing they are of sufficient slip resistance, externally. These tiles are, depending on thickness, suitable for domestic and commercial use. https://www.tiles.org.uk

## Slide 6: Tile trim (PVC)
A tile trim is an effective and functional method to provide a quality and robust finish to a corner and /or window/door detail.
Tile trim is manufactured in many colours, sizes, shapes and materials.
© 2021 Schlüter-Systems Ltd

## Slide 7: Adhesive
What is the purpose of adhesive?
Tile adhesive is the material that is used to create a mechanical bond between a background surface, such as a wall or floor, and a wall and floor tile.
What is meant by classification of adhesive?
Not all adhesives are manufactured in the same way. The reason for the many types of adhesive is to ensure the correct adhesive is formulated to work with the correct background and tile being used. Slide 8 gives an example of classification.

## Slide 8: Adhesive choice
Adhesive choice is based on tile type, location of tiling and nature of the substrate. Good quality products will carry a classification rating (e.g., C1TE).
https://www.tiles.org.uk
For example, a C1TE rated adhesive means:
Cement-based normal with reduced slip and extended open time.
EN12004 – Types of adhesives | 
C | Cement-based adhesive
D | Dispersion (ready-mixed) adhesive
R | Reaction resin adhesive
S1 | Deformable (flexible) adhesive
S2 | Highly deformable (flexible) adhesive
Classes of adhesives | 
1 | Normal adhesive
2 | Improved adhesive (usually with higher bond strength)
F | Fast-setting adhesive
T | Adhesive with reduced slip
E | Adhesive with extended open time

## Slide 9: Grout
What is the purpose of grout?
Tile grout is the material that is used to fill the joints between wall and floor tiles. This full joint increases the overall strength of the tiling and creates a water-resistant barrier to the background substrate.
Grout is manufactured in different colours that can give an aesthetic finish to the completed tile work.

## Slide 10: Grout types
Grout choice is based on tile type, location of tiling, service condition of the installation and colour preference.
Grout is a material which comes ready mixed or in powdered form. It is the material a tiler applies to the grout lines (joints between the tiles).
As with adhesive, grout has product classifications
The following are descriptions of the product classifications in accordance with the current European Standard EN 13888:
Types of grout:
Pre-mixed
Cement-based
Epoxy
Notes: https://www.tiles.org.uk

## Slide 11: Primer and bonding agent
Before undertaking any tiling work, the tiler must ensure the background has been prepared and the tile adhesive bonds to the background.
To achieve a good quality bond, tilers use primers and bonding agents.
Bonding agent
Bonding agents are used in cement-based mortars and adhesives to improve the physical performance, including adhesion, durability, flexibility, waterproofing and workability.
Primers, stabilise dusty surfaces and reduce the porosity of the background prior to fixing tiles.
Primer (acrylic)

## Slide 12: Levelling/smoothing compounds
Before tiling a floor, the tiler must check the floor which they are tiling for flatness and/or level. The case with existing areas may create an uneven floor surface due to factors such as wear and tear on the floor surface over time.
A tiler must ensure that the floor surface to be tiled is flat. If not, a smoothing/levelling compound can be applied during preparation process.
Self leveller being applied to an uneven surface

## Slide 13: Sealant (silicon)
Sealants are designed to be used in areas where a waterproof seal is needed between two materials.
Silicon sealant
Sealant being applied
to a bath and tile intersection

## Slide 14: Decoupling membranes
Decoupling membranes can be installed in tiling applications to control lateral movement (e.g. drying and shrinkage), and cracking in wall and floor tiling.
Decoupling membranes can be used in wet rooms and underfloor electric heating, on substrates such as concrete, screed and timber flooring.

## Slide 15
Any questions?