## Slide 1: PowerPoint 12: Planning the sequence of work
PowerPoint presentation
Unit 116: Wall and floor tiling

## Slide 2: Aim: To give learners an understanding of technical information and planning involved in wall and floor tiling. Outcomes: At the end of this session, the learner will be able to: Outcome 1: Interpret technical information to plan and set out the sequence of work effectively in relation to a task.
PowerPoint presentation

## Slide 3: Planning the sequence of work
PowerPoint presentation
Construction (tiling) is not just about getting a job done, a large part is about being able to:
interpret different types of technical information
plan and set out the sequence of works effectively
use common problem-solving techniques.

## Slide 4: Types of technical information
PowerPoint presentation
Different types of technical information are used to plan the sequence of work to be undertaken in wall and floor tiling.
Timescales
Drawings
Specifications
Manufacturer’s information
Technical product data
Material schedules
Resources
Instructions
Problem solving
Teamwork
Risk assessments/method statements (RAMS)

## Slide 5: Technical information: timescales
PowerPoint presentation
Work programme
A work programme is a method of showing very easily what work is being carried out on a building and when. The most common form of work programme is a bar chart.
Used by many site agents, or supervisors, a bar chart lists the tasks that need to be done down the left side and shows a timeline across the top. A work programme is used to make sure that the relevant trade is on site at the correct time and that materials are delivered when needed. A site agent or supervisor can quickly tell from looking at the chart if work is keeping to schedule or falling behind.

## Slide 6: Technical information: timescales
PowerPoint presentation
Timescales
Bar charts: the bar, or Gantt, chart is the most popular work programme.
It is simple to construct and easy to understand. Bar charts have tasks listed in a vertical column on the left and a horizontal timescale running along the top.
Time in Days |  |  |  |  |  |  |  |  |  | 
Activity | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Dig for foundation and service routes |  |  |  |  |  |  |  |  |  | 
Lay foundations |  |  |  |  |  |  |  |  |  | 
Run cabling, piping, etc. to meet existing services |  |  |  |  |  |  |  |  |  | 
Build up to damp proof course |  |  |  |  |  |  |  |  |  | 
Lay concrete floor |  |  |  |  |  |  |  |  |  | 

## Slide 7: Technical information: drawings
PowerPoint presentation
Production drawings
These are known as ‘working drawings’ and are used for the purpose of conveying precise constructional information for:
obtaining approval by the client.
obtaining approval by planning and other authorities.
providing information regarding material requirements.
obtaining tenders.
instructing the building contractor and other members of the building team.

## Slide 8: Technical information: drawings
PowerPoint presentation
The working drawings can be classified as:
location drawings
component drawings
assembly drawings.
Location drawings can be further classified into:
block plans
site plans
location plans.

## Slide 9: Technical information: drawings
PowerPoint presentation
Block plans: used to identify the site in relation to the surrounding area.
The scale is usually 1:2500 or 1:1250 and is too small to allow much more than an outline of the site and boundaries, road layouts and the other buildings in the near vicinity.
Brown Road
Plot 1
Plot 3
Plot 2

## Slide 10: Technical information: drawings
PowerPoint presentation
Site plans: used to show the position of the proposed building on the site, together with information on proposed road, drainage and service layouts, and other site information such as levels.
Scales of 1:500 or 1:200 are often used.

## Slide 11: Technical information: drawings
PowerPoint presentation
Location plans: are used to show the size and position of the various rooms within the buildings and to position the principal elements and components.
Scales of 1:5 or 1:100 are often used.

## Slide 12: Technical information: drawings
PowerPoint presentation
Sections: the sectional view of a building will show details which otherwise would not be seen on the plans and elevations.

## Slide 13: Technical information: specifications
PowerPoint presentation
The specification or ‘spec’ is a document produced alongside the plans and drawings and is used to show information that cannot be shown on the drawings.
Specifications are almost always used, except in the case of very small contracts.

## Slide 14: Technical information: specifications
PowerPoint presentation
A specification should contain the following.
Materials description – including type, sizes, quality, moisture content, etc.
Restrictions – what restrictions apply, such as working hours or limited access.
Services – what services are available, what services need to be connected and what type of connection should be used.
Site description – a brief description of the site, including the address.
Workmanship – including methods of fixing, quality of work and finish.
The specification may also name subcontractors or suppliers, or give details such as how the site should be cleared, and so on.

## Slide 15: Technical information: specifications
PowerPoint presentation
An example of a building site specification.

## Slide 16: Technical information: manufacturer’s information
PowerPoint presentation
This information can be found on the packaging. It outlines key aspects that are important to the product being used. Information includes:
material description
weight of the product
use of the product
coverage
mixing
safety warnings
manufacturer’s contact details
application.

## Slide 17: Technical information: technical product data
PowerPoint presentation
A technical data sheet (TDS) is a document provided with a product that lists various pieces of information about the product.
Technical data sheets often include product composition, methods of use, operating requirements, common applications, warnings and pictures of the product.
A technical data sheet may also be known as a product data sheet.

## Slide 18: Technical information: technical product data
PowerPoint presentation
Technical product data sheets are needed whenever a new product is used, as it advises of the COSHH information required for a company's health and safety plan.

## Slide 19: Technical information: resources
PowerPoint presentation
Resources for a tiling job should be identified before starting any work.
Resources include:
tiles
adhesives and grouts
trims, decoupling membranes, fixings, battens and primers
tools and equipment.

## Slide 20: Technical information: instructions
PowerPoint presentation
Instructions can be written and verbal.
Written instructions can be in the form of:
paperwork
forms
plans
diagrams.

## Slide 21: Technical information: problem solving
PowerPoint presentation
Being able to foresee a problem while undertaking tiling work is a skill that is learnt through knowledge and experience.
During the planning phase of any construction work, an understanding of the materials, backgrounds and work being carried out, such as tiling a wet room, is helpful to the tiler in respect of knowing how the sequence of work takes place.
Problem solving can save time, money and produce a better finished work product, benefitting the customer, tiler and/or contractor.

## Slide 22: Technical information: teamwork
PowerPoint presentation
There are many trades involved with construction work.
For example, when tiling a wet room, you may have to coordinate a tiler, plumber, plasterer, carpenter and electrician.
Teamwork is important, to be able to liaise with each other, and using a work programme, such as a Gantt chart, can ensure the work process is seamless so that any problem solving can be worked out in advance or as work proceeds.

## Slide 23: Technical information: RAMS
PowerPoint presentation
Risk assessments/method statements (RAMS)
The Management of Health and Safety at Work Regulations requires every employer to make suitable and sufficient assessment of:
the risks to the health and safety of their employees to which the employees are exposed to while at work.
the risks to the health and safety of persons not in their employment, arising out of or in connection with their work activities.

## Slide 24: Technical information: RAMS
PowerPoint presentation
Risk assessments/method statements (RAMS)
It is vital that you know how to carry out a risk assessment.
Often you may be in a position where you are given direct responsibility for this, and the care and attention you take over it may have a direct impact on the safety of others. You must be aware of the dangers or hazards of any task, and know what can be done to prevent or reduce the risk.
There are five steps to risk assessment.

## Slide 25: Technical information: RAMS
PowerPoint presentation
Risk assessments/method statements (RAMS)
The five steps to risk assessment are:
Step 1: Identify the hazards
Step 2: Decide who might be harmed and how
Step 3: Evaluate the risks and decide on precautions
Step 4: Record your findings and implement them
Step 5: Review your assessment and update if necessary

## Slide 26
Any questions?