## Slide 1: PowerPoint 14: Storing materials and components
PowerPoint presentation
Unit 116: Wall and floor tiling

## Slide 2: Aim: To give students an understanding of the importance of correct storage of wall and floor tiling materials and components. Outcomes: At the end of this session, the student will be able to: Outcome 1: Identify the correct method of storing a range of materials and components. Outcome 2: Identify a range of materials and components relating to storing wall and floor tiling materials. Outcome 3: Have an understanding of considerations needed to be taken when storing wall and floor tiling materials and components.
PowerPoint presentation

## Slide 3: The importance of correct storage Wall and floor tiling, like many other construction operations, requires many materials and components which are susceptible to damage if not stored correctly. Materials are not only expensive but are also produced from natural resources, so care is needed not to produce unnecessary waste which is bad for our environment.
PowerPoint presentation

## Slide 4: Storing different materials and components Wall and floor tiling materials and components are produced and stored in different ways according to the way they are to be used. Different types of materials have different characteristics:
PowerPoint presentation
loose
bagged
boxed
sheet
long lengths
rolled materials
containers and accessories.

## Slide 5: Materials type and storage: loose
PowerPoint presentation
Aggregates
Sand (fine aggregate)
Chippings (coarse aggregate)
Aggregates are usually delivered in tipper lorries, although nowadays 1-tonne bags are available and may be crane handled. The aggregates should be stored on a concrete base, with a fall to allow for any water to drain away.
Stores should be situated away from trees to protect aggregates from becoming contaminated with leaves and litter. It is a good idea to cover aggregates with a tarpaulin or plastic sheets.

## Slide 6: Materials type and storage: loose
PowerPoint presentation
Bulk bags
Concrete base

## Slide 7: Materials type and storage: bagged
PowerPoint presentation
Tile adhesive
Grout
Smoothing compound
Cement
Plaster
Bagged materials are usually available in 25kg bags. The bags are made from multi-wall layers of paper with a polythene liner. Care must be taken not to puncture the bags before use. Each bag, if off-loaded manually, should be stored in a ventilated, waterproof shed, on a dry floor on pallets. If off-loaded by crane, the bags should be transferred to the shed and the same storage method used.

## Slide 8: Materials type and storage: bagged
PowerPoint presentation
Bagged material stored inside and off the ground
Bagged material stored outside and off the ground covered with a plastic sheet

## Slide 9: Materials type and storage: boxed
PowerPoint presentation
Dust masks
Trims
Tiles
Screws
Nails
Nuts and bolts
Many materials and components are packaged to make them easier to store and find. The name, size and number of items is
marked on the package. Storage of boxed items should be placed in a dry area, on shelving, racks or pallets off the ground.

## Slide 10: Materials type and storage: boxed
PowerPoint presentation
Boxed items stored on shelving racks

## Slide 11: Materials type and storage: sheet
PowerPoint presentation
Plasterboard
Plywood
Cement boards
Plasterboard and plywood should be stored in a warm, dry place, stacked flat on timber cross bearers to stop them from sagging and to allow air to circulate. Sometimes sheets are stored on their edge in special racks. They should not be stored leaning against a wall because after a while they may bow.

## Slide 12: Materials type and storage: sheet
PowerPoint presentation
Sheets stored on edge tight to the wall
Sheets stored on edge bearers

## Slide 13: Materials type and storage: long lengths
PowerPoint presentation
Timber
Trim
Pipe
Conduit
Rain water pipes
Timber should be stored horizontally, off the ground, with cross bearers to stop them from distorting and to allow air to circulate.
Where possible, timber should be protected against the weather, either on covered racks or covered with waterproof sheeting.

## Slide 14: Materials type and storage: long lengths
PowerPoint presentation
Timber stored on bearers
Pipes stored on chocks

## Slide 15: Materials type and storage: rolled materials
PowerPoint presentation
Decoupling membrane
Roofing membrane
Plastic sheeting
Damp-proof membrane
This type of material needs to be stored upright to protect them from being crushed by other rolls on top.
They need to be enclosed in a frame to stop them from falling over.

## Slide 16: Materials type and storage: containers and accessories
PowerPoint presentation
Building chemicals, such as primers, bonding agents and sealants, are packaged in containers. They may contain hazardous ingredients so must be stored in a COSHH cabinet.
Tubs of ready-mixed adhesive are easy to stack on top of each other. They should only be stacked four to five tubs high, as the weight of more tubs may crush the lower ones.

## Slide 17: Materials storage: considerations
PowerPoint presentation
When storing store wall and floor tiling materials and components there are eight points to be considered.
1. Location
2. Access
3. Security
4. Shelf life
5. Stock rotation
6. Maintenance of area
7. Identification
8. Transportation

## Slide 18: Materials storage: considerations
PowerPoint presentation
1. Location
Before any work starts, during the planning stage, it is important to work out the best possible place to store your materials: starting with location.
Store materials near the work area.
Store on a flat, clean surface.
Weather proof materials if stored outside.
Do not store in the way of fire escapes and/or access and exits.
Check manufacturer’s instructions for storing the product correctly.

## Slide 19: Materials storage: considerations
PowerPoint presentation
2. Access
A common problem on building sites is ensuring that a delivery can be made safely and on time.
Tiling materials can be delivered by vans and lorries. Where some sites are located via narrow lanes/roads, information should be given to the company delivering the materials to warn them of the possible problem prior to dispatch.

## Slide 20: Materials storage: considerations
PowerPoint presentation
3. Security
Construction sites are easy targets for the opportunist thief: the high value of tiling materials and components can lead to quick and easy profit for the successful thief. Depending on locality, each site will have its own issues of concern.
Construction sites are subject to a number of threats, against which security should be applied by the site operator. These include theft and vandalism.

## Slide 21: Materials storage: considerations
PowerPoint presentation
3. Security (continued)
Theft is common. The high value of building and tiling materials, and the nature of a construction site with its constant change and movement, make this crime tempting for the opportunistic as well as the carefully planned crime.
Vandalism is also common and may occur as a result of political or commercial concerns on the part of the perpetrators as well mindless damage and destruction.

## Slide 22: Materials storage: considerations
PowerPoint presentation
4. Shelf life
Wall and floor tiling materials, like many other building materials, have a shelf life. This means that, from the time the product is manufactured, it is given a ‘best before end’ date in which to use the product.
Materials can go out of date.

## Slide 23: Materials storage: considerations
5. Stock rotation
Using materials that are out of date may cause problems with adhesives and grouts, such as increased setting times, not setting to its full strength, liquids and solvents drying out and separating, warping and shrinkage etc.
Before purchasing any materials, or when they are being delivered, dates on the packaging should be checked.
A good materials supplier (builders merchant) would rotate stock in conjunction with their deliveries. This is good material management. It means older stock is brought to the front of the shelf/display and newer stock is placed behind

## Slide 24: Materials storage: considerations
PowerPoint presentation
6. Maintenance of area
A work area should be cleaned regularly while carrying out tiling work in order to maintain a safe working environment.
The working area will contain tile debris, tools, equipment and some/all of the materials required for the work.
Careful planning is required to ensure that fire escapes, access and egress are kept clear and that materials are stored/stacked correctly.

## Slide 25: Materials storage: considerations
PowerPoint presentation
7. Identification
Most tiling materials are easy to identify visually. But it is important to identify them to know which material is the correct one to use.
Identification is found on the packaging in the form of batch numbers and codes and product name.
Tiles use batch numbers to identify the tile is of the correct colour, and codes to inform us of the material and type of tile. The product name will identify the product range and information on the packaging will advise on size, weight, use by date, safety data etc.

## Slide 26: Materials storage: considerations
PowerPoint presentation
8. Transportation
There could be access problems with getting to the site itself. In busy towns and cities parking restrictions, one-way streets and congestion charges need to be factored into the access and delivery plan.
There might also be access problems in the building you are working in, such as navigating around other trades working in/on the access route to the work area, or getting heavy materials up many floors, which means a hoist or crane time may be needed.

## Slide 27
Any questions?