## Slide 1: PowerPoint 4: Types of tools and equipment used in wall and floor tiling activities
PowerPoint presentation
Unit 116: Wall and floor tiling

## Slide 2: Aim: To introduce learners to the different types of tools used in wall and floor tiling. Outcomes: At the end of this session, the learner will be able to: Outcome 1: Identify hand tools and equipment (slide 3 to 28). Outcome 2: Identify power tools and equipment (slide 29 to 32). Outcome 3: Identify ancillary equipment (slide 33 to 42).
PowerPoint presentation

## Slide 3: Types of hand tools used in wall and floor tiling
https://www.merriam-webster.com
Definition of a hand tool
A small tool (such as a hammer or wrench) that usually does not use electricity.
What is meant by a hand tool?

## Slide 4: Basic tiling hand tools
Hand-operated tile cutter
Serrated tiling trowel
Bucket trowel
Tile wheel nippers/nippers
Sealant gun
Tile saw
Hammer(s)
Carborundum stone/rubbing block
Scribers
Mitre block
Spirit level
Chisels
Tile file
Trimming tool (tile trim cutter)
Hacksaw
Screwdrivers
Retractable knives
Tape measure/rule
Chalk line
Square
Squeegee
Grout float
Wash boy and sponge float
Scraper

## Slide 5: Types of hand tools used in wall and floor tiling
Hand-operated tile cutter
Used for cutting straight cuts in ceramic and porcelain tiles.

## Slide 6: Types of hand tools used in wall and floor tiling
Serrated tiling trowel
Used for applying tile adhesive to background surfaces.

## Slide 7: Types of hand tools used in wall and floor tiling
Bucket trowel
Sometimes referred to as a mud trowel.
These trowels are used to move adhesive and grout from inside buckets. They can have rounded corners minimise drag on bucket walls.

## Slide 8: Types of hand tools used in wall and floor tiling
Tile wheel nippers/nippers
Ideal for cutting awkward shapes in tiles, such as around pipes.

## Slide 9: Types of hand tools used in wall and floor tiling
Sealant gun
A sealant gun is used with a tube of sealant to apply a waterproof seal between materials.

## Slide 10: Types of hand tools used in wall and floor tiling
Tile saw
Used for cutting notches and semi-circles in ceramic tiles.
https://vitrex.co.uk

## Slide 11: Types of hand tools used in wall and floor tiling
Hammers
There are many types of hammers used in construction.
Tilers use mallets, claw hammers and lump hammers.
Mallet
Claw hammer
Lump hammer

## Slide 12: Types of hand tools used in wall and floor tiling
Carborundum stone/rubbing block
A rubbing block is used for smoothing the rough edge of a ceramic tile after cutting.
It has two sizes of grit: one rough side and one smooth side.

## Slide 13: Types of hand tools used in wall and floor tiling
Scribers
A tile scriber, sometimes referred to as a scorer, is a hand-held pencil shape tool used to scratch the glazed surface of a ceramic tile for cutting to a measured size.
https://www.vitrex.co.uk

## Slide 14: Types of hand tools used in wall and floor tiling
Mitre block
A mitre block, sometimes referred to as a mitre box, is a piece of equipment used by tilers to cut tile trims to 45 and 90 degree angles.
It is used in conjunction with a hacksaw.

## Slide 15: Types of hand tools used in wall and floor tiling
Spirit level
A spirit level, bubble level or simply a level, is an instrument designed to indicate whether a surface is horizontal (level) or vertical (plumb).

## Slide 16: Types of hand tools used in wall and floor tiling
Chisels
Chisels are used to cut through stone, brick and concrete. Tilers use chisels to chip up floor and wall tiles and during preparation works prior to tiling.

## Slide 17: Types of hand tools used in wall and floor tiling
Tile file
A tile file is used to smooth rough edges and shape tiles. When shaping tiles, files should only be used to remove small amounts as they work very slowly.

## Slide 18: Types of hand tools used in wall and floor tiling
Trimming tool (tile trim cutter)
Tile trim cutting tools are good for cutting PVC (plastic) trim (not for metal trim).
https://www.protilertools.co.uk

## Slide 19: Types of hand tools used in wall and floor tiling
Hacksaws (junior hacksaw)
A hacksaw is a fine-toothed saw, originally and principally made for cutting metal. Tilers use junior hacksaws for cutting PVC and metal trims, and large hacksaw blades can be changed for ceramic tile type cutting blades.

## Slide 20: Types of hand tools used in wall and floor tiling
Screwdrivers
Screwdrivers form an important part of a tiler’s tool kit, as on-site repairs and alterations to tile cutters and materials are often needed.
An assortment of sizes from PZ1, PZ2 and PZ3 are common in screws used on site.

## Slide 21: Types of hand tools used in wall and floor tiling
Retractable knives
Retractable knives, sometimes known as utility knives, are used by tilers to open packaging, sharpen pencils and cut decoupling membranes, as well as having many other uses.

## Slide 22: Types of hand tools used in wall and floor tiling
Tape measure/rule
Tape measures are one of the most important pieces of a tiler’s tool kit.
Used for measuring tile cuts and setting out tile work.
A steel rule is shorter but can also be used as a straight edge for marking tile cuts.

## Slide 23: Types of hand tools used in wall and floor tiling
Chalk line (and chalk)
A chalk line consists of a string line fixed in a container of chalk.
When the string is pulled tight against a wall or floor then let go, coloured chalk is transferred to the background surface.
It is an important tool for setting out tiling work.

## Slide 24: Types of hand tools used in wall and floor tiling
Square
Used for marking and measuring materials. The square refers to the tool's primary use of measuring the accuracy of a right angle (90 degrees).

## Slide 25: Types of hand tools used in wall and floor tiling
Squeegee
A large squeegee has a long rubber blade and is used for fast grouting of large tile areas
https://www.vitrex.co.uk

## Slide 26: Types of hand tools used in wall and floor tiling
Grout float
Grout floats are the tools used to apply grout to the joints between installed tilework.
The tool design ensures a full compact grout joint.

## Slide 27: Types of hand tools used in wall and floor tiling
Wash boy and sponge float
Consisting of a bucket, sponge float and rollers,
a wash boy is designed for fast and efficient cleaning of tile work after application of grouting, to achieve a clean finished tiled work product.
https://www.vitrex.co.uk/

## Slide 28: Types of hand tools used in wall and floor tiling
Scraper
A scraper is a simple but effective tool used by tilers for preparing backgrounds and for cleaning work.
Scrapers can be hand-held, for smaller jobs, and there are large-handled types for cleaning floors.

## Slide 29: Types of power tools used in wall and floor tiling
Tiling power tools
Electric tile cutter
Mixing paddle and drill
Cordless drill

## Slide 30: Types of power tools used in wall and floor tiling
Electric tile cutter
For straight and awkward tile cutting using a diamond cutting wheel.
These cutters use water to suppress dust, aid cutting and to keep the cutting wheel cool.
Advisable to use a 110v machine and to follow risk assessments.
Training is needed to operate and maintain an electric tile cutter.

## Slide 31: Types of power tools used in wall and floor tiling
Mixing paddle and drill
A mixing drill is a powerful tool designed for the purpose of mixing tile adhesives, self levelling compounds and grouts (if a large volume is required). It is advisable to use a 110v machine and to follow risk assessments.
Training is needed to operate and maintain an electric mixing drill.

## Slide 32: Types of power tools used in wall and floor tiling
Cordless drill
A cordless drill/driver is a versatile tool that's designed to drill holes and drive screws. Its keyless chuck accepts a wide variety of round- and hex-shank drill bits and screw-driving bits, as well as hole saws, rotary sanders, wire-wheel brushes, and other accessories.
As battery technology improves, a cordless drill is a safer option than a corded drill.

## Slide 33: Ancillary equipment used in wall and floor tiling
Sponge
Roller and tray
Brushes
Fixing batten/rule
Nails/screws
Polishing cloths
Buckets
Moving and handling aids
Protective sheets

## Slide 34: Ancillary equipment used in wall and floor tiling
Sponge
When grouting tiling work, a tiler will require a good quality sponge for cleaning excess grout from the surface of the fixed tilework.
A tiler’s sponge needs to be firm and free of defects that could damage the grout finish.
Sharp square edges provide access to internal grouting areas.

## Slide 35: Ancillary equipment used in wall and floor tiling
Roller and tray
A roller and tray can be used by a tiler to apply primers, sealers and waterproof tanking to wall and floor backgrounds/substrates.

## Slide 36: Ancillary equipment used in wall and floor tiling
Brushes
An essential part of being a tiler is cleaning your work area thoroughly.
You need to have the appropriate sweeping and hand brushes and dust pans to ensure a clean and safe working environment.

## Slide 37: Ancillary equipment used in wall and floor tiling
Fixing batten/rule
Batten/rule provides a support at the correct datum level for the first row of tiles during installation.
Battens can be timber or aluminium (tile tracker).

## Slide 38: Ancillary equipment used in wall and floor tiling
Nails/screws
Tilers use a variety of screws and nails.
There are many different types used in construction, but commonly used are PZ1, PZ2 and PZ3.

## Slide 39: Ancillary equipment used in wall and floor tiling
Polishing cloths
Polishing cloths give newly grouted wall and floor tiles a clean finished polished look.

## Slide 40: Ancillary equipment used in wall and floor tiling
Buckets
Buckets are used for carrying water and mixing adhesives and grout.

## Slide 41: Ancillary equipment used in wall and floor tiling
Moving and handling aids
A wheel barrow, shovel, sack truck, platform truck and pallet truck are all devices used to move heavy and awkward loads.

## Slide 42: Ancillary equipment used in wall and floor tiling
Protective sheets
When working in an existing building, there are items, such as carpets, kitchen worktops and bathroom sanitaryware, that need to be protected. Tilers use sheet materials to cover these fixtures and fittings.
Dust sheets

## Slide 43
Any questions?