## Slide 1: PowerPoint 9: Tools and equipment used in wall and floor tiling
PowerPoint presentation
Unit 116: Wall and floor tiling

## Slide 2: Aim: To give learners an understanding of preparing tools and equipment used for a wall and floor tiling scenario. Outcomes: At the end of this session, the learner will be able to: Outcome 1: Identify and describe the correct tools and equipment needed to tile a wall.
PowerPoint presentation

## Slide 3: Tools and equipment used in wall and floor tiling
You have been tasked with tiling a kitchen splashback (scenario).
The following slide identifies tools and equipment that may be required to complete this activity.
See Worksheet 22.

## Slide 4: Basic tiling hand tools
Hand-operated tile cutter
Serrated tiling trowel
Bucket trowel
Tile wheel nippers/nippers
Sealant gun
Tile saw
Hammer(s)
Carborundum stone/rubbing block
Scribers
Mitre block
Spirit level
Chisels
Tile file
Trimming tool (tile trim cutter)
Hacksaw
Screwdrivers
Retractable Knives
Tape measure/rule
Chalk line
Square
Squeegee
Grout float
Wash boy and sponge float
Scraper

## Slide 5: Basic tiling hand tools
Hand-operated tile cutter
These cutters consist of a scoring wheel which cuts into the surface glaze and provides a line for the tile to be cut along using pressure from the breaker.
https://vitrex.co.uk

## Slide 6: Basic tiling hand tools
Serrated tiling trowel
A serrating trowel, sometimes referred to as a notched trowel, is used by a tiler to apply tile adhesive to a background surface.
Because of the many different sizes of tiles available, the tiler must use the correct size of notch related to the size of tile being used.

## Slide 7: Basic tiling hand tools
Bucket trowel
Bucket trowels come in varying sizes and shapes, used by many wet trades.

## Slide 8: Basic tiling hand tools
Tile wheel nippers/nippers
The wheels on some designs are for scoring porcelain and ceramic tiles can double up as a breaker when pressed together on the tile.

## Slide 9: Basic tiling hand tools
Sealant gun
Tilers use sealant guns to apply a waterproof seal around baths and showers, as well as kitchen worktops and internal corners in wet areas.

## Slide 10: Basic tiling hand tools
Tile saw
The blades are changeable and only suitable for cutting ceramic tiles.
https://vitrex.co.uk

## Slide 11: Basic tiling hand tools
Hammer(s)
For tilers involved in refurbishment/renovation works, having a variety of hammers in a tool kit can help make a tiling project easier to work on. Mallets and hammers are used for removing tiles and nails.
Mallet
Claw hammer
Lump hammer

## Slide 12: Basic tiling hand tools
Carborundum stone/rubbing block
It has two sizes of grit: one rough side and one smooth side.
Good for use on ceramic tiles.

## Slide 13: Basic tiling hand tools
Scribers
A low quality scribe can be difficult to use as the tip needs to be hardened enough to penetrate the glaze.
https://www.vitrex.co.uk

## Slide 14: Basic tiling hand tools
Mitre block
Tilers use these to cut tile trims around windows, doors, and columns.

## Slide 15: Basic tiling hand tools
Spirit level
Tilers use levels for checking surfaces, setting out centrelines, installing battens, transferring datums and generally checking work as it proceeds

## Slide 16: Basic tiling hand tools
Chisels
Chisels can also be SDS type used in mechanical drills used for heavy duty removal.

## Slide 17: Basic tiling hand tools
Tile file
Good for shaping ceramic tiles.
Only used for removing small amounts of ceramic tile material.

## Slide 18: Basic tiling hand tools
Trimming tool (tile trim cutter)
This tool can only cut flat trim and not upright trim. It is used inside window and door openings where a hacksaw and mitre box is needed.
https://www.protilertools.co.uk

## Slide 19: Tools and equipment used in wall and floor tiling.
Hacksaws (junior hacksaw)
This is used in conjunction with a mitre box to cut tile trim.

## Slide 20: Basic tiling hand tools
Screwdrivers
A tiler may use a screwdriver for various operations during work on site.

## Slide 21: Basic tiling hand tools
Retractable knives
Used by tilers to open packaging, sharpen pencils and cut decoupling membranes.

## Slide 22: Basic tiling hand tools
Tape measure/rule
Used for setting out and measuring for cutting tiles.

## Slide 23: Basic tiling hand tools
Chalk line (and chalk)
An important tool for setting out tiling work, such as providing a visible line between datums to aid the tiler when fixing setting out battens.

## Slide 24: Basic tiling hand tools
Square
Tilers use squares to set out centre lines prior to tiling floors, or marking an electric back box position on a tile.

## Slide 25: Basic tiling hand tools
Squeegee
Simple to use in the application of grout to tile joints.
https://www.vitrex.co.uk

## Slide 26: Basic tiling hand tools
Grout float
The sponge or rubber surface will ensure the tile does not get scratched when applying grout to installed tilework.

## Slide 27: Basic tiling hand tools
Wash boy and sponge float
This has a large surface area, so it is good for use on large, newly grouted tile areas.
https://www.vitrex.co.uk/

## Slide 28: Basic tiling hand tools
Scraper
A simple but effective tool used by tilers for preparing backgrounds and cleaning work.

## Slide 29: Tiling power tools
Electric tile cutter
Mixing paddle and drill
Cordless drill

## Slide 30: Tiling power tools
Electric tile cutter
Used mainly for cutting awkward shapes in tiles, such as around sockets.

## Slide 31: Tiling power tools
Mixing paddle and drill
Tilers use these machines for mixing large volumes of tile adhesives and grouts.

## Slide 32: Tiling power tools
Cordless drill
Tilers will use a cordless drill to cut core holes, and screw battens to walls.

## Slide 33: Ancillary equipment
Sponge
Roller and tray
Brushes
Fixing batten/rule
Nails/screws
Polishing cloths
Buckets
Moving and handling aids
Protective sheets

## Slide 34: Ancillary equipment
Sponge
Used to clean off excess grout from tilework

## Slide 35: Ancillary equipment
Roller and tray
Used by tilers to prepare backgrounds with primers prior to fixing tilework.

## Slide 36: Ancillary equipment
Brushes
Often referred to as good housekeeping, using a brush maintains a clean and safe working environment.

## Slide 37: Ancillary equipment
Fixing batten/rule
Traditionally, timber is used and fixed to the background with nails or screws.
For masonry backgrounds, a hammer drill and masonry drill bit is needed.

## Slide 38: Ancillary equipment.
Nails/screws
These are used to fix a variety of tiling components such as cement boards and fixing battens.

## Slide 39: Ancillary equipment
Polishing cloths
Cloths should be free of dirt and soft enough not to scratch the tiles.

## Slide 40: Ancillary equipment
Buckets
Buckets are used for mixing and carrying adhesive, grout and water.

## Slide 41: Ancillary equipment
Moving and handling aids
Using handling aids can help prevent strains and spinal injuries.

## Slide 42: Ancillary equipment
Protective sheets
Ply can be used to protect kitchen worktops, and dust sheets can be used to cover carpets.
Dust sheets

## Slide 43
Any questions?