## Slide 1: Post-1919 painting and decorating
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
identify the different materials, tools and techniques used in the painting and decorating trade post-1919.

## Slide 3: Introduction
Post-1919 home design and painting and decorating style was Art Deco and Bauhaus inspired.
As the different types of paint available evolved to include emulsions, the colours available for the home increased dramatically.
The use of wallpaper increased as printing became mechanical and was mass produced, which made it readily available.
Power tools were becoming more popular and more efficient during the preparation process.

## Slide 4: Post-1919 paint material types (interior)
Non-vinyl emulsions
Original non-vinyl emulsions
Vinyl emulsions
Vinyl matt, silk and mid-sheen emulsions replaced the non-vinyl versions
Alkyd coatings
Alkyd coatings modified with linseed oil
Clear varnishes
Polyurethane and alkyd varnishes
The use of lead in paint manufacture was banned in 1992.

## Slide 5: Post-1919 paint material types (exterior)
Masonry paint
Acrylic exterior emulsions
Solvent-based pliolite resin coatings
Exterior gloss
Alkyd coatings modified with linseed oil.
Clear varnish
Alkyd exterior varnishes
Preservative woodstain
Alkyd exterior preservative
Protective woodstain
Alkyd exterior woodstain

## Slide 6: Post-1919 paint manufacture (water-based paint)
Mix a base containing extenders, pigments, preservatives and water.
Disperse at high speed.
Transfer base to finishing tank.
Add vinyl copolymer.
Add coloured pigments, then test colour.
Wikimedia photograph by Cjp24 under CC 3.0
Image of an industrial disperser
Deluxe Trade Vinyl Matt can
Notes: https://ijrorwxhmjkkll5p.leadongcdn.com/cloud/lqBpiKiqlqSRoiokpipliq/disperser.jpg

## Slide 7: Post-1919 paint manufacture (solvent-based paint)
Mix a base containing extenders, pigments, oil/resin.
Disperse at high speed.
Transfer base to finishing tank.
Add solvents and driers.
Add coloured pigments, then test colour.
Image of an industrial disperser
Image of a liquid drier
Crown Trade Full Gloss can
Notes: https://ijrorwxhmjkkll5p.leadongcdn.com/cloud/lqBpiKiqlqSRoiokpipliq/disperser.jpg
https://www.brewers.co.uk/product/BN06063Q

## Slide 8: Post-1919 wallpaper manufacture
Vinyl paper
Produced by laminating a film of PVC to a base paper then printing with heat-infused PVC inks
Wide-width vinyl paper
Wider-width commercial version of a vinyl wallpaper
Supplied in rolls of 30m × 1.3m
Blown vinyl paper
Produced by heat expansion process, before embossing
Image of vinyl paper
Image of blown vinyl paper
Notes: https://ae01.alicdn.com/kf/S204876a3c27143cdbb46841c8bad6aa6f/Metallic-Black-Plain-Faux-Grasscloth-Textured-Wallpaper-Vinyl-Solid-Color-Dark-Grey-Wall-Paper-Bed-Room.jpg
https://coveryourwall.co.uk/products/anaglypta-luxury-vinyl-amber-rd838

## Slide 9: Post-1919 wallpaper printing techniques
Block printing
Flexographic printing
Rotogravure printing
Silk screen printing
Rotary screen printing
Flatbed silk screen printing
Image of flexographic block printing machine
Image of rotogravure printing machine
Images of rotary screen printing machine
Image of flatbed screen printing machine
Notes: https://www.chprintingmachinery.com/professional-factory-for-flexo-block-making-machine-8-colour-stack-type-flexo-printing-machine-changhong-3-product/
http://witymachinery.com/2-1-gravure-printing-4.html
https://presscity.com/en/machines/chambon/15543-18695/komori-chambon-ic650.html
https://www.indiamart.com/proddetail/flat-bed-screen-printing-machine-2788480473.html

## Slide 10: Post-1919 preparation tools and equipment
Steam stripper
Electrically operated equipment that produces steam to enable easy removal of difficult wallpapers
Electric sanders
Electrically operated sanding equipment with operating belts/pads of abrasive paper make preparation process more efficient
Electric heat guns
Electrically operated paint stripping equipment.
Chemical paint strippers
Dichloromethane type chemical paint stripper

## Slide 11: Post-1919 preparation materials
Decorator’s caulk
Flexible acrylic gap filler for gaps between walls, trims and at angles
Two-pack filler
Two-part epoxy filler for more permanent repairs in wood and metal
Plaster-based cellulose filler
Plaster-based powder filler for interior walls and ceilings
Fine surface filler
A synthetic emulsion-based grain filler for finer surface irregularities

## Slide 12: Post-1919 wallpaper adhesive application
Wallpaper adhesive application evolved in the 20th century to include:
roller application
pasting machines
pre-pasted vinyls
non-woven paste-the-wall wallpapers.
Example of easy paste wallpaper machine
Example of roller scuttle kit
Image of Pollycell mixed adhesive
Notes: https://www.amazon.co.uk/Coral-Tools-61701-Wallpaper-Wallcoverings/dp/B00C7XAJNQ
https://www.duluxdecoratorcentre.co.uk/Dulux-Decorator-Centre-Woven-Polyamide-Roller-Scuttle-Kit-9
https://source.thenbs.com/product/polycell-trade-ready-mixed-adhesive/wbbT59utBKyR6UMWhi76W9/rgCBs22q2WwJwU5eykNRnt

## Slide 13: Post-1919 paint application techniques
Although paint finishes in the late 1900s were moving towards roller application, brushes were still used for the most part.
Smoother finish achieved with synthetic filament brushes
Most suitable for applying water-based and solvent-based paint and varnish to walls, ceilings, woodwork and trims
Economical with little splashing
Cheapest option for equipment
Slow and laborious for application to large areas
Excessive brush marks (ropiness) when natural bristle brushes are used to apply water-based coatings

## Slide 14: Post-1919 paint application techniques
Paint roller application
Two to three times faster than by brush
Most suitable method for applying water-based and solvent-based paints to large flat areas
Applies a thicker coating
No brush marks
Extension poles reduce the need for scaffold
Splashes/overspray
No accuracy/needs to be cut in to adjacent surfaces
Orange peel can be produced if incorrect roller sleeve and incorrect paint viscosity used
Cleaning can be time-consuming

## Slide 15: Post-1919 paint application techniques
Conventional spray systems
Conventional or air spraying is the earliest, most traditional method of paint application.
This uses compressed air to both suck the paint from a pressure pot and to atomise the stream of paint as it exits the nozzle of the spray gun.
When the trigger is pressed, the paint is sucked into the compressed air stream and is released into a fine spray.
It was developed in US in the early 1900s and became popular in the 1940s.
Image of a paint pressure tank with spray gun
Notes: https://www.amazon.co.uk/Commercial-Gallon-Paint-Pressure-Assembly/dp/B002ABWVRM

## Slide 16: Post-1919 paint application techniques
HVLP spray systems
High volume, low pressure (HVLP) means a high volume of air distributed at a low pressure.
The paint coating is atomised within the spray gun, before being blown onto the surface by compressed air produced by the turbine/compressor.
HVLP equipment became popular during the 1970s.
It is used to apply paint coatings to smaller areas (such as doors).

## Slide 17: Post-1919 paint application techniques
HVLP spray application
Four to five times faster than by brush
Most suitable for applying water-based and
solvent-based paints to smaller areas such as
doors and windows
Not suitable for heavy bodied, viscous paints
High-quality finish
No brush or roller marks
High overspray
Needs masking
Respirators/LEV equipment required
Paints need straining/thinning
Expensive purchase and maintenance of
equipment
Cleaning equipment time consuming

## Slide 18: Post-1919 paint application techniques
Airless spray systems
Airless spraying machines pump the paint under high pressure by forcing the liquid coating through a narrow opening and creating pressure (approximately 250 BAR) through to the spray gun.
The action is similar to a pressure washer, but with paint instead of water.
Example image
Notes: https://www.sprayfinishingsolutions.com/wp-content/uploads/2017/08/1007-17C336-1.jpg

## Slide 19: Post-1919 paint application techniques
Airless spray application
Approximately 30 times quicker than by brush
No air or air compressor required
No need to adjust the paint viscosity before application
Lower overspray
Thicker, more even application
More suitable for larger areas
Hazardous
Increased material volume – spraying uses about 33% more paint than a roller
Cannot be touched up
Expensive equipment cost initially

## Slide 20: Post-1919 paint application techniques
Electrostatic spray system
In electrostatic spraying (or powder coating), the equipment charges the paint particles with high voltage, causing them to be attracted to the surface to be coated and to actually wrap around it, which increases transfer efficiency.
The object being painted receives an opposite charge or is grounded.
Example image
Notes: https://anestiwata.com/wp-content/uploads/2012/01/aElectrostatic-E-M15B-solvent.jpg

## Slide 21
Any questions?