## Slide 1: Pre-1919 painting and decorating
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session, learners will be able to:
identify the different materials, tools and techniques used in the painting and decorating trade pre-1919.

## Slide 3: Introduction
Pre-1919 painting and decorating looked very different to the way it does today in the 21st century.
All tools were handmade using locally sourced materials, before the introduction of high carbon steel and precision plastics, so had to be maintained to prevent deterioration.
All paint materials were mixed by hand, using locally sourced natural, raw materials.
The techniques used in decorating buildings (such as spraying equipment) were all manual before the introduction of machinery.
The first mass-produced wallpapers were produced in approximately 1839 and pasted by hand before hanging.

## Slide 4: Pre-1919 paint material types
Limewash
Powdered slaked lime mixed with water before application to building exteriors
Linseed-oil house paint and varnish
Hardwearing oil-based paint made from linseed oil
White lead paints
Traditional paints contained lead as a pigment to provide added protection on external surfaces
Distemper
Water-based powder paints based on slaked lime, whiting or chalk mixed with casein or animal fats
https://www.lincolnshirelime.co.uk/120l-lincolnshire-lime-limewash---white-2278-p.asp

## Slide 5: Pre-1919 wallpaper types
Traditional fabrics, tapestries and weaves hung as wall art formed the basis for modern wallpaper.
Lincrusta Walton
Deeply embossed wall hanging manufactured from linseed oil putty on a heavy base paper
Woolstrand/hessian wallpaper
Fabric wall hangings woven from strands of natural jute or wool
Anaglypta/supaglypta papers
Produced by dry embossing and wet
embossing processes
Hand-printed ground wallpaper
Plain pulp papers hand-printed then coated with casein glue
Wikimedia Commons
Collection: Metropolitan Museum of Art at https://commons.wikimedia.org/wiki/File:The_Triumph_of_Fame_MET_DT4292.jpg
Example of Hessian fabric
Example of Lincrusta Walton wallpaper
Example of Anaglypta wallpaper
Notes: Images:
https://www.janeclayton.co.uk/lincrusta-italian-renaissance-wallpaper-paintable-rd1952fr/?gad=1&gclid=CjwKCAjwkeqkBhAnEiwA5U-uM2R4DQhlGK7ZKETP7EYpFGFCvb3xcW9vJOLrjKhQq4-ZYfupgTcYohoCDHkQAvD_BwE
https://www.fabricgiant.com/product/Fashion Fabrics/Hessian Fabric/FG-HES-002
https://www.gowallpaper.co.uk/anaglypta-original-wallpaper-dryden-rd335.html?utm_source=google_shopping&gclid=Cj0KCQjwz8emBhDrARIsANNJjS7gQTVKkT4h9P04B9q1x3K7uXBiyig5Rym16hrsd6Vpl5Hocq2gzCEaAgBNEALw_wcB

## Slide 6: Pre-1919 Wallpaper printing techniques
Block printing
Block printing by hand
Silk screen printing
Silk screen printing by hand
Example image
Notes: https://cdn11.bigcommerce.com/s-7psb023nit/images/stencil/original/products/8919/13864/107883_3__50775.1682003040.jpg

## Slide 7: Pre-1919 preparation tools and materials
Sandpaper
All abrading pre-1919 done by hand, using the original abrasive paper – silica sand particles bonded to card using casein glue
Cast-iron shave hook
Traditional paint scraper hand-crafted
from cast iron
Paraffin blow torch
Any loose flaking paint coatings traditionally removed using these
Linseed oil putty
Traditional glazing compound and stopper made from linseed oil and whiting

## Slide 8: Pre-1919 preparation materials
Pumice/soda blocks
Traditional organic powdered/solid abrasive
Alabastine filler
Traditional single-pack plaster-
based filler for interior repairs
Sand and cement/lime mortars
Traditional cement/lime mortars
for exterior repairs
Image of an alabastine filler
Image of a soda block
Image of a lime hydraulic bag
Image of a sand cement mortar bag
Notes: Images:
https://www.cromwell.co.uk/shop/abrasives/hand-sanding-blocks/c/091506
https://www.brewers.co.uk/img/product/nc1008h/nc1008h-alabastine-filler-1-8kg-interior-fillers-11689.jpg?v=1454538625
https://www.dwnye.co.uk/shop/natural-hydraulic-lime-nhl35-25kg-bag
https://www.howarth-timber.co.uk/hanson-sand-cement-mortar-plastic-handy-bag-20kg/

## Slide 9: Pre-1919 application tools and equipment
Horsehair paintbrushes
Paintbrushes hand-crafted using a horsehair filling
Pure bristle paintbrushes
Paintbrushes hand-crafted using natural bristle from wild boars from China and India
Washing-down brushes
Cheaper-quality brushes made using a fibre filling for washing down or applying cement/lime paints externally
Image of a pure thistle paintbrush
Horsehair paintbrush
Notes: https://i.ebayimg.com/thumbs/images/g/ItEAAOSwON9iYeCJ/s-l300.jpg

## Slide 10: Pre-1919 paint application techniques
All paint finishes pre-1919 were generally applied by brush.
Smoother finish achieved with synthetic filament brushes
Most suitable for applying water-based and solvent-based paint and varnish to walls, ceilings woodwork and trims
Economical with little splashing
Cheapest option for equipment
Slow and laborious for application to large areas
Excessive brush marks (ropiness) when natural bristle brushes were used to apply water-based coatings
Follow this link to learn about the Components of a Paintbrush
Notes: https://road-to-learning.com/2021/01/21/components-of-a-paintbrush/

## Slide 11: Pre-1919 wallpaper application techniques
Wall hangings
Fabrics, tapestries and weaves were normally pinned to the wall.
Wallpapers
The first mass-produced wallpapers included selvedges to protect the edges and were designed to be trimmed off prior to hanging using a track trimmer.
They were hung using flour pastes or glue made from animal fats.
Trimming was generally carried out using cast iron shears.
Learn more at A brief history of wallpaper.
Image of a vintage trimmer
Wikimedia Commons
Collection: Metropolitan Museum of Art at https://commons.wikimedia.org/wiki/File:The_Triumph_of_Fame_MET_DT4292.jpg
Example image of a vintage wallpaper
Notes: https://multibriefs.com/briefs/exclusive/brief_history_of_wallpaper.html
Images:
https://www.etsy.com/listing/1219961911/vintage-floral-wallpaper-antique-flowers
https://www.picclickimg.com/aPkAAOSwwlZjRakk/Vintage-RIDGELY-TRIMMER-Handheld-Wall-Paper-Cutter.webp

## Slide 12: Pre-1919 traditional specialist techniques
Graining and marbling techniques
Traditionally, expensive hardwood and marble furniture and components were desirable, so imitating expensive hardwoods onto inexpensive items was common practice.
These techniques were executed using mediums such as stale beer, vinegar and linseed oil using organic pigments.
Image of a worker graining furniture

## Slide 13
Any questions?