## Slide 1: 21st-century painting and decorating
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
identify the different materials, tools and techniques used in the painting and decorating trade in the 21st century.

## Slide 3: Introduction
21st-century painting and decorating is what we are currently seeing within the trade. However, the 21st century is still in its infancy and the future of paint and its application is still evolving.
21st-century technology includes paint materials that:
are more sustainable and eco-friendly
have more than one primary function
have selection processes that are up to date with modern technology
have application methods that are up to date with modern technology.
Image of a commercial painting drone
Notes: https://www.ddcoatings.co.uk/2640/commercial-painting-drones

## Slide 4: 21st-century paint material types
Acrylic emulsions
Scrubbable matt emulsions
Acrylic eggshells
Acrylic copolymer coatings
Multi-surface/multi-purpose paints
Hybrid/blended coatings
Water-based alkyd coatings
Fully acrylic finishes
Acrylic gloss, eggshell and flat matt finishes
For more information on hybrid paints see: Hybrid Paints
Image of Fully Acrylic finishes
Image of AllCoat Exterior Satin
Notes: Hybrid Paints - https://www.elegantpainting.com/hybrid-paints-the-best-of-both-worlds/#:~:text=What%20are%20Hybrid%20Paints%3F,based%20and%20water%2Dbased%20paints
Images:
https://m.media-amazon.com/images/I/71Auk7ThHML._AC_SL1500_.jpg
https://images.ctfassets.net/j001bqnk84dk/6NyxIFeadQlhLqzAJlRWYn/b12f15d308e9aa7196255dd4a1310898/product_641.png?fm=webp&w=868&h=551

## Slide 5: 21st-century paint colour selection
Colour selection apps
Modern colour selection phone applications are available to transform the way we choose colours.
Take a photograph of the room to be re-decorated and upload to see an augmented reality representation of the room.
See what the room will look like painted in any the full range of 2,000 available colours.
Learn more by clicking this link!
Notes: Dulux visualizer app - https://www.dulux.co.uk/en/articles/dulux-visualizer-app

## Slide 6: 21st-century preparation tools and equipment
Infra-red paint stripper
Electrically operated paint stripping equipment that produces infra-red heat at lower temperatures
Suitable for stripping lead-based coatings
Vacuum-assisted sanding equipment
Dust-less, vacuum-assisted sanding equipment for walls, ceilings and trims
Example of a wall sander and dust extractor
Example of an orbital sander
Example of an infra-red paint stripper
Notes: https://linseedpaint.com/speedheater-cobra/
https://mirka-online.com/miw950-de1230afc-4-mirka-leros-dust-free-solutions-kit-9in-wall-sander-dust-extractor.html
https://www.mirka.com/en-IN/Mirka-DEROS-680CV-150mm-CV-Orbit-80-MID6802011/

## Slide 7: 21st-century preparation tools and equipment
Battery-operated steam stripper
Electrically operated wallpaper stripping equipment that produces steam to enable easy removal of difficult wallpapers
Battery-operated electric sanders
Electrically operated sanding equipment with operating belts/pads of abrasive paper make preparation process more efficient
Battery-operated electric heat guns
Electrically operated paint stripping equipment
Example of an electric heat gun
Example of a steam stripper
Notes: https://www.bedienungsanleitu.ng/gallery/14368010.jpg
https://cdn.mscdirect.com/global/images/ProductImages/1642002-21.jpg

## Slide 8: 21st-century preparation materials
Eco-friendly paint strippers
These are caustic-soda type water-based paint
strippers containing sodium hydroxide.
Type 1 can remove up to 32 layers of older and oil-based coatings as well as paint suspected to contain lead.
Type 2 can remove up to 20 layers of modern and water-based coatings, where neutralising is not required.
A test must always be taken prior to applying the paint stripper, to determine which one is needed.
Watch the following YouTube video on how to use Peelaway and varnish remover: How to Use Peelaway 1 & 7 Paint & Varnish Remover
Notes: How to Use Peelaway 1 & 7 Paint & Varnish Remover - https://youtu.be/WxLq-bPxcto

## Slide 9: 21st-century preparation materials
Lightweight filler
Lightweight filler that does not shrink or sag and does not need to be sanded when dry
Ready-mixed filler
Multi-purpose ready-mixed filler supplied ready mixed in the container
Dry-lining compound
Modern gypsum-based material used as both a filler–surfacer and finishing compound for plasterboard jointing systems
Image of the Gyproc EasiFill 60
Image of a Dunlop filler
Image of the Pollycell multipurpose filler
Notes: https://www.paintinganddecoratingnews.co.uk/decorating-products/dunlop-fine-surface-filler/
https://www.google.com/imgres?h=600&w=600&tbnh=225&tbnw=225&osm=1&hcb=1&hcb=1&source=lens-native&usg=AI4_-kRLFg-yH5pTSuSGglRKF8I7eUNdEw&imgurl=https%3A%2F%2Fencrypted-tbn0.gstatic.com%2Fimages%3Fq%3Dtbn%3AANd9GcRZNWMJ_Cle7YMr471v4-sC8-hPXY9m_LwT-eZkGVoX39dc9iYx&imgrefurl=https%3A%2F%2Fwww.jtatkinson.co.uk%2Fpolycell-multi-purpose-polyfilla-ready-mixed-tub-1kg&tbnid=hKzqT97eKmGaXM&docid=4eh2Q4NFvSCpzM&ved=0CB0Qi8AJahcKEwigrq6L_dGAAxUAAAAAHQAAAAAQCA
https://media.diy.com/is/image/Kingfisher/gyproc-easi-fill-quick-dry-white-two-coat-filler-jointing-compound-5kg-bag~5015892846945_02c_bq?$MOB_PREV$&$width=768&$height=768

## Slide 10: 21st-century wallpaper – digital prints/photo murals
These are made from heavy-duty vinyl paper consisting of several panels printed with sections of a digital image.
They are supplied as single or multi-panels up to 1.270m wide.
Each panel contains a ‘selvedge’ to protect the end of the roll.
Joints are created by overlapping and splicing.
They are hung using specialist ready-mixed (fungicidally protected) PVA adhesives applied to the wall.

## Slide 11: 21st-century paint application – pressure-fed rollers
For more information, take a look at this video: Graco Pressure Roller - How To Use, Setup and Review
Transforms the paint sprayer into a rolling system for increased speed of application
Pressure-fed roller system four times faster than a traditional roller, while eliminating the mess of a roller tray
Attaches directly to the spray gun
Pressure on the trigger applies more paint onto the roller sleeve
Airless-fed roller system 2. Pressure-fed roller system
Example of a pressure roller
Example of a jet roller kit
Notes: Graco Pressure Roller - How To Use, Setup and Review - https://www.youtube.com/watch?v=73d-yLItd1M
Images:
https://www.spraydirect.co.uk/acatalog/New_JetRoller_Power_Roller.html
https://www.amazon.co.uk/Graco-244512-Pressure-Rollr-Kit/dp/B0021XZQ0S

## Slide 12: 21st-century paint application
Handheld cordless HVLP spray unit
Handheld cordless version of HVLP spray
unit powered by re-chargeable 18V battery
Portable equipment for small jobs
Reduces the need for power cables and
air/fluid lines
High-quality finish
High overspray
Example image
Notes: https://sherwin.scene7.com/is/image/sw/paint_template-1?$layer_1_src=SWP12101002

## Slide 13: 21st-century paint application
Handheld cordless airless spray unit
Handheld cordless version of HVLP spray unit powered by re-chargeable 20V battery
Portable equipment for small jobs
Reduces the need for power cables and air/fluid lines
Quicker speed of application
Reduced overspray
Example image
Notes: https://sherwin.scene7.com/is/image/sw/paint_template-1?$layer_1_src=SWP12101002

## Slide 14: 21st-century paint application
Air-assisted airless spray system
Air-assisted spray systems combine the high-quality finish of HVLP systems with the speed of application of airless systems.
Air-assisted airless spray guns firstly pump out paint under high pressure and, secondly, they complete the atomisation with small amounts of compressed air from the face and/or the horns of the air nozzle that they use.
Example image
Notes: https://fatllama.com/rentals/ottawa/hire-graco-paint-sprayer-airless-air-assisted-62428640

## Slide 15: Paint technologies of the future …
Self-cleaning paint
Nano technology
Smart paint
Self-healing wraps
Graphene paint
Solar paint
Rapid drying paint
Magnetic paint
Antimicrobial paint
Air cleaning paint
One-coat paint
Autonomous painting drone
For more information see:
Innovative Painting Technology Trends to Know Before You Start Home Or Office Painting
Image of a commercial painting drone
Notes: Innovative Painting Technology Trends to Know Before You Start Home Or Office Painting - https://www.bergerpaints.com/blog/decor-tips/new-painting-technologies-you-need-to-know-about-before-your-next-home-painting-project
Image - https://www.ddcoatings.co.uk/2640/commercial-painting-drones

## Slide 16
Any questions?