## Slide 1: 21st-century construction techniques and technologies
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Circular economy (CE)
A circular economy is an economic concept whose fundamental principle is to keep resources withdrawn and coming from the environment in the economic circuit, therefore extending their lifecycle and avoiding their return in the form of waste.

## Slide 3: Sustainability (T levels resources)
The construction industry is one of the largest users of resources and contributors to pollution.
Sustainability is most often defined as meeting the needs of the present without compromising the ability of future generations to meet theirs.
In our built environment, sustainable construction means building using renewable and recyclable materials and reducing energy consumption and waste. There are a wide range of solutions and strategies that can be incorporated into projects to improve sustainability and protect and preserve our natural environment.

## Slide 4: Sustainability (T levels resources)
The elements of sustainable construction include:
waste
materials
community and economy
procurement
climate adaptation
carbon and energy
environmental management
water
biodiversity.

## Slide 5: Design (T levels resources)
During the design phase of a project, sustainability should be a key consideration and priority.
Most decisions around building performance and specifying materials will be made during the design phase of a project. Architects and designers can help to influence and provide advice and guidance to clients to promote the use of sustainable products and materials.
Sustainable solutions can be explored during the design phase of a project.

## Slide 6: Energy consumption (T levels resources)
Reducing energy consumption and reliance on fossil fuels is a key focus of the construction sector.
The uptake and adoption of renewable energy systems is growing in the UK.
Solar energy
Solar panels can generate hot water or electricity, and once the cost of installation has been covered the energy they produce is totally free.

## Slide 7: Heating systems (T levels resources)
Ground source heat pumps
Ground source heat pumps (GSHP) extract heat from the ground. They use it to pre-heat water for space and water heating, so reducing the amount of gas, oil or electricity consumed. The UK has a consistent ground temperature of around 10°C, which is very suitable for GSHP systems.

## Slide 8: Heating systems (T levels resources)
Air source heat pumps
An alternative to a ground source heat pump is an air source heat pump (ASHP). It works in a similar way.
Instead of absorbing heat from the ground, an ASHP absorbs heat from the outside air, which is ingested into the system through a pump. This is then used to heat the home and produce hot water.

## Slide 9: External wall insulation
EWI is the abbreviation for external wall insulation, which is fixed to solid backgrounds mechanically, improving the insulation of the building.

## Slide 10: External wall insulation sustainable system
This diagram shows a sustainable EWI system fixed to a lime plaster background.
Diagram explaining external wall insulation
Notes: https://www.lime.org.uk/applications/retrofit-insulation-systems-for-old-buildings/external-wall-insulation-system/expanded-cork-insulation-system-7711.html

## Slide 11: Acrylic and silicone thin coat renders
Acrylic and silicone thin coat renders are applied over insulation and basecoat with reinforced fibreglass mesh embedded so it will hold the basecoat together and prevent cracking if there is structure movement. An attractive textured finish is produced using a polycarbonate float, which is low maintenance, waterproof, lightweight and breathable.
Example image
Notes: For more information, see Welcome to Wetherby Building Systems Ltd http://www.wbs-ltd.co.uk/
Image - https://www.wbs-ltd.co.uk/thin-coat-render-comparison/

## Slide 12: Machine-applied renders
When renders are applied via machine, the speed of production increases, with reduced labour time, increased consistency and higher quality of application and finish.
Image of a construction worker applying render
Notes: https://files.websitebuilder.prositehosting.co.uk/fasthosts28788/image/page-121.jpg

## Slide 13: Venetian plaster
Venetian or polished plastering resembles marbling and is used in bathrooms.
For example images, take a look at this link!
Notes: For more information, see Venetian Polished Plastering in London, Surrey & South East England http://www.colourandtexture.com/wp-Polished-Plastering-London
Image - https://www.colourandtexture.com/

## Slide 14: Liquid floor screeds
Liquid screed is a modern flooring solution applied over heating elements. It is a thick liquid mix that is applied by pouring or pumping from a mixing truck straight onto the area of (usually) concrete to be covered.
Example image
Notes: For more information, see FLOOR SCREEDING SOLUTIONS at https://floorscreedingsolutions.com/
Image - https://floorscreedingsolutions.com/services/

## Slide 15: Passive housing
Passivhaus is an engineered and detailed structure that is highly insulated with triple glazed windows and excellent airtightness with mechanical heat recovery and ventilation.
Read more about them on their website: www.passivhaustrust.org.uk
Notes: For more information, see PRECISE MEASUREMENT OF RETAIL, COMMERCIAL AND INDUSTRIAL PROPERTIES https://www.realserve.com.au/

## Slide 16: Retrofit
Retrofitting an existing building will improve its energy consumption and reduce emissions.
Retrofitting can include a number of factors, such as:
wall, floor and roof insulation
installation of windows
ventilation system
heating system.

## Slide 17: Building information modelling (BIM)
BIM is a process for creating and managing information on a construction project throughout its whole lifecycle.
As part of this process, a coordinated digital description of every aspect of the built asset is developed, using a set of appropriate technology.
Take a look at this flowchart of BIM here: BIM PROCESS MANAGEMENT
Notes: https://www.realserve.com.au/existing-conditions/bim-services/

## Slide 18: Advantages of BIM
Communication and teamwork throughout all stages of the construction process
Dynamic monitoring of changes in design
Visualisation at planning stage
Clash detection
Improved health and safety
Reliable budget control

## Slide 19: Disadvantages of BIM
Modelling software required
Training and staff
Trust and cooperation throughout the project
End-user engagement
Incompatibility with partners

## Slide 20: CAD
CAD (computer-aided design) is software used by engineers, architects, designers and construction managers to create designs. These designs are precise drawings or illustrations of new buildings or plans and can be either two-dimensional or three-dimensional.
AutoCAD is one such software.
Notes: https://www.autodesk.co.uk/products/autocad/overview?mktvar002=4341321|SEM|20191176657|153100676081|aud-457677323208:kwd-297121734871&utm_source=GGL&utm_medium=SEM&utm_campaign=GGL_ACAD_AutoCAD_EMEA_GB_eComm_SEM_BR_New_MIX_0000_4341321&utm_id=4341321&utm_term=aud-457677323208:kwd-297121734871&mkwid=s|pcrid|644077393197|pkw|autocad%20360|pmt|b|pdv|c|slid||pgrid|153100676081|ptaid|aud-457677323208:kwd-297121734871|pid|&utm_medium=cpc&utm_source=google&utm_campaign=GGL_AME_AutoCAD_EMEA_GB_eComm_SEM_BR_New_MIX_ADSK_3465264_AutoCAD&utm_term=autocad%20360&utm_content=s|pcrid|644077393197|pkw|autocad%20360|pmt|b|pdv|c|slid||pgrid|153100676081|ptaid|aud-457677323208:kwd-297121734871|&gclid=Cj0KCQjwoK2mBhDzARIsADGbjepm5VAOxKXCRY4dJ_WN5kyREOMHL22advd9Zp705b-kF9LU7Mq7qOkaAm-VEALw_wcB&ef_id=ZBRiLgAAAEacegN-:20230803131541:s&term=1-YEAR&tab=subscription&plc=ACDIST

## Slide 21: 3D modelling
3D modelling is the process of using software to create a mathematical representation of a three-dimensional object or shape.
The created object is called a 3D model. 3D models are used in a variety of industries.
Notes: For more information, see Index of /news/wp-content/uploads/2021/03/ https://www.pbctoday.co.uk/news/wp-content/uploads

## Slide 22: 3D printing
3D printing in construction is when companies or projects sequentially layer materials via computer-controlled processes to create three-dimensional shapes. 3D printers are useful for creating new structures onsite or for manufacturing components offsite for later assembly.

## Slide 23: Drones
Drones are used in construction for:
inspecting and surveying buildings for build progress or maintenance
surveying and monitoring to detect safety issues onsite
accessing structures such as bridges, roads and land.

## Slide 24: Augmented reality (AR)
By using AR you are able to see a visual overlay of computer-generated information on top of the real world.
On construction sites, AR can be used to visualise hidden structures, or compare a design model to what is actually built.

## Slide 25: Offsite manufacturing
Offsite manufacturing means that products are manufactured in
a factory and then transported and assembled and installed onsite. It is a modern method of monstruction (MMC) that aims to optimise the construction process.

## Slide 26: Advantages of offsite manufacturing
Efficient and predictable
Safety is increased
Sustainable development
Less labour required
Fewer trained operatives required
No disruption from adverse weather conditions
Less manufacturing waste
Example image
Notes: https://www.offsitehub.co.uk/assets/images/news/resized/_550x345_smaller_workforce.jpg

## Slide 27
Any questions?