## Slide 1: Post-1919 methods of construction
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify the National Occupation Standards (NOS) relevant to the groundworks profession
  list the other various standards the groundworks profession have to work to
  describe the post-1919 mechanisation of the construction industry
  explore the heavy plant associated with earth works
  investigate the evolution of materials
  examine modern construction materials.

## Slide 3: The National Occupational Standards of groundworks
These are a set of guidelines that outline the skills, knowledge and performance criteria required for those working in the groundworks industry.
These standards have been developed by the UK's Construction Industry Training Board (CITB) in consultation with industry experts and are regularly reviewed and updated to ensure they remain relevant.

## Slide 4: The National Occupational Standards of groundworks
The NOS provide a comprehensive framework for the training, development and assessment of those working in the groundworks industry.
Some of the key units within the NOS for groundworkers include:
Conforming to General Health, Safety and Welfare in the Workplace
Preparing and Installing Drainage
Preparing and Laying Pavements
Excavating and Laying Foundations
Notes: Conforming to General Health, Safety and Welfare in the Workplace – this unit covers the essential knowledge and skills required for safe working practices, including risk assessment, safe lifting and handling, and the use of personal protective equipment (PPE).
Preparing and Installing Drainage – this unit covers the installation of drainage systems, including the preparation of the ground, the installation of pipes and fittings, and the testing and commissioning of the system.
Preparing and Laying Pavements, Floors and Pathways – this unit covers the preparation and installation of different types of paving, including concrete, natural stone, and block paving.
Excavating and Laying Foundations – this unit covers the excavation and preparation of foundations for buildings and structures, including the use of equipment such as mini-diggers and excavators.

## Slide 5: Other relevant standards for groundworks
There are a range of standards that groundworkers have to comply with and organisations that set the standards. These include:
British Standards
Building Regulations
Department for Transport
Local Government Association
Notes: British Standards
The British Standards Institution (BSI) is the national standards body of the UK. It develops and publishes standards that cover a range of industries and disciplines, including construction. There are several British Standards that relate to groundworks, including:
BS 8004:2015 Code of practice for foundations
BS EN 12699:2013 Execution of special geotechnical works - Displacement piles
BS EN 1997-1:2004 Eurocode 7: Geotechnical design - General rules.
Building Regulations
The Building Regulations are a set of national standards that set out the minimum requirements for the design and construction of buildings in England and Wales. They cover areas such as structure, fire safety, drainage, and ventilation. Groundworks are an important part of the construction process, and as such, must comply with the Building Regulations.
Department for Transport
The Department for Transport is responsible for developing and implementing policies and regulations related to transport in the UK. This includes roads and highways, which require the construction of suitable groundworks. The department's policies and regulations can have an impact on the design and construction of groundworks for roads and highways.
Local Government Association (LGA)
The LGA is a membership organisation that represents local authorities in England and Wales. They provide advice and support to their members on a range of issues, including planning and development. Local authorities are responsible for enforcing the Building Regulations, and as such, their policies and regulations can have an impact on the design and construction of groundworks in their area.

## Slide 6: Some examples of modern aids
Mechanical saw
Handheld pneumatic breaker
Hydraulic breaker machine attachment
Notes: Discuss the use of the tools in aiding the role of the groundworker and other associated examples, such as a mechanical whacker plate. Explain how these save time and improve efficiency on tasks, but that there remain health and safety challenges that have evolved with them.

## Slide 7: Use of laser levels in groundworks
Watch this video:
Construction Laser Level & Grading
Notes: Lead a discussion on the use of laser levelling equipment and how it aids accuracy, etc., and therefore improves quality and also reduces the time needed for a task. Discuss drawbacks and challenges, including the potential lack of experience as the technology constantly evolves, and other related challenges.
https://www.youtube.com/watch?v=yTlMZU_5GI8

## Slide 8: Heavy plant
Heavy plant is the machinery and equipment used in the construction industry for a range of tasks, such as excavation, material handling, transportation and lifting. Heavy plant is essential in the construction industry as it enables the efficient and safe execution of large-scale projects.
The use of heavy plant in the UK construction industry is subject to various regulations, including the Provision and Use of Work Equipment Regulations (PUWER) and the Construction (Design and Management) Regulations (CDM).
These regulations place obligations on employers, equipment operators and other parties involved in the use of heavy plant to ensure that equipment is safe and fit for purpose, and that all necessary safety measures are in place to protect workers and the public.
Notes: Discuss the use of plant in groundwork projects – how it can speed up the process and be far more efficient, as well as the health and safety requirements and associated risks with using plant.
Using next two slides show learners examples of heavy plant and outline their usage in projects, including examples of different uses.

## Slide 9: Heavy plant commonly used in construction
Tracked excavator
Dump truck
Backhoe loader
Loader
Bulldozer

## Slide 10: Heavy plant commonly used in construction
Mobile crane
Concrete mixer truck
Concrete pump truck

## Slide 11: Paver machines
Tarmac paver machines, also known as asphalt pavers, are used to lay asphalt or tarmac surfaces for roads, car parks and other applications.
Tarmac pavers typically use a conveyor system to transport the asphalt mix from a hopper to a distribution auger, which spreads the mix evenly over the surface to be paved.
The paver machine then compacts the mix using a series of rollers, and a screed is used to level the surface and achieve the desired finish.
Notes: Discuss the use of pavers in the road building process.

## Slide 12: Slip form pavers
Slip form pavers are used for laying concrete surfaces such as highways, airport runways and other large-scale pavements.
Slip form pavers use a continuous process to lay concrete, with the concrete mix being poured into a hopper on the machine and then fed through a mold or form that is attached to the machine.
As the machine moves forward, the mold is continuously adjusted to maintain the correct level and finish of the concrete surface.
Vibration is used to consolidate the concrete, and finishing tools are used to achieve the desired texture and finish.
Notes: Discuss the use of slip form pavers in the building of concrete roads or other elements such as kerbs, advantages and disadvantages, and then show the examples on the next slide.

## Slide 13: Slip form paver machines
GOMACO slip form paver machine image 1
GOMACO slip form paver machine image 2
Notes: https://www.gomaco.com/resources/photos/gp2600/gp2600_08_16/HW-110313-D001.jpg
https://www.gomaco.com/resources/photos/3300/update_03_18/CG-111624-D-09-B.jpg

## Slide 14: Modernisation of drainage pipework
The drainage industry has seen significant developments over the past century.
In the 1940s, rigid plastic and bituminous fibre pipes were introduced. However, these pipes were not widely used due to their disadvantages.
In the 1960s, smooth plastic drainpipes were introduced. These pipes were more durable than their predecessors, but they still had some disadvantages.
In 1963, corrugated plastic drainpipes were introduced. These pipes addressed the disadvantages of smooth plastic pipes.
Notes: Discuss how pipe systems have changed from the use of cast iron and clay, and have been phased out over time. Explain why plastic took precedence over other forms of pipework for drainage applications. Also discuss the rise and use of concrete prefabricated pipework for larger drainage applications such as sewers, storm drains and culverts. Use the information on the next few slides to facilitate this discussion.

## Slide 15: Modernisation of drainage pipework
Plastic drainage has been used in the UK construction industry for over 70 years. It was first introduced in the 1950s as a replacement for clay pipes.
Plastic drainage quickly became popular due to its durability, lightness and cost-effectiveness. Today, it is the most widely used material for drainage in the UK.
Benefits of plastic drainage include:
durability
lightness
cost-effectiveness
sustainability.

## Slide 16: The decline of clay pipes
While clay pipes were commonly used for drainage in the past, they are not as prevalent in modern construction projects in the UK.
This is because other materials, such as plastic (e.g. HDPE, PVC) and
concrete offer advantages over clay pipes in terms of cost, durability, ease of installation and maintenance.

## Slide 17: Concrete pipes
Concrete pipes offer several advantages, such as strength, durability and fire resistance, which make them suitable for heavy-duty applications such as underground drainage systems, culverts and stormwater management.
Concrete pipes have a long service life and require minimal maintenance, making them a cost-effective choice in the long run.
Concrete pipes are heavier and more difficult to install compared to plastic pipes, which can be a disadvantage in some situations.

## Slide 18: Rise of prefabricated concrete elements
The use of precast concrete products, including kerbs, became more widespread in the 1950s and 1960s as new production techniques and materials were developed.
Since then, precast concrete products have been a common feature of road construction and other infrastructure projects.
As well as precast/prefabricated elements that have standardised construction of elements there is also another option.
Bespoke elements such as manholes can be made to measure for specific applications and situations. These also carry the same advantages of prefabrication.

## Slide 19: Some examples of prefabricated concrete elements
Precast culverts
Precast retaining structures
Precast kerbs and pavers
Drainage channels
Notes: Discuss the benefits of using precast standardised products and their application in groundworks, including benefits and drawbacks of using precast elements.
Use this website to demonstrate range of retaining structures: https://www.jpconcrete.co.uk/concrete-bolt-down-retaining-wall/

## Slide 20
Any questions?