## Slide 1: Pre-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Types of pre-1919 plasterwork
Plasterwork pre-1919 was fibrous plasterwork consisting of ornamental enriched designs dating back many years and, today, this is classed as heritage work.

## Slide 3: Types of moulding work
This picture shows the different types of plaster moulding.

## Slide 4: Types of construction
Walls were mainly solid construction, being either built from brick or stone which contained timber lintels above doorways and windows.
Floors were either suspended, with timber floorboards or covered with flag stones, clay tiles or slate.
Partitions and ceilings were constructed of timber and covered with lath and plaster.
Roofs were covered in slate fixed to timber laths and the underside was plastered with lime mortar.
Some walls would contain slate or bitumen damp courses and no foundation, leading to rising moisture from the ground.

## Slide 5: Lime plastering
Traditional materials, such as lime mortar, would be used to plaster the walls. This allowed moisture to evaporate naturally. However, lime-based plasters are slow-setting and weak.
Image of lime torching on the underside of slate
Example image of lime plaster
Notes: Lime plaster - http://www.trowelworks.co.uk/_gallery-image.aspx?ID=39556
Lime torching - https://jdbsurveys.com/wp-content/uploads/2021/01/roof-torching-image-2.jpg

## Slide 6: Hydraulic lime
Feebly hydraulic lime (NHL 2) contains less than 12% clay, which means it is slower to set (about 20 days in water).
Moderately hydraulic lime (NHL3.5) contains 12%–18% clay, which gives a slightly faster set (15–20 days in water).
Eminently hydraulic lime (NHL5) has up to 25% clay content, which means that a much faster set is achieved (hours/days).

## Slide 7: Hydrated lime
Hydrated lime is also used for internal plastering. However, it does not contain a set like hydraulic lime. It will set far more slowly under carbonation.
Hydrated lime is made into lime putty – a process that is carried out by soaking lime in water for a minimum of 24 hours.
Using hydrated lime or putty can be deemed weaker than NHL, but it does have some benefits. Lime added to a cement-based mix will improve the mix’s workability and adhesion and help prevent shrinkage. Another benefit of lime is that it creates suction.
Lime putty for internal plastering is used on lathwork or cob, which is weaker than solid backgrounds.

## Slide 8: Listed buildings
A listed building is a building, object or structure that has been judged to be of national importance in terms of architectural or historic interest.
When a building is listed, it is listed in its entirety, which means that both the exterior and the interior are protected.
These buildings are included on a special register, called the List of Buildings of Special Architectural or Historic Interest.
Listed building control is a type of planning control, which protects buildings of special architectural or historical interest.
Section 7 of the Planning (Listed Building and Conservation Areas) Act 1990 (LBCA Act) covers listed buildings.

## Slide 9: Classification of listed buildings
Grade I – buildings of exceptional interest (approximately 2% of all listed buildings).
Grade II* – particularly important and more than special interest (approximately 4%).
Grade II – buildings of special interest, warranting every effort being made to preserve them (94%).

## Slide 10: Sharp or coarse sand aggregate
Sand is an aggregate used to bulk the mix. Without sand, cement mixed with water would be too hard and would crack. There are many different types of sand used in construction. Sand used for rendering should contain a mixture of small, medium and large grains and contain as little silt as possible.

## Slide 11: Reinforcement
Goat hair or horse hair is added to the mortar to help reinforce the material due to its weak strength.

## Slide 12: Additives used in lime mortar plaster
Pozzolan additives are materials that enable lime mortars to set more rapidly and add strength.
Pozzolans are fine stone, brick dust or ash mixed into the mortar.
Approximately one part of pozzolan is used for every nine parts of mortar (by volume).
This must be mixed just before use, as the mortar will start to set once the pozzolan is added.

## Slide 13: Lime wash
Earth pigments are most commonly used to produce a wide range of lime wash colours, ranging from pale creams and pinks to strong yellows, dark purples and rich browns.
The pigments are added when the lime wash is made and used to paint the plaster surface, allowing it to breathe.

## Slide 14: Lath and plaster
Laths were traditionally used on timber backgrounds. They consist of thin strips of wood over which plaster can be spread. It can be a time-consuming process to prepare, fix and plaster this surface. This type of background is still used in the restoration of listed buildings.

## Slide 15: Types of timber lath
Lath can be made of different types of wood and can be either machine sawn or riven (hand split).

## Slide 16: Tools
The tools used during this era mainly consisted of timber and mild steel, which meant that they required extensive maintenance.
Timber tools were produced from polyurethane and polycarbonate, which made them light and simpler to use.
Materials were mixed by hand and gauged in boxes.

## Slide 17: Gauging trowel
When mixing is in progress, this tool can be used to clean the rim of the mixing bucket, moving dry unmixed plaster back to the centre of the bucket.
It is also used for cleaning and removing excess material from the straight edge and to clean plaster droppings by scraping the floor.

## Slide 18: Corner tools
Corner tools can be used when finishing opposite walls to avoid damaging the surface and finish both internal angles at the same time.

## Slide 19: Lath hammer
A traditional tool used by plasterers, before plasterboard was widely used, to cut wooden laths when lathing. Also used for hacking off old sand–lime plaster from walls and for hammering in plasterboard nails.
Image of Lath Hammer
Notes: https://tooltique.co.uk/shop/vintage-j-tyzack-sons-no-1-strapped-slaters-roofing-lathing-hammer-axe/

## Slide 20: Wooden float
Used to consolidate screed, as well as to provide a finish.

## Slide 21: Casting brushes
Used to brush plaster into enrichments in reverse moulding and then to brush and splash plaster when casting.

## Slide 22: Water level
Used for setting a datum line, particularly in floor screeding.
Photo credit: user:Obersachse
Available at https://commons.wikimedia.org/wiki/File:Schlauchwaage_Schematik.svg

## Slide 23: Follow the link for further research
Understanding Traditional (pre-1919) and Historic Buildings for Construction and Built Environment Courses
Notes: Understanding Traditional (pre-1919) and Historic Buildings for Construction and Built Environment Course: https://cadw.gov.wales/learn/education/teaching-resources/understanding-traditional-pre-1919-and-historic-buildings

## Slide 24
Any questions?