## Slide 1: 21st-century construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify materials relevant to bricklaying
  identify modern techniques relevant to bricklaying.

## Slide 3: Materials
Cavity walls require the use of a number of components in order to weatherproof the structure.
A plastic damp proof course (DPC) is laid horizontally to prevent moisture rising through the masonry.
Vertical DPC can be plastic material or cavity closers that protect against moisture penetration and make the cavity airtight at the reveals.

## Slide 4: Materials
Plastic DPC is manufactured in specific widths for use as horizontal DPC in cavity walls and also for solid walls where required.
Half brick thick wall with horizontal DPC
While the plastic material used is durable, it must be laid carefully to avoid puncturing it.
Holes in the DPC would compromise the moisture barrier, leading to potential long-term problems.

## Slide 5: Materials
Cavity closers seal the cavity at the reveals of openings to comply with regulations regarding maintaining airtightness of the structure.
Preventing air leakage adds to the energy efficiency of a building by reducing heat transfer.
Cavity closers also provide an efficient DPC and incorporate insulation to prevent cold bridging at the reveal.
The window frame is omitted here.

## Slide 6: Materials
Insulation is fixed securely to the inner leaf of the cavity wall using plastic clips fixed to wall ties.
Gaps between the insulation sheets should be avoided because they would allow heat transfer to take place.
Note the insulation within the cavity closer.
This would reduce the energy efficiency of the building.
To ensure airtightness, the joints between rigid insulation sheets should be taped. (Note that the tape is not shown on the image.)

## Slide 7: Modular construction
Modular construction is a method where production takes place offsite.
The method combines factory produced pre-engineered units to form elements of a structure.
Modules can be completed offsite to include fitted doors and windows, pre-installed services and internal and external finishes.
Completed modules are delivered to site to be fitted together to form a complete building.

## Slide 8: Modular construction
Offsite modular construction can utilise low-energy manufacturing processes, using sustainable, eco-friendly and even recycled materials.
Components can be produced with consistent accuracy to maintain high standards of quality.
Weather-dependent site activities are minimised, allowing deadlines to be met and work programmes to be achieved more reliably.
The safety of personnel can be enhanced through controlled working conditions.

## Slide 9: Sustainability focus
All forms of modern construction must continuously focus on sustainability.
Previous methods and materials have often not been environmentally friendly. For example, concrete produces large amounts of carbon during manufacture and transportation.
Efforts are being made to utilise recycled aggregate in concrete production to reduce carbon emissions.

## Slide 10: Sustainability focus
Cement-free mortar and concrete is now being produced, and it is claimed that it substantially reduces the carbon emissions created by construction activities.
Prefabrication and modular construction methods have the advantage of shifting a large proportion of construction work offsite, reducing dust and noise, and lowering carbon emissions.
It uses ground granulated blast furnace slag, which is a by-product of iron and steel making. This forms the binder for mortar and concrete.
The process can be fast, efficient and precise. Reductions in waste can be achieved and accidental damage to materials and components can be minimised.

## Slide 11
Any questions?