## Slide 1: Post-1919 and modern construction techniques
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Post-1919 and modern construction techniques
Cement and sand plaster and render development
The introduction of cement used for solid plastering and rendering provided strength and faster setting times compared to using lime. Therefore, production of work would dramatically increase.
Cement mixes were also enhanced with additives, such as waterproofer and plasticiser, which worked well in areas that had been affected by moisture.
Some problematic issues that occur with cement-based plaster or render are that it can become brittle, develop shrinkage cracks and become powdery if used in direct sunlight.

## Slide 3: Gypsum pre-blended plasters
Gypsum pre-blended plasters were developed and had many advantages over lime- and cement-based plasters for internal plastering work.
They contained a gypsum binder and a lightweight aggregate – perlite and vermiculite.
The different plasters were developed to be compatible with various types of backgrounds. They also had greater thermal resistance.
However, gypsum plasters were deemed to not be as strong and were problematic in moisture-affected walls.

## Slide 4: Manufactured beads
Beads were manufactured to simplify the plaster and render application, providing a profile to aid the application process.
Beads replaced the use of timber rules, which was time consuming. They provided accuracy and reinforcement to finished surfaces, produced from galvanised, stainless steel and plastic. Types of bead include:
standard angle beads
thin coat angle beads
stop beads
expansion beads
bell cast beads.

## Slide 5: Plasterboard
Plasterboard development began in the early 1950s, fixed with galvanised nails to timber, which reduced intense labour and drying times.
Plasterboard is a rectangular sheet manufactured from a Gypsum core, sandwiched between lining paper on both sides. Known as dry lining, it is fixed to timber and metal backgrounds.
Plasterboards today are fixed with screws or adhesives.
Today, there are different types of performance plasterboard that have been developed to meet the building regulations that govern construction development.

## Slide 6: Pre-blended renders
This type of product was developed to improve the quality of render installation on the facade of buildings.
It was produced and bagged in batching plants to remove human error when mixing and only required clean water when mixed.
One advantage of using pre-blended render is that it has been tested before production and it is supported with manufacturer’s instructions.
Colour-through renders also contain a polymer additive for improved adhesion, and an installation guarantee that favours designers.

## Slide 7: Tools
Tools for plastering required less maintenance. Tools that were produced from mild steel were replaced with stainless steel and carbon.
Timber tools were produced from polyurethane and polycarbonate, which made them light and simpler to use.
Portable power tools, such as dry-wall and self-feeding collated drills, were developed to increase the speed for fixing plasterboard.

## Slide 8: Equipment
Mechanical mixing equipment was used to speed up productivity and remove additional labour from hand mixing.
Mechanical drum mixers were used for mixing. This increased consistency and reduced the amount of labour that was used when hand mixing.
Mixing drills and whisks are used today for mixing pre-blended plasters and renders.
Spray machines were developed to reduce hand application on large commercial buildings.

## Slide 9: Post-war prefabricated housing
Prefabricated homes (‘prefabs’) were temporary homes built in the factory at the close of the Second World War. They were built to rehouse those who had lost their homes during the Blitz or to house servicemen returning from the war and their young families.
Example image
Notes: https://thelondonphile.files.wordpress.com/2014/03/img_5957.jpg

## Slide 10: Cavity construction
The cavity is partially filled with insulation as required by the building regulations, to reduce heat loss and save energy.
The most common type of external walling used today is cavity wall construction. Cavity walls are two masonry walls built side by side to form an inner and outer leaf (sometimes called skins). The leaves are held together with wall ties.

## Slide 11: Timber-framed walls
Timber framing is both a traditional and modern method of building. Traditional buildings using timber framing were made mostly from oak with various infills, such as brick or plaster, to form the walls.
Modern timber-frame homes are generally built from softwood and have an outer skin of masonry or are clad with timber or plaster to waterproof the structure.

## Slide 12: Metal-framed systems
Metsec’s steel framing system is a fast-track steel-stud panel frame that is fixed as infill between the main structural frame members. It provides a carrier for insulation, exterior cladding and interior wallboard.

## Slide 13: Prefabricated construction
SE-SIP construction system is a new generation of timber structures. It is unmatched in terms of construction speed, versatility, high-strength and thermal insulation properties, which makes it a highly efficient construction system for the construction of net zero energy and passive buildings.
Take a look at the following links for more information:
SE-SIP – CONSTRUCTION SYSTEM
SIP Europe - Construction
Notes: SE-SIP construction system - https://www.sipeurope.eu/en/se-sip-construction-system/
SIP Europe - Construction - https://www.sipeurope.eu/en/construction-services/construction/

## Slide 14: Modular buildings
Modular buildings are a combination of components that are manufactured offsite
in a factory environment, then transported to site and connected to form the building.

## Slide 15
Any questions?