## Slide 1: Pre-1919 methods of construction
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify the tools used by pre-1919 groundworkers
  examine the materials used in pre-1919 groundworks/civil engineering processes
  analyse the different processes used in pre-1919 groundworks/civil engineering processes.

## Slide 3: Session objectives
  Learners will know:
  the methods of ground working and civil operations
        hand cutting or dressing stone
        hand laid roads and footways
        combined drainage systems
    relevant resources
        natural stone and cobbles for paving and walling
        hammers/mallets
        chisels
        water levels.

## Slide 4: Tools of a pre-1919 groundworker/civil engineer
Prior to 1919, construction relied heavily on manual labour and simple tools and techniques and methods of hand cutting/dressing of stone and combined drainage systems.
Hand tools included picks and shovels, spades, wheelbarrows and tamping tools, to name but a few.
Notes: Discuss the tools used by the pre-1919 ground worker, giving consideration to the following:
the lack of safety regulations
the limitations imposed by lack of technology
the achievements, considering the limitations of the technology
how labour-intensive projects were compared to modern-day mechanised projects
the types of tools used by the groundworkers of the time
how materials, such as stone, were dressed by hand and the tools associated with these activities.

## Slide 5: Pre-1919 measuring/surveying equipment
Click on the links and take a look at the images:
Image of a theodolite
Image of a plumb bob line
Notes: Lead a discussion on the equipment shown on this slide, as well as types of measuring surveying equipment used, including water levels, tapes, etc.
Discuss chainage and the associated measurements, and how the term ‘chainage’ is still in use.
Discuss the levels of accuracy achieved at the time compared to modern methods.
Theodolite - https://victoriancollections.net.au/items/521605fa19403a17c4ba0b37
Plumb bob line - https://www.cef.co.uk/catalogue/products/584920-225g-plumb-bob-line?gclid=Cj0KCQjw2qKmBhCfARIsAFy8buJ7hz8w83D77_-SUE9H96azNloKeTHpKGpyg5okSSOHYV8oT4l-Nj4aAjo8EALw_wcB&gclsrc=aw.ds

## Slide 6: Horse-powered machines
Scroll down to “3. History of Road Roller” section of Road Roller for an image of the first roller!
Here is another one, the Galion Pony grader: Pull Grader Power Ratings.
Notes: Road roller – https://dreamcivil.com/road-roller/
Galion Pony grader - https://www.oemoffhighway.com/trends/article/21073488/historical-construction-equipment-association-hcea-pull-grader-power-ratings

## Slide 7: The age of steam
The age of steam saw animals phased out in favour of steam tractors.
These replaced the traditional oxen- and horse-drawn appliances. Steam tractors were shown to be more efficient and effective.
Graders and other equipment were drawn by the steam tractor, and the tractor took the up the task of the roller as well.
Notes: Lead a discussion on the age of steam and the transition from using animal-powered machinery to steam-powered systems.

## Slide 8: Pre-1919 drainage and sewers
Prior to 1919, drainage systems in the UK typically relied on a combination of natural and human-made drainage methods. There were several different types of drains and sewers employed during this time period, each with their own unique features and construction methods.
        Open drains
        Closed drains
        Brick sewers
        Stone sewers
        Cast iron sewers
        Clay pipes
        Culverts
Notes: Lead a discussion on the different options of pre-1919 drains. Learners can research each method and feedback.
Open drains – these were shallow channels dug into the ground that allowed water to flow through them by gravity. They were typically lined with turf, stones, or bricks and were used to drain fields and roadways.
Closed drains – these were similar to open drains, but were covered over with slabs or arches to create a closed channel. Closed drains were used in areas with heavy traffic or where open drains would pose a hazard.
Brick sewers – these were cylindrical or egg-shaped conduits made of brick that were used to collect and transport sewage and wastewater. They were typically laid in trenches and were joined together with mortar.
Stone sewers – these were similar to brick sewers, but were made of stone instead of brick. They were typically used in areas where high-quality stone was readily available.
Cast iron sewers – these were made of cast iron pipes and were used in areas where the ground was too hard or rocky to lay brick or stone sewers.
Clay pipes – these were used to create smaller-scale drainage systems, such as those found in domestic and agricultural settings. They were typically laid in trenches and joined together with cement or mortar.
Culverts – these were typically used to divert water around an obstacle, such as a road or railway line. They were typically made of brick or stone and were arched to allow water to flow through them.

## Slide 9: Materials used in pre-1919 drainage and sewers
Notes: Lead a discussion around the materials shown on the slide and why they are phased out, including:
cost
effectiveness
drawbacks of use.

## Slide 10: Materials used in pre-1919 drainage and sewers
Take a look at the London Sewage system being built in 1860
Notes: Lead a discussion to reiterate the challenges of pre-1919 construction methods, including:
safety challenges
timescales
tools used in complex engineering projects.
https://en.wikipedia.org/wiki/File:London_Sewage_system_being_built_in_1860.jpg

## Slide 11: Constructing London's mains sewers
Watch this video:
How Did London Get Its Sewers?!?
Notes: https://www.youtube.com/watch?v=2xAUfh_cCDM

## Slide 12: Pre-1919 road construction
There were several common types of road coverings used in the UK before 1919.
These included crushed stone or gravel, bricks, cobblestones, asphalt, concrete and wood.
Crushed stone or gravel was often used as a base layer for the road or footway, while larger stones were sometimes used for the surface layer, particularly in rural areas.
Bricks were used in some urban areas to create a durable surface for roads and footways, while cobblestones were used to create a hard-wearing surface, particularly in areas with heavy traffic.
Notes: Lead a discussion on the following:
What were the typical road materials used?
Why were these materials used?
What were the drawbacks to the using these road surfaces (giving consideration to typical liquid waste disposal at the time and the public health implications)?

## Slide 13: Pre-1919 road construction
Asphalt was used in some urban areas as a surface layer, although it was not as common as it is today.
Concrete was used in some areas, particularly for footways and cycle paths and, in some rural locations, wood was used to create a surface for footways and small roads.
Overall, the choice of materials used depended on factors such as local availability, cost and intended use.

## Slide 14: Cobble and paved road examples
Cobble roads
Stone-paved roads
Cobble and stone setts were used in pre-1919 road construction due to their durability and hard-wearing nature that could withstand heavy traffic without damage. They had a smooth surface, drained water quickly and were easily accessible, making them a cost-effective option for road builders.

## Slide 15: Use of tar as a road surface
Before 1919, tar was used as a road surface in the UK for its ability to provide a relatively smooth and durable roadway.
The process involved spreading layers of crushed stone or gravel on the roadbed and then covering it with hot, liquid tar.
This combination created a solid, water-resistant surface that could withstand the weight of vehicles and reduce dust and mud on the road.
However, this method had its limitations as it was less flexible and susceptible to cracking in extreme weather conditions compared to modern asphalt.

## Slide 16: Edgard Hooley and tarmac
During a leisurely walk in 1901, Edgard Hooley stumbled upon an industrial site in Derbyshire, England.
As he made his way near an ironworks, he couldn't help but notice a remarkably smooth stretch of road. Locals informed him that a dray delivery had accidentally dropped some barrels of tar, causing them to burst open.
In a bid to cover up the mess, some of the locals poured waste slag from nearby burners onto the tar. Much to their surprise, the unintended combination resulted in a solid surface that had no ruts or dust formation.

## Slide 17: Edgard Hooley and tarmac
Hooley quickly patented the concept of heating tar, applying slag to the mixture and breaking up stones to create a viable road surface.
By 1903, Hooley created Tar Macadam Syndicate Ltd, registering the word ‘tarmac’ and trademarked the name.

## Slide 18
Any questions?