## Slide 1: Pre-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify materials relevant to bricklaying
  identify tools relevant to bricklaying
  identify techniques relevant to bricklaying.

## Slide 3: Materials
Brick, stone and timber have been used in construction for centuries.
Bricks
In the past, bricks were manufactured to imperial dimensions. This means the dimensions were measured in inches.
Modern bricks are manufactured to metric dimensions. This means dimensions are measured in millimetres.
Imperial bricks were much larger than modern bricks
Image: Mike Jones

## Slide 4: Materials
Bricks
External brick walls were usually constructed in a solid form with the bricks laid in specific patterns or ‘bonds’.
There are two popular bonds which were used pre-1919 and are still in use today:
English bond
Flemish bond
Solid walls are strong, but are not completely effective in preventing moisture entering a building.

## Slide 5: Materials
Bricks
English bond
This bond consists of alternating courses of stretchers and headers.
This is the strongest brick bond.
Note the cut brick used to create the correct overlap or bond.
This is called a queen closer.

## Slide 6: Materials
Bricks
Flemish bond
This bond consists of alternating stretchers and headers in each course.
The pattern of this bond can add interest to the appearance.
queen closer

## Slide 7: Materials
Stone
Stone is laid in various ways, depending on its type and availability and the design of the structure.
Stone can be shaped or ‘dressed’ to produce a pleasing appearance, and to form specific architectural features.
Used in its natural form taken from a quarry, less time will be spent shaping the material.

## Slide 8: Materials
Stone
Cut and dressed stone can be laid in regular patterns or courses.
Note the use of a different type of stone that has been dressed to form the quoins and other architectural features.

## Slide 9: Materials
Stone
Uncut stone can be used in a more random form, often referred to as ‘random rubble’.
Prior to 1919, most brick and stone structures used lime mortar to bond masonry when building walls.
This actually made the wall air permeable to a limited degree.

## Slide 10: Materials
Stone
Slate is a type of stone that can be sourced in Wales.
We frequently see it used to provide a weatherproof covering for roofs after being split into sheets.
It can also be used to build walls.

## Slide 11: Materials
Timber
Timber has been in use to create structural frames for buildings for many years. Some timber frame structures have been in use for centuries.
This building dates back to the early 17th century.
The panels between the beams of the timber frame can be filled with special types of lime plaster or brick, or a combination of both.

## Slide 12: Tools
Power tools as we know them today were not available in the past. A range of hand tools were used instead.
The bricklayer’s basic tools – a trowel, spirit level, string line and hammers have changed very little over many years.
Research other vintage hand tools like these that a pre-1919 bricklayer might use.

## Slide 13: Tools
Hand tools for stonemasonry included a greater range of chisels and other cutting tools.

## Slide 14: Techniques
Working methods and techniques for building solid walls have changed little since pre-1919. Whether building in brick, stone or slate, the method is similar:
Build corners accurately or set up profiles at the end of the wall to attach a string line as a guide.
Spread a mortar bed with the trowel.
Lay the masonry component to the string line.
Ensure all perpendicular joints are filled with mortar.

## Slide 15: Protecting the fabric of the building
Solid walls in brick, stone or timber can sometimes allow moisture to penetrate through them to the interior of a building, creating damp conditions in the living or working area.
Damp can cause damage to the fabric of a building and affect the health of the occupants.
To assist in controlling damp, ventilation is very important, especially in pre-1919 buildings.

## Slide 16: Protecting the fabric of the building
A key factor in maintaining ventilation was the fireplace. This provided natural ventilation to reduce damp by drawing air into the building through doors and windows, and up through the chimney.
The permeable materials, such as lime mortar used in the walls, also contributed to natural ventilation by providing a measure of ‘breathability’.

## Slide 17
Any questions?