## Slide 1: Emerging methods for the 21st-century construction industry
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify how to stay up to date in a quickly evolving industry
  investigate the circular economy and sustainable design
  appraise modern methods of construction (MMC) used in ground working and civil operations
  assess modern surveying/setting-out equipment
  explore the use of building information modelling (BIM) and the emerging technologies in construction.

## Slide 3: Keeping up to date in a evolving industry
In a rapidly evolving construction industry, it is important for groundworkers and other tradespeople to keep up to date with new developments, techniques and regulations. They can do this by:
attending industry events
continuing professional development (CPD)
reading industry publications
joining industry associations/professional bodies
using online resources/manufacturer’s information.
Notes: Attend industry events
One of the best ways to stay up to date in the construction industry is to attend trade shows, conferences, and other industry events. These events provide opportunities to learn about new products, technologies and best practices, as well as network with other professionals in the field.
Continuing professional development
Many organisations offer training courses for construction professionals, ranging from basic safety training to advanced techniques and technologies. These courses can be taken online or in-person and can help groundworkers and other tradespeople stay up to date with the latest industry standards and best practices.
Read industry publications
There are many publications that cover the construction industry, including magazines, newsletters, and blogs. These publications provide news and insights on new developments, techniques, and regulations, as well as case studies and interviews with industry experts.
Join industry associations
Joining industry associations can provide access to a wealth of resources, including training programmes, networking events, and access to industry publications and research. Many associations also offer certification programs that can help groundworkers and other tradespeople demonstrate their expertise and stay up to date with industry standards.
Use online resources
There are many online resources available to construction professionals, including websites, forums, and social media groups. These resources provide opportunities to learn from others in the industry, ask questions, and share knowledge and best practices.

## Slide 4: The circular economy: construction perspective
The circular economy is a model of economic development that aims to reduce waste, promote sustainability and create a closed-loop system of resource use.
In construction, it’s about creating more sustainable and efficient use of resources, prioritising the reduction of waste, extending the lifespan of materials and promoting environmental stewardship.
Notes: Further reading on this topic can be found at:
https://green-alliance.org.uk/publication/circular-construction-building-for-a-greener-uk-economy/
https://www.linkedin.com/pulse/circular-economy-construction-industry-advantages-challenges-ku%C5%9Fcu?trk=public_profile_article_view
https://ukgbc.org/our-work/topics/circular-economy/
https://www.linkedin.com/pulse/circular-economy-connection-between-climate-change-tech-michael-mori

## Slide 5: Sustainable design in 21st-century construction
Sustainable design in the UK construction industry refers to the process of designing and constructing buildings and infrastructure that minimise negative environmental impacts, promote social equity and inclusivity, and prioritise economic feasibility in the long run.
Sustainable design takes into account the full lifecycle of a building, from the sourcing of raw materials to construction, operation, maintenance and eventual disposal or repurposing of the building.

## Slide 6: MMC in civil engineering and groundworks
Modern methods of construction (MMC) are innovative and advanced construction techniques that aim to improve the efficiency, quality and sustainability of construction projects.
In civil engineering and groundworks, MMC can be used to enhance the construction process by
adopting new technologies and processes to improve the speed, safety and cost-effectiveness of the work.

## Slide 7: Some examples of MMC
Prefabrication and modular construction
3D printing
3D volumetric construction
Building information modelling (BIM)
Green roofs and walls
Ground improvement
Notes: Prefabrication and modular construction
Prefabrication involves manufacturing building components in a factory and assembling them onsite. Modular construction involves the use of pre-made modules or sections that can be easily assembled into a complete structure. Prefabrication and modular construction can reduce onsite construction time, improve quality control, and minimise waste.
3D printing
3D printing involves creating three-dimensional objects from a digital model by depositing layers of material, such as concrete or plastic. 3D printing can be used for creating complex shapes, reducing material waste, and improving speed and accuracy.
3D volumetric construction
3D Volumetric Construction is a modern construction method that involves manufacturing building components (such as walls, floors, and ceilings) in a controlled factory environment as complete three-dimensional units. These units, known as modules or pods, are then transported to the construction site and assembled to form the final building. This approach offers several benefits, including faster construction, improved quality control, and reduced on-site waste.
Building information modelling (BIM)
BIM is a digital model-based process that enables architects, engineers, and construction professionals to collaborate and visualise a project in a virtual environment. BIM can help to improve project planning, reduce costs, and enhance safety.
Green roofs and walls
Green roofs and walls involve planting vegetation on the roof or walls of a building. They can help to improve air quality, reduce urban heat islands, and provide additional insulation.
Ground improvement techniques
Ground improvement techniques, such as geotextiles and geogrids, can be used to enhance the strength and stability of soil. These techniques can help to reduce the need for excavation, reduce the amount of imported fill, and minimise the environmental impact of the project.

## Slide 8: What is modular construction?
Modular construction involves the use of prefabricated building components or modules.
They are manufactured offsite in a controlled factory environment. They are then transported to the construction site and assembled onsite to form the final building structure.
Modular construction also allows for greater design flexibility and accuracy. Using computer-aided drafting (CAD) allows for more accurate design and production of the modules.
This results in greater precision and consistency in the construction process, reducing the risk of errors or design conflicts during construction.

## Slide 9: Benefits of modular construction
There is a reduction in construction time and cost.
It also allows for greater design flexibility and accuracy.
It offers greater precision and consistency in the construction process, reducing the risk of errors or design conflicts during construction.
It is also more sustainable than traditional construction methods.
The factory-controlled environment allows for better management of materials and waste, reducing the amount of waste produced during the construction process.
The use of standardised components also allows for better recycling and reuse of materials.

## Slide 10: What is 3D volumetric construction?
3D Volumetric Construction is a modern method of construction (MMC) that involves the fabrication of entire building modules in a factory setting, which are then transported to the construction site and assembled into a three-dimensional (3D) structure.
The construction industry has been exploring the use of 3D volumetric construction as a way of increasing efficiency, reducing waste and improving safety in the construction process.
Notes: Share some examples of 3D volumetric construction being used in groundworks/civil engineering projects in the UK.
New Addenbrooke's Hospital – in 2015, a new building was constructed at the Addenbrooke's Hospital in Cambridge using 3D volumetric construction. The hospital was able to remain operational during the construction process, which took just 78 weeks from start to finish.
Manchester Airport Terminal 2 – in 2017, Manchester Airport began construction on a new Terminal 2 building using 3D volumetric construction. The project is expected to be completed in 2024 and will increase the airport's capacity to handle 45 million passengers per year.
The Collective, Canary Wharf – The Collective is a co-living company that has built several residential properties using 3D volumetric construction. The company's Canary Wharf location is a 10-storey building with 209 individual rooms, which were assembled using 546 modular units.
University of Winchester – in 2019, the University of Winchester completed construction on a new student accommodation building using 3D volumetric construction. The building consists of 256 en-suite bedrooms and was constructed in just 10 months.
Citu Home – Citu Home is a sustainable housing development in Leeds that uses 3D volumetric construction to build energy-efficient homes. The development uses renewable energy sources, such as solar panels and a communal heating system, to reduce energy consumption and carbon emissions.

## Slide 11: Benefits of 3D volumetric construction
There is increased speed of construction, as the manufacturing and assembly process can be completed simultaneously.
It reduces waste, as the manufacturing process is optimised to minimise material usage.
It provides improved quality control, as the modules are manufactured in a controlled factory setting.
Safety is also improved, as much of the construction work can be completed offsite, reducing the risk of accidents on the construction site.

## Slide 12: Precast flat panel modules
Precast flat panel modules (PFPM) are a modern method of construction that involves the fabrication of flat concrete or steel panels in a factory setting.
These panels are then transported to the construction site and assembled into a three-dimensional structure, typically using a steel frame.
Notes: Share some examples:.
Crossrail project – in the Crossrail project, precast flat panel modules were used to construct the tunnels for the new railway line. The panels were prefabricated offsite and transported to the construction site for installation. This method allowed for a faster and more efficient construction process, reducing the amount of time required onsite.
Battersea Power Station – the redevelopment of Battersea Power Station in London included the use of precast flat panel modules for the construction of the new buildings. The panels were manufactured offsite and transported to the site for installation. This method allowed for a more efficient construction process and reduced the amount of waste produced during construction.
Manchester Engineering Campus Development (MECD) – the MECD project used precast flat panel modules for the construction of the new engineering campus at the University of Manchester. The panels were manufactured offsite and transported to the site for installation. This method allowed for a faster and more efficient construction process, reducing the amount of time required onsite.
The Scalpel – The Scalpel is a new office building in London that used precast flat panel modules for the construction of its facade. The panels were manufactured offsite and transported to the site for installation. This method allowed for a more efficient construction process and reduced the amount of waste produced during construction.
The O2 Arena – the O2 Arena in London used precast flat panel modules for the construction of its facade. The panels were manufactured offsite and transported to the site for installation. This method allowed for a more efficient construction process and reduced the amount of time required onsite.

## Slide 13: Benefits of PFPM
The use of PFPM can significantly reduce onsite construction time, as the panels are manufactured offsite and can be assembled quickly onsite.
PFPM can also improve the quality of construction, as the panels are manufactured to strict quality control standards in a factory environment. This ensures that each panel is consistent in terms of size, shape, and finish, and that the overall structure is structurally sound.

## Slide 14: Hybrid concrete building technique
The hybrid concrete building technique is a modern construction method that combines traditional and advanced materials and techniques to create a high-performance building system.
It uses cast-in-situ reinforced concrete, prefabricated concrete elements and lightweight steel framing to create a modular system that is customisable to meet project requirements.
This technique is well suited for mid-rise and high-rise buildings, offering advantages such as speed, cost-effectiveness and sustainability.
The use of prefabricated elements and lightweight steel framing reduces the carbon footprint of the building, and the modular design allows for easy disassembly and recycling.
Notes: Hybrid concrete building techniques have been increasingly used in groundworks and civil engineering projects in the UK. Share some examples.
The Laidlaw Library, University of Leeds – this project used a hybrid concrete structure to achieve a unique and innovative design. The building features precast concrete panels that form the structural shell of the building, with steel and concrete columns to support the weight of the building.
The Silsoe Odour Laboratories, Bedfordshire – this project used a hybrid concrete frame structure, combining precast concrete columns and beams with in-situ concrete floors and walls. The hybrid construction allowed for a faster and more efficient construction process.
The John Radcliffe Hospital, Oxford – this project used a hybrid concrete frame structure to support the weight of the new building. The hybrid construction allowed for the use of prefabricated precast concrete elements for the structural frame, with in-situ concrete used for the floors and walls.
The British Airways i360 Tower, Brighton – this project used a hybrid concrete and steel structure to support the weight of the tower. The structure consists of a precast concrete core, steel columns and beams, and precast concrete slabs for the floors.
The Brent Civic Centre, London – this project used a hybrid concrete and steel structure to achieve an innovative and sustainable design. The building features precast concrete columns and beams, with in-situ concrete floors and walls. The hybrid construction allowed for a faster and more efficient construction process, while also reducing the amount of construction waste produced.

## Slide 15: Benefits of hybrid concrete building technique
Speed: the use of prefabricated concrete elements and lightweight steel framing can significantly reduce the construction timeline, allowing for faster project completion.
Cost-effectiveness: the system can help to reduce material waste and lower construction costs, while also offering greater flexibility in design.
Sustainability: the use of prefabricated elements and lightweight steel framing can reduce the carbon footprint of the building, while the modular design allows for easy disassembly and recycling at the end of the building's lifecycle.

## Slide 16: Let’s remind ourselves … what is BIM ?
Watch this video to Understand BIM in 1 minute
Notes: Lead a recap of BIM, covering key points, such as:
what the BIM Levels are
what the BIM Dimensions are and what they mean in relation to GW/Civils Projects
government-mandated Level 2 on all public projects
the benefits of BIM
the key ethos of BIM.
https://www.youtube.com/watch?v=omaw1mdk9xg&t=1s

## Slide 17: Building information modelling
Building information modelling (BIM) is a digital process used in civil engineering to create and manage a 3D model of a building or infrastructure project, improving accuracy, efficiency and quality.
BIM allows for the integration of multiple design disciplines into a single model, improving coordination and reducing errors.
BIM facilitates collaboration and communication between stakeholders, enabling efficient decision-making and reducing the risk of errors and conflicts.

## Slide 18: Benefits of BIM on civil engineering/ground working
In civil engineering, BIM is used to model and manage the construction of roads, bridges, tunnels and other infrastructure projects. BIM allows for the integration of multiple design disciplines, such as structural, electrical, mechanical and plumbing, into a single model, improving coordination and reducing errors.
One of the key benefits of BIM is its ability to facilitate collaboration and communication between different stakeholders in a construction project, including architects, engineers, contractors and owners.
By creating a shared model that can be accessed and updated by all stakeholders, BIM enables more efficient decision-making and reduces the risk of errors and conflicts.

## Slide 19: What is BIM and how it is changing construction?
Take a look at this video: What is BIM and how it is changing the construction industry?
Notes: Lead a discussion on BIM, giving consideration to the following:
how BIM can positively impact ground working/civil engineering industry
accuracy of drawings
currency of information onsite
reduction in waste, both money and time due to reduced errors
limitations of BIM
safety benefits.
https://www.youtube.com/watch?v=cUkW2jjNC_w

## Slide 20: 21st-century surveying/setting out
GPS on plant
Robotic total station
Robotic total stations measure distances and angles on a site, creating detailed 3D models and plans.
GPS uses satellites to measure location and elevation, mapping out a site and tracking equipment and materials.
Combining these provides highly accurate measurements and data, reducing errors and minimising rework, ultimately saving time and money.
Notes: Robotic total stations measure distances and angles on a construction site. This tool can be controlled remotely and can be used to measure various points across the site. The data collected can be used to create detailed 3D models and plans, which can aid in the design and construction process.
GPS technology uses satellites to measure the location and elevation of specific points on the construction site. This information is then transmitted to a receiver on the ground, allowing surveyors to map out the site and create accurate 3D models. GPS technology can also be used to track equipment and materials, making it easier for project managers to monitor progress and allocate resources.
When used in combination, robotic total stations and GPS can provide highly accurate measurements and data that are essential for successful construction projects. The technology can help to reduce errors and minimise rework, saving time and money in the long run.

## Slide 21: Drone surveying in construction
Drone surveying, also known as aerial surveying, involves the use of unmanned aerial vehicles (UAVs) or drones to capture high-resolution images and data from construction sites.
This data can be used to create 3D models, topographic maps and other visualisations that can help project managers make informed decisions about design, scheduling, and resource allocation.
Example image
Notes: Drone surveying has become an increasingly popular tool in the construction industry due to its numerous advantages over traditional surveying methods.
One of the primary uses of drone surveying in construction is to capture accurate and detailed images and maps of construction sites. Drones can capture images from various angles and heights, providing a comprehensive view of the construction site.
Drone surveying can also be used to improve safety on construction sites. By using drones to inspect hard-to-reach or dangerous areas, construction companies can reduce the risk of injury to workers. For example, drones can be used to inspect roofs, towers, and other structures that would be unsafe for workers to climb.
In addition, drone surveying can help construction companies save time and money. Traditional surveying methods often require large teams of surveyors and can take weeks or even months to complete. Drone surveying, on the other hand, can be completed in a matter of days, and the data can be processed quickly using specialised software. This can reduce the time and cost of the surveying process, allowing construction companies to complete projects faster and more efficiently.
https://wingtra.com/drone-photogrammetry-vs-lidar/

## Slide 22: Autonomous robotic scanning ‘Spot’
Learn more about this robot: Advancing Robotics In Construction With Spot
Notes: Lead a discussion on how this could benefit the ground working/civile eingineering industry. Give consideration to:
safety
accuracy
efficiencies
cost of use
drawbacks.
https://www.youtube.com/watch?v=76XzCoVShCE&t=1s

## Slide 23
Any questions?