## Slide 1: Post-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify materials relevant to bricklaying
  identify tools relevant to bricklaying
  identify techniques relevant to bricklaying.

## Slide 3: Materials
Bricks and blocks were still common materials for constructing masonry walls. Stone was not so frequently used for structural work, but could be used more for its decorative qualities.
Bricks
Bricks became available in a vast range of colours and textures.
Different materials can be selected to suit a variety of conditions and environments.
Special-shaped bricks can be used to create architectural features.

## Slide 4: Materials
Blocks
Blocks are manufactured from a range of materials.
Dense concrete blocks are used in locations where higher load bearing qualities are needed, for example in substructures.
Thermal insulation blocks are manufactured from materials that contain tiny air bubbles and are used in the walls of a superstructure to reduce heat transfer. They are easy to cut.

## Slide 5
Solid walls
Solid walls were commonly used in houses and other buildings pre-1919.
Their use is now more common when building walls for structures that are not intended for living or working in.
Solid retaining walls can be constructed in brick or block or a combination of both.
Boundary walls may be constructed in brick to create an attractive appearance.
Inspection chambers are usually constructed in brick if masonry materials are specified.

## Slide 6
Cavity walls
Post-1919, and especially from the 1950s onwards, buildings intended for human occupation were constructed using cavity walls.
This is because of their greater effectiveness in preventing moisture from entering the living and working space of a building compared to solid walls.
Cavity wall design consists of two leaves (or skins) with a gap (cavity) between them. Wall ties between the two leaves provides stability.
In modern cavity walls, the outer leaf is often constructed in brick and the inner leaf can be constructed in block.

## Slide 7
Insulation
Initially, the cavity was left empty. No insulation was provided and often both leaves were constructed in brick. Later, insulation blocks were used for the inner leaf.

## Slide 8
Insulation
Some time after the introduction of cavity walls, designers realised that the cavity provides an opportunity to improve levels of insulation by adding sheets of insulating material.
The cavity is now typically 150mm wide.
The thickness of insulation has increased from 50mm to 100mm and more.

## Slide 9
Damp proof courses (DPC)
DPC is built into cavity walls to prevent rising and penetrating damp.
Usually made from strong plastic materials, horizontal DPC protects against rising damp.
Vertical DPC around opening reveals protects against penetrating damp.

## Slide 10
Timber frame
Timber frame construction of cavity walls includes a barrier that is airtight but allows moisture to escape from within the structure.
This is called a vapour permeable membrane.
In the past, the cavity was ventilated. Modern cavity wall construction requires that the cavity is sealed, and ventilation of the interior of the building is allowed through controlled vents.

## Slide 11
Machinery
While hand tools were still widely used, power tools and machinery were increasingly used to maintain efficiency, accuracy and productivity.
Cutting masonry materials is now often done by using powered masonry saws. These can be handheld or bench mounted, powered by electricity or by a petrol or diesel powered engine.

## Slide 12
Resources
Pre-1919 methods have given way to innovative construction techniques that speed up construction times and require less reliance on skilled labour.
An example is prefabrication of concrete units that include insulation and are built off site.
These can be quickly installed on site and a brick cladding can be added to produce a building with a traditional appearance.

## Slide 13
Any questions?