## Slide 1: Post-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify materials relevant to wall and floor tiling post-1919
  identify tools relevant to wall and floor tiling post-1919
  identify techniques relevant to wall and floor tiling post-1919

## Slide 3: Tiles post-1919
During this period tiles became more widely used and produced. Indoor plumbing became more common during this period, which lead to an increase in the use of ceramic bathroom tiles.
Tiles were popular in bathrooms as they were water-resistant and easy to clean.
The main types of tiles used at this time were:
quarry tiles produced in Wales
dust pressed tiles manufactured in Manchester and Dorset.

## Slide 4: Materials
Quarry tiles, known for their strength and durability, have been used for centuries. They are manufactured in a similar way to bricks, from quarried materials like clay and shales, fired at a high temperature. This production process makes them much stronger than clay tiles.
Quarry tiles were larger and thicker than other ceramic tiles and were commonly used for flooring.

## Slide 5: Materials
During the latter half of the century, porcelain tiles were increasingly used. Porcelain tiles were hardwearing and available as wall or floor tiles, for use internally and externally.
Unlike ceramic tiles, porcelain tiles did not need to be soaked before fixing, as they have a lower porosity level.

## Slide 6: Materials
Carter's Industrial Tile Manufactory in Dorset, now called Poole Pottery, began in the 1920s.
The Carter company produced many of the tiles used in London Underground stations built in the 1930, some of which can still be seen in stations.
The company continued producing tiles during and after World War II.

## Slide 7: Materials
In 1935 Albino Quiligotti established a company manufacturing Terazzo in Manchester.
They continued to expand over the years and are still production Terazzo tiles today.

## Slide 8: Materials
Lime mortar was commonly used up until the 1930s, when cement mortars gradually lime.
Over this period advancements were made in the production of plastics and resins. Whereas previously the same mortar used to fix the tiles was used for grouting, these advances resulted in the development of new types of adhesives and grouts. However, product choices were still fairly limited.
In earlier times, from the 1950s to the 1970s, grout was a more economical component, compared with tile cost per square foot, and a very wide joint — from 1/2 inch to 1 inch — was added to the installation. Color choice of grouts were very basic, with white cement wall grouts and gray cement and sand floor grouts.
Technical Focus: The Evolution of Grouts and Mortars | Floor Trends Magazine

## Slide 9: Industry standards: CP202
During this period, new industry standards were introduced.
What is an industry standard?
Standards are agreed ways of doing something, written down as a set of precise criteria so they can be used as rules, guidelines or definitions.
Information about standards | BSI (bsigroup.com)
The primary standard for tiling was CP202, which was published in 1972. It applied to all work involved in the laying and maintenance of clay floor tiles, concrete tiles, terrazzo tiles and slabs, brick floors, stone floors (both natural and cast, including marble, granite, quartzite and slate) and asphalt tiles bedded on a solid base.

## Slide 10: Tools
Advancements were also made in the development of electrically operated cutting tools. These tools, such as electric tile cutters, made tiling quicker and less messy work.
First Tile Cutter Invented by Boada Brothers
Electric tile cutter
Notes: First tile cutter © Kippelboy, https://commons.wikimedia.org/w/index.php?curid=19221371

## Slide 11: Techniques
Techniques for laying floor tiles depended on the construction of the floor. Tiles were laid in mortar either on a concrete base or a bed of hardcore, ashes or earth.
When tiles were installed on a timber substrate, either bitumen or a reinforced sand/cement screed was installed first.
For more information on flooring during this period: Evolution of Building Elements (uwe.ac.uk)

## Slide 12
Any questions?