## Slide 1: Wall and floor tiling Pre-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify materials relevant to wall and floor tiling used pre-1919
  identify tools relevant to wall and floor tiling used pre-1919
  identify techniques relevant to wall and floor tiling used pre-1919.

## Slide 3: Materials: tiles
From the mid-19th century tiles have been used on floors, hallways, porches and paths. In the late 1800s homeowners also began installing decorated wall tiles.
During this period, tiles were sourced from factories predominantly based in Stoke-on-Trent, which is known as the birthplace of the ceramics industry in the UK. Factories in this area are sometimes referred to as 'The Potteries’ and have shaped the industry for over 300 years.
The local availability of clay meant that the pottery industry grew in the area and new ceramic manufacturing techniques were developed by potters such as Wedgwood and Spode.

## Slide 4: Materials: tiles
Herbert Minton began encaustic-tile making again in England about 1843. This method was gradually overtaken by machine pressing drier clay to mass produce tiles.

## Slide 5: Materials: tiles
Ceramic tiles fall into two categories, according to their method of manufacture.
Extruding tiles: whose body is shaped in the plastic state in an extruder and the resulting column cut into tiles of predetermined thickness.
Dry-pressed tiles: which are formed of powder or small grains, shaped in moulds under high pressure before firing. These tiles are generally are made to finer dimensions than extruded tiles.

## Slide 6: Materials: tiles
A ceramic tile is made up of clays and other materials, which is formed when malleable then dried and fired in a kiln. The main body of the tile is called the bisque (or biscuit), and the face side can be glazed, partly glazed, unglazed (better for slip resistance), polished, textured or profiled.
Ceramic tiles were manufactured in a range of sizes and thicknesses. They were predominantly of square or rectangular shapes, but other geometrical shapes were available.
Ceramic tiles are suitable for fixing to walls and floors, but not all ceramic tiles can be used for floor applications. This is because most types of ceramic tiles have a higher water absorbing property, making them weaker than porcelain tiles.

## Slide 7: Tools
Power tools as we know them today were not available during this period. A limited range of hand tools were used instead.
What is meant by a hand tool?
A small tool (such as a hammer or wrench) that usually does not use electricity.
https://www.merriam-webster.com

## Slide 8: Types of hand tools used in wall and floor tiling
Basic tiling tools – such as trowels, hammers and chisels – have changed very little over many years.
Research other vintage hand tools like these that a pre-1919 tiler might use.

## Slide 9: Techniques: fixing and grouting
During this period, tiles were usually fixed with lime-based mortar.
Victorian buildings decorated with tiles prior to 1860 can be typically found to have either lime plaster or lime mortar used as the adhesive layer. Post 1870 the tile industry moved wholesale into the use of Portland cement as a medium for fixing and grouting tiles, and it is unusual to find any other medium used, but during the intervening decade either types of mortar can be found.
Nineteenth-Century Tiles (cam.ac.uk)

## Slide 10: Techniques: fixing and grouting
Because of their porosity, the tiles had to be soaked in water before they were set, in order for the cement to adhere to the tiles.
At this time, it was standard practice for the same mortar that was used to fix the tiles (sand and Portland cement) was also used for grouting. Tile joints were typically larger than they are today, due to the higher manufacturing tolerance size of the period.

## Slide 11
Any questions?