## Slide 1: 21st-century construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Session objectives
At the end of the session learners will be able to:
  identify materials relevant to wall and floor tiling
  identify modern techniques relevant to wall and floor tiling.

## Slide 3: Construction methods
Many of the materials, tools and techniques used for wall and floor tiling in the past are still relevant today, but there are also new products and systems available.

## Slide 4: Large/panel tiles
Today, there are a huge range of tile types to choose from. Large format tiles and panel tiles (tiles with surface area >1m² and any tile edge >1200mm) are increasingly popular.

## Slide 5: Large/panel tiles
can require specialist tools and equipment to move and install. These include:
Handling frames
Trolleys
Work benches
Suction pads.

## Slide 6: Large/panel tiles
When installing large or panel times, tilers need to be particularly aware of:
Manufacturing tolerances for the tile
Type of adhesive required
Correct application of tile adhesive
Tiles larger than 0.1m2 to be fixed above 3m from floor level should be secured by mechanical fixings

## Slide 7: Levelling sytems
Lipping, or lippage, is the term used to describe the difference in height of the installed tiles, which can be unsightly and hazardous. Lippage can be particularly noticeable when using larger tile sizes.
Levelling systems can be used to reduce lippage. These work by locking the edges of the tiles together to keep them level with each other. They are removed once the tiles are set.

## Slide 8: Uncoupling membranes
Uncoupling membranes can be installed over the floor substrate to reduce the risk of cracking or damage to the tiles caused by the substrate movement.
The uncoupling membrane sits below the tile and absorb the stresses that can occur between the substrate and tile.
Manufacturer instructions should be followed when installing tile on top of an uncoupling system.

## Slide 9: Tiling over underfloor heating
There are two types of underfloor heating tilers need to be aware of:
Hot water pipe
Electric
To counteract the shrinkage that can occur due to the changes in the floor temperature, special consideration must be paid to:
Preparation
Movement joints
Type of adhesives and grouts used.
Manufacturer’s instructions

## Slide 10: Tiling over underfloor heating
With underfloor heating, floors are subjected to significant thermal changes. The correct placement of movement joints is critical. Floors should be divided up into bays of size no greater than 40m² (25m2 for resin agglomerate tiles) with an edge length no greater than 8m. Movement joints must be formed around the perimeter (min 6mm).
Tiling-Guide-Download.pdf (tiles.org.uk)

## Slide 11: Tiling over acoustic systems
When installing floor tiles over acoustic systems, there is a risk of cracking caused by movement in the floor.
Flexible adhesives and grouts should be used to reduce cracking and manufacturer specifications must always be followed. Specialist membranes may also need to be installed between the acoustic system and the tiles.

## Slide 12: Pedestal systems
Adjustable pedestal systems can be used for outdoor tiling. They provide a raised, level surface that can be tiled without using adhesive, grout or mechanical fixings. They also create a gap beneath the tiles for water drainage.
The tiles are laid on top of the pedestals and the height can then be adjusted once they are in situ, to create a level surface.

## Slide 13
Any questions?