## Slide 1: PowerPoint 1: Pre-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Examine changes in construction methods over time
Objectives
Identify the materials and tools used in construction pre-1919
Explain the techniques used in construction pre-1919

## Slide 3: Methods of construction
    Pre-1919, it was common for buildings to be built from either solid brick (normally one brick thick, often referred to as a 9-inch solid wall), stone or timber. These materials were often locally sourced.

## Slide 4: Vernacular buildings and lime
    Buildings before 1919 were built using vernacular (locally available) materials, because transportation of materials only available in other areas was difficult. For example, areas of North Wales are well known for their slate quarries, so many of the older buildings in these areas are built from this material.
    Portland cement was not invented until 1824, so buildings before this date, and for some time after, were built using lime mortar. Lime mortar is more permeable and breathable than cement, meaning that:
    it takes longer to set, but
    buildings dry out independently as moisture can pass through the mortar and plaster more easily.
    This was important, as buildings were not required to be damp-proofed until 1875.

## Slide 5: Timber frame
    In addition to brick and stone, timber was used as it was still abundant throughout the UK. This was often called ‘post and beam construction’ as it consisted of frames of linked posts and beams. Carpenters built these frames and erected them to form the main supporting structure of the walls and roof.
Traditional woodworking joints were used to hold the timber together; for the most part, only hand tools were used.

## Slide 6: Carpentry tools
Pre-1919, carpentry was a little different to today. Hand tools would have been used to complete nearly all tasks. A carpenter's tool set would have included:
measuring and marking tools
handsaws
hammers, mallets and chisels
hand drills and drill bits
planes.

## Slide 7: Carpentry methods
Some of the techniques used pre-1919 are still used today but some were quite different. Obvious differences include the way in which people completed or used the following:
suspended ground floors
large supporting trusses in traditionally cut roofs
timber lintels and bressummers
trussed partitions.

## Slide 8: Suspended ground floors
These were used during the late Victorian period and still are today, although they are not as common. They consist of a series of timbers (joists) laid on the external walls at equal centres (normally 400mm or 16”). They are supported mid-span by a wall known as a sleeper wall. In addition to this, air bricks are installed at each end of the property to allow air to flow underneath the floor. This reduces the likelihood of damp and moisture damaging the floor and joists.

## Slide 9: Traditional trusses
Trusses have been used to construct roofs for many, many years. They consist of beams, posts, principal rafters and struts. For a traditional roof, they were used to support the ridge board/beam and purlins. They were normally made from oak and were joined together using mortice and tenon joints which were drawbore dowelled with large wooden pegs. The two most common types were king post and queen post trusses.
Also take a look at this labelled diagram of an early timber floor here.
Wikimedia Commons
Drawing by Bill Bradley at https://commons.wikimedia.org/wiki/File:Trad-queen-post.png
Notes: https://fet.uwe.ac.uk/conweb/house_ages/elements/section3.htm

## Slide 10: Traditional trusses
Mortice and tenon joints were used on oak trusses to join all of the components together. It is rare for any fixings other than wooden pegs to have been used. The joints were normally drawbore dowelled and that is where the pegs were placed to pull the joint tight.
Watch this video on how to make an oak truss.
Click here for another video on a drawbore!
Notes: https://www.youtube.com/watch?v=5ORTBR2uQ3Y&t=282s&ab_channel=FrenchFarmhouseDiaries
https://www.youtube.com/watch?v=w4hP6A68IFE&ab_channel=WoodByWrightASMR

## Slide 11: Traditional trusses
Trusses like these were placed on the external walls. A ridge beam and purlins sat on top of the truss or several trusses, depending on the size of the building. The carpenter hand cut each rafter and fixed it to the wall plate, purlin and ridge. The roof was then battened and covered.

## Slide 12: Bressummers and lintels
A bressummer is a large piece of timber used in timber framing to support the walls above it. They often span large distances. Wooden lintels are large timber sections used above openings such as windows and doors.
Normally the longer the span, the larger the section of timber that is needed.

## Slide 13: Trussed partition walls
Trussed partition walls were like a traditional roof truss: the main supporting elements were the diagonal rafter-like timbers and the timber at the base was like that of the bottom chord. The rest of the partition was very similar to a modern-day stud wall. The walls were designed to be self-supporting and also able to support loads from above.
Available at http://chestofbooks.com/
Notes: https://chestofbooks.com/architecture/Cyclopedia-Carpentry-Building-1-3/Trussed-Partitions.html

## Slide 14: Trussed partition walls
Some structural partitions were built not to be self-supporting but to support weight from above. The partition in the image is known as a braced partition.
Both types of partition walls were covered with laths (thin strips of timber). Plasterers would then cover this with a mixture of lime plaster and animal hair for binding.
Image provided courtesy of InspectAPedia.com ©
Notes: Image of plaster covering partition wall - https://inspectapedia.com/interiors/Wood_Lath_Plaster_Ceilings_Walls.php
InspectAPedia.com who contributed images or other material to this article is an independent publisher of building, environmental, and forensic inspection, diagnosis, and repair information for the public - InspectApedia.com has no business nor financial connection with any manufacturer or service provider discussed at that website nor here.

## Slide 15: Ironmongery and joints
Carpenters used woodworking joints far more often than metal fixings. Compared to today, ironmongery generally took much longer to make; there was no mass manufacturing or supporting infrastructure. Nails were produced by individual nailers, ironmongers or blacksmiths using wrought iron.
Scarf joint
Diagram of a tusk tenon joint
Example image of a mortice and tenon
Example image of cut nails
Photograph by Jay Rhind
Notes: https://www.woodsmith.com/article/loose-wedge-mortise-tenon-joints-basic-tusk-tenon/
https://www.vermonttimberworks.com/learn/timber-frame-joinery/traditional/
https://dontai.com/wp/2019/06/12/scarf-joint-for-wood-elegance-and-strength/
https://www.popularwoodworking.com/techniques/nails-for-woodworking/

## Slide 16
Any questions?