## Slide 1: PowerPoint 2: Post-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Identify post-1919 construction methods
Objectives
  Identify materials
  Identify tools
  Identify techniques relevant to roofing

## Slide 3: Materials
Slates and tiles are still common materials used for constructing roofs. Welsh slate is not so frequently used for roofs due to cost and availability. Slate may be used more for its durability qualities and specification requirements.
Tiles are available in a vast range of colours and textures.

## Slide 4: Materials (continued)
Different materials can be selected to suit a variety of conditions and environments.
Specially-shaped bonnet hip tiles can be used to create architectural features.

## Slide 5: Materials (continued)
Tiles
Tiles are manufactured from a range of materials.
Clay tiles have a more durable life span, with most manufacturers guaranteeing the colour and longevity for 60 years.
Concrete tiles are readily available and are the most used on new house construction where there is high demand.
Clay tiles
Concrete tiles

## Slide 6
Welsh slate roofs
Due to the high cost of production and availability, slate roofs are mainly installed on prestigious roofs and architect-specified roofs. They can last over 100 years when they are installed correctly and are graded/fixed into thin, medium and thick to ensure a perfectly finished roof.

## Slide 7
Installation of a slate roof
Slate roof installation has not really changed over the years, fixed with two copper nails and three nails to a slate and half.
Hook fixing slates is the preferred option in European countries but not in the UK, with only a few specified roofs being hook fixed.
Hook fixing slates
Copper nail fixing slates

## Slide 8
Roof tiles and felt underlay
Post-1919, and especially from the 1950s onwards, as demand for housing increased, mass-produced concrete roof tiles became a popular choice for roofing.
This is due to their greater availability, low-cost production and the speed of installation. The introduction of 1F felt underlay as a secondary protection helped to reduce air pressure in the loft space and prevent tiles being blown off the roof.
.

## Slide 9
Dry/wet fix ridge installation
Modern-day roof construction has seen the introduction of pre-formed dry fix systems for verges and ridges, as opposed to wet fix cement mortar, due to its low maintenance and easy fix with power tools, such as an impact driver.
Dry ridge system
Courtesy of Klober Ltd
Wet ridge system
Photograph by Chris Messenger

## Slide 10
Dry/wet fix verge installation
Usually made from strong plastic materials, dry verges are a quick and maintenance-free installation and can be fitted in adverse weather.
Wet fix is still required on listed buildings, but can only be installed in good weather, usually at a 3–1 ratio of sand and cement, unless lime mortar is specified.
Courtesy of Marley Limited
from https://specificationproductupdate.com/2019/02/26/marley-expands-dry-verge-range/

## Slide 11
Roof underlay
Modern roofs have underlay beneath the tiles/slates that includes a barrier that is airtight but allows moisture to escape from within the structure.
This is called a vapour permeable membrane.
The underlay below the tiles should be sealed with double sided tape on every lap to provide an airtight seal, which allows air out but prevents any water ingress.
Photograph by Chris Messenger

## Slide 12
Machinery
While hand tools are still widely used, power tools and machinery are increasingly used to maintain efficiency, accuracy and productivity.
Cutting masonry materials is often done by using powered masonry saws. These can be hand-held, or bench mounted, powered by electricity or by a petrol engine.

## Slide 13
Resources
Pre-1919 methods are giving way to innovative construction techniques that speed up construction times and require less reliance on skilled labour.
One example is prefabrication of GRP dormers and chimney units that include insulation and are built off-site.
These can be quickly installed on-site to produce a building with a traditional appearance.
Take a look at the images of GRP chimneys on ManFriday
Notes: https://manfriday.co.uk/grp-chimneys.php

## Slide 14: GRP roof products
Modern options for roof valleys
include glass reinforced plastic as opposed to traditional lead valleys.
The benefits of GRP valleys include: a product cost saving, as lead is more expensive; they are easy to install; there is good availability. GRP valleys come in three metre lengths and overlap by six inches (150mm), unless otherwise specified.
Manufacturer’s fitting instructions are on all products supplied.
Images of GRP roof products such as a valley trough and a dry fix valley can be viewed by clicking on the respective links.
Notes: https://www.roofgiant.com/grp-valley-troughs/hambleside-danelaw-3m-x-380mm-valley-trough-10-per-pack/
pp.smartsheet.com/sheets/283r2jwcR7hgQpg4v7Vp36WH76Wr8JJ5rMg77Cm1

## Slide 15: Roofing tools
Here are a small selection of common roofing tools and impact drivers used by the modern-day roofer.
Image of a slate knife and break iron
Slate pick
Courtesy of Collection of Auckland Museum Tamaki Paenga Hira
Impact driver for fixing GRP roof products
Image of a slate ripper for slate repairs
Image of a bench slate break iron
Image of a slate cutting and strike line products
Notes: https://www.burtonroofing.co.uk/index.php/slaters-axe-right-hand.html
https://www.roofingsuperstore.co.uk/product/roughneck-slater39s-ripper---one-piece-forged.html
https://www.roofingsuperstore.co.uk/product/roofers-edma-two-point-break-iron.html
https://www.burtonroofing.co.uk/edma-roofers-slaters-box-set.html

## Slide 16: Lead work as a roof weathering
Lead has been the preferred
weathering for roofs for
many years as it is a
malleable product and can be easily shaped.
With specialist tools, lead
can be formed to the required roof details needed and can last a long time.
Photograph by Chris Messenger
Image of a specialist roof tool

## Slide 17: Roof windows
Roof windows have developed over time from a single glazed piece of glass, to a cast iron top-opening window, to a modern wood/PVC window with pre-formed aluminium flashings.
Heritage windows are also available to suit listed buildings. They are mass produced in a factory so are a cost effective and quick installation option.
Take a look at examples of Heritage conservation windows here.

## Slide 18: Polymer-modified mortar
Preparing polymer-modified mortar can be done by mixing powdered or liquid form additives to the mortar mix and curing as normal on the roof, providing a much stronger bond of the ridge tiles to the roof. Unmodified mortar is simply a 20mm bedded mortar that does not contain polymer in the dry mix and is not as strong when cured.
Photograph by Chris Messenger
The polymer-modified mortar sets and hardens fast to give a repair of high performance, strength and hardness with a smooth finish, adding strength to the wet bedded ridge and verge mortar on a roof.

## Slide 19
Any questions?