## Slide 1: PowerPoint 1: Pre-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Identify pre-1919 construction methods
Objectives:
  Identify materials
  Identify tools
  Identify techniques relevant to roofing

## Slide 3: Materials: Timber for roofs
Timber has been used in construction for centuries.
In the past, roofs were constructed out of individual sections of oak timber and put together with mortice and tenon joints. These were held in place with oak pegs.
Photograph by Aleister Crowley under CC3.0 from Wikimedia Commons https://commons.wikimedia.org/wiki/File:Cruck.JPG

## Slide 4: Materials: Cruck roofs
Cruck roofs are still popular today but are very costly to produce. Restoration projects require the skills needed to construct this type of roof, dating back over 500 years.
Cruck roofs are strong, but require a lot of labour, expensive oak and traditional tools and skills.

## Slide 5: Materials: Oak pegs
Oak pegs are bevelled to be slotted into pre-drilled holes in the mortice and tenon joints and are very strong once in place.
.

## Slide 6: Tools required
Adze
A woodworking tool with a sloping steel or iron blade square off a wooden handle.
Hand-adze
A small lightweight tool meant to be used with one hand.

## Slide 7: Materials: Lime mortar
Lime mortar hardens at a slower rate than modern sand and cement mortar, which makes it easier to work with. Horsehair can be added to lime mortar to give added strength, and is a requirement for listed/ conservation buildings.

## Slide 8: Materials: Slate roofs
Slate has been used for many years to create a long-lasting weathering for buildings. Some slate roofs have been in use for centuries.
The process started with slate that was quarried by hand pre-1919.
Black and white print on engraving by William Banks & Son from Wikimedia Commons https://commons.wikimedia.org/wiki/File:Penrhyn_Slate_Quarries_(1131579).jpg

## Slide 9: Materials: Slate roofs (continued)
Prior to 1919, almost all roof
coverings were natural slate
quarried in Wales, Cumbria and Cornwall. The reason for this is because it was readily available and there was plenty of labour to quarry the slate.
Slate needs dressing from the bed of the slate to create a riven edge on the face of the slate.
Photograph by Chris Messenger

## Slide 10: Materials: Slate roofs (continued)
We frequently see it used to provide a weatherproof covering for roofs after the rock has been split into slates of the required size.
Photograph by Chris Messenger

## Slide 11: Materials: Slate roofs (continued)
Slates are dressed from the bed of the slate to show a riven edge on the face of the slate. On mitred slating, the slate is dressed from the face of the slate.
Cut and dressed slates can be laid in regular courses or diminishing courses.
When laying the slates, it is important to use a variety of widths and to keep at least 75mm (3 inches) side-lap (no less than the head-lap used).
Head lap is the distance the slate overlaps, not with the slate below but with the slate below that, to keep the roof watertight.
Photograph by Chris Messenger
Narrow slates, known as ‘backs’, should be seamed in on the next course above. It is advisable to lay the tails to a struck chalk line on the course below, to keep a straight and uniform margin.

## Slide 12: Tools
Power tools as we know them today were not available in the past. A range of hand tools were used.
The slater’s basic tools were:
a slate knife
a break iron
a hole scribe.
These tools have changed very little over many years.
Courtesy of Amgueddfa Cymru – National Museum Wales

## Slide 13: Setting out processes
Setting out the roof for slate includes a greater range of measuring and setting out processes in preparation for the slate roof.
Slates need to be graded into thick, medium and thin to ensure a well laid roof is installed.

## Slide 14: Techniques
Working methods and techniques for preparing and setting out slate roofs have changed very little since pre-1919.
Take a look at a labelled diagram of the structure of a slate roof.
Notes: https://www.pinterest.co.uk/pin/307441112052067108/

## Slide 15: Protecting the fabric of the building
Slate roofs have provided a long-lasting weathering to buildings for many years.
Weathering is very important, especially in pre-1919 buildings.
One issue that has caused slate roofs to fail is nail sickness, where the copper nail fails and slates then slide out of position.

## Slide 16: Thatched roofs
Thatched roofs have a long history that began with temporary shelters many years ago. Thatch was the most common roof covering throughout Britain until the end of the 19th century, and remains a viable, sustainable roof covering for rural and protected roofs. However, new thatched roofs require upgrading to meet fire prevention regulations.
Thatch roofing requires a high level of traditional skills to install, mainly by specialist roofing companies.
Click on this link for a diagrammatic explanation of thatching.
Notes: http://www.alanlewis-masterthatcher.co.uk/thatching-explained.html

## Slide 17: Stone slate roofs
Stone slate roofs are a natural stone product produced from local stone quarries. Splitting and dressing was and still is done by hand. The fixed hole was created by a pointed chisel, and oak pegs secured the slate by the hanging method on the lathe. Modern fixing is by plastic and aluminium pegs, but oak reed pegs are still needed for listed roofs.
Photographs by Chris Messenger

## Slide 18: Stone slate roofs
Photographs by Chris Messenger
Stone roofs are set out like slate roofs, using the same formulas. First batten is the length of slate, minus two inches plus half the batten (one inch). The batten gauge is the length of the slate-head lap (three inches) divided by two inches. Stone slate comes in diminishing sizes so, when changing sizes on a roof, half the difference in slate size must be taken from the above batten gauge to maintain head lap on the roof.

## Slide 19: Trussed roofing
Trussed roofs are a modern method of roof construction. They are factory manufactured quickly from architect's drawings and benefit from quick site installation.
Trusses come in many shapes and sizes and are held together with ‘gang nails’.
Kingpost
Double Fink
Inverted
Piggyback
Double Howe
Queenpost
Fink
Hip
Scissors
Studio
Howe
Fan
Modified Queenpost
Monopitch
Cathedral
Sloping Flat
Coffered
Dual Pitch
Attic
Gambrel
Stub
Flat

## Slide 20: Traditional or cut roofs
Traditional or ‘cut roofs’ require a lot of skill from the joiner to work out the geometry needed to cut the ‘bird’s mouth’ (beak) and the compound mitres needed for the roof. The joiner needs to have the skill to cut off the roof and put it together with great accuracy and a high level of finish.
Hypotenuse
Run
Rise
Angle “A”
90°
Tangent = Cosine =
The Right Triangle
Refer to the diagram given under the heading ‘Common rafters’ on Carpentry-Pro-Framer
Refer to the diagram given under the heading ‘Hip rafter side cut angles’ on Geocities
Refer to the diagram showing different types of rafters on Hammer&Hand
Notes: Websites referred to:
https://www.geocities.ws/xpf51/HVFRAMING/framing_angle_hip.html
https://www.carpentry-pro-framer.com/rafter-cuts.html
https://hammerandhand.com/field-notes/yamhill-vineyard-residence-rafters-set-for-pyramidal-hip-roof/

## Slide 21: Protecting the fabric of the building
Pre-1919, a key factor in maintaining ventilation in a building was the fireplace. This provided natural ventilation to reduce damp by drawing air into the building through doors and windows and up through the chimney.
The permeable materials such as lime mortar used in the walls also contributed to natural ventilation by providing a measure of ‘breathability’.
Diagram by Mike Jones

## Slide 22
Any questions?