## Slide 1: PowerPoint 1: Pre-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Examine changes in construction methods over time
Objectives
Identify the materials and tools used in construction pre-1919
Explain the techniques used in construction pre-1919

## Slide 3: Methods of construction
    Pre-1919, it was common for buildings to be built from either solid brick (normally one brick thick, often referred to as a 9-inch solid wall), stone or timber. These materials were often locally sourced.

## Slide 4: Vernacular buildings and lime
    Buildings before 1919 were built using vernacular (locally available) material, because transportation of materials only available in other areas was difficult. For example, areas of North Wales are well known for their slate quarries, so many of the older buildings in these areas are built from this material.
    Portland cement was not invented until 1824, so buildings before this date, and for some time after, were built using lime mortar. Lime mortar is more permeable and breathable than cement, meaning that:
    it takes longer to set, but
    buildings dry out independently as moisture can pass through the mortar and plaster more easily.
    This was important, as buildings were not required to be damp-proofed until 1875.

## Slide 5: Timber frame
    In addition to brick and stone, timber was used as it was still abundant throughout the UK. This was often called ‘post and beam construction’ as it consisted of frames of linked posts and beams. Carpenters built these frames and erected them to form the main supporting structure of the walls and roof.
    Traditional woodworking joints were used to hold the timber together; for the most part, only hand tools were used.

## Slide 6: Carpentry tools
Pre-1919, joinery was a little different to today. Hand tools would have been used to complete nearly all tasks. A joiner’s tool set would have included:
measuring and marking tools
handsaws
hammers, mallets and chisels
hand drills and drill bits
range of planes for mouldings.

## Slide 7: Sliding sash windows
The traditional sliding sash window was originated from the Yorkshire sliding sash and developed into what we know today. It was traditionally made with hand tools and simple woodworking joints.
Take a look at another image here
Notes: Another example image - https://chameleon-decorators.co.uk/wp-content/uploads/2022/06/period-sliding-sash-window-1024x768.jpeg

## Slide 8: Sliding sash window
This type of window was simple and effective to manufacture and to use.
The sashes are connected to sash cords, which have weights tied to the end.
The chords run over pulleys which assist with lifting the sash.
The weights are hidden in the external box and are accessible through a small opening on the inside of the frame for maintenance purposes.
These types of windows tend to be draughty, and maintenance is more time-consuming than that of a standard casement window.

## Slide 9: Sliding sash window – components
The components of sliding sash windows (see image on next slide) include some with unique names.
The design and manufacture of these windows was straightforward, matching the technology of the time. The processes have been adapted so that modern sliding sash windows comply with current building standards.

## Slide 10: Sliding sash window – components

## Slide 11: Sliding sash windows – construction
These windows were made originally by constructing a ‘box frame’ that would sit inside the window opening. The joints commonly used included:
housings and tongue and grooves (often used to join the box frame together)
mortice and tenons (used to join the frame to the sill and on the sashes).
Take a look at these images of 'Traditional Sash Window Working Drawings'
Notes: https://sashwindowspecialist.com/blog/drawings-and-profiles/

## Slide 12: Casement windows
    A casement window is another major element of pre-1919 architectural joinery, invented during the 18th century.
    The industrial revolution meant that stone and iron windows were phased out in favour of oak. Wooden frames were faster to produce and had thermal benefits.

## Slide 13: Casement windows – benefits
A casement window is less draughty than a sash window.
Maintenance is easier because all components are visible and easily accessible.
Greater ventilation and unobstructed views can be achieved as the entire area of window can be opened, unlike that of a sliding sash.

## Slide 14: Casement windows – manufacturing
    The casement window consists of an outer frame and a sill connected using mortice and tenons. Openings are created by joining mullions and transoms to the outer frame and each other as desired. The sashes are made, again using mortice and tenons, and then fitted to the frame with hinges.

## Slide 15: Casement windows – components
Find a labelled diagram here.
    A timber casement window has several components including:
    top rail
    friction hinge
    top hung fanlight
    head
    window frame
    transom
    jamb
    mullion
    cill
    locking handle
    direct glaze
    bottom rail
    stay
    casement
    stile.
Notes: https://www.bereco.co.uk/blog/timber-casement-windows

## Slide 16: Adhesives and glues
Glues used 100 years ago were very different from the array of specialist adhesives we use today. Glues were made from fish, milk (casien) and other mainly animal products.
The most popular interior glue was derived from the prolonged boiling of rabbit skins. This created a flake that was later dissolved in water and heated in a pot before use.
Scotch glue was made by boiling the skin and hooves of cattle and horses.
Wikimedia Commons
Photograph by Simon A. Eugster at https://commons.wikimedia.org/wiki/File:Rabbit-skin_glue_top_view.jpeg

## Slide 17: Primer paint
Windows during this time were often painted (except some that were made of oak). Regular painting was needed to preserve windows.
Most paints are part of a system of different layers; for timber windows it is often primer, then undercoat, then finish. Pre-1919, linseed oil and lead-based paints were often used.
Primers assist with the overall finish and offer a degree of protection to the timber. Therefore, it is best practice to apply primer as soon as possible, even if there is a delay before they are fully painted.

## Slide 18: The industrial revolution
One of the greatest impacts of the industrial revolution was the development of the factory process and machinery.
Before the industrial revolution, traditional hand tools were used to produce joinery items. This took many hours and required intricate methods, making the finished products expensive and almost exclusive to the wealthy.
The invention and use of the steam engine allowed for many machines to be powered via a spindle and leather belts.

## Slide 19: Powered machines
A series of belts, pulleys and shafts were connected to a power source, which could be a steam engine, turbine or even a water wheel. This power source would turn the belts, shafts and pulleys, which would then turn the machine.
Belt-driven tools were common and there was little regard for health and safety, as most of the components were unguarded.
Click here for an example image!

## Slide 20: Traditional machinery
    Following the industrial revolution, although there were some machines they could not perform all tasks and were not widespread. Therefore, many tasks would still be done by hand, particularly in smaller companies.
    Basic machines such as circular table saws, planers and band saws would have been common in workshops.

## Slide 21
Any questions?