## Slide 1: PowerPoint 2: Post-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Examine changes in construction methods over time
Objectives
Describe the evolution of modern construction methods and techniques
Describe the changes of materials and tools used in construction post-1919

## Slide 3: Methods of construction post-1919
    Following World War 1, there was a large drive towards building new homes. There were also some significant changes in how they were built, including:
    the introduction of cavities in external walls
    the use of concrete foundations
    incorporation of damp-proof course (DPC) in the walls.
    Taken together, these changes meant that homes were drier, more thermally efficient and more solid structures that were less susceptible to movement, cold and damp.
Cavity wall cross section diagram
Notes: https://probuildermag.co.uk/features/houses-time-safeguard-wars-part-two

## Slide 4: Post-1919 construction
After World War 2, the country needed rebuilding and there was a great strain on resources and workers. High quality design and efficient use of resources including timber were essential due to the reduced availability.
Homes were built in vast numbers following WW2 and so quality standards and manufacturing processes had to improve.

## Slide 5: Timber
    Construction methods and materials used began to change. Improved transportation and low local availability of some materials meant that the UK began to import more resources.
    For example, timber was imported from Canada and Scandinavia. To ensure imported timber was of consistent quality and size, the Canadian Lumber Standard (CLS) was introduced. Imported timber was milled to set sizes that we still use today.

## Slide 6: Timber preservatives
    For hundreds of years, tar oils and natural products such as pitch have been used as preservatives to protect and extend the working life of timber. As technology advanced post-1919, three main types of chemical preservatives emerged:
    water-borne
    oil-borne
    light organic solvent.
    Initially, they were applied using a brush or spray. In the 1960s, pressure treatment was developed.
Click here to take a look at a pressure treatment in process
Notes: https://www.brookridgetimber.co.uk/high-and-low-pressure-timber-treatments-the-difference-and-the-benefits/

## Slide 7: Timber framing
Following World War 2, there was an urgent requirement for many homes to be built quickly. Initially, timber framed houses were built and clad with asbestos. They were only intended to last around a decade until more permanent traditional buildings could be built, although some still do stand today.
Later, the construction process for timber framed houses was improved with the introduction of standardised timber and preservatives. More uniform pieces of preservative-treated timber meant that houses became easier to build, stronger and more durable.
    Click here to see an example image
Notes:     https://heritagecalling.com/2022/08/04/a-brief-history-of-prefabs/

## Slide 8: Sheet materials
    From the mid-1800s, layered sheet materials such as plywood were made from hardwood.
    During the 20th century, softwood began to be used. Softwood sheets were cheaper to manufacture and could be used for less decorative items.
    Glue technology also improved; animal-based glues were replaced with synthetic glues. This meant that sheet materials such as plywood were more reliable and easier to manufacture.

## Slide 9: Fixings – screws
Screws had been used for hundreds of years, but in 1932 and 1933 the Phillips screw and screwdriver were invented. This made screws much easier to fix and so they became a much more popular method of fixing.
This change accelerated after the Pozidriv was patented by GKN Screws and Fasteners in 1962.
These inventions, alongside the introduction of power tools, revolutionised the construction industry.
Take a look at the patents that revolutionised the industry!
Notes: https://www.wired.com/2011/07/0707phillips-screw-patent/

## Slide 10: Fixings – nails
From 1800 to 1900, the process of manufacturing nails improved significantly. Wire nails were easily made and were produced in large quantities.
In 1913, 90% of manufactured nails were wire nails, and they still dominate the market.
Nails went from being rare and precious to become a cheap, mass-produced commodity. How nails are made.
Click here to learn about the history of nails
Notes: https://www.youtube.com/watch?v=CUTTmtLKD2g&t=48s
Image https://www.fastenerdata.co.uk/nail
.

## Slide 11: Ironmongery
Ironmongery
During this time proprietary ironmongery became more readily available this meant that a variety of ironmongery from one range was available. This and mass manufacturing assisted the industry by giving consistency.
Click here for examples of connectors
Notes: https://www.strongtie.co.uk/en-UK/product-lines/connectors-for-masonry-timber-and-steel-construction

## Slide 12: Fixings – joist hangers and truss clips
During the 20th century, proprietary fixings such as joist hangers and truss clips were developed. These replaced complicated woodworking joints that were time-consuming to produce.
This increased greatly the speed of construction.
The joist hanger was invented in 1956 and is still used today.

## Slide 13: Power tools
1889 – the first electric drill was invented in Scotland; however it was very large and immovable, so was used only in factories.
1916 – Black and Decker invented a portable handheld drill with a pistol grip.
1932 – Bosch produced the first hammer drill.
1961 – Black and Decker produced the first cordless drill.
Milwaukee, Dewalt, Bosch, Fein and Festool were just a few of the other companies that further developed these power tools, which revolutionised the construction industry.
History of Power Tools
Image of an electric drill
Notes: https://www.ecmag.com/magazine/articles/article-detail/your-business-100-years-innovation-history-electric-drill

## Slide 14: TRADA
    TRADA (the Timber Research and Development Association) was formed in 1934.
    It is an international organisation that provides information about the timber industry to stakeholders, ranging from producers and manufacturers to the end users.
    TRADA had a large impact on the carpentry and joinery industry:
    They pushed for timber to be used more in construction.
    They tested, inspected and certified timber to ensure it met strength standards that we still follow today.
    Please note that the TRADA brand is no longer in existence; it has been superseded by the merger of Timber Trade Federation and TRADA, the new entity being Timber Development UK.
Notes: https://trada.azurewebsites.net/

## Slide 15: Span tables
    Towards the end of the 20th century, span tables were introduced to enable people in the construction industry to determine what sizes of timber would be required for a variety of spans.
    This method can still be used today as a guide. However, in most cases nowadays these sizes are determined by a structural engineer; they are not decided by a joiner.
Click on this link to take a look at examples of span tables
Notes: https://nhbc-standards.co.uk/6-superstructure-excluding-roofs/6-4-timber-and-concrete-upper-floors/6-4-8-timber-joist-spans/

## Slide 16: Modern roof truss
    Until the 1960s, timber trusses were used in the construction of roofs and steel bridges with the help of timber joints.
    In 1955, the gang-nail connector plate was invented: a metal tie for timber construction that required no screws, glue or other nails. They are used to this day.
    In the 1960s, the modern timber roof truss using gang-nail plates was introduced. They are used to this day.
    Today, trusses are made offsite and then lifted into position, normally at 600mm centres. This is a much quicker method for producing roofs.

## Slide 17
Any questions?