## Slide 1: PowerPoint 3: 21st century construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Examine changes in construction methods over time
Objectives
Describe 21st century construction techniques and technologies
Describe the principles of the circular economy, sustainable design and retrofit
Explain the techniques of insulation and ventilation
Identify new and emerging technologies in construction

## Slide 3: Surveying
    Surveying methods have changed significantly with the use of new technology. The traditional process of surveying involved using equipment such as chains, levels and theodolites (optical instruments) to determine the terrain and locate existing elements of land or buildings.
    Modern methods incorporate the use of drones, laser scanners and other measuring devices.

## Slide 4: Design – changes in technology
    Technology has revolutionised the design process for construction.
    Traditionally architects would draw and amend plans for buildings by hand, which was a time-consuming process.
    In the 21st century, buildings are designed on computers. They enable us to visualise what buildings will look like and anticipate any complications that may arise during the construction process.

## Slide 5: Design – CAD, 3D modelling, AR/VR simulation, BIM
    Design and construction teams use computer-aided design (CAD) software, 3D modelling and simulation within virtual or augmented reality (VR/AR). Not only do these processes directly assist those teams, but also they enable the client to see the design and visualise the end-product in much greater detail than ever before.
    Building information modelling (BIM) brings together the outputs of these processes and helps to reduce cost and time on construction projects.

## Slide 6: 21st century construction methods
    In our current age, construction has changed greatly from its humble origins, particularly in the last 100 years. There is now a large number of regulations and standards that we must follow. Some methods are entirely new, but in many cases previously existing methods have been adapted. For example, the cavity masonry wall is still widely used; but floors and walls now accommodate modern standards of insulation and damp proofing.
Take a look at a rough diagram illustrating floor insulation

## Slide 7: 21st century construction methods
    Technology is always advancing, so it stands to reason that the construction industry is doing the same. Modern construction methods include:
    prefabrication
    volumetric
    panelisation
    timber frame
    modular.

## Slide 8: Methods – prefabrication
    Prefabrication or ‘prefab’ is a building process that involves parts of a building being built offsite, for later assembly onsite. Materials used in prefab include timber, concrete and composite materials.
    For example, modern timber frames are often built offsite, then transported to the construction site and assembled there.
Take a look at an example of an offsite location
Notes: https://www.stocorp.com/panelization-us/

## Slide 9: Methods – volumetric
    Volumetric construction is used in the fabrication of modular buildings. It involves making offsite factory-finished modules that are then stacked, joined and assembled onsite to form a complete building.
Click here to see an example image of repeat design in construction

## Slide 10: Methods – panelisation
    Panel units are produced 'offsite' in a factory under a quality-controlled process, then assembled onsite to produce a three-dimensional structure. The panels may consist of wall, floor or roof units, sometimes referred to as ‘cassettes’.

## Slide 11: Methods – timber frames
    You may think that timber framing is nothing new. This is true, but the methods have changed and become far more efficient both in their design and their construction.
    Timber framed buildings are often built offsite in factories or warehouses. This process helps reduce waste and causes less impact on the environment. It also reduces the impact of external factors such as the weather on the construction process.

## Slide 12: Methods – modular
    Another type of prefab building. Modular buildings are when entire sections of buildings e.g. rooms are constructed in a factory or warehouse. This method is very useful when repeat design is required, for example in blocks of flats or student accommodation.

## Slide 13: Key elements – circular economy and sustainability
    Circular economy – an economic system based on the reuse and regeneration of materials or products, especially as a means of continuing production in a sustainable or environmentally friendly way. For example, planting trees to replace what we use or recycling materials.
    Sustainable design – building design intended to reduce impacts on the environment and the health and well-being of the building’s users. Modern materials and techniques create buildings that are efficient in several ways, e.g. they require minimal energy to heat. Methods used include moisture management, ventilation and products such as insulation. This enables us to control the operation of the building in a far better way and ensure that it continues to perform as required in the future.

## Slide 14: Key elements – retrofitting
    Retrofitting – ‘retrospectively fitting’ is a change to the building after it has been completed. As there are always advances in technology and construction methods it is inevitable that this will take place. Examples include:
    installing UPVC windows to replace timber-framed windows
    installing external and internal wall insulation (EWI and IWI).
    These two examples of additions to buildings can greatly improve their thermal efficiency. However, if they are used on an unsuitable building or are installed incorrectly, they cause more problems than they fix.

## Slide 15: Materials
    The construction industry has developed techniques to produce a vast range of composite and modified materials, such as:
    composite timber
    acetylated timber
    reinforced concrete.
    Products made from these materials improve quality, performance and aesthetics. Examples include:
    cladding
    doors
    decking.
Example of woodgrain wall cladding
Example of Accoya wood

## Slide 16: Power tools
    With battery technology ever advancing, the ability to use cordless power tools has greatly increased. There is now a very wide range of corded and cordless tools that are safer, easier and lighter to use than ever before.

## Slide 17: Keeping up to date
    Trade bodies such as Build UK, FENSA, NHBC and the Federation of Master Builders all provide information on construction and its ever-changing techniques and priorities. Joining these bodies can help you maintain your knowledge and provide you with continuing professional development (CPD) opportunities.
    Product manufacturers also provide vital information; this gives the best up-to-date advice on installation, usage, care and maintenance of a product.

## Slide 18
Any questions?