## Slide 1: PowerPoint 2: Post-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Examine changes in construction methods over time
Objectives
Describe the evolution of modern construction methods and techniques
Describe the changes of materials and tools used in construction post-1919

## Slide 3: Methods of construction post-1919
    Following World War 1, there was a large drive towards building new homes. There were also some significant changes in how they were built, including:
    the introduction of cavities in external walls
    the use of concrete foundations
    incorporation of damp-proof course (DPC) in the walls.
    Taken together, these changes meant that homes were drier, more thermally efficient and more solid structures that were less susceptible to movement, cold and damp.
A labelled diagram of a cavity wall
Notes: https://probuildermag.co.uk/features/houses-time-safeguard-wars-part-two

## Slide 4: Post-1919 construction
After World War 2, the country needed rebuilding and there was a great strain on resources and workers. High quality design and efficient use of resources including timber were essential due to the reduced availability.
Homes were built in vast numbers following WW2 and so quality standards and manufacturing processes had to improve. The introduction of joinery manufacturing standards by organisations like the EJMA (English Joinery Manufacturers Association) helped drive these improvements.

## Slide 5: Timber developments
Post-1919, comb (or finger) jointing became more commonly used to end joint timber. This was a more economic way of using raw materials. It also meant that manufacturers could create longer pieces of timber and boards.
Photograph by Jay Rhind

## Slide 6: Engineered timber
Engineered timber was introduced for a number of reasons. It makes use of the less desirable sections of timber left over from a sawmill: rather than having to find large sections of timber, smaller sections can be glued together and provide the same (if not better) strength and quality as solid timber.
Examples of engineered timber include:
acetylated timber
laminated veneered lumber (LVL)
laminated strand lumber (LSL)
oriented strand board (OSB)
plywood
glulam.

## Slide 7: Acetylated timber
This type of timber originated in the 1930s. It is softwood that goes through a chemical process.
During the process, the timber is made more stable by reducing its hygroscopic properties. This means that the timber is less likely to take on water from its surroundings, so that it is likely to shrink or expand.

## Slide 8: Sheet materials
    From the mid-1800s, layered sheet materials such as plywood were made from hardwood.
    During the 20th century, softwood began to be used. Softwood sheets were cheaper to manufacture and could be used for less decorative items.
    Glue technology also improved; animal-based glues were replaced with synthetic glues. This meant that sheet materials such as plywood were more reliable and easier to manufacture.

## Slide 9: Adhesives
Adhesives developed hugely post-1919. Animal-based glues were replaced with a range of synthetic adhesives that were tailored to specific uses and based on different raw ingredients. For example, adhesives can be on water-, rubber- and plastic-based. Some adhesives are also waterproof.
Examples include:
polyvinyl acetate (PVA)
polyurethane
cyanoacrylate
epoxy.

## Slide 10: Timber preservatives
    For hundreds of years, tar oils and natural products such as pitch have been used as preservatives to protect and extend the working life of timber. As technology advanced post-1919, three main types of chemical preservatives emerged:
    water-borne
    oil-borne
    light organic solvent.
    Initially, they were applied using a brush or spray. In the 1960s, pressure treatment was developed.
Click here to see the pressure treatment process!
Notes: https://www.brookridgetimber.co.uk/high-and-low-pressure-timber-treatments-the-difference-and-the-benefits/

## Slide 11: Ironmongery
Developments in manufacturing improved the ironmongery used in joinery. More reliable and accurate hinges and locks improved the security and heat performance of windows and doors.

## Slide 12: Machinery
Machinery advances provided a greater range of more developed machines. For example:
spindle moulders for profiling
finger joint machines
sanding machines.
These machines provided greater accuracy and improved the reliability of products. They also enabled the use of more complex jointing methods without increasing the time needed to make the joints.

## Slide 13: Power tools
1889 – the first electric drill was invented in Scotland; however it was very large and immovable, so was used only in factories.
1916 – Black and Decker invented a portable handheld drill with a pistol grip.
1932 – Bosch produced the first hammer drill.
1961 – Black and Decker produced the first cordless drill.
Milwaukee, Dewalt, Bosch, Fein and Festool were just a few of the other companies that further developed these power tools, which revolutionised the construction industry.
History of Power Tools
Image of an electric drill
Notes: https://www.ecmag.com/magazine/articles/article-detail/your-business-100-years-innovation-history-electric-drill

## Slide 14
Any questions?