## Slide 1: PowerPoint 1: Pre-1919 construction practices
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Aim: To explore pre-1919 construction practices
Objectives
  Explore the impact of transport constraints on material choices.
  Compare the different materials used in pre-1919 construction.
  Identify the common binders and mortars used pre-1919.
  Discuss the use of lime in pre-1919 construction.
  Describe pre-1919 internal and external finishes.

## Slide 3: Transport constraints on material choices
  Pre-1919 construction resources in Wales were predominantly sourced and used locally due to transport constraints.
  The availability of local materials heavily influenced the type and look of buildings in the region during that time.
  The predominant use of locally sourced materials was largely influenced by the transportation limitations of the time.
  Before the advent of modern transportation infrastructure, such as railways and highways, the movement of heavy construction materials over long distances was laborious and expensive.
  As a result, builders relied on resources available near to the construction site, leading to the distinctive regional architectural styles.

## Slide 4: Materials used in pre-1919 construction: stone
  Wales is known for its abundant natural resources of various types of stone, such as limestone, sandstone and slate.
  This stone were extensively used in construction.
  Quarrying was the primary method of sourcing stone.
  Local quarries provided easy access to these materials, minimising transportation costs and logistical challenges.
  The use of local stone resulted in the distinct appearance of Welsh buildings, characterised by their sturdy and durable nature.

## Slide 5: Materials used in pre 1919 construction: slate
  Wales, particularly North Wales, was renowned for its high-quality slate deposits.
  Slate quarries, such as those in Blaenau Ffestiniog, Llanberis, and Bethesda, produced large quantities of slate for roofing and cladding.
  The transport of heavy slate slabs over long distances was impractical due to the logistical difficulties of moving such weighty materials.
  As a result, the use of slate was prevalent in local construction, giving rise to the distinctive appearance of Welsh slate roofs.

## Slide 6: Materials used in pre 1919 construction: timber
  Wales had substantial woodland resources and timber was an essential construction material.
  Local forests provided a ready supply of timber for framing, flooring and joinery.
  The transport of large timber beams or planks over long distances was challenging, so the use of local timber was a practical choice for builders.

## Slide 7: Materials used in pre-1919 construction: bricks
  While stone and slate were the primary construction materials, bricks were also used, particularly in urban areas.
  Brick production in Wales was limited compared to other regions, and the availability of suitable clay deposits played a crucial role in the production of bricks.
  Local brickworks were established near areas with accessible clay deposits which ensured a local supply and reduced transportation costs.

## Slide 8: Binders and mortars used pre-1919
  Various binders and mortars were employed in building construction in Wales before 1919. These materials were critical in connecting and stabilising the structural parts, giving overall strength and longevity.
  Different types of lime were used for the construction of buildings. Lime played a crucial role as a binder in mortars, plasters and other applications, providing strength, durability and workability to the construction materials.
  Other mortars and binders include clay and cement. These mortars were used in specific cases, depending on factors such as availability, cost and specific construction needs.
  These different binders and mortars contributed to the distinct construction techniques and architectural styles of the time.

## Slide 9: Binders and mortars used pre-1919
Cement mortar
  While not as common as lime-based mortars, cement mortar was employed on occasion in pre-1919 Welsh building.
  During that time, the most frequent form of cement was Roman cement, which is a naturally occurring hydraulic cement.
  It was created by combining clay and limestone and burning them together.
  Cement mortar was stronger and set faster than lime mortar, although it was often more costly. Its applicability was restricted to certain applications requiring greater strength or faster building schedules.

## Slide 10: Binders and mortars used pre-1919
Clay mortar
  Clay mortar was used in some rural locations when the supply of lime or cement was restricted.
  When clay soil was combined with water, it created a workable mortar that could be used to join bricks or other building materials.
  While clay mortar offered some cohesiveness, it was less robust and more prone to water damage than lime or cement mortars.

## Slide 11: Use of lime in pre-1919 construction
Various varieties of lime were used in pre-1919 Welsh building.
  Fat lime, also known as non-hydraulic lime or quick lime, was the most widely used because of its outstanding workability and self-healing qualities.
  Fat lime is characterised by its plasticity and workability, making it suitable for creating flexible mortars and plasters.
  It has excellent self-healing properties, allowing it to accommodate slight movements in the building without cracking.
  Fat lime mortars were used for bonding stone and brick masonry, as well as for rendering and plastering interior and exterior surfaces.
Notes: Lime is produced by calcining (burning) limestone at relatively low temperatures, typically around 900-1000 degrees Celsius.
Fat lime does not possess hydraulic properties and sets solely by carbonation, which is the absorption of carbon dioxide from the air. It is often obtained from limestone with a low clay content.

## Slide 12: Use of lime in pre-1919 construction
  Hydraulic lime offers increased strength and faster setting times compared to fat lime. It is suitable for applications that require higher load-bearing capacity or exposure to dampness.
  Hydraulic lime mortars were used in areas such as foundations, basements or in buildings subject to more significant water ingress or higher mechanical stresses.
  There were different categories of hydraulic lime, distinguished by their hydraulic strength and setting properties including: feebly, moderately hydraulic lime and eminently hydraulic lime.
  The selection of the appropriate type of lime depended on factors such as the specific requirements of the construction project, local availability, and the desired performance of the mortar or plaster.
Notes: Hydraulic lime is a type of lime that possesses both hydraulic and non-hydraulic properties. It sets and hardens through a combination of carbonation (like fat lime) and hydraulic reactions with water. Hydraulic lime is produced by calcining limestone containing a higher clay content, typically between 5% and 30%. The presence of clay imparts the hydraulic properties to the lime.
Feebly Hydraulic Lime: This type of hydraulic lime has a relatively low hydraulic strength and sets slowly. It was suitable for applications where moderate strength and slow curing were desired, such as in damp or wet environments.
Moderately Hydraulic Lime: Moderately hydraulic lime has a higher hydraulic strength and sets more rapidly than feeble hydraulic lime. It was used in applications requiring a balance between strength and setting time.
Eminently Hydraulic Lime: Eminently hydraulic lime has the highest hydraulic strength and sets rapidly. It was used in applications where quick setting and high strength were crucial, such as in marine or industrial environments.

## Slide 13: Pre-1919 internal and external finishes
  Plaster was a widely used finish for interior walls and ceilings. Lime plaster, made from a mixture of lime, aggregate (such as sand) and water, was commonly used.
  Lime plaster had excellent breathability, allowing moisture to evaporate and preventing trapped moisture from damaging the walls.
  Heavy timber-framed buildings had infill panels made of lime and mud-based daub applied onto thin wooden slats or a lattice of woven sticks called wattle.
  Later, lime plaster was applied onto riven or sawn timber laths nailed to the timber framing. In some areas, timber framing was clad with timber boards or clay tiles.

## Slide 14: Pre-1919 internal and external finishes
Timber floorboards, stone flooring, quarry tiles and cement screeds were common in pre-1919 residential buildings.
Construction methods were labor-intensive, relying on traditional craftsmanship and manual techniques.
Solid flooring was made of earth or concrete slabs and was typically completed with stone slabs or clay tiles. Plaster was also used in regions where gypsum was abundant.
Floors were built on timber or stone subfloors supported by wooden joists, and the choice of flooring material reflected practical needs and local resources, contributing to the building's character and functionality.

## Slide 15: Pre-1919 internal and external finishes
  The roof structure was generally composed of wood and built using traditional methods.
  Rafters, purlins, ridge beams and supporting struts formed the timber structure and they mostly remained exposed.
  Welsh slate was commonly employed because to its durability, while clay tiles were an alternative.
  Thatch roofs were widespread in rural regions and the primary material for the roof construction was timber.
  The choice of roofing materials and construction techniques contributed to the architectural character and regional identity of the buildings.

## Slide 16
Any questions?