## Slide 1
PowerPoint presentation
Unit 202: Changing practices over time
PowerPoint 3: Know the changes in construction methods over time

## Slide 2: AIM: 21st century construction techniques and technologies for chosen trade
Objectives
Electrical installation: electric vehicle charging points, smart metering, battery technologies, smart homes, controls, 3D modelling/printing and immersive technology.
Learners to know how to access information on new developments in their trade, such as through professional engineering institutions, industry bodies and trade associations, articles, trade press, formal CPD, manufacturers information etc.
Learners to be able to recognise how keeping up to date with industry initiatives and developments can help BSE businesses, the sector and the environment.

## Slide 3: Traditional versus modern – pre- and post- 1919
Most traditional (older) buildings were made of permeable (not waterproof) materials that do not provide a barrier to external moisture.
This creates a ‘breathable’ form of construction. As a result, the permeable fabric tends to absorb moisture which is then released by internal and external evaporation.
This can lead to the ingress of “damp” that will in turn cause damage to the structure of the building or, worse, the health of the occupants.
With the introduction of industrialised manufacturing and improved material technology, there was greater control of the quality and standard of the build.

## Slide 4
Components are constructed in a factory or workshop situation, transported to site and erected.
There are four main types of offsite construction.
Offsite manufacturing

## Slide 5
In panelised systems, all the panels required to construct the building are made off site then assembled on site.
Panelised systems
Notes: https://www.willmottdixon.co.uk/expertise/off-site-manufacturing

## Slide 6
“Modules” such as bedrooms and bathrooms are pre-made and joined together on site.
They are also pre-fitted with all services, such as electrical, plumbing etc.
Volumetric modular systems

## Slide 7
Hybrid systems are a mix of volumetric and panelised systems.
Take a look at the diagrams given under “Figure 1: Forms of offsite construction” here: Offsite construction and pre-manufacture.
Hybrid systems
Notes: https://www.pbctoday.co.uk/news/mmc-news/offsite-construction-landscape/80122/

## Slide 8
Sub-assemblies are constructed offsite and then joined together onsite to create structural units onsite.
Examples include stairs, dormers, chimneys and electrical wiring.
Sub-assemblies and components
Example image
Notes: https://camtechbp.co.uk/2021/03/18/who-knew-prefabricated-chimneys-could-look-this-good/

## Slide 9
Safety can also be improved by using offsite construction.
Examples include reducing the amount of time workers spend working at height.
Offsite manufacturing

## Slide 10: Wiring systems for prefabricated or modular systems of building
Wiring systems for prefabricated or modular systems of building are often referred to in generic terms as ‘modular wiring’ or ‘plug-and-play’.
There is still a requirement to keep to BS 7671, however there is an accompanying standard for prefabricated wiring systems which is BS 8488:2009+A1:2010.
The following specification should also be considered: Specification of prefabricated wiring systems - Wiring matters.

## Slide 11: Wiring systems for prefabricated or modular systems of building
Take a look at (PDF) page number 9 of this document to see an image of an area distribution box: Prefabricated Wiring System Specification Explained
Notes: C:\Users\User\Downloads\PrefabricatedWiringSystemSpecificationExplained.pdf

## Slide 12: Pros and cons of prefab or modular build homes
Advantages
      Easy to build
      Cheaper
      Consistent quality
      More eco friendly
      Quicker to build
Disadvantages
      Can be difficult to get a mortgage for non-traditional builds
      Land restriction on the types of building that are allowed
      Resale issues, including value
      Equipment access required
      Changes can be difficult
      Problems may only be apparent on delivery onsite

## Slide 13
Conserving energy in older houses
It is also important to make existing houses more energy efficient.
By adding insulation, double glazing and more efficient heating systems, older houses can be brought up to date with modern energy requirements.
By not demolishing and not building a new building, fewer raw materials and less waste disposal is required.

## Slide 14
Conserving energy
Energy can also be saved by fitting items such as movement sensitive lighting, which will switch off if no one is in the room.
Solar panels and ground source heat systems can also be installed.
Follow this link to view a diagram of a ground-source heat pump.
Notes: https://www.pinterest.co.uk/pin/dispelling-the-myths-of-ground-source-heat-pumps--687784174336471482/

## Slide 15
EV charging
The government plan to phase out cars that use fossil fuel by 2030 and hybrid vehicles by 2035. However, recent budgetary pressures have thrown this timetable into doubt.
This means that the only viable alternative available at the moment is an electric vehicle.
There has to be a widespread national installation campaign to provide chargers, not only at home but also on the road. This requires a major increase in power generation capacity.
There are currently EV installation incentives for the government to offer up to 75% of the costs.

## Slide 16
EV charging
Off-road parking must be used.
A normal socket outlet only allows a trickle charge and can take 30 hours for a full charge.
EV chargers cannot be connected
to the popular TNCS supply. A TT
provision must be installed.
Typical 7KW EV unit installation
still takes about 10 hours for a full
charge.

## Slide 17
Smart homes
In 1999, an American company called IBM coined a phrase “The Internet of Things” (IoT).
It refers to a network of devices or appliances that have network (typically internet) connectivity that allows them to collect and share data and perform functions.
These devices, also known as “smart objects”, can range from simple “smart home” devices like smart thermostats, to wearables like smartwatches.

## Slide 18
Smart homes device examples
Examples of smart devices used in the home include:
wireless thermostat
smoke alarms
intruder alarm systems
video doorbells
entertainment systems
Alexa or Google assistants
heating controls
lighting controls
protection device monitoring
Smart metering.

## Slide 19
Smart meters
Nearly half of all domestic and small business meters are now smart meters.
A smart meter has two main parts. The meter itself, which uses a secure wireless link to automatically to send your meter readings and the in-home digital display that shows you what energy you’re using, when and how much it costs.

## Slide 20
Advantages of a Smart meter
Cheaper tariffs are made available
You can understand your usage more clearly
No need to have or send meter readings
More accurate bills as no estimates are needed
Incentives to switch are available
Contributes to greener energy because demand planning is more accurate.

## Slide 21
Immersive technology
Designers, Engineers and technicians use immersive technology to help them understand and investigate the layout of a building and the performance of building material and design.
This is sometimes known as augmented or virtual reality.

## Slide 22
Immersive technology and VR in construction
3D visualisation of a building design
It can be used onsite to see where
equipment is to be installed.

## Slide 23
3D modelling and printing
To shorten the development time from concept through to final product, design houses can produce a 3D model of their design very quickly by using a 3D printer.
Whether its a building, a new remote control or a new socket outlet design, the design aspects and production feasibility of the product can be tested very quickly by printing a prototype.
3D printing is used as a method of creating a three-dimensional object layer-by-layer using a computer created design. The 3D printer lays down dots of hot plastic to create a 3D part that is to be tested/investigated.

## Slide 24
3D modelling and printing
A 3D printer can be used to create complex designs in order to explain ideas
Image of a 3D printer showing
the filament reel

## Slide 25
Continual professional development (CPD)
An electrician will never stop learning throughout his/her career.
The demands on any electrician will include:
Regulatory and legislative requirements. BS 7671 is typically revised every two to three years.
New product and installation techniques.
The latest materials, cables and power tools.
New technology or services that the customer is interested in buying.
Heating system developments.
This can only be achieved through regular and committed CPD.

## Slide 26
Ways to achieve CPD
CPD is key to keeping relevant and competent. The following resources can help:
professional magazines or journals
books
electrician forums
new qualifications (EV, solar, I&T)
updated courses (BS 7671)
manufacturer’s data
YouTube videos or similar
open discussions with peers and colleagues
coffee culture at the wholesalers or testing ideas with others.

## Slide 27
Any questions?