## Slide 1
PowerPoint presentation
Unit 202: Changing practices over time
PowerPoint 1: Know the changes in construction methods over time

## Slide 2: AIM: Know the changes in construction methods over time
Objectives
  Understand local needs and geographical influences
  Know the basic qualities and uses of mortars, aggregates, binders, internal and external functional and decorative finishes, stone, slate, timber and earth
  Understand construction materials available within a locality, including an understanding of local geology, and the accessibility of these materials, including local quarries and transportation links both past and present
  Know the permeable nature of lime and earth mortars

## Slide 3: Pre-1919 construction methods
When man stopped roaming and began farming, humans were rooted to the area they farmed. Societies started to build structures where they would be protected from the elements (weather).
One contentious theory says this happened 11,000 years ago in a place called Göbekli Tepe in modern-day Turkey.

## Slide 4: Transporting materials
Before the industrial revolution, builders had to use materials which were close at hand as it was very difficult to transport materials using just a horse and cart.
The industrial revolution began in earnest by the 1830s and, in Britain, by the 1840s.

## Slide 5: Diagram of an older building
Glass, for example, was hand blown till the 1919–1920 when mechanised rolling was developed.
Slate
Quarried locally
Hand made window from local timber
Local stone
Lime wash paint / render
Thatch
Farmed locally

## Slide 6: Building materials in older buildings
The materials used for building depended on where in the UK the house was being built.
Areas such as North Wales had easy access to stone and slate whereas, in other areas, timber was plentiful so timber-framed houses were built.

## Slide 7: Timber-framed buildings
Timber-framed buildings were a quick and cheap way to put up the structure. However, the voids needed to be filled with methods like brickwork or wattle and daub which can be a render or a plaster.

## Slide 8: Diagram of an older building
Timber frame
Larger stones
Smaller stones or bricks
Infill construction
Solid wall
Clay tiles
Wood shingles
What is the problem with this wall?

## Slide 9: Flint
Some areas of the country had access to a hard stone called flint.
Here is a wall made partly from flint.

## Slide 10: Local building materials in older buildings
Limestone
Sandstone
Slate
Granite
South Yorkshire / Derbyshire
Wales, West of Scotland
Wales (thinnest slates), Cornwall
Scotland, Wales (radon is an issue)

## Slide 11: Local building materials in older buildings
Chalk
Marble
Flint
North and South Downs
Iona and Connemara
Norfolk, Suffolk. Found in chalk as nodules

## Slide 12: Early high-status buildings
Before the industrial revolution, some people who could afford the high cost of transport could construct their buildings with materials from around the country.

## Slide 13: Transportation of materials
As canals and railways were built during the industrial revolution, more buildings were built using materials from further afield. These included schools, factories and bigger houses for the middle classes.
During this time, bricks were used more frequently as they required less skill to lay than stone and could be transported more easily.

## Slide 14: Binding agents
A binding agent, or binder, is a material used to form materials into a cohesive whole as a means of providing structural stability. Binding agents harden chemically or mechanically. Binding agents have been commonly used in construction for a very long time, for example, the use of straw and natural fibres to strengthen clay in wattle-and-daub construction.
Lime is a binding agent commonly used before the widespread introduction of Portland cement that was manufactured in large quantities in 1824. A very common binding agent used in contemporary construction is cement, which is used to make concrete. Other common examples include bitumen binder, which is used for asphalt pavements and clay which is used for binding bricks and tiles.

## Slide 15: Lime mortars, plaster and renders
Before cement-based mortars and plasters increased in use after the second world war, lime mortars and plasters were used. Lime mortar remains more flexible than cement-based mortar and is ideal for brick and stonework.
Lime plasters and renders are permeable (breathable) so allow water vapour to escape through non-cavity walls to prevent damp.
Lime products are also easily removed from brick and stone, allowing the stone to be reused when the building is no longer required. Lime mortar is also softer which can be good, but this also means it wears away over time, especially with acid rain.

## Slide 16: Bricks
Bricks used to be made by hand but are now mostly made in large, modern factories.
Older handmade bricks could be of different sizes.
Modern bricks are all the same size and are mostly very straight and are sometimes described as “boring and lacking character”.

## Slide 17: Types of brick wall
Flemish bond solid wall (typical pre-1919 construction) - no cavity
English bond solid wall (typical pre-1919 construction) - no cavity

## Slide 18: Problems with non-cavity walls
All walls breathe and allow the movement of moisture in both directions. Single skin walls will allow the ingress of moisture into a building.
The thermal properties of a non-cavity wall allows the external cold to conduct easily to the inner surface. This creates excessive moisture on the cold surface of the internal wall as the warm air of the interior condenses on it.
This meant that older properties had to be well ventilated to prevent the growth of mould and fungi.

## Slide 19: Problems with non-cavity walls
Non-cavity walls have poor thermal insulation values, allowing too much of the heat in a home to escape through the wall itself.
Single cavity walls tend to be weaker and are prone to movement during the life of the building.
Sound insulation is also a problem as noise can be more easily transmitted from one room (or space) to the next.

## Slide 20: Cavity walls
Cavity wall (outer skin) - typical post 1920 construction
Modern cavity wall with insulated cavity
Insulation between inner blockwork and outer brickwork
Stainless steel wall tie
Wikimedia Commons
Photograph by Sweetean
Learn the difference between a solid wall and a cavity wall here!
Notes: Diagram showing cavity vs solid wall - https://www.arktek.co.uk/what-solid-wall-insulation/

## Slide 21: Cavity walls in modern buildings
Black waterproof damp proof membrane
Modern cavity wall with insulated cavity

## Slide 22: Importance of ventilation

## Slide 23: Roof coverings
Slate is an excellent roofing material being durable, fairly easy to fit and pleasing to the eye.
Stone tiles are durable, but very heavy and require very strong timberwork to support it.
Thatch provides a waterproof covering and is good for insulation too, but needs to be redone after 25–40 years.
Clay tiles are durable and fairly easy to fit, but some styles can be very expensive.

## Slide 24
Slate flags are durable, damp resistant and smooth.
Stone flags such as sandstone and limestone are durable, permeable and not as smooth as slate.
Clay tiles are durable, damp resistant and easy to lay.
Suspended timber floors can rot if not ventilated but can be warmer if there are no gaps between floorboards.
Pre-1919 ground floors

## Slide 25
Solid floors are prone to creeping damp.
Ground floor joists are laid to allow infill.
Suspended timber floors are used for floors above the ground floor.
Pre-1919 ground floors

## Slide 26: Pre-1919 plastering
Pre-1919 plastering (dado rails and ceiling rose)
Pre-1919 plastering (decorative finish - a cornice)
Plain cornice

## Slide 27: Plastering and rendering
External wall insulation. Normally finished off with a render.

## Slide 28: Plastering and rendering
Wattle and daub

## Slide 29: Plastering and rendering

## Slide 30: Lath and plaster wall
This strips of wood (lath) are run with a gap just wide enough for the lime plaster to squeeze through and secure (hold) the weight of the covering.
Over time, the weak (narrow) point of the plaster cracks and the covering is prone to falling off.

## Slide 31: Lath and plaster ceiling

## Slide 32
Any questions?