## Slide 1: PowerPoint 4: Sustainable practices and regulatory requirements
PowerPointpresentation
Unit 202: Changing practices over time

## Slide 2: Aim: Understand sustainability and industry regulation
Objectives
  Explore key government policy on sustainability and retrofit.
  Explain what retrofit is.
  Identify the key points of responsible retrofit.
  Explain who BRE are and what BREEAM is.
  Examine the role of BREEAM in sustainable construction.
  Identify how design can improve a building’s energy efficiency.
  Explore smart buildings.
  List the key elements of Part L1A and L1B.
  Explore thermal imaging and construction.
  Explore the Passivhaus concept.

## Slide 3: What are the key government polices on sustainability?
The Welsh Government has implemented several key policies and legislations to promote sustainability in the construction industry.
Some of these statutes include:
  Environmental Protection Act 1990
  The Well-being of Future Generations (Wales) Act 2015
  Building Regulations
Other Guidance includes:
  PAS 2030:2019
  PAS 2035:2019
Notes: Remind learners that only some powers are devolved to the WG, and Westminster still has the authority to set some laws for Wales, equally laws passed before Devolution where passed by Westminster.

## Slide 4: The Environmental Protection Act 1990
The EPA 1990 plays a significant role in regulating environmental protection and pollution control in the Welsh construction industry.
The Act sets requirements for waste management, pollution prevention, environmental permitting and environmental impact assessments.
Construction companies operating in Wales must comply with the provisions of the EPA 1990 and associated regulations to ensure they meet the required environmental standards and protect the environment during construction activities.
Notes: Environmental Permits: The EPA 1990 introduced the concept of environmental permits, which regulate certain activities that have the potential to cause pollution or harm to the environment. In Wales, the EPA 1990 has been implemented through the Environmental Permitting (England and Wales) Regulations 2016. Construction activities that have the potential to cause significant pollution, such as waste management operations or installations that emit pollutants, may require an environmental permit. This means that construction companies engaged in such activities must comply with the permit conditions, including pollution prevention measures and environmental monitoring.
Waste Management: The EPA 1990 places responsibilities on waste management, including waste collection, disposal, and treatment. Construction activities generate significant amounts of waste, and the legislation requires proper waste management practices to be followed. Construction companies in Wales are required to ensure that waste is appropriately classified, handled, and disposed of in accordance with the relevant waste management regulations, such as the Environmental Permitting (England and Wales) Regulations 2016 and the Waste (England and Wales) Regulations 2011.
Control of Pollution: The EPA 1990 includes provisions to control pollution from various sources, including air, water, and land. Construction sites can be potential sources of pollution, such as dust and sediment runoff, noise, and emissions from machinery. The legislation requires construction companies to take measures to prevent or minimize pollution, including implementing best practices for controlling dust, noise, and emissions, as well as managing the storage and handling of hazardous substances.
Duty of Care for Waste: The EPA 1990 imposes a duty of care on waste producers, carriers, and receivers. Construction companies have a responsibility to ensure that waste generated on their sites is properly managed and transferred to authorized waste carriers or facilities. They must keep records of waste transfer and disposal, ensuring that waste is handled by licensed and regulated entities.
Environmental Impact Assessments (EIAs): The EPA 1990 provides a framework for conducting environmental impact assessments for certain projects. In Wales, this is further regulated by the Environmental Impact Assessment (Land Drainage Improvement Works) (Wales) Regulations 2017. Construction projects that fall under the scope of EIAs, such as large-scale developments or infrastructure projects, may need to undergo an environmental assessment to evaluate and mitigate potential environmental impacts.

## Slide 5: The Well-being of Future Generations (Wales) Act 2015
The Act has several implications for the Welsh construction industry.
A need to focus on sustainability.
A need to consider the impact of construction on local communities.
A need to use construction to improve the well-being of people.
The Act is helping to ensure that construction in Wales is sustainable, socially responsible and beneficial to the well-being of people.
Notes: Wales is responding to these challenges:
Sustainability: The construction industry is using innovative technologies and materials to reduce the environmental impact of construction. For example, they are using recycled materials, energy-efficient lighting, and rainwater harvesting systems.
Social responsibility: The construction industry is working with local communities to develop projects that meet their needs and aspirations. For example, they are building schools, libraries, and community centers.
Well-being: The construction industry is building projects that provide social and recreational facilities for local communities. For example, they are building parks, playgrounds, and sports facilities.

## Slide 6: What is retrofit?
In the construction industry, retrofit is the process of making changes or upgrades to an existing building or structure in order to improve its usefulness, performance, energy efficiency or aesthetics. It entails modifying the building's systems, components or layout to meet modern requirements or to solve special needs.
Retrofitting might include adding insulation, upgrading HVAC systems, replacing windows, enhancing lighting, installing renewable energy systems or changing the architecture of the building to accommodate new applications or technologies.
The purpose of retrofitting is to improve a building's performance, extend its lifespan and maximise its energy efficiency without requiring total reconstruction or demolition.

## Slide 7: Responsible retrofit
This involves making energy efficient and sustainable improvements while preserving their historical or architectural value, such as:
          energy assessment
          preservation of heritage
          insulation and air sealing
          efficient heating and cooling systems
          lighting upgrades
          window and glazing improvements
          renewable energy integration
          water efficiency measures
          indoor environmental quality
          monitoring and optimization.
Notes: Energy Assessment: Conduct a thorough energy assessment to identify the building's energy performance, including insulation, HVAC systems, lighting, and renewable energy potential. This assessment helps determine the most effective retrofit strategies.
Preservation of Heritage: For traditional buildings with historical significance, prioritize the preservation of their architectural features and materials. Use appropriate conservation techniques and materials that maintain the building's character while improving energy efficiency.
Insulation and Air Sealing: Enhance the building's insulation by adding insulation to walls, roofs, and floors. Address air leaks and drafts by sealing gaps, cracks, and openings. These measures improve thermal comfort and reduce energy waste.
Efficient Heating and Cooling Systems: Upgrade heating and cooling systems to more energy-efficient alternatives. Consider installing high-efficiency boilers, heat pumps, or district heating systems. Balance the need for modern comfort with preserving the building's aesthetics.
Lighting Upgrades: Replace outdated lighting fixtures with energy-efficient alternatives, such as LED lights. Incorporate smart lighting controls, occupancy sensors, and daylight harvesting to optimize energy use.
Window and Glazing Improvements: Upgrade windows to double or triple glazing with low-emissivity coatings, improving thermal performance without compromising architectural integrity. Retain original windows where feasible and enhance their efficiency with weather stripping or secondary glazing.
Renewable Energy Integration: Explore opportunities for incorporating renewable energy technologies like solar panels or small wind turbines. Consider their compatibility with the building's aesthetics and historical value.
Water Efficiency Measures: Implement water-efficient fixtures and systems to reduce water consumption. Install low-flow toilets, faucets, and water-saving appliances to conserve water resources.
Indoor Environmental Quality: Enhance indoor air quality through proper ventilation systems and control of moisture levels. Use low-VOC (volatile organic compounds) materials and finishes to minimize off-gassing and create a healthy indoor environment.
Monitoring and Optimization: Implement monitoring systems to track energy consumption, indoor environmental quality, and occupant comfort. Analyze data to identify areas for improvement and optimize the building's performance over time.

## Slide 8: Responsible retrofit
Retrofit has many benefits, including the upgrading of the current building stock to move towards meeting net zero targets.
All retrofit planning and activity must be approached with a sensitivity to the building that the technology is going to employed in.
This is especially prevalent in all pre-1919 construction where the building fabric behaves very differently to modern building fabrics.
Before undertaking any works on a pre-1919 building, retrofit or otherwise, it would be good practice to seek advice from the relevant conservation and planning/building control bodies to ensure compliance with all relevant regulations and preserve the buildings heritage and history.

## Slide 9: Retrofit standards: PAS 2030:2019
PAS 2030 is a Publicly Available Specification for the installation of energy efficiency measures in existing buildings.
PAS 2030 sets out the requirements for competence, technical ability and overall requirements for quality that all installers will follow to ensure work carried out has met the required standard.
PAS 2030 is a certification which businesses can achieve to demonstrate the compliance of their installations.
PAS 2030 is updated every two years.

## Slide 10: Retrofit standards: PAS 2035:2019
PAS 2035 is a Publicly Available Specification for the energy retrofit of domestic buildings. It was published by the British Standards Institute (BSI) in 2019 and is updated every two years.
PAS 2035 focuses on the assessment, design, specification, installation, commissioning and monitoring of energy retrofit projects in domestic buildings.
It sets out the requirements for the whole process of retrofitting a home, from initial assessment to final handover.
Both PAS 2030 and PAS 2035 are important for ensuring that energy efficiency measures are installed to a high standard and that the benefits of retrofitting are realised.

## Slide 11: Some Of The Key Requirements of PAS 2035
The project must be assessed to identify the potential for energy savings.
The design of the project must be based on the principles of whole-house retrofit.
The project must be installed by competent installers using approved materials and products.
The project must be commissioned to ensure that it is operating as intended.
The project must be monitored to ensure that the energy savings are being achieved.

## Slide 12: Who is the Building Research Establishment (BRE)?
    BRE, formerly known as the Building Research Establishment, is a UK-based research and consultancy organisation focused on the built environment.
    It conducts research and development activities to improve building design, construction and operation.
    BRE is known for developing industry standards and certification schemes, such as the Building Research Establishment Environmental Assessment Method (BREEAM), which assesses the environmental performance of buildings.
    It offers consultancy services on sustainable design, energy efficiency, fire safety and building information modelling.
    BRE's expertise and research are used to drive sustainable practices and support the construction industry in achieving higher levels of performance, environmental responsibility and safety. Watch this YouTube video on BREEAM: What is BREEAM? | The Pros & Cons
Notes: What is BREEAM? | The Pros & Cons https://youtu.be/ieisJlS-Ahg

## Slide 13: Improving sustainability by design
The Welsh Construction industry can improve its sustainable outcomes by complying with all of the legislation and various government policies and initiatives.
At a trade level, the conscious choice to use more environmentally friendly practices, actively manage waste and recycling and other sustainable approaches all contribute to the sustainability ethos.
The last option is to employ sustainability at the design stage. This means, in practice, that sustainability is actively considered when designing the built environment.

## Slide 14: Improving sustainability by design
To improve sustainability through design, the following strategies could be considered:
using sustainable materials
designing for energy efficiency
water management
construction waste reduction and recycling
increasing biodiversity and green spaces
lifecycle assessment
collaborative approach.
Notes: Sustainable Materials: Selecting and specifying sustainable materials is crucial. This includes using materials with low environmental impact, such as recycled or reclaimed materials, responsibly sourced timber, and low-carbon alternatives. Designers should consider the life cycle of materials, their embodied carbon, and their potential for reuse or recycling.
Energy Efficiency: Designing buildings with a focus on energy efficiency is vital. This involves optimizing building orientation for natural light and solar gain, incorporating high-performance insulation, specifying energy-efficient HVAC systems and appliances, and integrating renewable energy sources such as solar panels or ground-source heat pumps. Energy modeling and analysis can help identify opportunities for energy reduction and inform design decisions.
Water Management: Designing buildings with efficient water management systems helps reduce water consumption and promotes sustainability. This can include incorporating rainwater harvesting systems, graywater recycling, low-flow fixtures, and water-efficient landscaping. Designers should also consider strategies to mitigate stormwater runoff and promote natural drainage, such as green roofs or permeable surfaces.
Waste Reduction and Recycling: Implementing design strategies to minimize construction waste and promote recycling is essential. This can involve modular construction techniques to reduce material waste, specifying products with take-back schemes, and incorporating design for disassembly principles. Designers should consider the ease of material separation and recycling during the end-of-life phase of the building.
Biodiversity and Green Spaces: Integrating green spaces, biodiversity enhancements, and ecological features into building design can improve sustainability. This can include rooftop gardens, green walls, wildlife habitats, and native plantings. Designers should consider the overall impact on the local ecosystem and create opportunities for wildlife habitats and urban biodiversity.
Lifecycle Assessment: Conducting lifecycle assessments (LCA) during the design phase helps identify the environmental impact of a building from construction to demolition. Designers can use LCA to inform material and system choices, identify areas for improvement, and optimize the overall sustainability performance of the building throughout its lifespan.
Collaborative Approach: Adopting a collaborative approach involving architects, engineers, contractors, and other stakeholders is crucial for sustainable design. This promotes knowledge sharing, innovation, and a holistic understanding of the project's sustainability goals.

## Slide 15: Smart buildings
Using smart technology can also impact on the sustainability of the built environment by, for example, using sensors to detect a range of inputs, such as:
ambient temperature
water usage
natural light levels
air quality
room occupancy.
Notes: Energy Efficiency: Smart homes equipped with energy sensors can monitor energy consumption patterns and optimize energy usage. Sensors can detect occupancy in rooms and adjust lighting and heating accordingly, reducing energy waste. They can also automate the control of appliances, ensuring they are only active when needed, further conserving energy.
Intelligent Lighting: Sensors can detect natural light levels and adjust artificial lighting accordingly, minimizing the use of energy-consuming lights during daylight hours. Additionally, motion sensors can turn off lights in unoccupied rooms, preventing unnecessary energy consumption.
Efficient Heating and Cooling: Smart homes can use temperature sensors to adjust heating and cooling systems based on occupancy and ambient conditions. By maintaining optimal temperatures only when necessary, energy waste can be minimized, resulting in significant energy savings.
Water Conservation: Sensors can be utilized to monitor water usage in smart homes. They can detect leaks, irregular flow rates, and excessive water usage, alerting homeowners to potential issues and promoting water conservation. Smart irrigation systems can also use moisture sensors to optimize watering schedules based on soil moisture levels, preventing overwatering and reducing water waste.

## Slide 16: Smart buildings
Smart homes leveraging sensors provide valuable data and automation capabilities that enable energy-efficient and sustainable practices.
By optimising energy usage, reducing water waste, managing waste efficiently and improving indoor air quality, these homes contribute to a more sustainable and environmentally friendly living environment.
By harnessing the power of sensors and smart technologies, smart homes enhance energy efficiency, optimise resource utilisation, promote water conservation, reduce waste and improve occupant comfort.
These contributions align with the goal of achieving net-zero emissions and creating sustainable living environments.

## Slide 17: What is Part L?
    Part L of the Building Regulations in Wales sets energy efficiency requirements for buildings.
    It includes standards for the building fabric, insulation, heating, cooling and lighting systems.
    Buildings must meet target emission rates to ensure energy efficiency. Part L also addresses air permeability, promoting controlled air leakage to reduce heat loss.
    It emphasises the conservation of fuel and power through efficient systems and encourages the use of renewable energy sources.
    Compliance is required through energy calculations and certificates. Building control authorities enforce these requirements.
    It is important to consult up-to-date regulations and local authorities for accurate information.

## Slide 18: What is Part L of the Welsh building regulations?
Part L of the Welsh building regulations is the section of the regulations that deals with the conservation of fuel and power in buildings. It sets out several requirements that must be met to ensure that buildings are energy efficient. The key points of Part L include:
    insulation
    windows and doors
    ventilation
    renewable energy sources
    design
    By following the requirements of Part L, you can help to save clients' money on their energy bills and make a positive contribution to the environment.
Notes: Insulation: Insulation is one of the most important ways to improve the energy efficiency of a building. It helps to prevent heat from escaping, which can save money on energy bills.
Windows and doors: Energy-efficient windows and doors also help to improve the energy efficiency of a building. They let in less heat in the summer and more heat in the winter, which can also save money on energy bills.
Ventilation: Proper ventilation is important to prevent mould and mildew, which can damage a building and make it unhealthy to live in.
Renewable energy sources: Renewable energy sources, such as solar panels or heat pumps, can help to reduce a building's reliance on fossil fuels and save money on energy bills.
Design: The design of a building can also affect its energy efficiency. Buildings that are designed to make the most of natural light and ventilation will be more energy efficient.

## Slide 19: Part L1 A and Part L1 B
Part L1A and Part L1B are the two parts of the Building Regulations in Wales that deal with the conservation of fuel and power in buildings. Part L1A applies to new dwellings, while Part L1B applies to existing dwellings.
The main difference between Part L1A and Part L1B is the level of energy efficiency that is required. Part L1A requires new dwellings to be more energy efficient than existing dwellings. This is because new dwellings are built to modern standards, while existing dwellings may not have been built with energy efficiency in mind.
Part L1A and Part L1B both set out several requirements that must be met to ensure that buildings are energy efficient.

## Slide 20: Part L1 A and Part L1 B
In addition to the requirements in Parts L1A and B, there are a number of other things that homeowners can do to make their homes more energy efficient. These include:
using renewable energy sources, such as solar panels or heat pumps
designing the home to make the most of natural light and ventilation
using energy-efficient appliances and lighting.
By taking these steps, industry can help to create homes that are not only energy efficient, but also comfortable and healthy to live in.

## Slide 21: Thermal imaging and construction
Construction experts can use thermal imaging cameras to discover areas of heat loss, air leakage and insulation inadequacies within a building envelope.
These insights aid in making informed decisions about insulation upgrades, gap sealing and overall energy efficiency.
Thermal imaging allows for the early diagnosis of possible problems such as insufficient insulation, thermal bridging or moisture penetration, all of which can result in energy waste and lower comfort.
Energy efficient construction practices can be introduced quickly by resolving these challenges, resulting in decreased energy consumption, cheaper utility costs, and enhanced indoor comfort for inhabitants.

## Slide 22: Thermal imaging and construction
Thermal imaging can also be used during the commissioning phase and after construction to validate the effectiveness of energy-saving measures and uncover operating inefficiencies.
This enables continuous monitoring and optimisation of energy performance throughout the building's existence.
Thermal imaging is valuable in energy-efficient construction because of its capacity to pinpoint regions of energy loss, detect thermal vulnerabilities and permit targeted modifications, resulting in increased energy efficiency, sustainability and cost savings in building operations.
\s

## Slide 23: What is the Passivhaus concept?
Developed in Germany in the 1990s, Passivhaus is a quality assured standard and methodology for low energy building, which can help create buildings which use around 75% less energy than standard practice for UK newbuild. Watch this YouTube video: What is a PassivHaus / Passive House?
The actual construction methods of Passivhaus buildings will vary, but they all have the following key features: super insulation, stringent levels of airtightness, minimal thermal bridging, optimisation of passive solar gain, mechanical ventilation with heat recovery, simple compact shape.
Notes: What is a PassivHaus / Passive House? https://youtu.be/zWZ2HyrdTQY

## Slide 24: Passivhaus building methodology
A Passivhaus building's methodology differs from that of certain carbon neutral buildings, which use a combination of energy efficiency and sustainable energy generation to offset any energy use.
A Passivhaus building is designed to use less energy in the first place by being well-sealed against the elements.
Passivhaus design strives to eliminate the need for space heating and cooling and is founded on the idea that minimising heat loss is the most cost-effective and durable approach for creating a low-carbon structure.
Notes: Passivhaus design is based on a simple 'tea cosy' effect that maximises the use of super insulation and severe airtightness while paying great attention to the removal of thermal bridges. Passivhaus design can create healthy and comfortable buildings that require minimal heating by combining this with passive solar gain, mechanical ventilation, and heat recovery technologies.
A Passivhaus designed building consumes only minimum space heating to be pleasant to live in due to the mechanical ventilation and heat recovery system. Unless on really cold days, the sole heating required for Passivhaus buildings is generally derived from incidental gains from residents' body heat and cooking/showering activities.

## Slide 25
Any questions?