## Slide 1: PowerPoint 3: 21st century construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Aim: Explore 21st century construction techniques
Objectives
    Explain what sustainable construction means for 21st century building projects.
    Describe the pressures of climate change and embodied energy.
    Summarise the key points of the Well-being of Future Generations (Wales) Act 2015 for the construction industry.
    Explore the need for sustainability in relation to existing building stock.
    Differentiate between natural and manufactured materials.
    Appraise the benefits of off-site construction.
    Differentiate between traditional and modern design and planning techniques and tools.
    Assess the limitations of a planning and design in construction when using 2D and 3D software.

## Slide 3: What is sustainability in construction
Let’s go back to basics and define sustainability from a construction point of view:
Sustainability in the construction industry can be defined as the practice of designing, constructing, and operating buildings and infrastructure in a way that minimises environmental impact and promotes social and economic well-being.

## Slide 4: Let’s break that down…
There are many ways to achieve sustainability in the construction industry.
Some of the most common methods include:
Using sustainable materials, such as recycled materials and materials that are locally sourced.
Designing buildings that are energy efficient and water efficient.
Using construction techniques that minimise waste and pollution.
Creating workplaces that are healthy and safe for workers.
Building communities that are socially and economically sustainable.

## Slide 5: Embodied energy and energy efficiency
Energy efficiency and embodied energy play crucial roles in meeting the zero-carbon target in construction.
Embodied energy refers to the energy consumed throughout a building's life cycle, including materials extraction, manufacturing and transportation.
By choosing low embodied energy materials and sustainable construction practices, the carbon footprint of the building can be minimised.
By integrating energy efficiency and considering embodied energy, construction projects contribute to the goal of zero carbon emissions, promoting sustainability, reducing reliance on fossil fuels and creating environmentally friendly built environments.

## Slide 6: The Well-being of Future Generations (Wales) Act 2015
The Well-being of Future Generations (Wales) Act 2015 is a significant legislation in Wales that has implications for various sectors, including the construction industry. Watch the following YouTube video: Well-being of Future Generations (Wales) Act 2015
It aims to promote the well-being of present and future generations by requiring public bodies in Wales to consider the long-term impact of their decisions and take actions that contribute to the well-being goals outlined in the Act.
Notes: Well-being of Future Generations (Wales) Act 2015 https://youtu.be/RuYzNgUZi98

## Slide 7: What does it mean for construction?
The Act sets out a framework to promote the sustainable development of Wales and to improve the well-being of present and future generations through:
emphasis on sustainable development
long-term planning and decision-making
collaboration and integration
assessing and reporting well-being
public engagement and participation
monitoring and accountability.
Notes: Emphasis on sustainable development: The Act places a strong emphasis on sustainable development, which requires balancing environmental, social, and economic considerations. The construction industry is expected to prioritize sustainable practices, including energy efficiency, waste reduction, responsible material sourcing, and consideration of the social and environmental impacts of construction projects.
Long-term planning and decision-making: The Act requires public bodies, including local authorities and public sector organizations involved in construction projects, to take a long-term view and consider the impact of their decisions on future generations. This means that construction plans and projects need to align with the well-being goals defined in the Act and demonstrate how they contribute to the sustainable development of Wales.
Collaboration and integration: The Act promotes collaboration and integration across different sectors and stakeholders. In the construction industry, this means that professionals, including architects, engineers, contractors, and developers, need to work together to achieve sustainable outcomes. Collaboration with communities, local authorities, and relevant organisations is encouraged to ensure that construction projects align with the well-being goals and address local needs.
Assessing and reporting well-being: The Act requires public bodies, including those involved in construction, to conduct well-being assessments and report on their progress in achieving the well-being goals. This may involve assessing the social, economic, environmental, and cultural impacts of construction projects. The construction industry needs to consider the well-being of communities affected by their projects and demonstrate how they contribute positively to the well-being of future generations.
Public engagement and participation: The Act promotes public engagement and participation in decision-making processes. The construction industry is encouraged to involve local communities, stakeholders, and future users of buildings in the planning, design, and construction phases. This ensures that their voices are heard and that construction projects reflect the needs and aspirations of the community.
Monitoring and accountability: The Act establishes mechanisms for monitoring and evaluating progress towards the well-being goals. Construction projects may be subject to scrutiny and evaluation to ensure compliance with sustainable development principles. The construction industry needs to demonstrate transparency, accountability, and a commitment to continuous improvement in achieving sustainable outcomes.

## Slide 8: Traditional materials in construction
There are a range of buildings materials that have stood the test of time these include:
limecrete
lime renders
stone
timber.
These materials all have their own range of advantages and disadvantages, including environmental impact, cost, useability as well as the skills to use/install and their respective availability.

## Slide 9: Modern materials in construction
As industry advances, the materials we use have evolved. Some modern examples of these materials include:
engineered timbers, such as acetylated wood and glulam
(re)engineered bricks and blocks
crushed concrete
glass aggregate as insulation or fine aggregate
aerated blocks and bricks.
Similarly, these materials have their own advantages and disadvantages.
Notes: Activity
Divide the class into groups of 3 or 4 and ask them to research 1 traditional and 2 modern materials. Ask each group to give a 5 min presentation on their chosen materials.
The presentation must include the following, advantages and disadvantages related to this material:
uses, useability,
environmental impact,
potential carbon footprint (rated, low, medium or high).
Add any others as needed.
Materials can include those listed on slides as well as any trade specific materials both modern and traditional.

## Slide 10: 21st century green buildings
Watch the following YouTube video to learn about 21st century green building: Wales Institute for Sustainable Education at the Centre for Alternative Technology
Notes: Wales Institute for Sustainable Education at the Centre for Alternative Technology https://youtu.be/m0kFtt-Hbfo

## Slide 11: Modern methods of construction
Modern techniques of building is a broad phrase. It encompasses a variety of off-site manufacturing and on-site procedures that offer alternatives to standard home construction methods.
Off-site construction allows most building phases to be completed concurrently, all while site preparation, foundations and utility connections are being prepared.
Fully finished units can be constructed at a factory and then assembled and finished on-site.
According to a new study from the University of Cambridge and Edinburgh Napier University, factory-produced houses can create up to 45% less carbon than traditional residential construction methods.
(www.protrade.co.uk,2022)
Notes: Ask learners to use the internet to research the benefits of off-site construction, including the commonly used materials used in their manufacture. Lead a discussion on findings.

## Slide 12: The benefits of off-site construction
  These are some of the benefits of off-site construction, including:
  speed and efficiency
  improved quality and consistency
  cost savings
  sustainability and waste reduction
  enhanced health and safety outcomes
  flexibility and adaptability
  reduced disruption and site impact
  improved energy efficiency.
Notes: Speed and Efficiency: Off-site construction significantly reduces project timelines compared to traditional on-site construction methods. With pre-fabricated components being manufactured simultaneously while on-site preparations are underway, the construction process becomes faster and more efficient. This leads to reduced labor requirements and costs, as well as minimized disruption to the surrounding environment.
Improved Quality and Consistency: Manufacturing modules in a controlled factory environment allows for precise quality control measures and standardized production processes. Off-site construction ensures consistent quality across multiple units, reducing the risk of errors and defects. The use of advanced technology and automation further enhances accuracy and precision in construction.
Cost Savings: Off-site construction can deliver cost savings through various means. Reduced labor requirements, shorter construction times, and improved resource management contribute to lower overall project costs. Additionally, the controlled factory environment enables better procurement and bulk purchasing of materials, leading to cost efficiencies.
Sustainability and Waste Reduction: Off-site construction promotes sustainability by minimizing waste generation and optimizing material usage. The factory-based manufacturing process allows for careful material planning and waste reduction measures. Construction off-site also reduces the carbon footprint associated with transportation of workers and materials to and from the site
.
Enhanced Health and Safety: By shifting construction activities to a controlled factory setting, off-site construction improves health and safety conditions for workers. The factory environment allows for better management of potential hazards, adherence to safety protocols, and reduced exposure to inclement weather conditions and other on-site risks.
Flexibility and Adaptability: Off-site construction offers greater design flexibility and adaptability. Modular units can be easily reconfigured, relocated, or expanded, providing versatility in meeting changing requirements. This flexibility allows for efficient modifications and additions to existing buildings or quick assembly of structures in remote or challenging locations.
Reduced Disruption and Site Impact: As much of the construction work is carried out in a factory environment, off-site construction minimizes disruption to the surrounding community and reduces on-site noise, dust, and traffic. This is particularly beneficial in urban areas or sensitive locations where traditional construction methods may cause significant inconvenience or disturbance.
Energy Efficiency: Off-site construction techniques often integrate energy-efficient design principles and technologies. Modules can be constructed with high levels of insulation, energy-efficient windows, and advanced heating, ventilation, and air conditioning (HVAC) systems. This results in buildings with improved energy performance, reduced operational costs, and lower environmental impact.

## Slide 13: BIM vs traditional methods of design and construction
Building Information Modelling (BIM) was introduced to help make the workflow in a construction project more efficient and less wasteful. Traditional approaches tend to have issues with information interpretation on site, resulting in time and money being wasted.
When it comes to saving on energy, carbon and money, BIM can be used to effectively do this, with users being able to expect a 20–30% gain when making the most of BIM.
Notes: BIM is not a software package or 3D design but actually refers to a collaborative way of working using 3D design software and other software packages along side a collaborative approach to design and construction.

## Slide 14: 21st century surveying
Traditional surveying methods used manual techniques and measuring tools like chains, compasses and theodolites. This resulted limited accuracy, efficiency and time-consuming labour-intensive work.
Modern surveying methods employ advanced technology such as GPS, remote sensing, laser scanning, aerial photography and drones to capture data that can be used in 2D drawings and 3D models.
These methods offer greater precision, quicker data collecting and increased automation by working with computers to analyse and assess data in real time to produce 3D/2D representations of the surveyed area.

## Slide 15: 21st century surveying
LIDAR laser scanning and drones provide comprehensive 3D models with great accuracy and density over large areas. As well as aerial surveying, LIDAR/3D surveying can be used in buildings as well.
Mistakes in data processing and analysis are reduced by digital operations.
Modern surveying technologies improve efficiency and production by shortening survey times and allowing surveyors to cover more regions in less time.

## Slide 16: Smart enabled tools and technologies in construction
This refers to the application of advanced digital systems and devices that enhance productivity, safety and efficiency in the construction industry. Here some smart-enabled tools and technologies used in construction:
      Building Information Modelling (BIM)
      Internet of Things (IoT)
      drones
      augmented reality (AR) and virtual reality (VR)
      robotics and automation
      wearable technology
      cloud computing and mobile applications.
Notes: Building Information Modelling (BIM): BIM is a digital representation of a building's physical and functional characteristics. It allows architects, engineers, and contractors to collaborate and coordinate design and construction activities. BIM enables 3D modelling, clash detection, cost estimation, and project scheduling, improving efficiency and reducing errors.
Internet of Things (IoT): IoT connects various construction devices and equipment to a network, enabling data collection, monitoring, and control. IoT devices, such as sensors, wearables, and tracking systems, can provide real-time information on equipment performance, safety conditions, material usage, and energy consumption.
Drones: Unmanned aerial vehicles (UAVs), or drones, are used in construction for site surveying, mapping, and inspections. Drones can quickly capture aerial imagery, generate accurate topographic maps, monitor construction progress, and improve safety by reducing the need for manual inspections in hazardous areas.
Augmented Reality (AR) and Virtual Reality (VR): AR and VR technologies are utilized in construction for design visualization, virtual walkthroughs, and training simulations. AR overlays digital information onto the real-world environment, aiding in design reviews and on-site instructions. VR creates immersive virtual environments that allow stakeholders to experience a project before it is built.
Robotics and Automation: Robots are increasingly used in construction for tasks such as bricklaying, concrete pouring, and demolition. Robotic systems improve precision, speed up construction processes, and reduce labour-intensive work. Automation technologies, such as robotic total stations and autonomous vehicles, enhance accuracy and efficiency in surveying and material handling.
Wearable Technology: Wearables, such as smart helmets, safety vests, and GPS-enabled devices, are used to monitor worker safety, health, and productivity. These devices can track vital signs, detect hazardous conditions, provide real-time notifications, and improve communication among workers.
Cloud Computing and Mobile Applications: Cloud computing allows construction teams to store and access project data and documents from anywhere, facilitating collaboration and data sharing. Mobile applications enable on-site data collection, task management, reporting, and communication, enhancing efficiency and reducing paperwork.

## Slide 17: Current limitations of 2D and 3D software
While 2D and 3D software technologies have greatly enhanced the planning and design processes in construction, they do come with certain limitations, including:
    lack of real-world representation
    limited collaboration and communication
    technical expertise requirements
    scalability and performance
    cost and accessibility
    integration and data interoperability
    limitations in representing
    time and phasing.

## Slide 18
Any questions?