## Slide 1
PowerPoint 2: Know the changes in construction methods over time
presentation
Unit 202: Changing practices over time (Electrotechnical)

## Slide 2: AIM: Know the changes in construction methods over time
Objectives
Know the typical methods of construction for post-1919 buildings, including the materials tools and techniques relevant to their chosen trade.
Understand the development of construction practice within their chosen trade, for example:
            brick cavity methods of construction and later variations of cavity wall design
            prefabricated floor, wall, roof and joinery components.

## Slide 3: Traditional versus modern – pre- and post-1919
                In early electrical systems, the materials available for conductors and insulators was in its infancy. Typically, in these circumstances, the materials used were redeployed from other applications.
                This meant that the electrical systems did not age well, were not fit for the application or did not stand up to any degree of wear and tear.

## Slide 4: Materials pre-1919
                Pre-1919, the materials used before the advent of plastics had to be grown or dug out of the ground.
                For example, the fuseboard shown below is mainly made from glass, wood and porcelain.
Fuse box at Tatton Hall: Electric lighting was installed in 1884

## Slide 5: Early electrical cables
                In 1882, Thomas Edison developed the first power distribution system in New York City using copper rods, wrapped in jute and placed in rigid pipes filled with a bituminous compound.
                Cable Community
Notes: https://cablecommunity.com/

## Slide 6: Early electrical cables
The first electrical cables were uninsulated and it soon became apparent that, without some sort of insulating material, the ability to use multiple wires or to have large current wires would be problematic.
Rope twine was one of the first insulating materials but it was time consuming to weave around the bare copper wires and was soon replaced by other, easier to manufacture materials.

## Slide 7: Early electrical cables
Here is a timeline of mass-produced insulation materials:
1810 unvulcanised rubber
1841 Gutta Percha (a form of natural latex)
1844 vulcanised rubber – Goodyear patent
1879 parafined jute and vulcanised bitumen
1880 natural rubber
1884 paper cable (vegetable fibre)
1885 oil impregnated paper
1933 PVC first used in cable insulation
1942 Polyethylene (PE) developed
1970 Polytetrafluoroethylene (PTFE) cables

## Slide 8: Early electrical cables
In the 1880s, the first insulated cables were insulated with gutta percha, a natural latex material produced from the sap of trees of the same name. This insulation needed to be kept constantly wet or it would dry out and fail.
This material was largely replaced by rubber and vulcanised bitumen. To protect the rubber insulation from mechanical damage, it was surrounded in a woven fabric.
It would crumble and perish over a period of time.

## Slide 9: Early electrical systems
The electrical supply industry was quite disjointed. There wasn’t a national grid, so each area had their own supply arrangements. It wasn’t until the Electricity (Supply) Act 1919 when things started to change.
Up to this point, the only electrical circuit in the home was for lighting. There were no electrical appliances, so there was no need for socket circuits.
It wouldn’t be till the 1930s when electric cookers started to replace gas cookers in the home.
Learn about an electric cooker made in the 1930s by clicking this link: BBC History of the world
Notes: https://www.bbc.co.uk/ahistoryoftheworld/objects/C-dCHv9UQ0WATlInMqradA

## Slide 10: Early electrical systems – slip conduit
To provide some protection from damage, a simple fit slip tube system was used.
Before multicore cables were
available, circuits were run in singles
in a simple conduit system.
The joints were a push fit and were
clamped in place.
Grub screw to secure connection

## Slide 11: Early electrical systems – vulcanised rubber
By 1960, the circuits in the home for the UK were starting to standardise. However, rubber was still being used which would perish over time.
                Note the “old” colours in the image given here.
Notes: https://mytrustedelectrician.com/blog-1/f/how-old-is

## Slide 12: Early electrical systems – Bakelite
                Early Bakelite equipment and accessories.

## Slide 13: Early electrical systems – Bakelite
                One of the first, early versions of plastic as we now know it was called Bakelite (trade name) and was made from phenol and formaldehyde.
                Bakelite started to transform the design and form of equipment into what we now know as modern life. It was named for its inventor, Leo Hendrik Baekeland (1863–1944), who discovered the durable plastic in 1907.
Take a look at this video on The BPF Plastics Timeline
Switch to wood retailer
Notes: https://www.youtube.com/watch?v=IBFMLMxGANc

## Slide 14: Modern plastics
                The real expansion into modern plastics occurred in the 1930s.
                This is when the extruding machine was developed and Polythene was invented.
                PVC was already known but it wasn’t manufactured industrially till the 1930s.
                In the1950s, plastic became available to the general public in consumer products.
                Learn more at: A History of Plastics
Notes: https://www.bpf.co.uk/plastipedia/plastics_history/Default.aspx

## Slide 15: Early electrical systems
                In the 50s and 60s, appliances and cookers once more became affordable, new circuits were added by using two, three or four-way boards.
                This is why old installations had multiple fuseboards.
Take at a look at the image provided under Case Study 7: 1930s fusebox still in use.
Notes: http://www.eec247.com/gallery/fuseboxes/fuseboxes.html#consumer_unit_3

## Slide 16: Early electrical cable – PVC insulated PVC sheath circa 1970
PVC was the first twin and earth cable which incorporated a bare CPC conductor running through the centre of the cable. Sometimes, the conductors were tinned to prevent corrosion.
In the early years, aluminium conductor versions were manufactured due to shortages. However, they had to be much bigger and they were not as pliable.
Some of the plastics in these early cables reacted with the conductors and produced a green slime.

## Slide 17: Early electrical systems – 1970s
                In the 1970s, circuits started to look similar to the modern circuits we see today. Cable sizes, protection device sizes were adjusted in line with the new, standardised Wiring Regulations 15th Edition.
                Radial circuits (from the cooker or similar 6mm² circuits) were being replaced by a ring main which, in recent years, has become known as a ring final circuit. Indeed, all circuits that are not distribution circuits are known as a final circuit.

## Slide 18: BS 7671
                1981 became the year the new size format and alignment with the rest of Europe occurred with the introduction of the 15th Edition of the Wiring Regulations.
                The Institution of Engineering and Technology (IET) co-publishes BS 7671 with the British Standards Institution (BSI) and is the authority on electrical installation.

## Slide 19: Modern consumer unit

## Slide 20: Modern consumer unit
Take a look at the diagram of basic modern wiring.
Notes: Modern wiring diagram - https://wiki.diyfaq.org.uk/index.php/File:BasicWiringLayout.gif

## Slide 21: Evolution of colour coding
                Up to May 2004, black was used to denote neutral and red was used to denote live.
                After a two-year transition period, the new colours were compulsory from 2006.

## Slide 22: Modern wiring systems

## Slide 23: Modern wiring systems
Modern wiring systems use new materials and cater for building management systems, as well as lighting and power.
The image here shows the emergency systems run alongside, but separated from, data cables and final circuits.

## Slide 24: Post-1919 building materials
After 1919, more building materials became available to the UK builder due to mass manufacturing and motor vehicle transport.
Some of the materials were more convenient than the older materials, but not all were better or more sustainable than the older materials.
This also led to houses and other buildings looking the same, no matter what part of the country you lived in.
Although materials were easier to obtain and standardised for easier use, many local skills were lost and houses lost their local character.

## Slide 25: New roofing materials
Concrete roof tiles are cheap and durable, but boring to look at and require power tools to cut.
Asbestos roof tiles were cheap and easy to lay and cut, but asbestos proved to be dangerous to health.
Asbestos corrugated roofing sheets were used for industrial buildings but proved to be dangerous to health.
Note: Asbestos panels are sometimes known as AIB – (Asbestos impregnated board).

## Slide 26: New roofing materials
Corrugated metal roofing sheets are easy and quick to fit, durable if coated and can be prefitted with insulation.
They are now used for industrial and retail buildings.
Both square and round profiles are available.

## Slide 27: Metal roofing materials
Aluminium roofing is cheap and durable, but boring to look at and requires power tools to cut.
Copper roofing (cupric oxide) is liable to verdigris which is the common name for blue-green, poisonous, copper-based pigments that form a patina on copper, bronze and brass.
Corrugated metal roofing sheets are used for industrial and commercial buildings.

## Slide 28: Fibre cement roof tiles
Fibre cement roof tiles are fairly new roof tiles, designed to imitate natural slate.
They were created to replace the asbestos tiles, due to asbestos causing health problems.
They are easy to cut and fix and cheaper than natural slate, but they are not as durable.
Example image
Notes: https://build4less.co.uk/products/marley-thrutone-fibre-cement-slate-600mm-x-300mm-blue-black

## Slide 29: Tesla solar roof tiles
Take a look at more images here!
Notes: https://www.checkatrade.com/blog/cost-guides/solar-roof-tiles-cost/

## Slide 30: Cement-based mortars and plasters
Watch this video on
Understanding Concrete, Cement, and Mortar | Ask This Old House
Learn the differences between cement, concrete and mortar by clicking here!
Notes: Differences between the three – https://www.thespruce.com/difference-between-cement-concrete-and-mortar-2130884
Video - http://www.youtube.com/watch?v=CJIk453_j0I

## Slide 31: Cement videos
Basic cement mix video Use of plasticiser in cement Mixing a batch of cement
Is Your Mortar weak And Crumbling?
Everbuild Mortar Admix
Bricklaying Mortar Mix Explained

## Slide 32: Cement-based mortars and plasters
If used correctly, cement-based mortar is very good for new build brickwork.
However, for older properties, the mortar can be too hard and damage the brick or stone.
A lot of energy is required to produce cement, so it is not a sustainable material.
Watch this video on mixing quicklime mortar.
Notes: https://www.youtube.com/watch?v=_1JpAilh5t8

## Slide 33: Concrete
Concrete is mostly used for floors in buildings, but can be used for walls, roofs and bridges.
It is very strong, and can be moulded to any shape.
The Largest Concrete Dome Ever Built
Notes: https://www.concretenetwork.com/concrete-history/
Largest concrete dome video - http://www.youtube.com/watch?v=NZo1otIjfl4

## Slide 34: Imported softwoods
Most softwoods are imported from northern Europe and Russia.
They are pre-sawn or planed to standardised sizes and are much cheaper than using UK hardwoods.

## Slide 35: Screeded floors
Screeded floors are put on top of the concrete floor slab to produce a flat even floor.
This can be done by hand with a sand and cement mix and leveled with hand tools, or pumped in as a self-levelling compound.

## Slide 36: Pre-fabricated floors
To save time and money, parts of the building structure can be produced off-site.

## Slide 37: Concrete blocks
Concrete blocks can be hollow or solid or aerated lightweight blocks to improve insulation.
(hollow)
(solid)
(aerated lightweight)

## Slide 38: Gypsum based plaster
Gypsum based plaster was designed to replace lime plaster.
It dries quicker than lime plaster, is non-breathable but is not waterproof.

## Slide 39: Damp proof membrane (DPM) or damp proof course (DPC)
DPC is made from plastic and laid near the bottom of the wall to prevent rising damp.
DPM is made from plastic and is laid under a floor to prevent damp rising through the floor.
Black waterproof damp proof membrane

## Slide 40: Plastic windows and fascias
Plastic windows are designed to reduce the maintenance involved with timber windows.
They last longer than poorly maintained timber windows and fascias.

## Slide 41: Composite materials
Composite materials are made from fibre reinforced polymer (FRP) (plastic) which is very strong and waterproof.
Example image
Notes: https://www.fbmsales.com/products/fiberglass-reinforced-plastic/

## Slide 42: Steel
Steel is used to create high rise and industrial buildings.
It is very strong and can be recycled.

## Slide 43: Standardised building materials
Materials have standardised sizes across the UK.
There are standard sizes of timber, plasterboard, pipes, cables, steel, slates, roof tiles etc.
Some benefits of standardised building materials include:
  workers are used to dealing with set size materials
  planning and pricing of jobs is easier
  different building components interface better with each other.

## Slide 44
Any questions?