## Slide 1
PowerPoint presentation
Unit 202: Changing practices over time
PowerPoint 1: Know the changes in construction methods over time

## Slide 2: AIM: Know the changes in construction methods over time
Objectives
  Understand local needs and geographical influences
  Know the basic qualities and uses of mortars, aggregates, binders, internal and external functional and decorative finishes, stone, slate, timber and earth
  Understand construction materials available within a locality, including an understanding of local geology, and the accessibility of these materials, including local quarries and transportation links both past and present
  Know the permeable nature of lime and earth mortars
  Describe limitations of pre-existing services
  Discuss key sources of legislation
  Identify a range of common materials

## Slide 3: Pre-1919 construction methods
When man stopped roaming and began farming, humans were rooted to the area they farmed. Societies started to build structures where they would be protected from the elements (weather).
One contentious theory says this happened 11,000 years ago in a place called Göbekli Tepe in modern-day Turkey.

## Slide 4: Transporting materials
Before the industrial revolution, builders had to use materials which were close at hand as it was very difficult to transport materials using just a horse and cart.
The industrial revolution began in earnest by the 1830s and, in Britain, by the 1840s.

## Slide 5: Diagram of an older building
Glass, for example, was hand blown till the 1919–1920 when mechanised rolling was developed.
Slate
Quarried locally
Hand made window from local timber
Local stone
Lime wash paint / render
Thatch
Farmed locally

## Slide 6: Building materials in older buildings
The materials used for building depended on where in the UK the house was being built.
Areas such as North Wales had easy access to stone and slate whereas, in other areas, timber was plentiful so timber-framed houses were built.

## Slide 7: Timber-framed buildings
Timber-framed buildings were a quick and cheap way to put up the structure. However, the voids needed to be filled with methods like brickwork or wattle and daub which can be a render or a plaster.

## Slide 8: Diagram of an older building
Timber frame
Larger stones
Smaller stones or bricks
Infill construction
Solid wall
Clay tiles
Wood shingles
What is the problem with this wall?

## Slide 9: Flint
Some areas of the country had access to a hard stone called flint.
Here is a wall made partly from flint.

## Slide 10: Local building materials in older buildings
Limestone
Sandstone
Slate
Granite
South Yorkshire / Derbyshire
Wales, West of Scotland
Wales (thinnest slates), Cornwall
Scotland, Wales (radon is an issue)

## Slide 11: Local building materials in older buildings
Chalk
Marble
Flint
North and South Downs
Iona and Connemara
Norfolk, Suffolk. Found in chalk as nodules

## Slide 12: Early high-status buildings
Before the industrial revolution, some people who could afford the high cost of transport could construct their buildings with materials from around the country.

## Slide 13: Transportation of materials
As canals and railways were built during the industrial revolution, more buildings were built using materials from further afield. These included schools, factories and bigger houses for the middle classes.
During this time, bricks were used more frequently as they required less skill to lay than stone and could be transported more easily.

## Slide 14: Binding agents
A binding agent, or binder, is a material used to form materials into a cohesive whole as a means of providing structural stability. Binding agents harden chemically or mechanically. Binding agents have been commonly used in construction for a very long time, for example, the use of straw and natural fibres to strengthen clay in wattle-and-daub construction.
Lime is a binding agent commonly used before the widespread introduction of Portland cement that was manufactured in large quantities in 1824. A very common binding agent used in contemporary construction is cement, which is used to make concrete. Other common examples include bitumen binder, which is used for asphalt pavements and clay which is used for binding bricks and tiles.

## Slide 15: Lime mortars, plaster and renders
Before cement-based mortars and plasters increased in use after the second world war, lime mortars and plasters were used. Lime mortar remains more flexible than cement-based mortar and is ideal for brick and stonework.
Lime plasters and renders are permeable (breathable) so allow water vapour to escape through non-cavity walls to prevent damp.
Lime products are also easily removed from brick and stone, allowing the stone to be reused when the building is no longer required. Lime mortar is also softer which can be good, but this also means it wears away over time, especially with acid rain.

## Slide 16: Bricks
Bricks used to be made by hand but are now mostly made in large, modern factories.
Older handmade bricks could be of different sizes.
Modern bricks are all the same size and are mostly very straight and are sometimes described as “boring and lacking character”.

## Slide 17: Types of brick wall
Flemish bond solid wall (typical pre-1919 construction) - no cavity
English bond solid wall (typical pre-1919 construction) - no cavity

## Slide 18: Problems with non-cavity walls
All walls breathe and allow the movement of moisture in both directions. Single skin walls will allow the ingress of moisture into a building.
The thermal properties of a non-cavity wall allows the external cold to conduct easily to the inner surface. This creates excessive moisture on the cold surface of the internal wall as the warm air of the interior condenses on it.
This meant that older properties had to be well ventilated to prevent the growth of mould and fungi.

## Slide 19: Problems with non-cavity walls
Non-cavity walls have poor thermal insulation values, allowing too much of the heat in a home to escape through the wall itself.
Single cavity walls tend to be weaker and are prone to movement during the life of the building.
Sound insulation is also a problem as noise can be more easily transmitted from one room (or space) to the next.

## Slide 20: Cavity walls
Cavity wall (outer skin) - typical post 1920 construction
Modern cavity wall with insulated cavity
Insulation between inner blockwork and outer brickwork
Stainless steel wall tie
Wikimedia Commons
Photograph by Sweetean
Learn the difference between a solid wall and a cavity wall here!
Notes: Diagram showing cavity vs solid wall - https://www.arktek.co.uk/what-solid-wall-insulation/

## Slide 21: Cavity walls in modern buildings
Black waterproof damp proof membrane
Modern cavity wall with insulated cavity

## Slide 22: Importance of ventilation

## Slide 23: Roof coverings
Slate is an excellent roofing material being durable, fairly easy to fit and pleasing to the eye.
Stone tiles are durable, but very heavy and require very strong timberwork to support it.
Thatch provides a waterproof covering and is good for insulation too, but needs to be redone after 25–40 years.
Clay tiles are durable and fairly easy to fit, but some styles can be very expensive.

## Slide 24
Slate flags are durable, damp resistant and smooth.
Stone flags such as sandstone and limestone are durable, permeable and not as smooth as slate.
Clay tiles are durable, damp resistant and easy to lay.
Suspended timber floors can rot if not ventilated but can be warmer if there are no gaps between floorboards.
Pre-1919 ground floors

## Slide 25
Solid floors are prone to creeping damp.
Ground floor joists are laid to allow infill.
Suspended timber floors are used for floors above the ground floor.
Pre-1919 ground floors

## Slide 26: Pre-1919 plastering
Pre-1919 plastering (dado rails and ceiling rose)
Pre-1919 plastering (decorative finish - a cornice)
Plain cornice

## Slide 27: Plastering and rendering
External wall insulation. Normally finished off with a render.

## Slide 28: Plastering and rendering
Wattle and daub

## Slide 29: Plastering and rendering

## Slide 30: Lath and plaster wall
This strips of wood (lath) are run with a gap just wide enough for the lime plaster to squeeze through and secure (hold) the weight of the covering.
Over time, the weak (narrow) point of the plaster cracks and the covering is prone to falling off.

## Slide 31: Lath and plaster ceiling

## Slide 32: Life span of an electrical service or installation
Currently, the life span of a new electrical Installation is 50 to 70 years.
All installations deteriorate over time due to wear and tear, alterations/changes and age.
Older systems had a shorter life span. Before PVC, rubber insulation used to dry out and crumble. Tough rubber sheath cables (TRS) have a life expectancy of 20 to 30 years.
Electrical installations have a maximum interval between inspections of ten years. Rented properties and public buildings are typically shorter.

## Slide 33: Risks to an electrical installation that affect life span
There are a number of risks that can affect the life span of an electrical installation.
These include:
corrosion due to moisture or dissimilar metals used in electrical connections
polystyrene used as cavity wall insulation
aggressive chemicals (like creosote) attacking cable sheaths
poor quality design and installation.

## Slide 34: Examples of copper corrosion (verdigris)

## Slide 35: Shared water main
Many older properties, especially terraced houses, are supplied by a shared water main. This pipe provides water to a block of houses from one single connection to the water main.
Lead was commonly used for these supply pipes, which are often inadequate in size for the water requirements of a modern system.
Pressure can be poor, especially during peak demands, and is affected by other properties on the supply.
Watch this video on
supply pipe ownership
Notes: https://www.youtube.com/watch?v=jWkYRDvL9ws

## Slide 36: Hot and cold lead pipework
Although the use of lead pipes has been prohibited for use on hot and cold water supplies, many older properties that have not undergone renovation are likely to still have underground and/or internal lead pipework.
Lead lock compression fittings allow a connection between lead and copper (or MDPE).
Lead lock sizes vary from 5lb to 11lb for different diameters of lead.

## Slide 37: Legislation
Water Regulations Advisor Scheme (WRAS)
It is a legal requirement for hot and cold water supplies to use WRAS-approved fittings to comply with the Water Regulations. Not only are they of high quality and resistant to corrosion in their specific surroundings, but they are also manufactured from non-contaminating materials.
WRAS provide guidelines and requirements for the installation of fittings and materials, including restrictions on the use of lead pipes and fittings. These regulations mandate the use of approved materials and products that comply with safety standards and reduce the risk of contamination. WRAS approved fittings will then be badged as shown.
WRAS
Notes: https://www.wrasapprovals.co.uk/

## Slide 38: Fittings and materials
Lead and copper were used for underground wholesome water supplies. These materials have now been replaced with MDPE (medium density polyethylene)​. New water mains should be laid at depth of 750mm (minimum) to 1,350mm (maximum).
Press-fit fittings require an electrical crimping machine for jointing. The machine crimps the fittings onto the tube to create a watertight seal on the ‘o’ ring. They are ideal for use when hot works (soldering) is not permitted.

## Slide 39: Fittings and materials
Push-fit polybutylene pipe has become popular in recent years due to the ease of installation. A stainless-steel grab ring locks the pipe onto the fitting and an ‘o’ ring creates a watertight seal onto the pipe. Pipe inserts are required for plastic pipe. This jointing method does not require hot works.

## Slide 40: Soil and vent pipes
Traditionally-cast iron was used for a whole host of applications, including foul waste removal (soil pipe), guttering and baths.
Cast iron requires painting to protect it from atmospheric corrosion,
Today, PVC is preferred for guttering and soil stacks.
Drain connectors or flexy seals can be used to change from imperial cast or clay to metric PVC.

## Slide 41: Below ground drainage
A collapsed or cracked drain requires immediate attention and remedial action.
Symptoms of a cracked or collapsed drain include:
      slow drainage
      foul odors
      leaking sewage
      mould on wall or ceilings
      foundation and wall cracks.
      Imperial to metric flexy seal adaptors provide a solution for connecting PVC drainage pipes.

## Slide 42: Lead waste pipes
In the past, waste pipework was traditionally crafted from lead and connected using lead wiped joints.
In the process of renovations, it is good practice to upgrade lead waste pipework to plastic, which features a larger internal bore.

## Slide 43: Cold water storge cisterns
Traditionally, cold-water storage cisterns were made from galvanised metal and held together with studs.
Over time the zinc coating is removed, exposing the steel and leading to corrosion.
Ferrous oxide (rust) would contaminate the cold-water storage cistern, so it requires immediate attention once identified.
Galvanic cisterns are no longer approved for new cold water storage cisterns.

## Slide 44: Dezincification
Brass (copper and zinc) components can have zinc leached out as fresh water passes through them. It leaves the brass fitting weak and brittle, quite often covered in white powder (zinc oxide).
Valves and fittings showing signs of this type of corrosion require replacing.
Modern brass components are dezincification resistant and have DZR or DZ stamped on them.

## Slide 45: Structure
Pipework is generally installed under suspended floors which may require drilling or notching the joists.
Building Regulations Document: A sets out requirements for notching, drilling and pipe chases and must be always followed.

## Slide 46
Any questions?