## Slide 1: PowerPoint 2: 21st century construction techniques and technologies
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Awareness of new and emerging technologies
Objectives
  Discuss key sources of information and legislation (Building Regulations Part L)
  Describe the key features of smart controls
  Compare the benefits and limitations of smart heating controls
  Discover new and emerging environmental technologies
  Explore 3D modelling
  Recognise building services trade associations and industry bodies

## Slide 3: Sources of information
The Building Regulations Part L 2010 deal with the conservation of fuel and power.​
The document is split into four parts:​
L1a – New dwellings
L1b – Existing dwellings
L2a – New buildings other than dwellings
L2b – Existing buildings other than dwellings
Volume 1: Dwellings
Volume 2: Buildings other than dwellings
These Regulations give a minimum requirement for the control of heating and hot water systems within dwellings which influences the layout and control of heating systems.​

## Slide 4: Sources of information (continued)
New boiler regulations state that any boiler installed from April 2018 and beyond must have an ErP (Energy-related Products) efficiency rating of at least 92%.
Efficient heating and hot water systems can significantly reduce energy consumption. There are several measures that can improve the efficiency of your heating and hot water systems. These include:
upgrade an existing boiler
regular maintenance of existing system
renewable energy options
using individual room controls
upgrading to smart heating controls.

## Slide 5: Smart heating controls
Smart thermostats are designed to learn and adapt to the heating and cooling patterns of your home, considering factors such as the home's insulation, size and the time it takes for the temperature to change.
They use advanced algorithms to analyse this data and optimise the heating and cooling cycles accordingly.

## Slide 6: Smart thermostats
One of the key features of smart thermostats is their ability to use auto-schedule settings. With auto-schedule, you do not need to manually programme temperature settings for different times of the day. Instead, the thermostat learns from your behaviour and creates a schedule based on your patterns.
By using sensors and connectivity with your phone, smart thermostats can detect when you have left the house and can automatically adjust the heating to conserve energy.

## Slide 7: Benefits and limitations of smart heating controls
Benefits | Limitations
A range of automation features | Internet dependent
Remote control of heating and hot water through smartphone apps | Compatibility with existing heating and hot water system
Auto-schedule feature learns from your behaviour and intelligently adapts | Expensive to install compared to standard programmable thermostats
Allows used to monitor and stay informed of energy usage | 

## Slide 8: Smart TRVs
A smart TRV (Thermostatic Radiator Valve) is a device that allows you to control the temperature of individual radiators in your home remotely using a smartphone or other smart devices.
They offer more localised and precise control over room temperatures compared to traditional valves.

## Slide 9: Benefits and limitations of smart TRVs
Benefits | Limitations
Independently control time and temperature in each room | Internet dependent
Remote control and monitoring through smartphone apps | Compatibility with existing valves
Energy savings | Expensive to install compared to standard TRVs
Reduced fuel consumption | 

## Slide 10: Environmental technologies
The UK is committed to having “net zero” emissions by 2050. Most UK homes are heated by natural gas, which produces carbon dioxide (CO2). Natural gas produces approximately 20% of all global greenhouse gas emissions
Low carbon technologies for heating and hot water are crucial for reducing greenhouse gas emissions and addressing climate change. Here are some examples of such technologies.

## Slide 11: Environmental technologies – heat pumps
Heat pumps are devices that extract heat from the air, ground or water and use it to heat buildings and water. They are highly efficient and can provide both space, heating and hot water. Heat pumps run on electricity and, if the electricity comes from renewable sources, they can be almost carbon-neutral.
Two most common types are:
  air source heat pumps (ASHP) and
  ground source heat pumps (GSHP).

## Slide 12: How heat pumps work
The basic working principle of a heat pump involves the transfer of heat from a low-temperature source to a higher-temperature sink using a refrigeration cycle. Released heat is used to provide space heating and stored hot water.

## Slide 13: Advantages and disadvantages of heat pumps
Advantages | Disadvantages
Reduced carbon emissions | Expensive to install
Long life span and relatively low maintenance | Existing heating systems may require extensive upgrades
Financial incentives to help offset the initial installation costs | Temperature limitations
High energy efficiency | Not suitable for every home

## Slide 14: Environmental technologies – hydrogen
Renewable hydrogen refers to hydrogen gas that is produced using renewable energy sources, such as solar, wind, hydro or biomass. It is considered a clean and sustainable form of hydrogen because the energy used to produce it comes from renewable sources, which do not produce greenhouse gas emissions or other harmful pollutants.
The process of producing renewable hydrogen typically involves electrolysis, where water (H2O) is split into hydrogen (H2) and oxygen (O2) using an electrical current.
The resulting hydrogen gas can then be captured and stored for various applications, including space heating and hot water.

## Slide 15: Environmental technologies – hydrogen
Hydrogen can have zero or near-zero carbon emissions throughout its lifecycle, contributing to a sustainable and low-carbon future. Green electricity produces hydrogen which can be transported through the network and used in zero carbon heating for homes.
Take a look at the diagram showing the generation of green hydrogen at fuelcellsworks.
Notes: https://fuelcellsworks.com/news/sgn-a-world-first-green-hydrogen-project-wins-uk-government-funding/

## Slide 16: Advantages and disadvantages of hydrogen
Advantages | Disadvantages
Potential for zero emissions | Energy intensive production
Clean and environmentally friendly | Highly flammable and volatile
Abundant and renewable | High production and infrastructure costs
Reduced dependence on fossil fuels | Difficult to store
 | Expensive to produce

## Slide 17: 3D modelling
3D modelling in building services refers to the creation of three-dimensional digital representations of building systems and components used in the design, construction and maintenance of a building.
It involves using specialised software to generate accurate and detailed 3D models that depict various building services, such as HVAC (Heating, Ventilation and Air Conditioning), electrical systems, plumbing, fire protection and more.
Learn more here: 3D Bathroom Planner.
Notes: https://www.villeroy-boch.co.uk/bathroom-planner.html

## Slide 18: Sources of information
Planning
Installing
Commissioning
Servicing
Maintaining
Manufacturer's instructions are a key source of information when:

## Slide 19: Trade Associations and Industry Bodies
The Chartered Institute of Plumbing and Heating Engineering (CIPHE) is a membership body for those involved in all aspects of the plumbing and heating industry.
The CIPHE aims to help members be the very best they can be, providing access to technical, training and professional development support.
CIPHE
Gas Safe Register is the official gas registration body for the United Kingdom.
Gas Safe
Notes: https://www.ciphe.org.uk/professional/
https://www.gassaferegister.co.uk/

## Slide 20: Trade Associations and Industry Bodies
WaterSafe is a free online directory and national accreditation body for competent and qualified plumbers, water supply pipe installers and other water services specialists in England, Scotland, Wales and Northern Ireland.
HIP is a leading trade publication, which is distributed to over 190 colleges every term. The magazine primarily focuses on sharing information with students on the best ways to establish a career within the industry.
WaterSafe
HIP Magazine
Notes: https://www.watersafe.org.uk/
https://www.hip-magazine.co.uk/magazines/

## Slide 21
Any questions?