## Slide 1: PowerPoint 1: Pre-1919 construction methods
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: AIM: Know typical methods of construction for pre-1919 buildings
Objectives
  Explore traditional space heating and hot water systems
  Describe limitations of pre-existing services
  Discuss key sources of legislation
  Identify a range of common materials
  State actions to be taken where unsafe building services are discovered

## Slide 3: Space heating
During the early 1900s, the primary method of space heating in most homes were wood or coal fires.
In the 1970s and 1980s, hydronic (wet) central heating systems became widely installed in British homes, marking a significant shift to the heat emitters we use today.

## Slide 4: Chimneys
Class 1 chimneys are characterised by a brick-built structure positioned on an internal or external wall.
These chimneys are designed to accommodate multiple flues, allowing for the installation of multiple fires. Their purpose is to provide space heating to bedrooms and living areas.
Take a look at the diagrams of different chimney structures here.
Notes: https://www.discountplansltd.com/chimney-breast-removal-attic-space

## Slide 5: Flues
When fires burn, they release combustion gases that are vented out of the home through a flue. Each fireplace will have its own separate flue which is divided by the mid feathers.
A chimney breast commonly contains two flues: one for the fireplace in the lounge itself and another for the fireplace directly above it in the bedroom.

## Slide 6: Chimney pots
The usage of chimney pots gained popularity during the 18th and 19th centuries, coinciding with the widespread adoption of coal as a heating fuel in households.
These pots served as a cost-effective method to enhance the height of chimney stacks, thereby improving the airflow and draft within the chimney system.
Each chimney pot serves a separate fireplace and its flue.

## Slide 7: Damage to chimneys
A damaged or collapsed chimney will significantly affect the air flow and draft of the flue, potentially leading to deadly products of combustion entering the property, posing immediate danger.
Any chimney showing signs of structural movement will require immediate attention.

## Slide 8: Hot water
While a kettle on a kitchen fire or stove could provide limited amounts of hot water, the primary method for obtaining large quantities of hot water was using a "copper" water heater.
The coal fire beneath the water container was used to heat the water. Coppers had to be filled manually.
Example image
Notes: https://www.nationaltrustcollections.org.uk/object/40098

## Slide 9: Shared water main
Many older properties, especially terraced houses, are supplied by a shared water main. This pipe provides water to a block of houses from one single connection to the water main.
Lead was commonly used for these supply pipes, which are often inadequate in size for the water requirements of a modern system.
Pressure can be poor, especially during peak demands, and is affected by other properties on the supply.
Watch this video on
supply pipe ownership
Notes: https://www.youtube.com/watch?v=jWkYRDvL9ws

## Slide 10: Hot and cold lead pipework
Although the use of lead pipes has been prohibited for use on hot and cold water supplies, many older properties that have not undergone renovation are likely to still have underground and/or internal lead pipework.
Lead lock compression fittings allow a connection between lead and copper (or MDPE).
Lead lock sizes vary from 5lb to 11lb for different diameters of lead.

## Slide 11: Legislation
Water Regulations Advisor Scheme (WRAS)
It is a legal requirement for hot and cold water supplies to use WRAS-approved fittings to comply with the Water Regulations. Not only are they of high quality and resistant to corrosion in their specific surroundings, but they are also manufactured from non-contaminating materials.
WRAS provide guidelines and requirements for the installation of fittings and materials, including restrictions on the use of lead pipes and fittings. These regulations mandate the use of approved materials and products that comply with safety standards and reduce the risk of contamination. WRAS approved fittings will then be badged as shown.
​
WRAS
Notes: https://www.wrasapprovals.co.uk/

## Slide 12: Fittings and materials
Lead and copper were used for underground wholesome water supplies. These materials have now been replaced with MDPE (medium density polyethylene)​. New water mains should be laid at depth of 750mm (minimum) to 1,350mm (maximum).
Press-fit fittings require an electrical crimping machine for jointing. The machine crimps the fittings onto the tube to create a watertight seal on the ‘o’ ring. They are ideal for use when hot works (soldering) is not permitted.

## Slide 13: Fittings and materials
Push-fit polybutylene pipe has become popular in recent years due to the ease of installation. A stainless-steel grab ring locks the pipe onto the fitting and an ‘o’ ring creates a watertight seal onto the pipe. Pipe inserts are required for plastic pipe. This jointing method does not require hot works.

## Slide 14: Imperial copper
In the 1970s, the UK transitioned from the imperial measurement system to the metric system. In the old British imperial copper pipe, the size was denoted by the inches of its nominal bore, resulting in the outside diameter being larger than the named size. In metric diameters, the size of the pipe refers to its outside dimension.
Outside diameter
Nominal bore

## Slide 15: Imperial copper sizes
Imperial nominal bore | Imperial outside diameter | Metric outside diameter
1/2 inch | 0.596" / 15.14mm | 15mm
3/4 inch | 0.846" / 21.49mm | 22mm
1 inch | 1.112" / 28.24mm | 28mm
1-1/4 inch | 1.362" / 34.59mm | 35mm
1-1/2 inch | 1.612" / 40.94mm | 42mm

## Slide 16: Below ground drainage
S&VP: Soil and vent pipe
RWG: Rainwater gully
IC: Inspection chamber
Rainwater
Foul water drain
Sewerage systems have developed since Victorian times. Combined sewerage systems take both rainfall and waste water to the sewage treatment works.
As towns and cities expanded, separate sewers were introduced to accommodate the increase volume in surface and foul water.

## Slide 17: Soil and vent pipes
Traditionally-cast iron was used for a whole host of applications, including foul waste removal (soil pipe), guttering and baths.
Cast iron requires painting to protect it from atmospheric corrosion,
Today, PVC is preferred for guttering and soil stacks.
Drain connectors or flexy seals can be used to change from imperial cast or clay to metric PVC.

## Slide 18: Below ground drainage
A collapsed or cracked drain requires immediate attention and remedial action.
Symptoms of a cracked or collapsed drain include:
      slow drainage
      foul odors
      leaking sewage
      mould on wall or ceilings
      foundation and wall cracks.
      Imperial to metric flexy seal adaptors provide a solution for connecting PVC drainage pipes.

## Slide 19: Lead waste pipes
In the past, waste pipework was traditionally crafted from lead and connected using lead wiped joints.
In the process of renovations, it is good practice to upgrade lead waste pipework to plastic, which features a larger internal bore.

## Slide 20: Cold water storge cisterns
Traditionally, cold-water storage cisterns were made from galvanised metal and held together with studs.
Over time the zinc coating is removed, exposing the steel and leading to corrosion.
Ferrous oxide (rust) would contaminate the cold-water storage cistern, so it requires immediate attention once identified.
Galvanic cisterns are no longer approved for new cold water storage cisterns.

## Slide 21: Dezincification
Brass (copper and zinc) components can have zinc leached out as fresh water passes through them. It leaves the brass fitting weak and brittle, quite often covered in white powder (zinc oxide).
Valves and fittings showing signs of this type of corrosion require replacing.
Modern brass components are dezincification resistant and have DZR or DZ stamped on them.

## Slide 22: Structure
Pipework is generally installed under suspended floors which may require drilling or notching the joists.
Building Regulations Document: A sets out requirements for notching, drilling and pipe chases and must be always followed.

## Slide 23
Any questions?