## Slide 1: PowerPoint 6: Effective waste management – benefits and regulatory requirements
PowerPoint presentation
Unit 202: Changing practices over time

## Slide 2: Aim: Waste management in construction
Objectives
  Describe what waste is.
  Explore waste classification.
  Discuss the benefits waste segregation.
  Identify techniques to reduce waste.
  Review the WRAP protocol.
  Disposal of waste in line with COSHH.
  Examine waste and regulatory requirements.

## Slide 3: What is waste in relation to construction
Any material produced as a result of construction work that is discarded, whether or not it has been processed or stored beforehand, is referred to as "construction waste."
It consists of a variety of leftover materials from site clearing, excavation, construction, renovation, demolition, and road work.
Always think about which waste is recyclable and reusable before disposing of anything on site.
Remember that the Waste (England and Wales) Regulations 2011 demand that companies use the waste management hierarchy when transferring waste.

## Slide 4: The waste hierarchy
Notes: Discuss the financial and environmental impact of sending waste to landfill.

## Slide 5: Waste classifications: non-hazardous/hazardous
Waste can generally be classified as hazardous or non-hazardous.
Construction waste that doesn't endanger the environment or human health is referred to as non-hazardous waste. The most typical kind of construction waste has a wide range of recycling and reuse options.
Construction waste that poses a risk to the environment or human health is referred to as hazardous waste. It is created when buildings, roads, and other structures are being built or demolished.
Notes: Discuss the different waste streams
Discuss inert waste and what it means,

## Slide 6: Waste segregation
Segregating waste on site into separate material streams can help minimise costs and maximise the opportunities for recovery and recycling.
When possible, use different skips to separate different types of waste as they are produced (given the space available).
Skips for wood, inert, and mixed materials ought to be available at the very least.
If there isn't enough room for multiple skips use a licenced waste management company. They may be able to recover recyclable materials from mixed skips.
Notes: Discuss the value of certain waste streams such as copper and how they hold value, and also discuss the public register of scrap metal dealers in Wales
Discuss the importance of recycling
Remind learners that metal based and plastic based materials are finite

## Slide 7: Duty of care and waste
Under the Waste (England and Wales) Regulations 2011, the Hazardous Waste (England and Wales) Regulations 2005 and the Environmental Protection Act 1990, construction businesses, which include the trades, are legally obligated to produce, store, transport, and dispose of their business waste in a manner that does not harm the environment. It is referred to as their duty of care.
Notes: All waste which leaves site and transfers to another party (e.g. waste carrier) must be accompanied by documentation which acts as a record of the waste movement.
For Non-Hazardous waste, a waste transfer note must accompany each movement.
For Hazardous waste, a hazardous/special waste consignment note must accompany each movement. Waste transfer notes must be kept for 2 years and consignment notes for 3 years, and they must be available to the regulator upon request.

## Slide 8: Transporting waste
As part of the duty of care, all waste (recycling, non-hazardous or hazardous) must be disposed of by licensed carriers.
This process is closely monitored through a system of waste transfer notes, creating an auditable trail that follows the waste from source to its destination.
The Hazardous Waste Regulations (2005) require that any hazardous waste produced by a company must be collected separately to other waste for it to be treated and disposed of correctly.

## Slide 9: Techniques for waste reduction on site
Effective ordering:
  Do not order more materials than needed.
  Have materials delivered to site when needed.
  Reject materials that were damaged in transit and ask the supplier to send them back.
Effective storage:
  Plan where bulk materials are stored to minimise transportation and avoid breakages.
  Keep protective packaging on and ensure storage areas are secure and weatherproof.
  When bad weather is forecast secure and protect materials.

## Slide 10: Techniques for waste reduction on site
Site activities
Make sure options for using recycled and reclaimed building materials that adhere to material specifications are taken into account.
To reduce the need for material transportation, recycle on site any suitable spoil, demolition waste and surplus building materials.
To minimise material losses and waste, keep the area clean.
Training
Increase awareness of good practises such as waste segregation as part of on-site health and safety orientation or training.
Notes: .

## Slide 11: The WRAP protocol
The WRAP Protocol is a set of guidelines for managing construction waste
The WRAP Protocol covers all aspects of construction waste management, from planning and design to demolition and disposal.
The WRAP Protocol aims to reduce the amount of construction waste that is sent to landfill. It also aims to improve the recycling and reuse of construction materials.
Notes: The protocol provides guidance on how to achieve these goals, including:
Planning and design: The WRAP Protocol recommends that construction projects be designed with waste reduction in mind. This can be done by using materials that are easily recycled or reused, and by designing buildings that are easy to demolish and deconstruct.
Construction: The WRAP Protocol recommends that construction projects be managed in a way that minimizes waste. This can be done by segregating waste at the source, and by using waste minimization techniques such as lean construction.
Demolition: The WRAP Protocol recommends that demolition projects be managed in a way that maximizes the recycling and reuse of materials. This can be done by using a controlled demolition method, and by separating materials for recycling and reuse.
Disposal: The WRAP Protocol recommends that construction waste be disposed of in a safe and environmentally responsible manner. This can be done by recycling, reusing, or composting materials whenever possible, and by sending hazardous waste to a licensed disposal facility.

## Slide 12: WRAP Quality Protocols
The Quality Protocols (QPs), developed by WRAP in collaboration with the Environment Agency, provide clear guidelines for transforming waste into non-waste products or materials.
These protocols outline the necessary steps to be followed, allowing businesses and industries to reuse the recovered products or supply them to other markets.
By adhering to the QPs, recovered products can be utilised without the need for strict waste regulation controls.

## Slide 13: Disposal of hazardous waste
  The disposal of hazardous waste in construction follows a specific process to ensure the safe and proper handling of potentially harmful materials.
  When dealing with hazardous waste, it must first be classified, this classification is based on the type of waste.
  The hazardous nature of the waste can be determined by the manufactures data sheet and the COSHH Assessment.
  All hazardous waste must be stored in line with COSHH storage requirements relative to the hazardous substance.
  The waste must be treated/disposed of in line with COSHH and environmental legislation.
  Segregation of hazardous waste is required by law.

## Slide 14: Consequences of not disposing of hazardous waste safely
There are a range of consequences for not properly disposing of hazardous waste including:
immediate harm to you or others
harm to you or others over time
harm to the environment.

## Slide 15: Hazardous waste on site
Types of hazardous waste on site may include
asbestos
asbestos containing materials
containers that held chemicals such as brick acid, concrete additives or paints
contaminated soils
contaminated packaging.

## Slide 16: Dealing with asbestos
All asbestos waste is defined as 'hazardous waste' Wales when it contains more than 0.1% asbestos
Asbestos waste must not be mixed with other types of waste.
Any waste that contains asbestos, or is contaminated with asbestos, must be double-bagged and placed in a covered, locked skip.
This includes overalls, over-shoes, sampling wastes and respiratory protection equipment that have come into contact with asbestos.
If you discover asbestos on site, do not disturb the material, stop work and tell your supervisor.

## Slide 17: Legislation affecting waste management
The Environmental Protection Act of 1990 is a crucial UK law focusing on environmental management and protection, particularly in the construction industry. It emphasises waste management, pollution prevention, and environmental compliance, promoting sustainable practices and environmental protection.
The Hazardous Waste Regulations 2005 address hazardous waste management in construction activities, establishing a classification system for businesses to ensure safe handling, transportation, and correct disposal. Construction firms must prioritise prevention, minimisation, reuse, recycling, recovery, and safe disposal while ensuring that the necessary licences and permissions are in place under these regulations.
Notes: Key Features of the EPA 1990
Duty of Care: The EPA imposes a duty of care on individuals and businesses to properly manage and dispose of waste. This means that construction companies have a legal obligation to ensure that waste generated from their activities is handled, transported, and disposed of in a responsible and compliant manner.
Waste Management Licensing: The EPA requires waste management facilities, such as landfill sites and waste treatment plants, to obtain an appropriate license from the environmental regulator, typically the Environment Agency. Construction companies need to ensure that they use licensed waste management facilities when disposing of waste to comply with this requirement.
Environmental Permits: The EPA establishes a permitting system for activities that have the potential to cause significant environmental impact. Construction projects involving activities such as waste incineration, landfill operations, and hazardous waste treatment may require an environmental permit. These permits outline specific conditions and requirements to ensure proper environmental management.
Duty to Prevent Pollution: The EPA places a duty on individuals and businesses to take all reasonable measures to prevent pollution and minimize environmental harm. This duty applies to activities within the construction industry, such as preventing the release of pollutants into watercourses, air emissions control, and minimizing soil contamination.
Contaminated Land: The EPA includes provisions for the identification, assessment, and remediation of contaminated land. Construction projects involving brownfield sites or activities that may potentially result in soil contamination must comply with the relevant provisions to ensure proper assessment and remediation of contaminated land.
Enforcement and Penalties: The EPA grants regulatory authorities, such as the Environment Agency, the power to enforce compliance with environmental regulations. Authorities have the authority to inspect construction sites, issue enforcement notices, and impose penalties for non-compliance, including fines and prosecutions.

## Slide 18: Legislation affecting waste management
The Pollution Prevention and Control Act 1999 is aimed at preventing and controlling pollution from industrial activities, including construction. It introduced the concept of Integrated Pollution Prevention and Control (IPPC) and promoted Best Available Techniques (BAT) to minimise pollution.
The Act establishes a unified environmental permitting system, enforces compliance, and promotes transparency and accountability through public participation.

## Slide 19: Legislation affecting waste management
The Control of Pollution Act 1974 regulates and prevents pollution in sectors like construction, including noise, air pollution and noise control.
It grants local authorities power to control air pollution, requiring companies to minimise dust and emissions. Abatement notices and penalties for pollution control violations can result in fines or prosecution.
Local authorities and the Environment Agency enforce the Act's provisions, contributing to a healthier environment, improved quality of life, and sustainable practices.

## Slide 20: Legislation affecting waste management
  The Waste Electrical and Electronic Equipment (WEEE) Regulations 2013 control and manage the disposal and recycling of electrical and electronic equipment.
  Construction companies, involved in equipment installation or replacement, have responsibilities as producers under the regulations. They require separate collection, segregation and proper recycling to minimise environmental impact.
  Construction companies must send waste to authorised treatment facilities and maintain accurate records of equipment.
  By adhering to the WEEE Regulations, the construction industry can contribute to responsible waste management and recycling, reducing environmental impact and promoting sustainable practices in equipment disposal.

## Slide 21
Any questions?