## Slide 1: PowerPoint 3: Cultural requirements for different buildings and structures
PowerPoint presentation
Unit 101: Introduction to the built environment

## Slide 2: Gofynion crefyddol - Religious requirements
Religion has shaped the design of buildings for thousands of years. Some religious places of worship were the largest buildings in the world before the use of steel and concrete enabled skyscrapers to be built.
Eglwysi - Churches: These normally face east to west, with the altar at the east end and the façade and main entrance to the west. Different versions of Christianity have variations of this form, with Catholic churches and Cathedrals laid out in the shape of a cross, while Methodist churches tend to be less ornate, both externally and internally, with a square or rectangular footprint.
St David’s Cathedral
Congregational chapel in Bala; a typical example of 19th-century Methodist religious architecture in Wales

## Slide 3: Gofynion crefyddol - Religious requirements
Synagogau - Synagogues: These do not have any set design layout as historically Jews were not allowed to own their own land and so any elaborate architectural build would have been unlikely. Modern synagogues tend to be either square or oblong, with the only stipulation being that they must have windows to remind those praying of the outside world. They also contain a holy arc placed on an east wall to hold the scrolls.
Abandoned Merthyr Tydfil synagogue

## Slide 4: Gofynion crefyddol - Religious requirements
A courtyard large enough to hold the entire local male population.
A mihrab, which is a shallow niche in a wall that faces Mecca.
A minaret, which is a tower adjacent to the mosque from which the call to pray is announced.
A dome that represents the vault of heaven.
Mosgiau - Mosques: The architecture of a mosque is shaped most strongly by the regional traditions of the time and place in which it was built. As a result, style, layout, and decoration can vary greatly. Nevertheless, because of the common function of the mosque as a place of congregational prayer, certain architectural features appear in mosques all over the world:

## Slide 5: Gofynion dinesig - Civic requirements
A civic building is a central landmark in the geographical or business centre of a town or city. They are frequently the pride of a district and foster a strong local, regional and national identity, as well as providing public services and having a positive impact on a neighbourhood. They often include registry offices, libraries, government offices and multi-prayer rooms. They are designed to be multi-functional with a network of spaces or buildings tailored to meet the specific needs of the community, so designs will vary across the country in size, scope and appearance.
Swansea civic centre
Cardiff civic centre

## Slide 6: Gofynion o ran y celfyddydau - Arts requirements
Art galleries and museums need to be versatile spaces, allowing for a range of exhibits as well as permanent facilities, in order to meet the welfare needs of their clientele. Some are modern purpose-built buildings, with plenty of glass to let in light and give a feeling of space. Others are in old traditional buildings, giving a feeling of grandeur and importance.
Examples of arts requirements can include:
Administration offices Storerooms Security Large exhibition space/display areas Small amphitheatres Foyer/Gathering spaces Galleries Conservation laboratories Cafeteria / restaurant Art and gift shops Workshop space Sculptural gardens Auction rooms

## Slide 7: Gofynion o ran y celfyddydau - Arts requirements
Theatrau - Theatres are designed specifically to hold plays, show films and host music. The seating layout is designed so everyone can see the stage and the ceiling, and wall configurations are designed to enhance the acoustics so there are no echoes and sound travels to all corners of the venue. There are no external windows to stop unwanted light in the space.

## Slide 8
Any questions?
Unrhyw gwestiynau?

## Slide 9: PowerPoint 4: Societal requirements for communities
PowerPoint presentation
Unit 101: Introduction to the built environment

## Slide 10: Seilwaith a chysylltiadau trafnidiaeth Infrastructure and transport links
Much of the country now has a network of easily accessible transport links, i.e. trains, bus routes and roads that link villages to towns and these towns to other towns and cities. This has enabled the population to choose where they live, rather than being bound to their hometown.
The factors that help individuals decide where they live depend on the social and cultural needs of the individual – some choose to live in larger established communities that provide a safe and secure base for both work and personal life, with local retail, leisure and entertainment facilities. Others choose to live in a more remote location where they can enjoy outdoor spaces and a peaceful, relaxed lifestyle.
These choices would not be possible without the implementation of local development and town planning.

## Slide 11: Cynlluniau Datblygu Lleol - Local development plans
Each local authority draws up a five- or ten-year development plan that includes the location of housing, and commercial and industrial developments.
Through the 19th and up to the mid-20th century, infrastructure was more limited. The working-class often did not have their own transport so local industry, homes and commercial premises were built close together for convenience. The development of public and private transport, along with changes in public attitudes, led to demands for cleaner, healthier places to live. Local authorities moved to segregate industrial and commercial businesses from domestic housing in existing towns and villages. This approach shaped the development of all new housing estates, industrial estates and shopping complexes.

## Slide 12: Enghraifft o dref ddiwydiannol cyn cynllunio trefol Example of an industrial town pre-town planning

## Slide 13: Ar ôl cynllunio trefol – Caerdydd heddiw Post-town planning – Cardiff today

## Slide 14: Rheoliadau adeiladu Building regulations
Building regulations are there to ensure that any new building, extensions, conversions or renovations are complete to a standard that meets the minimum acceptable level of safety for the end user and are energy efficient. The regulations are made up of a series of parts, each covering a specific area.

## Slide 15: Dogfennau cymeradwy rheoliadau adeiladu Building regulations approved documents
Part | Title
A | Structure
B | Fire safety
C | Site preparation and resistance to contaminants and moisture
D | Toxic substances
E | Resistance to the passage of sound
F | Ventilation
G | Sanitation, hot water safety and water efficiency
H | Drainage and disposal
J | Combustion appliances and fuel storage systems
K | Protection from falling, collision and impact
L | Conservation of fuel and power
M | Access to and use of buildings
N | Glazing safety (withdrawn in England 2013)
P | Electrical safety
Q | Security
R | Physical infrastructure for highspeed electronic communication networks
REG 7 | Materials and workmanship

## Slide 16
Any questions?

## Slide 17: PowerPoint 5: Know the different types of structures in the built environment
PowerPoint presentation
Unit 101: Introduction to the built environment

## Slide 18: Transport infrastructure
People and goods are transported around the country and the rest of the world using a range of interlinking networks.
Ffyrdd - Roads: link local and national locations, towns, cities, airports, docks etc.
Rheilffyrdd - Rail: links major towns and cities to docks and airports.
Awyr - Air: airports link regional and internal destinations, carrying people and goods.
Dŵr - Water: canals were traditionally used to transport goods before the railways were built but are now mainly used for leisure. Modern ports are all deep water to accommodate large ships and tankers transporting raw materials and goods internationally.

## Slide 19: Highways
Types of highways in the UK include:
Traffyrdd - Motorways: A network of major roads, normally three lanes wide, connecting all parts of the UK and
avoiding built-up areas.
Ffyrdd A/ Cefnffyrdd - A/Trunk roads: Major roads between towns and cities that can be both single and dual carriageways. There are over 28,000 miles of A roads in the UK.

## Slide 20: Highways (continued)
Ffyrdd B a ffyrdd diddosbarth - B and unclassified roads: Minor roads often serving smaller towns and villages, ranging in size from dual carriageways to single lane with passing points.
Llwybrau beiciau - Cycle paths: A UK-wide network of paths and routes for walking and cycling. These can run alongside an A/B road or be an altogether separate path.

## Slide 21: Pontydd - Bridges
A bridge is a structure that crosses an obstacle such as a river, valley or another road, without impacting on the obstacle. Bridges can be built using one of five main construction methods, or by a mix of these.
2. Pont drawst - Beam bridge – e.g. road bridge in Cardigan
1. Pont fwa - Arch bridge – e.g. Inigo Jones bridge, Llanrwst, North Wales

## Slide 22: Pontydd - Bridges
3. Pont Graffrwym - Truss bridge – e.g. Ballachulish Bridge, Glencoe
5. Pont Grog - Suspension bridge – e.g. Menai Suspension Bridge
4. Pont Gantilifrog - Cantilever bridge – e.g. The Forth Bridge

## Slide 23: Traphontydd a thraphontydd dŵr - Viaducts and aqueducts
A viaduct is a long bridge-like structure consisting of a series of arches that carries a road or railway across a valley or gorge.
An aqueduct carries water from a source to a distribution point. Canals often have aqueducts to cross valleys or low-lying areas in much the same way as a viaduct.
Pontcysyllte aqueduct
Chirk and Cefn Mawr viaduct

## Slide 24: Twnelau - Tunnels
Tunnels are artificial underground passages built to go through an obstacle, such as a hill, or under buildings, roads or a body of water.
Types of tunnels
Torri a gorchuddio - Cut and covered: A simple method of constructing a shallow tunnel, where the ground is excavated, and a supporting overhead structure is installed then back-filled.
Turio - Bored: This involves drilling through a solid land mass or under a body of water and then lining the tube.
Tiwb wedi’i drochi - Immersed tube: A concrete structure is prefabricated on land and floated out to its final location, where it is sunk, joined together and then the water is pumped out to leave a dry tunnel.

## Slide 25: Enghraifft o dwnnel wedi’i durio - Example of a bored tunnel
Notes: data:image/jpeg;base64,/9j/4AAQSkZJRgABAQAAAQABAAD/2wCEAAkGBxMSEhUSExMVFhUVFxcXFxYYFxgXGBcaFxcWFxoXFRcYHSggGBolGxUXITEhJSkrLi4uFx8zODMsNygtLisBCgoKDg0OGg8QGi0eHSUvLS0tLS4tLS0tLS0rLjctLS0tLS0vMy0rLSsrKy01Ky0tKy0tLS0rListLS8tLSstLf/AABEIALcBEwMBIgACEQEDEQH/xAAbAAABBQEBAAAAAAAAAAAAAAAAAQIDBAUGB//EAEMQAAEDAQQGBQoEBgEEAwAAAAEAAhEDBBIhMQUTQVFh8AYicYGRFBYyQlKSobHR4WJywfEVI1OCotLCc4OTsgczQ//EABoBAQEBAQEBAQAAAAAAAAAAAAABAgMEBQb/xAAsEQEAAQMCBQIGAgMAAAAAAAAAAQIREwMSBCExQVEiUjJxgZGh8GGxIyRC/9oADAMBAAIRAxEAPwDm0LW83q34fe+yXzerfh977L9Vvp8vx+OrwyFctDAKNIwJLqsnaYuRPifFW/N2tub732U9XQlY02MhvULzN7O9d4fhWZri8c/2zdNE2nl+3YKFr+blf8HvfZL5uV9zfe+y1vp8sbKvDHSrX826+5nvfZL5tV9zPe+yb6fJsq8MdC2fNmvuZ732R5sV9zPe+yZKfJsq8MZb1n6PB9nbVFQ33U31BThhm5U1d0de/jnN2BBkqMdF7RuZ732V6no23Np6prwGQRAcBg43iL129BJOErnqVTMRsmIddKIiZ3xdUPRO0B112rb6IkuIEufqw3KZvEDKMQZIxUY6M2iGOLWi/kJMjqucCQAZkMODZOWGIWg/R9vJkvbMtOBaJLXXw4w3E3sZzJzlKNH2/DrsMSMbhkEOaWulvXbD3C66QA4wue7V90OltL2yrt6KuAdrKtNjm62Rjhq6bKkk7GkPGyRhvgVKOgnF9dj3tY6gGk7b157WdUj84PeBtkaVTR1vcHA1GkPm8JbjLBTPq4SxoGG4Jg0Rbb73323qgh5vDrDDMRHqjwSKq+9UExp9qZQ1OiNbWOawse0FwD5w6tQ07roGDpHYN8Jmiejjq9J72uh7KrKdwjO8QHOmcLsyeAKsWmhbqTXPL5AvOIF1/pOvuddLYm91pzGyFm6HdaXk06DnDNxxgCWlhJPFriO9X/LNM+qP3yn+KKo9Mr1t6J1WufqyH02uAa49UvkMJMYgAawZmcDAMFRU+i1dzwxppkkYEOJEh7qZbIGBDmkE5cVeOjrec6jTJBklpIIu+ibstHUZIGBuiZTqNh0gz0ajc73qmDec+8JaYN57jOfWKzu1bfFDUxpTN9ssqy6IaawpvqXBqmVZN0El9NjwwFzg1pN8AFxHjgrNp6LuE3ajcHVARU/llrabGPL3YkRDxkTmCCZU1LQ9ta/WBzb1wMJkEFgAaGFpbDmw1ogjYE+po23uDgagIeXF3WGN5oYdmALQBAwgDcFZqrvyqhIjTtzplSp9GqtzWOLQ0sc4OByhrXdaQMIdm2du0Qs3Sti1FapRvB2rcW3hkY4bOxdC/R1vLS01GwRBxaJF0M6xDZcbrQJOOAVS1dHrXUeXvLHOdiTeAJMRJgZ4LVFdV/VVDOpTRMemJu55C3fNS0bme99knmraNzPe+y7ZKfLhjq8MNC3PNS0bme99keato3M977Jkp8myrwxFbLB5PegTrYnbFyY8Voeato3M977KfzdtGq1cM9O/N/8ADdjJZqrp5WlqmiefJzqRbnmraNzPe+yPNa0bme99lrJT5Z2VeGGlW35rWjcz3vsk81rRuZ732TJT5NlXhipFuea1o3M977ITJT5Nk+HZ6pApLU1HBLqOC+dkfRxyy9Unapaeo4JdRwUyGKWZqeCXVcFpajgl8n4JkXFLN1PBLqlpahLqFMhhZupS6krR1CXUpkXCzdUUuqK0dQjUKZDCztUUuqK0NSl1KZFws7VpdWtDUo1KZDCz7ihsthZTBDGBoJJMbSVrakJdSEyGFn3EXFoagI8nCZFwyz7iLi0PJwjycJkMMs64i4tHycJPJwmSDDLPuJNWtHUJNQmRMLP1aTVrR1CNSmQws7Vo1a0dSk1PBMiYmfq0ataGoSGgrkMShcSXFoahJqEyQmKVC4hXtQhN5ild1aNWtC5wS3OC8mR9HEztUlFJaIZwTrn4VMhiZ2pSijxWjc/ClufhUyNYoZ4ocUvk60QzgluLOSVxM8WZL5Mr9xLcTJK4oUPJ0eTK/cRcUyLjhQ8mR5MFfuIuJkMUKHk/BLqOCvXEtxMhjhQ1PBGqG5X7iLimQxwoaobkuqG5XriLibzGo6oeyjVD2VeuIuJvXGo6obkakbleuJLibzGpakbijUjcrtxF1XemNS1HBGoG5XbiLibzGpajgk1HBXdWjVpvMal5PwSGzq7q0apN5jhRNnSGzq9qe1IaHFXImOFDyZCvahCuRMS1CW6vOrLpq0033zVNRowNNxABnjGBxzWo7psGu61CpdjEgtJnDAAwIzxncvnRxVH/AHen5/tnpnl2djdS3VnWDStGsAWVWyQDdJAcOBbmCtALvFUVReJuFhF1KhVSQi6lQgSEQlQgSEQlQgSEEJUiCF9pYL0uAuRex9GcRO5ShZlr0UXuebwAfMiM4Y0NnscJ70N0Y68SXSC6e0Xr0HsGG3uyW7U26uO6u/wtJ7gBJyCjqWhjSGlwBMQO0wPE4LNdop/tD0bs4zF0iMt+OfdtVq12NznhwIHoicQcCTkMHAzkcktT5N9dvhXGuBEgyEgqCYkTu7p+RWY3RRDY6uTQN0Bzid8SCNhyT7Jo5zS0uIcWnjlca3D3Z70tT5Irr5elpwiEqFh2JdRdSoQJdRdSoQJCISoQJCISlRms0YFw8QpcPhEKG0WynTF572MBwBc4NBO4Elc3bOn1kZkXvguButw6piZJAIMYEdqxVq0U/FNk5OqhJdVDR+nLPWANOswmA67eF4A+0MwVafbKYxL2DtcAtRXTMXiVS3UKidOWYYa+l77fqhZzUe6PunJ57BTh8E1pTpXndkT6LDmAtPRulqtBoYw9UeqcRjxzVAJYUimKZvEc0tDbf0prn0dUO1rj8Q8fJVz0rtmxtnPYH/q5ZQcgnmCu9OvVHaJc6tGKu8x8paPnhbBnRp9zXH5PTvPO1DOi33Kn1WbCJ2yuscVHeiHCeFq7aktLz5q7W0x3OH6p7em9TdT/AMvqsy8ePimlgOYB7RPzW44nT70flieG1u2p+GyOmj91P4/VOHTJ+6n8fqsA2ZhzYzuAHyUJ0dTPqkdjnfVbjiNCetMuc6HFR0qif35OnHTJ25nx+qd54u3M5/uXLfw2nud7xUZ0Ww5OqDscD82rUa3Dz5YnS4yO8T9XXeeJ3N5/uSeeJ3N5/uXHO0YP6lQdsfZV36POyse9uHiHLUV8NPf+2Ko42O35h3HnkdzOe9HnmdzPj9V5++wVf6jPF/8Aqm+Q1dtVn+f+q3/r+6HLfxvtl6D55ncz4/VMPTR25ngf9lwJsh21j3MB+bgjycbX1P8AEfVZmvho7/23FPHT2/MO6d02fuZ7rv8AZRnpzU9lnuu/2XDGi3fUP9zR/wAEoa0erP5nOPyhZnW4eP5ajR42e9vq7Y9PKvs0/dd/smnp9V9mn4O/2XGGqdgaP7G/qEeUv9qOwAfJc54jS7UO0cNxHfUdk3p7WJhtNhPBrj8nId04tP8ASpjtBHzeuHq13nAucRuJJCqP38VmeIp7UQ6Rw2p31Jd67p/aBmLOO0k/Bryfgonf/JNUerTd2Mc0e858/wCK4Qjn7Jplc6taZ6REO1Gjt61TP1dTpTp3aqzXMljGuBBDRjHa7nFc6bY/f8Bj8FCecUc/Jeeqimqb1Rd2tCx5Y/ePAfRJ5a/f8GqABLHas4dP2x9ktCbyx59buw+iPKn+0e6AoYlL488/BMWn7Y+y2hJ5Q72neJQmgneha2U+IHagnd8TPglBG9EonYstlnn6puMft90s7AgZfSEConnBNOHelHOXjggUHakEzsj4oDUsIG3ezwSzP7EIkbEsT+/0QNEZ71QtdGrrA+mXEAAFt4gHrtnqEhs3L/7wtAc/sqFtsL3PDg4XbsXDIBl9N0EiRBDCCY27VYFYNtkDFkwScG4ODHQBwL7sncpaLbQagL4uguEC7EF1OCBPWF0OxMEYp9jstVhZeqzESJ9IAOB2ZyWHuO9QNsldrWjWtAEDMn2RMlu3EXeOcwiNRwULiqdWzV5wqCIyJxOJmSG45jHZd4qCjYqodfc+ThMEmerTDsC3D0XH+5FXH88/dROUzlDU4oInKFxUrionFBE5NTiE1xhWEJKjcnk8/eE0qojlQvUplRVFREUkoPOfO5EIhUD5IlHP2+SA8OxKDzz3Jo8fH6J4Y7cfA70UwlOaeHMbE9tmf7Dz2Nd27lLTsFY5UqnuO+iCuQd6FdGiq/8ASqe45CDrvLH5B7MfwU0028zGspzhhcZOJIGzeCFns0PTG1xxvSSJxc12YG9g+KZ/BKcAS/D8uMBzcerBwcR38FhWu20vOIcw/wDbYf0TRa35Xm/+Nn0UNCiGANGQ5x4qWEupzrW8CbrH8CwCRwuwrVkqUKwyuHdMhU+BVGu0sdeGR+BSJHQVdEkYgyFUfZXDYn6N0oRtW1SrsfmraJHOGmRsKbK6SpYwclTq2Dgm0ZCoWvR7nuLhULZAERIwIOMnLAiBvK3Kli7VTqlo9b9fkp0GT/CHzOtPDAyM8Qb2cEY/hGaWnotwImqXQ5rsQfVcxwjrZm7iYxnILTG+D4IDkuWRlQv7lO5QvUELlDUCmfzyVC7eghKiKleFG9UROTSrDLM92Qw3nAKdminHMx2AlIRmymlbdLRdPJz3fIfZadn0NTzDQeJx+atyzjyCcgTwCkZoys7KmeEwP/Zd9Q0eBkIV2lYQrzLQ4Cz9FqzjiWt8StWydCgfSe49kAfGV17ixnFZlv0oYgYBBRdoSx0BLm3iNhJd88Asa39IBTN2jRpNH5Z58FFpbSBg49i50knEmT+31QbR6T19lwdjG/RMd0ltPtx2NAWPHPO1Kql2oekFp/qu7kx2mrQc6z/ErOS8/BC67/E639V/ifqhVQ3iPihLDtRhyN6VLKFzaNBE/dOCCUkn7oAJHMkQcinApIQZrSWOjwO8LVslrVe1UL44jJUrPVhWJHW2a28VcqWxjWlzzAGZ52rmbPXVTSmkR1nOxp0o6ux9Q5A8MD3Ard0T6Y0yIvPkNOLKTYvvHtOOTW8fAHNcraNPWpxIpRRbj6AAO/Gq/EnsI7FFbNISL7zee4nbnkAPjAA3di57SOla7JAe9rXYENwJG6ZGGOW+dkLVNKTLRdpa0TPllaf+s/6wum6K6UtDrQKNqdrGODgC8AuDmi9hUbjkHYErzJtMwHNktJz4mZByIO3PZtXR6L0laQ5rjUcbhF0klxHAEzhsA38AVvl3R6bbbO0OLWOkgFxYfSDRgXD2mgkYjKRKz37vgsXSOmXV2U67OpVoOBvtIggksOH5oBGIx7lt07Q2rTbWaAA7BzRk17YvNHDEOHAhca6bdGonygO3JQ1MlM5QvWVQuV+y2FoGsqmGjhOPstHrO+A2pujqF50kwBJJ3ACSe4Kva7driCBDB1Wt9jbDvxbTv7FqijckzYaT029o/kNDI9YgPee9whvcO9URpiuSSa1X0SfTcPgCr1DR5fhvSWDRV6WlpvAlnol2e+Bhkuuxi6vT03XBALi9sYioA8bMJdiO4rW0ZpQOP8vqP/pkyx/BhOIPA9xWfatFOYTI/YfeVnVaZWZpIl6XYNIsqNkCHDBzTm0pLTbFx1h0gSNb67IbU/Gw4Bx4jI9y1q1pnEbVluElqtaxLZasySpLTWXP6StMy0bM+1Z6qhtNa+Se4KGOYSJeC0yVIefmkP1/ZOhEA5+CUDZ+nf4Jv7pQPh9EDpHP7ISXRzKEHcjtSHn7IhC5tgHn7JbyQDGeec0oQBKEkJN6B0qhb6WN8d/1V/nNNDp47N+xBn0q0Cd2KwdPVTq6Td4dUPEuddHwZ/kti2UrkjYQY8MljaZp3mU3RgaYHeHPW6eqS5rTFWnTqtbUNSboaA1rSOsBMy4YEncclXtFvLbpDDdEtv8AtgEmXA4CRhh4rp7XoqzWio81WVDUaGuZdMS1zGOBjbiVxLW1HOeyQ0SWbi6JwwzEb16tLr/LlXHLn0SNrS5zyfWBicCJIj5eCu2PSTg0uLZYZkwBtx9HZB3bNsrIpUpY4RjIGeEycBzsKsubUvBpeHNDC2TJIAui60k4CIIicoVjnTN+hPWLOl6P6Rp1Kjmay+0gsMAtAa8QDiBEGTH4QtjoTbi4VqRIPVbUHAscGmO1tT4Bczo2wUrOalx7nC4XuvAYNYyodg7PFafQQRVeYOFB/Zi6m35kLhMRZ07uweoXFSuyUTlxaTVagZZ3TgHlrJxgDF5kgGBLW+KzrPZ3SHNh0gRiMRGR2H5haRBdREOukVB3y3D/ANSqdGzODvSA2yBEz8D916NOPS51dW1ZLYaLAX04kQHSIkYfMKjXFS+XmpGsEm6JE5RiR1sst5VttnvMAYKhLSZMgCAdk4TABUllszcDMwZiJju2Htw/TrKH6Dddq06VcX6dSWsdJEYls75kEEHJU+kmidVUc0GQDgfiOeC1rNT19ek1uTHmo92Ybg0RIzMMBPEntUHSu0B9VxBzPwAjeszCuW0a6KobsqSw/wBwj5we5XbNXOrE7JHgqVjb/Np/naT4gpKdeGE7JJXCvq1SNIWmBAzOSxz4p9WpeJJ/ZN4c96zEEyQt5570oHP6/NAPP6JAefoqhePP7ZoA2oEoJ5/UoAcPslA557vBCUc8EC4bvgEIA5hCDuYSBIUELm2AEADntUVqtLKYvPMDATBzOQwUjXgiZGIB3Z9qBwCE2+N4w4qNtqYYAcOtJHEAgEjvIQS5xz8UQJ5+Sa94AJJECcczhmiQBs44gCeP2QMr0g4XSeztxWDUaTSfQI6zHhwwxumRhtiSD3ro2ztVDSdlcSKtMfzGbMw4bWnx+KsTYcvUsAiKzKjq9EgBnqVqb3Xg01GOkkdYgt9oDZjyOlqRDqnVcwCS0DHAFwIkDGCHCeC7fSFHWUzVp1Aw02wb+Gqa0CLxGJAIz3RkuatGn3SadSjTtJaYq1QwF7sIGIAMwIBwnCZK66VVU3mXTXoopttm91SzvL67aJphtEkDWwcGmP5l/bnOfxW7S0aGVC24BfIaC2Sy6260kB7nEXsOqSeu8DItXMUasvADKwbfEDVCQJwnr/GF1lnttZ1WrSY1tK7JbaSCXBreq917EtkAi9EwMCISq+63ZKaaZov1m/4Rafm5Ua260VLnVDLphhl4z6suDXZn0CtXolZLlC9trER/02Tj3un3E9nRylRdUZVc+pRLabqTg8XqpcA8BxxJHWExEnHPBbNCkcyADAAaMA1ogBoGwAALnFU2tLevFEVRs8R9w+dyhIjep3Dn7qFyjidQF4OpTF8CD+JpkZb8R3qJthjNzjwkx3hMf8efBXaNoFXA4P2j2uLeO8Lrp1dpZqhcsFtuYZDcrxqUX4vaJWC7OAmueYXdh0FXSrabblMBoO7PvXNW20lxPFLVM5qIMgEuIAGbvpvPBZmRGHXGufti638zhGHYJKzqrsA3YPmpq9fWERIY30R2+seJVd5XCZvN20JTSrlfR9VoY9zDdfF2IM3heGAylskTnCqmdx5/TiiADn5pvPPO1SPaRMgiM5GXA7ipKNne5wa1jiSWiI2ugNHCTETwQQXecUqlNB4AddMXrsxtADss5uwUlOk4kAAycRkJzxBOzBBEU4c/RBaRszxxH12Z/JK089yBQRuCE0uPP7oQd0EJBzCVc21e2UQ9t0mBLTMx6Lg/afwrNq6DYZl5MggYM6odrIPdrXY8Fct2jWVXNc/1YjAH12P277kdhKpU+jzQQdYeq1rBLQQbuqi8Mnf/AFDdmeEVDDoikXSHHBwa4DDrS50uiOt18zuVuroprrgvehIGDTINRjyR7JmmBIykqKroGmfWIMEEgNGYpjYB/TwH4ipKOhGNqCoCcDIbkB6XogQB6RmQZS4o1LBZm3mOq43KjMgIF0Mc7KC5oGLt5xUNtsFB4Ip1mBzw8G9AyFR73XbplwFoB2GLuIlav8JBBaXZi0NEbq7rxmRmFXd0cYSCXuzJwgDEUw4DDJzad0/nKXGrZ7S2oLzHBwwxHEBwPeHA96lJ5zVPRtg1IImR1ADwYxjMeMg/BXYUVQtmjA832ksf7Q2/mG1YdfQjh/8AkMz16NwHHPqPaQJzMNC6oJVYqmBxbtDNJBu2i8Mzq6WOcYXLo2YxOHctSw2B7GlrKQYHGXF10Xjvcym1rXf3NK6BAKszdbyo0rGG9Ykud7R2dg2J7lO9QPWUQvHMqNxUr1C9BA4TmoarfhtGxTuPYonFUK23PHpAP4nB3e7b3yippFpEFlQdkH6KJxTCFqKpZmE1TSRPo0u9x/QQqdUueZqOmMgPRHYBgpU0q3uInFQvU7lC4INenpa0FofcJpMYKRANzFtMMkPHWvwc8Yvbipj0otF2dWz03PDrpOIeKpBEzduuu/lcc81S0Xpt9ANaGhwa8vgkxJNE5f8AaHvFWKPSmo0NlodDS0kuMukUQb0g/wBFu444EHFauiLTGlazi1jmXdW/WXYz6tNovgABwAp7vWKv2bpFWBD20C7WOJbLnvvFpD3ReOQvA9WMDtzUI6V1ceoMZAxkibogXger1chnOYVep0iealKpcxpFzovOxvta1wb7DergBlKXE9DpTUBEUxgIxJc6Ja4dZ04ywY7jGGBVWrpyo40nGmJpNI24gtDNmwBuHhMQBPR6SvYG3WAEFhJvO61zUDuBFnaCPxOTqXSuo0EXW5QJMwLtNoiQQG/ypI23jiEuKOnLfUquDarbrm3jEnDWXXRmYEQR2rOB555wU9utGtqF7hEhogZdVrWf8R4qELIUE8/uhEnZCEHbl0eKUoQubZAgmEIQJgQljCPohCAnnnsQUiEDgEhQhAAIPDnxQhAJCY2IQgY4889qiehCCF3OSichCIgeVC4zj4IQgjcmpULUCMuTShCqI3ujNROSoVEDkQkQiHBJOSRCBxwSIQgXYgH5lCEDweCEIQf/2Q==

## Slide 26: Enghraifft o dwnnel trochi yn cael ei osod yn ei le Example of an immersed tunnel being lowered into position
Notes: data:image/jpeg;base64,/9j/4AAQSkZJRgABAQAAAQABAAD/2wCEAAkGBxAQEA8PDw8QDRAPDxAQDw8NDxAQDw8OFRUWFhYVFhUYHSggGRolGxUVITEhJSkrLi4uGB8zODMtNyktLisBCgoKDg0OGhAQGislHSAvLS0tLSstLSstLS0tKystLS0tLS0tLy0tKy0rKystLS0tLS0tLS0tLS0tLS0tLS0tLf/AABEIALUBFwMBEQACEQEDEQH/xAAbAAEBAAMBAQEAAAAAAAAAAAAAAQMEBQIGB//EAEsQAAECBAMBCQ0FBQYHAAAAAAEAAgMREhMEITEFBhQiMkFRYZHRFSNSU2JjcXOBkqGy0jNCk7HBdIKis8IWVHKEo8MHJENkg+Hw/8QAGgEBAQADAQEAAAAAAAAAAAAAAAECAwQFBv/EADwRAAEDAQMGDAYCAQUBAAAAAAABAhEDBCExEhVBUaHhBRMiMlJhcYGxwdHwFBZTYpGSM3KyBiNCgsLx/9oADAMBAAIRAxEAPwDctr3z5cW1QLagFtCC2hRbQC2gFtALaAW0AtoQW0AoSQKFZBaEkpKEkChJIKEkChSQKEkChJAoSQKEkChJAtoUW0AtoBbQC2gFtALaAW0AtqgW1ALaA2raxkotpIFtJAtpIFtJAtpIFtJAtpIFtJAtpIFtJAtpIgW0kQS2kgttJAtpIFCSBQkiBbSQLaSIFtJEChJEC2kiBbSRAtpIFtJAtpIFtJAtpIFtJAtpIFtJAtpIFtJAtpINq2sJMoFtJEC2kiBbSRAtpIgW0kQLaSIFtJEC2kiBbSRAtpIgttJEEtpIgCGrIgW0kgtpJYKYaEg821JLBbasiBbSRAtpIgW1JEFtqyIFtJEEtqSIFtJEC2kiBbSRAtpIgW0kQLaSIFtJEC2kiBbSRAtpIg2zDWEmcEtpIgttJEC2kiBbSRAtqyIFtSRAtqyIFtSRAtpIgUJIgUKyIFtSRBr42AXQ3NaA4mQkTKYnnn6JqOVVS4ypwjkVTRh7Lcb8QYcEQYIiPFyHMNFw5ZZngnqC5XvyFvbt3HdTpcY252HVvMOCwpqYGwpGG+bnF7JU1PYZADyXdQ51sbM4bdxpfkwvKW/q3nbtrok5YFCkiCiGrIgW1JEC2kiCW0kQW2rIgUJIgghqSILbSRAtpIgW0kQLaSIFtJEC2kiBbSRBLaSILbSRAtpIg2yxYSZwS2rIgtCSIJbUksFtpJIFCSIFCSIFCSIIGJIgttWRBLaSIPLpAgEgF05DnlmVMqCo1VvPVtJJBLasgrGyZj+CT/yRzEpDgx9c559AOnIuS0c5D0LJzF7Tm7Ohd9jmlzdc3Om09/j6CZl1Bb24r70qcj+anvQh0XNAzOmXxyWcmtGltqyIFtSSQAxWSwW2pIgGGkkgltWRB5hycA5pBB0IzBUR0lVqosKehDSSQKEkQKEkQKEkQLaSIFtJLAoSSQLasiC20kQS2pIgUJJYNq2sJM4I5gHtyHpSRBbasiBbUkQLasiAYaSIFtSSwLaSIFtWSQLaSXJFtJJkmviWAOhE5Cp8ydOI7VRVvQya25fek4m0NpYoRIogCCYbQ2kxA6sEw6s5H259GS8m28Kts9TIXVO2PQ9OycHJWp5S6zu4N4iMa7U0tqlzkTy1yXqo6TzFZCwIgAZjgagTgTKQdLi4jWQlzSmtFbnIddmTkr2mjsmGLkcTiOkM7jXAfbYjQkAH2Lc1bzmelye9CGbbTQIQLi9rRGgVmG5zXBhiNDpSz0msKz0axXKtyEZDVl2BxsZi8IWR7WJxhiUmyDGjyqpGvt51yfFU1uRy7TalWldhf1bj6e3LLPLLnXoSaIIYfQkkgtCSIObtvFPhtaIFBiGIxsog4MjPLXUgHTmXNa7UlnpLUXBDpslm46ojdZg2Hjo0Rz24gQ2nvdFrThBxkZmecsvaOha7FbUtLVcmhYNltsfEKiJpSTo7PZOFCMtWNXY1bjkqJylNgw1lJjAtqSIIIaSIFtJLBbaskgltJLAtqSILbSRAtpJIBhpIgW0kQbRYBrl0lYybMk5O3YkMb3rxDsNDOIlEiQi0uAtRHDItd95rOTlWLspbm3qbaSNReXgedg4hj7hbin4loEHhRaAWvLJvAk1vKUTLbz0gtVGKvIwOyGDUEEdGYWUmrJFtJJAoSRAtpIgW1JLBzsTtnCwnFkSPDY4AEtJnKfoWKvRNJklJy4Icrb26bDtgl0CJCjvrZ3twcQWzzyCwqVYbLb1LxT0SYPnTuyfMHe+GEjPKG/PLlzXP8TU6BMmp0V/Jr4rdY95aaMNDLZkSYdTLORd0LU61uXRCmLaqtWFacrfkObZQcJIEEzhAz405mrlq/hbzLji56X8rrvS6Ll0a+06s4PlvIw23zfd3dh0Nnbo7FQZCwpaSSGlgk0mU5SOmWnSV0UKzqTUbjGvH2vu40VrStR2Vkx2f/D6jc7te/htpvNphZhHgMhgBrwGR3TMyTlV1LobVWokqhvs7lVq3e7j5XA7rXh0WQwsQOYGiTRweHFM5h2vC/JYraXJ/xOZ73IiclfcdRsY/dW6MwsMLDMmWmpjTPIg+F0LXVtC1GKyMTU5yqkQvvuOQMY0FxAgzdrMTHKchVzkrlRFlMbjGVuxu96juP3ZuOkHCDMHJp5CD4S7vjHdE2cYupffcU7s3mXecIJGfFOeREjwun4KfGO6I4xdXv8D+2j5g2cLkCJSMs5eV0fFPjHdEZa6l99xzMZtgRnmJEhYVxkWtBhghgJLss88yuWu5azkVZSFRYTBepdaLpOmlbHU2qiMxSN+GgxYXaAhlrmwsMHtBFYhgEgtDSDn0dbjoqx2RUV6aYu0XTo65vDra5zMlWa+3w0HUwm6t0NjWCDhnymAXNcScyfC/+kuptrdgjTTluetzV/O49ndfEplvfDzDZB1D6py111WfxNSOYX/cnmr77j7OFugwZaCcTCBIBIq0PKuvLTWXiXajewOMgxpmDEZFpMjQZyOv6hVHIuBirFTFDZMNWTGBbVkQLSSWBbSSQLaSINHbRLIERwiGDTSbjQ0loqbMycCNJ8ixWdBmxEyr8DnbKjNdiGth4+JjG28S57XNgSbRFYyGZtY05tcTqo1KiLy0VO1DbVSnHIj8nftrOTng+K3Y7tt7xYcJmGbHhlrItUZ5hze15mymkzAk0z8pc1eo6mqIqHqWGyNtLVc12F2G9D5DbO7HfMK1vOFB78YtbIkzmHCniDwvgtbLZkrzdu47HcEKuD1/G88bH3X72huh70hxqorIlT4kiKXAylQcjL4o+2ZUcnDr79QbwQqYvX8bz6jczu9dFjPh7xkx5MUjDxGucyTGMya4NBzaOUarKjVWo6EQ5bbYW2emj3P6r07etT7B26LDDJxiQz5cJ4APNVKR9hXVkuTQeYjmLgplG2oHnPw3K5D9RjxlPWO7MDzn4TuxOLfqHGU9ZW7ZgeX+E/sTIfqHGU9Z+UYqZiOIJAqdUJa8L0elca4npJgeSB5XW5AY4k8pVAcuRzGXR6VAfc7htoQ4cCKHh4JxDiJQ3OyohjkHOCuik1ypKIcloe1HIiqdfH7Xgl+GIrk2MSZwomlqIObnIWTmOlLjBlRkOv0eaG53agec/Cidiz4t+ow4xnSML8YIgxjmB5a7Bhn2T5l4Ec+wCoci0VWqjoU6qD2qxVRTT2btNgixXPJpc1oZTBiT+1xDs9eR45BqtqU3zgc7qtOEv93HS7tQPOfhROxZZD9RhxrOkBtqB5z8GJ2Jxb9Q4xnSHdrD+c/BidiZD9Q4xmsd2oHnPwYnYmQ/UONZrHdqB5z8GJ2JkP1DjGdI8RtswKXZxOKf+lE5vQorH6ipUZPONfY21oAw2GDq5tw8IEWohzDBPkUax2SlxnUqMR636VPkN2uKZExQcyqVhgzhubnU/nC01UVFvOmg5HMuU4NQ5j7h7FrNp5e6YMpg8hpPYgQ7m4jENh4oOiVZQogJEN5z4PMFnSaquuNVdyI28/QO7OH53/gRvpXTkP1HFxlPWhhZugwpMg95I1FmNMfwrGHKZKrUSVUyd28MBMucANSYMUS/hVyH6iZbF0mI7o8NIll6NLkhwImfoc4Bp60RrlwQquYmKofn+1v+IIdEjsfs5hNL4DbsUFzJF4qlbMjmMgeTVcT7RCqioe1R4NymNej8YXA0tobu4cVsZo2bBhGLDYwObEBLC1znVDvQzNUuTRRlqyXI7JwM3cEqrVTL2L6mhsXdUMPEc92EZiQYbmBsR8gCS01ZsPgy9q31+EeNROTh17jVS4FVk8vYvqfo+4/dYzE4eqLCdAMNwhNDbkYRA1jeFMMEsycuhZ0FdUbKIcFtpMs9TIV3XqNPH7Ngx6b0JsWmdNXJPXT0BdtSkypzkk8uhaatCeLcqTian9msF/dofW7tWv4Sj0TozrbPqKX+zWC/u0P+LtT4Sj0RnS2fUXYbOB2XAgFxgwmwy6VRbOZA5M1sp0WU+akGiva61eEqOVYNtbDmMRwrNQKDrNhLJnplr7VMlDPKUlt40eHdERon1tlLqKl6CWroAiuHGhkc5Ya2j8nfBXKXSghNC+R8ZEiNL3SP3iZaHXm1Xkrip7zcEChQhT6Tc19k71p+Vq9CyczvPJt38idnmpuYzjwPWn+W9bH85vb5KaaXNf2f+kNkLYaTq7K+wxmU+9HMnTgRJLitH8ie9J6Vj/id70HDww4TsgOCMxy8J+uS624nA/BE94IZ1lJgVAJIAgCoPMQZH0FRcCtxMOA+yheqZ8oWFLmN7E8DZX/lf2r4nA3SDvw9W383LjtXP7j0bD/F3+hzJLmOsiFOhufjNEbn727JgLjqOQZrfZl5fccltT/b7z6QRXniw5dMRwHtk2fxkvQldCHkwmlfwQYc5kvlPW20Nq9JMz1SUyS5XtT03DMBnKpw0c8l7h7TMqo1CK9xlVMTl4vc7hIr3RIkEF7pFxDntmdJyBlNaH2Wk92UqXnfR4StVJiMY+ETDD0MR3K4LxH+pF+pY/B0ej4mzO9s+psT0B3KYLxH+pF+pPg6PR8SZ3tnT2J6HTweFhwWNhwm22NnICfKZnXpW9jGsbktS44a1apWer3rKqZisjAAICoAqQKAIUIAEIfLxdhxiTNrCJk5uBXnrZnyeu22UkRMTx3Aj8lI9D5jqOinw1QvxtL2gGw8SOSG79+ntT4aoPjaPX+DrbHYYLHNitcwl5IMqmyk0TqbMDTlkuqg1WNhxxWl6VHZTdRkxeMhl8CmJDcLpmREb4Dh7dZ+xV7kymxr8lMaTHZL5TR5objY7CQA9pJIAAe2ZJ0Gq2K9qJKqam03OXJRMTr7OjwRCxUnQ3SgkVOe0iI6l85Zzp5BLUCfKvOqqrnIq6dh69HJaxUbo2nJLoQ4THtofMtm8Fwkc2O6QT7QQeVdtJ6XouKHnV6aoqObzV2dRN8M8NnvBbZTWc8LqG+Ifhs94JKaxkrqLvhnhs94JKaxkrqJeZ4bPeCSghdRbrfDb7wSUGSp4jR2hrjU3JriBUM8lHKkKVrVykMOBxcMQoIc9gNpkgHtJPB5Of2LCm5MhvYhsrtdxr4TSvicza2DixoodDYS2gCb+9iczyOkeXmWitSc98tQ6rNWZSZDlvntNPuHiTyMHQ17Ses9i1fDVDo+No69gO5+NytDvS9pHVonw1QfG0tew6GxdmxYUSpzQG0EZOBzJHIFuoUXsdKnNarTTqMyWrpO4uw88KFIgCAIAhCoCFAEAQFQoQgQoQBUgQEUKJoBNAegUIcB2JawQ2mZc8SaANZCZz0GQOq8OvWZSlzvd+8+jo03PREaYTtHyPv2+MONOXNouTOFKcFwnRqnWdHwj9aA7R45tzoIaeFqSGnLLygmcKcoiIt/Z19fUX4V996XEftAgxBbHAY154ZkQatOD5J61inCNNURclb1jR1dfWVbI6+/AyQ8cJhrmlpcKgQQ4ATAz0OpHIt1G2U6qxELMefka6lnexJDNoQzlJwyccxyNBJ+UrY20UnLCLsUwWjURJVDwdpaFsPIxDD4bqSHAuB0B8Erndb6aKqIirdPh6m5LK+Jkh2keEbY4ERsMyfq51InxdOGOoqJwhTuSFvSdGievqC2V+tCxdoUiITDnbbUZO1Ep5ZKt4QpuVqQvK7PULZXpN6XHrfwqLTDMw0OMi05EkdHMjeEKKoi33rAWyVE1G1gorXugvZmHOcQZEEi2/kOa9Wyqi1EVOs8y2oqUlnq8TsL0zxiTUKVCQRAVAEKEBFSFUKAqQIAoUhwx8a7qh/SvEzhW6j6BeDKHX+dw3q7xr+qH9KucavUTNlHr/O4hgPGj6jzPAAPtaMvisqfCL55SJBjU4Lp5PIVUXrvPLIgJkZtdytdrLn6R0jJenSrMqpLVPIrUH0XQ9PQyLaaSICoRQUKhAoUFCFCoKgPk8X9phf3v5b18twpzV7/APJp9XYfTwUwu4v+a/3F5SY/9PI79Hf5kfpiPWw/khI3Gn2L4uC4O7fJD1H42J9Qz/dWLObT/sv/AJK7F3Z6nuXfIY83/XDXVYv5E/sv+LjTaeYvZ5oa2HOf/jjH2SiD9QttmYqVFnQl/wCDCq5MhOtU8TIzRn7VF+eKuJcV/qng06EwTtXxUsQcGL+0QvmhI3nN/qvg4LgvanihMXxMV6v+gpS51Lt8w/B3Z5GSIO+v9QPmetbf407fJDJed3G9sE8DC+35Ii+rsGKd/mfPcI8x3d5HfXrniBAVCEQoQFQBAQqkPAeXZMFRnImcmNPMTz9A+Gq5a9rZSuxXUdtnsVStfgmtfLWZW4d3K/0yYAPzXn5xq6kPSzXR1rs9AcO7w/4QmcaupPfeXNdHWv53De7vD/gCmcaupBmqjrX8p6HupcB6IqUKKlSHiK0OEnCfNyEHnBGiya5zVykW8j2NemS5JQwmpus4g5wOGPSBr7OperQ4QRbqn5PGtHBipfS/Hoe2uBAIIIOhC9JFRUlDyVRWrC4lSAEBZIAgCECok+UxfHwvoP8ALcvleFOb+f8AJp9ZYfTwUw/d/wA0f5q8rT/08jv0d/mSIMsR61nyQkbjT7F8XBcHdvkh7xAzxPqG/lFWLMKf9l/8lXF3Z6mRv20L1Y+di6rF/In9l/xU02nmL2eaGrgzxz/28f5nLro/y1e80VOYzuMkPis/aov8yKvLXFf6p4NOxME7V8VEU8F/7RB+eEq3nN/qvg4LgvankTGcTFer/oSnzqfb5h2DuzyM0Qd8f6ofM5YJ/Gn9vJDJecvZ6m5sPiYb0u+SIvqrBi3v8z57hHmO7vI+gXrniBARCBChAFSHiJFDZTzJ0aM3H0D9VrqVGsTKctxspUn1XZLElSCGXcfgjwGnUeUf0HWV5Fe3udcy5Nu49yzcGsZyql67N5sNIGQEgNAMgPYvPPRLUqUVoCVIQw1KAtSFFSAVKyAXoDE9mc2mh3OMwf8AE3l/PpW+haH0luW7Uc1ezU6ycpL9ekMjyMniknIH7rj0Hn6D8V7NC1sq3YLqPCtFhqUb8U1p5mYLpOQqAiAqENbHB5aKKp1CdBANMjznnktVXKyeTib6GRl/7mBzYmBqoJgxJsnTJwEspeFnkV51SxrUue2T1WW2mzmujuX0PI2YJStRONXx/vTnPjc61Ztb0NEd35M85J09m4HZg4XeonCILuHqQAPC8kdSJwa27kYde/rGck6ezcU7NBqnCicJoa7h6tE/K6T1onBrUjkYX47+oZyTp7NxW7Pk4OtRJgSBLp5TnpV0BZM4PyFlrPf5I7hBrkhX7Nx4h7LDZygxM2uaQXzFLjM6u6VkliVFVUbiRbcxURFdh2+g7ljIWouTi8cP7xJJPG53HrWvNjeh1e7+ozzknT2bh3LGYtRM3Bx4f3gQQeN5I6kza3odXu/rGck6ezcV2ywagYcQ1iTuHqJS8LmRODWpEMw695M5J09m4p2dmTbiTIkeHyZ+V0lTNjYjI27zLOSY5ezcem4Z7GBsOHEaWA2yCJgyI1J6TquplCqzmpBzvtFGpc9Z/J2l6Z44UAVIJKKUjnAAkmQGZJyAHSmAxwNcxXO4vBHhuGf7rf1PUV59fhBreSy9dh6dm4Nc/lVLk1adxkhMDdNTq45ud6T+i8l9Rz1lyntU6bKbclqQhkqWs2HmpUha0KK0IKlAYakAqQCpCipCEqQCpUBxBEjmDkQdCEB4a4t4vCb4JOYHkn9D8F30Le9lz702nm2jg5lS+ncuzcbEKM12hzGoOTh6QvXp1W1ElqyeJVovpOyXpB7Ww1hQEQp6QBARAJoAgLJARAEIUICFAJqlE1AEBUBgiYgAybwnDUA5D/EeT0a9C561qZSxvXUdVnsdStelyazERMgvNZBmORrT0D9SvGr2qpVxuTUe7Z7JTo4Xrr94GSpcx1AuQCpUhKlAKkAqQCpAYakKKkAqQgqQoqQCtCCpCipCEdIy1BGhBkR6Cs2VHMXKasKYvptqJkuSUPTMU8GTqSPDz+IH5j4LtfwrUYyUp5S9Sx5KeW/glqu5LoTsk3RBeQCDDIImCCSCF5y/6oaly0l/bcMz/fs3lsRPI63difNLfpL+24Zn+/ZvLYieR1u7E+aW/SX9twzP9+zeLETyOt3YnzS36S/tuGZ/v2bxYieR1u7E+aW/SX9twzP9+zeLMTyOt3YnzS36S/tuGZ/v2bxZieR1nsT5pb9Jf23DM69PZvJZieR1u7E+aW/SX9twzP8Afs3izE831u7E+aW/SX9twzP9+zeLETzfW7sT5pb9Jf23EzP9+zeDBieb63difNLfpL+24Zn+/ZvJZieb953YnzS36S/tuLmf79m8WIvm/ed2J80s+kv7bhmf79m8tiL5v3ndivzQz6S/lPQZo+/ZvMcZzmCbzDA5OE4knmApmVspf6k412Syiqr2p6EXghU/57N5qOjPfr3seC103EdLuT0DrXZV4Re5IakbTbR4MpsWXrPgGkDIZAaAaBefpPTgVIC1oBWgJUgFSAVIC1IBUgMFSoFSAVIBUgFSAVKAVoBWhBUhRWqBCiubxHFk+QSInzyOU+lc9azUqt72yv48AZN+RfGu92F9K05vs/R2r6llRvuL453uwvpVzfZ+jtX1JKjfcXxzvdhfSmb7P0dq+olRvuL453uwvpTN9n6O1fUSo35F8a73YX0pm+z9HavqJUb7i+Nd7sL6UzfZ+jtX1EqN9xfHO92F9KZvs/R2r6iVG+4vjne7C+lM32fo7V9RKjfkXxrvdhfSmb7P0dq+olRvyL40+7C+lM32fo7V9RKl35F8afdh/Smb7P0dq+pZUb8i+Nd7sL6VM32bo7V9RKk35F8a73YX0K5vs/R2r6iVMRfnMkucdXOzP/odAyXTTptptyWJCELWswSpUFrQCtQCpUCpQCpUCpAKkAqQGvWoQVoBWhRWhC1oBWgJWhS1oBWhBUhRUgFSAlaELWgFaAVoBWgFaAlSAVIBUgLWgFaFFSAVIBWgFaEJWgLWhRWhCVoBWgFaAVoBWgMNSFFSAVIBUgFSAVIBUgFSoFSgFaAVoC1oCVoBUgFSAVIBUgFaAVoBWgFSAVIBUgFSAVoBUgFSAVIBUgFSAVIBUgFSoFSAVIDBWoBWgFaAVoBWgFaAVoBWgFaAVoBWqBWgFSgFSAVIBWgFSAVIBUgFSAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAwVKgVIBUgFSAVIBUgFSAVIBUgLUgFSAVIBUoBUgFSoJUgLUgFSgFSAVKglSAVKAVIC1IBUqCVIC1KAVICVKgVIBUgFSAtSgFSAVIDBWqBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVqAVoBWqBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAwzQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQH/2Q==

## Slide 27: Dosbarthu gwasanaethau Service distribution
Services are transported across the country via a network of underground or overground pipes and cables that carry gas, electricity, water and telecommunications to both homes and businesses.
Pylons carry high voltage electricity (often exceeding 765,000 volts) from power stations to local substations before been stepped down to 240 volts for use in domestic properties.
Electricity and phone cables usually cross the country on overground poles, while water and gas are usually piped underground.
Notes: https://upload.wikimedia.org/wikipedia/commons/b/bf/Overhead_power_lines_in_Dnipro%2C_Ukraine.jpg

## Slide 28: Tyrau - Towers
Tyrau ffonau symudol - Mobile phone towers: These act as though they are large antennae, transmitting and receiving radio waves to a radio base station. From here, the call is either sent via a fibre optic cable or forwarded to another base station via a satellite link.
Notes: https://mattata30.files.wordpress.com/2012/12/gsm.png
https://image.slidesharecdn.com/cdocumentsandsettingss05299219desktop2mobilephonesstrengthweaknesses-100220003926-phpapp02/95/test-3-728.jpg?cb=1266626404

## Slide 29: Rheoli llifogydd ac amddiffynfeydd arfordirol Flood management and coastal defences
Flood management and protection of Wales’s coasts is increasingly important with the pressures of climate change and weather unpredictability.
Argaeau - Dams: Designed to regulate the flow of water and to form reservoirs for domestic and commercial use, as well as to generate hydroelectricity.
Dalgylch dros dro - Temporary catchment area: To prevent flooding caused by run-off, all new developments must have included in their planning catchment areas that hold back water to allow a slower release into main water courses.
The Craig Goch Dam, Elan Valley Reservoirs in Mid-Wales
Notes: https://www.elanvalley.org.uk/sites/default/files/fileman/claerwen.png

## Slide 30: Rheoli llifogydd - Flood management
Amddiffynfeydd afonydd - River defences: Rivers are regularly dredged to maintain flow. Levees, bunds and weirs assist in regulating water flow and reducing the risk of erosion and flooding.
Gorlifdiroedd - Flood plains: These are natural low-lying areas that naturally flood when rivers burst their banks after heavy rainfall. When houses are built on flood plains, they are at an increased risk of flooding should the levees break.
Notes: https://i.pinimg.com/564x/2e/47/15/2e47159ab31d89dd3859ef7443ee99e1.jpg

## Slide 31: Weirs, bunds, levees, floodgates and barriers
Cored) - Weir is a small dam designed to regulate the flow of water to help prevent erosion.
Bwnd - Bund is a wall built of stone or soil formed into an embankment that holds back water.
Llifglawdd - Levee is like a bund but is normally formed naturally by the river.
Llifddorau - Floodgates are designed to control water levels in flood barriers, reservoirs, rivers and levee systems.
A temporary flood barrier in Ironbridge
The weir on the Afon Twrch
Notes: https://i.pinimg.com/originals/bb/81/99/bb8199587af52ada4f5b6adcdbc06361.jpg
https://www.southwalesargus.co.uk/resources/images/11077271.jpg?display=1&htype=0&type=responsive-gallery

## Slide 32: Amddiffynfeydd arfordirol - Coastal defences
To prevent land being eroded by the sea a number of techniques have been adopted dependent on the location.
In seaside towns and areas that are prone to the full force of storm surges, sea walls often form part of the promenade and protect the land from erosion.
Storm Ciara, Porthcawl in South Wales

## Slide 33: Coastal defences
Grwynau - Groynes are low walls or barriers built out into the sea to help stop erosion and prevent beaches from drifting or washing away.
Caergewyll - Gabions are a versatile form of erosion protection. They are cages filled with bricks or stones and placed in areas prone to erosion, as the contents allow water to flow through them and so they prevent erosion by decreasing the velocity of the water.
Waliau cynnal - Revetments are sloping structures made from timber, rocks, concrete blocks or paving that are built along shorelines, cliffs and sea walls to absorb the energy from waves, preventing erosion.
Notes: https://lh3.googleusercontent.com/proxy/JtkevScYsHV3yKFFBB1nCCrnhgfZLQA9VbWbanxY9DTovUv5LOUW1g7wBEpnKhQ66ehs9EtEUAss7aTWQfuyHLmccWu52DOX_VtJKmRZ4c1QDmV3PFZsZlDAs4SqVbcVMJntcgCPbvmCdWPNX7yfwP1wNWQ
https://ichef.bbci.co.uk/images/ic/320xn/p033wrp3.jpg

## Slide 34: Strwythurau camlesi a dyfrffyrdd Canal and waterway structures
With the construction of canals, goods and building materials could be cheaply transported across the border and so coal from South Wales powered the industrial cities of England.
On canals, locks are used to raise and lower boats between stretches of water at different levels, allowing a barge to travel over obstacles.
Notes: https://lh3.googleusercontent.com/proxy/JtkevScYsHV3yKFFBB1nCCrnhgfZLQA9VbWbanxY9DTovUv5LOUW1g7wBEpnKhQ66ehs9EtEUAss7aTWQfuyHLmccWu52DOX_VtJKmRZ4c1QDmV3PFZsZlDAs4SqVbcVMJntcgCPbvmCdWPNX7yfwP1wNWQ
https://i.pinimg.com/originals/c0/7a/40/c07a409ccb70923f126bcfa6ea9e9fc4.jpg

## Slide 35: Quays, docks and piers
Ceiau - Quays are stone or metal platforms that are built alongside or project over the water, allowing ships to dock while loading and unloading cargo.
Dociau - Docks are man-made, enclosed structures normally surrounded by warehouses where ships dock to load and unload cargo.
Dociau sych - Dry docks are man-made structures where a ship sails into a dock that is then drained so that work on the ship can be undertaken. The dock is re-flooded so the ship can sail out again.
Pierau - Piers are raised structures that usually extend from the shore into the sea. These were traditionally used for boarding boats at sea but most are now used for recreational purposes.
Notes: https://encrypted-tbn0.gstatic.com/images?q=tbn%3AANd9GcSE-5DyddP1rhY5kcXm98UqZv_oZjidCl5THw&usqp=CAU
https://lh3.googleusercontent.com/proxy/D4O7-WMxrWMXVPXRDUTyiVmS7SnoOctKrNy2dbljVZPZUE7TVU5ZnBCOZMB3ItdjkkFfEx1fOYOrb9NR3nlTCIc2v0pfjuEekrKuU9d3rSJL_91kbYqp-8MTAghMAl2eRDgvesT9f86ZU2q2
http://www.simplonpc.co.uk/Piers-Wales/Tenby-01_b.jpg

## Slide 36: Ynni adnewyddadwy - Renewable energy
With the rise of global warming and the depletion of fossil fuels, the production of energy from renewable sources is becoming more and more important. The following are the most common ways of producing energy which feeds into the National Grid:
Ffermydd gwynt - Wind farms produce clean electricity from wind turbines.
Symudiad y llanw - Tidal movement is being harvested to produce electricity.
Ffermydd solar - Solar farms produce electricity from sunlight.
Boeleri biomas diwydiannol - Industrial biomass boilers using wood pellets or timber are being used to replace fossil fuels to produce sustainable electricity.

## Slide 37: Ynni adnewyddadwy parhad - Renewable energy continued
Renewable energy generation is a major design feature in new buildings. Buildings can be heated and generate electricity from renewable sources. These technologies include:
System wresogi dŵr solar - Solar water heating which directly absorbs the heat of the sun and circulates it through a heat exchanger into the hot water storage tank of the building.
Boeleri biomas domestig - Domestic biomass boilers, fueled with wood pellets or timber that can be used to heat a building and hot water.
Pympiau gwresogi o ffynhonnell aer - Air source heat pumps transfer heat from the air outside a building using a refrigerant system.

## Slide 38: Ynni adnewyddadwy parhad - Renewable energy continued
Pympiau gwres o’r ddaear - Ground source heat pumps use a ground heat exchange loop placed underground. Water is naturally heated underground and is pumped back to the surface where it is used to run heating systems and produce hot water.
Celloedd ffotofoltaidd - Photovoltaic cells can be positioned on a roof or on the ground and supply electricity to a building. Any excess electricity is then fed into the National Grid.

## Slide 39: Pwmp gwresogi o ffynhonnell aer - Air source heat pump
Notes: https://www.staticwhich.co.uk/media/images/trusted-trader/desktop-main/air-source-heat-pumps-465255.jpg

## Slide 40: Pwmp gwres o’r ddaear - Ground source heat pump

## Slide 41
Any questions?
Unrhyw gwestiynau?