## Slide 1: PowerPoint 12: Power tools - Offer pŵer
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Working with power: electrical safety
Electricity is a very dangerous form of energy:
  it is invisible - mae’n gudd
  it can start fires - mae’n gallu dechrau tanau
  it can kill - mae’n gallu lladd.
  In the construction industry, electrocution causes a significant number of serious injuries and deaths each year. It is a serious hazard.
Notes: Title
Working with power: electrical safety
Electricity is a very dangerous form of energy:
  it is invisible;
  it can start fires;
  it can kill.
    In the construction industry about 7 people are killed each year by electrocution.
    Many more are seriously injured.

## Slide 3: Working with power tools - Gweithio gydag offer pŵer
Some tips for safe use of power tools:
  Follow - dilynwch the safety procedures and never tamper with live electrical cables or machinery.
  Make sure any items of electrical equipment, including power tools, are in good condition and safe to work with.
  Do not plug in the power tool before trying it.
  If you plug in the power tool and there is a fault, you could be seriously injured or killed.
  Minor shocks can trigger a secondary accident, such as a fall from height - syrthio o fan uchel.
Notes: Title
Working with power tools
Some tips for safe use of power tools:
  Never tamper with live electrical cables or machinery.
  Make sure any electrical equipment including power tools are in good condition and safe to work with.
  Follow the safety procedures.
  Do not plug in the power tool before checking it out.
  If you plug in the power tool and there is a fault, you could be seriously injured or killed.
  Minor shocks can trigger a secondary accident such as a fall from height.

## Slide 4: Working with power tools
Before use always check the body of the power tool:
    is it clean?
    is it dry - sych?
    Portable Appliance Testing (PAT) label
    no visible cracks
    no loose or missing parts - darnau.
Notes: Title
Working with power tools
Before use always:
Check the body of the power tool:
      is it clean?
      is it dry?
      Portable Appliance Testing (PAT) label;
      no visible cracks;
      no loose or missing parts.

## Slide 5: Working with power tools
Before use always check the cable of the power tool for:
    bare wires - wifrau noeth
    frayed ends
    cuts or burns
    other obvious damage - difrod amlwg arall.
Notes: Title
Working with power tools
Before use always:
Check the cable of the power tool for:
      bare wires;
      frayed ends;
      cuts or burns;
      other obvious damage.

## Slide 6: Working with power tools
Before use always check the voltage label of the power tool:
    is it 110 volts?
    does it have a 110-volt yellow plug?
Check the plug of the power tool for:
    cracks
    loose or misshapen - ddi-siâp pins.
Notes: Title
Working with power tools
Before use always:
Check the voltage label of the power tool:
      is it 110 volts?
      does it have a 110 volt yellow plug?
Check the plug of the power tool for:
      cracks;
      loose or misshapen pins.

## Slide 7: Working with power tools – summary
Don’t forget!
  Check the voltage – is it 110 volts? Does it have a 110-volt yellow plug?
  Are the tool, cable and plug all in good condition - cyflwr da?
  Know how to isolate power in an emergency.
  Although there is no set order for checking portable power tools, it is good practice to plan your own procedure.
  Get into the habit of checking every power tool before you use it - cyn eu defnyddio.
  Your life may depend on it!
Notes: Title
Working with power tools – summary
Don’t forget!
  Check the voltage - is it 110 volts, does it have a 110 volt yellow plug?
  Is the tool, cable and plug in good condition?
  Know how to isolate power in an emergency.
  Although there is no set order for checking portable power tools, it is good practice to plan your own procedure.
  Get into the habit of checking every power tool before you use it.
  Your life may depend on it!

## Slide 8: Drill driver - Dril pŵer
The drill driver is highly versatile and can be used with different bits.
They insert and remove screws, cut circular holes with a saw cutter, or buff and polish - sglein a pholish.
Various designs of chuck are available for rapid interchange of bits.

## Slide 9: Percussion drills - Driliau taro
This drill has a percussive hammer effect which enables it to bore into hard materials, such as bricks, blocks, stone and concrete - cerrig a choncrid.
This percussive action is optional and is brought into operation by means of a switch.
It can also drill free from percussion and be used to drill holes into materials such as timber, plastic or steel - plastig neu ddur.

## Slide 10: SDS hammer drill - Dril morthwyl SDS
This drill has a hammer effect which is used to bore holes into hard masonry products such as bricks, blocks, stone and concrete.
The rotation action is operated by a switch and is easy to discard.
The still hammer action may be used when chasing walls - gerfio waliau.
This drill also has a unique chuck which requires the drill bits to have a certain style of insert end.

## Slide 11
Nail guns come in two forms: gas and battery. The gas nail gun also depends on battery power.
They are used to drive nails into the surface, saving on time, labour, damage and vibration.
The nails come in strips and are inserted into the bottom of the guns and are fed up through the gun as each nail is fired.
Nail gun - Gwn hoelion

## Slide 12
Unrhyw gwestiynau?
Any questions?

## Slide 13: PowerPoint 13: Plant and machinery - Peiriannau a pheirianwaith
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 14
The transformation by construction of a design into a useful structure is accomplished by people using technology and machines (plant).
As machines evolve and technological capabilities improve, the way in which projects are constructed also changes.
But working near moving plant and machinery can be a high-risk activity. It is essential to ensure the safety of people working at or near locations where plant is used.
Use of plant and machinery - Defnyddio peiriannau a pheirianwaith

## Slide 15: Machine utilisation
Selecting the right machine is important because, unlike most other classes of machine, even a slight increase or decrease in physical size can greatly affect application.
There are three key considerations:
transport - cludiant
productivity - cynhyrchiant
site constraints - cyfyngiadau o ran y safle.

## Slide 16: Plant - Peiriant
Plant is a machine that is either tracked or wheeled and used for clearing land, pushing soil, excavating or loading into trucks.
It is generally something that can be ridden upon and driven, whereas equipment generally refers to hand-held tools or similar.

## Slide 17: Equipment - Cyfarpar
Earth-moving equipment - Cyfarpar symud pridd
Hauling equipment
Hoisting equipment - Cyfarpar codi
Conveying equipment
Aggregate and concrete production equipment
Pile-driving equipment

## Slide 18: Machinery use - Defnyddio peiriannau
Excavation - Cloddio
Digging and moving large quantities of earth
Placement
Compacting
Levelling - Lefelu
Dozing
Grading - Graddoli
Hauling operations involved in construction

## Slide 19: Trenching machine or excavator
Used for excavating trenches for laying pipelines, sewer, cables etc.
Operation is quick, giving the required depth or width – dyfnder neu'r lled
Two types of trenching machine: wheel type, ladder type.

## Slide 20: Scrapers - Crafwr
Unique machine for digging and long-distance hauling of plough-able materials.
Self-operating machine
It is not dependent on other equipment.
Wheels of machine cause some compaction.
The basic parts of scrapers are the bowl, apron and tail gate or ejector - alldaflwr.

## Slide 21: Bulldozer - Chwalwr
The heavy blade attached to the tractor pushes the material from one place to another.
The tractor can be of the crawler or the wheeled type.

## Slide 22: Dump trucks - Tryciau dadlwytho
These are used for earth moving - symud pridd.
The selection of the type of dump trucks for a specific job depends on the soil condition.
These are heavy duty trucks, with a strongly built body which is hinged on the truck chassis at the rear end and one side respectively, and can be fitted to the rear in the case of rear dump and to the hinged side in case of the side dump, through the action of hydraulic jacks.
These trucks are suitable for use in hauling wet clay, sand, gravel, quarry rocks etc.

## Slide 23: Hoisting equipment - Cyfarpar codi
Hoisting is the lifting of a weight from one location and moving it to another location which is at a reasonable distance. Big projects such as construction of dams, industrial buildings etc. require hoisting equipment.
Hoisting equipment includes jacks, winches, chain hoists and cranes. A crane is the only machine which, as a single piece, is capable of providing three-dimensional movement of a weight.
Cranes are broadly classified as:
1. Stationary or derrick cranes 2. Mobile cranes - Craeniau symudol 3. Overhead or gantry cranes 4. Traveller cranes 5. Tower cranes

## Slide 24: Mobile cranes - Craeniau symudol
These cranes are mounted on mobile units which are either crawler type or wheel type.
Truck cranes have high mobility while the crawler-mounted cranes move slowly.
Crawler-mounted cranes are capable of moving on rough terrain - tir garw.
These types of cranes consist of two main parts: the bridge and the crab.

## Slide 25: Tower cranes - Craeniau tŵr
A tower crane consists of a derrick crane mounted on a steel tower.
Tower cranes are usually used for industrial and residential high-rise buildings. They are commonly used for assembly of industrial plants with steel structures.
The main parts of tower crane are under carriage, slewing platform, tower with operator’s cabin and jibs.
The tower has a truss structure welded from steel bars and channels.

## Slide 26: Belt conveyor - Belt cludo
Used when large quantities of materials have to be conveyed over long distances at fast speed.
It consists of a belt running over a pair of end drums or pulleys and supported at regular intervals by a series of rollers called idlers. These idlers are supported on a conveyor frame.
The middle sag provided in the belt prevent the spilling of material. Generally, rubber is most commonly used as conveyor belt.
The belt can be used to transfer loose aggregate and material up a height or around the site.

## Slide 27: Hazards - Peryglon
Plant and machinery can be particularly hazardous when operated in situations where:
people or other vehicles share the same site. Pedestrians are particularly vulnerable in areas where mobile plant and machinery is operated as the operator’s vision may be restricted
entry to the site is uncontrolled
work is being carried out in the vicinity of electrical equipment or in hazardous atmospheres
the plant/machinery is damaged, poorly maintained, used on unstable base or used incorrectly
the load exceeds the capacity of the plant.

## Slide 28: Risk control measures - Mesurau rheoli risg
These include the following:
isolate vehicles and plant used in or around the site and work area from the people on site
provide separate routes or pavements for pedestrians to keep them away from plant and machinery (e.g. footbridges, crossing points)
use fences, barriers and safety signs to secure the area
plan the direction that plant moves, so the visibility of operators is not restricted
use spotters to control traffic movement
implement safe working distances
use audible reversing alarms – larymau
ensure notices are in place at all entrances and exits
use designated delivery and turning areas.
make sure all visitors report to the site office.

## Slide 29
Unrhyw gwestiynau?
Any questions?

## Slide 30: PowerPoint 14: Areas of specific risk - Meysydd risg penodol
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 31: Session overview
In this session you will learn about dangers associated with the construction industry - diwydiant adeiladu.
You will find out about safe methods of identification, protection, commissioning and decommissioning of services.
Failure to follow guidelines when working on site can lead to accidents and even fatalities.

## Slide 32: Confined spaces - Lleoedd cyfyng
A confined space:
is large enough that an employee can enter physically and carry out a task
has limited or restricted means for entry or exit.
is not designed for continual occupancy.
This could be a tank, vessel, chamber, pit, silo, vault or hopper.

## Slide 33: Confined spaces
A safe system of work is needed for a confined space operation, requiring:
planning the work - cynllunio’r gwaith
safe access
use of cable- and pipe-locating devices
safe digging practices - arferion cloddio diogel
safe egress.

## Slide 34: Confined spaces
Some confined spaces require a permit to carry out any work within them. If they do, they usually contain a potential to cause harm such as:
hazardous chemicals - cemegion peryglus
electrical transformers
plant room.

## Slide 35: Establish command - Pennu pwy sy’n rheoli
Any team member can be command:
  usually highest trained
  can be passed as more people arrive
  need to know the ICS
  trained in CSR.

## Slide 36: Responsibilities while working in an area of danger
Make initial assessment and evaluation.
Establish goals and objectives - Pennu nodau ac amcanion.
Determine additional resources.
Establish a command post.

## Slide 37: Key checks prior to entering a confined space
Once information indicates that PPE on hand is adequate:
  obtain air monitoring samples
  assess hazards
  characteristics of space - nodweddion y lle.

## Slide 38: Safety precautions
Perimeter control - Rheoli perimedr:
  may need police
  barrier tape, ropes, barricades.

## Slide 39: Hazards present
Atmospheric
Energy sources - Ffynonellau ynni
Entrapment
Fall
Fire/explosion - Tân/ffrwydrad
Hazardous material

## Slide 40: Industries engaged in excavation
Water, sewer, pipeline contractors
Communication and power line contractors
Concrete worker and drilling contractors

## Slide 41: Hazards of excavation work - Peryglon gwaith cloddio
Cave-ins - Waliau’n syrthio i mewn
Underground utilities
Materials/equipment falling into excavation sites
Struck-by accidents
Asphyxiation - Mygu
Explosions
Falls
Electrocutions - Cael eu trydanu
Drowning - Boddi

## Slide 42: Safety considerations - Ystyriaethau o ran diogelwch
Excavation is one of the most hazardous types of work in the construction industry.
Accidents result from inadequate planning.
Build safety into pre-bid planning.

## Slide 43: Safety considerations
Plan safety into the job. Consider:
  traffic - traffig
  proximity of structures and their conditions
  soil - pridd
  surface and ground water
  water table
  overhead/underground utilities
  weather - tywydd.

## Slide 44: Locating utilities - Lleoli cyfleustodau
Employers must determine the estimated locations of utility installations.
Contact utility companies before starting excavation.
Utility owners must attempt to find exact location of utilities.
Proceed with caution if the exact location of utilities cannot be found.
Use safe and acceptable means to locate exact locations of installations.

## Slide 45: Safety starts at the surface - Mae diogelwch yn dechrau ar yr wyneb
Warn mobile equipment operators about the edge of the excavation site.
Ensure there is adequate access and egress.
Take care when walking near excavation sites.
Barricade or cover wells, pits, shafts.
Use appropriate PPE.

## Slide 46: Protecting utilities - Diogelu cyfleustodau
Exact locations of utilities must be determined.
Utilities must be exposed before digging - cloddio.
Excavation sites must be protected and supported to safeguard employees.
Approach utility lines with care.

## Slide 47: Employee access/egress from excavations
Ramps must be designed by a competent person.
Ramps must be structurally sound and not create a tripping hazard.
Use surface treatments on ramps to prevent slipping.

## Slide 48: Employee access/egress from excavations
Trenches that are more than 1.2 m or 4 feet deep need a safe means of egress:
  stairway - grisiau
  ladder
  ramps - rampiau.
Means of egress must be fixed and secure.

## Slide 49: Employee access/egress from excavations
Means of egress must be within 7m of workers.
Ladders must extend a minimum of 90cm above the landing.
Use metal ladders with caution around utilities.

## Slide 50: Hazardous atmospheres
Explosive - Ffrwydrol
Flammable - Fflamadwy
Poisonous - Gwenwynig
Corrosive - Cyrydol

## Slide 51: Loose rock and soil as hazards - Cerrig a phridd rhydd yn beryglon
Prevent loose rock/soil/ spoil from falling onto employees in excavation sites.
Use barricades to contain material.
Keep surface materials at least 1 m from the edge of excavation sites.
Keep employees off sloped surfaces at levels above other employees.

## Slide 52: Support, shield, and protective systems
Shoring systems support the sides of the excavation with:
  timber - pren
  aluminium - alwminiwm
  hydraulic, pneumatic, or mechanical systems.

## Slide 53: Daily inspections - Archwiliadau dyddiol
Inspect excavations for possible:
  cave-ins
  failure of protective systems
  hazardous atmospheres - amgylchedd peryglus
  other hazardous conditions.

## Slide 54: Dangers while working around electricity
Electricity injuries are usually caused by the explosive effects of arcing current, and by any associated fire or flames which may result, when a live cable is penetrated by a sharp object such as the point of a tool.
Such effects can also occur when a cable is crushed severely enough to cause internal contact between the conductors or between metallic sheathing and one or more conductors - dargludyddion.
Injuries are typically severe, potentially fatal, burns to the hands, face and body and electric shock is less likely.

## Slide 55: Dangers while working around electricity
Incidents may also arise from cables which have been damaged but left unreported and unrepaired.
Other nearby services, such as plastic gas pipes, may also be at risk from damaged live electricity cables.
This could result in explosions and a greater fire risk - risg o dân.
Great care is needed when working in and around electricity – trydan.

## Slide 56: Gas pipes - Pibellau nwy
Damage to gas pipes can cause leaks which may lead to fire or explosion
There are two types of damage:
that which causes an immediate leak
that which causes a leak some time later.
The damage may occur at the time the work is carried out or subsequently: for example, poor reinstatement may leave a pipe inadequately supported or subject to unequal forces.

## Slide 57: Water pipes and sewers - Pibellau dŵr a charthffosydd
Although damage to water pipes is less likely to result in injury, the following may occur:
A jet of water from a main can injure a person. It may also contain stones or other hard objects ejected from the ground around the pipe.
Leaks of water from underground pipes can affect adjacent services and reduce support for other structures, for example: damage to mains can result in flooding, leading to subsequent risks from drowning or the rapid collapse of support to the sides of an excavation; water can enter gas pipes if they are also damaged.
While some sewage is pumped at pressure, sewers are generally gravity-fed, and the main hazard from damage to a sewer is the possibility of contamination.

## Slide 58
Unrhyw gwestiynau?
Any questions?

## Slide 59: PowerPoint 15: Waste and pollution - Gwastraff a llygredd
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 60: People problems
Within the construction industry, as well as in the wider working environment, most waste problems arise from people not segregating their rubbish - sbwriel.
This happens despite numerous environmental awareness campaigns.

## Slide 61: Site practices - Arferion ar y safle
On site it is good practice to monitor segregation of waste so that where possible it can be recycled – ailgylchu.
Wood, brick, concrete, glass, plastic, rubber and metals are some of the materials that can be recycled from a construction site undergoing demolition - ddymchwel.
On new builds, there is an even bigger focus on the need to recycle as work is proceeding.

## Slide 62: Benefits of recycling - Manteision ailgylchu:
Benefits of recycling:
Conserves resources for future generations.
Prevents emissions of many greenhouse gases.
Prevents water pollutants.
Saves energy.
Supplies valuable raw materials to industry.
Creates jobs.
Stimulates the development of greener technologies.
Reduces the need for new landfills and incinerators.

## Slide 63: Construction waste classifications
Unwanted materials: generated during construction processes. For example: demolished concrete fragments, brick pieces, wood, plastic wastes etc.
Reuse - Ailddefnyddio: the process of using a material again for the same or a different function. For example: using coarse aggregate, obtained from concrete waste, for preparation of fresh concrete.
Recycling - Ailgylchu: the process of converting waste materials into new ones for reduction of waste of potentially useful materials.

## Slide 64: Concrete waste - Gwastraff concrid
When structures made of concrete are demolished or renovated, concrete recycling is an increasingly common method of utilising the rubble.
Concrete was once routinely delivered to landfills for disposal, but recycling has several benefits that have made it a more attractive option now we have greater environmental awareness, more environmental laws and the motivation to reduce construction costs.
Concrete aggregate collected from demolition sites is put through a crushing machine. Crushing facilities accept only uncontaminated concrete, which must be free from impurities.

## Slide 65: Concrete waste continued
Metals such as rebar are accepted, since they can be removed with magnets and other sorting devices and melted down for recycling elsewhere.
The remaining aggregate chunks are sorted by size. Larger chunks may go through the crusher again. After crushing has taken place, other particulates are filtered out through a variety of methods including hand-picking and water flotation – arnofio.
Smaller pieces of concrete are used as gravel for new construction projects.

## Slide 66: Concrete waste continued
Construction and demolition waste consists of concrete, bricks, timber, sanitary ware, glass, steel and plastic.
One reason for the increase of construction and demolition waste is that many old buildings, concrete pavements, bridges and other structures have overcome their age and limit of use, due to structural deterioration beyond repair, and need to be demolished - dymchwel.

## Slide 67: Construction recycling problems - Problemau ailgylchu yn y diwydiant adeiladu
One of the main issues for construction and demolition waste management is the lack of appropriately located recycling facilities.
If the site does not have a recycling facility set up on the site, this could lead to illegal practices performed by contractors to save money on skips. This dumping of rubbish is also called ‘fly tipping’ - ‘tipio anghyfreithlo’.

## Slide 68: Site waste management plans - Cynlluniau rheoli gwastraff safleoedd
A key requirement of a waste management plan is to determine the types, quantities and qualities of waste that need to be removed from the site.
On-site waste sorting areas would need to be set up, such as designated skips for plasterboard or a location for decommissioned cable, pipework or ducting until they can be disposed of.

## Slide 69: Outcomes of a waste management plan
Reduced consumption of resources - Defnyddio llai o adnoddau.
Reduction of emissions and other byproducts of the process to air, water and land.
Reduction of production (of waste) and increased recycling of waste.

## Slide 70: Leaving the site in a good condition
Prior to the site being set up there should be a site investigation to determine whether there has been any initial ground contamination. If so, its extent should be established during soil investigation - ymchwiliad pridd.
If contamination is found, necessary actions should be enforced to restore a polluted site into a condition suitable for safe construction work.

## Slide 71: Waste management and pollution control
Waste should be prevented or reduced at the source by proper planning and designing whenever feasible.
Waste that cannot be prevented or reduced should be reused whenever feasible.
Waste that cannot be prevented, reduced or reused should be recycled in a safe and environment friendly manner. (Recycling means treating the material to recover a useful product.)
Waste that cannot be prevented, reduced, reused or recycled should be treated in an eco-friendly manner, and energy should be derived from it, if possible - os oes modd.

## Slide 72: Air pollution control - Rheoli llygredd aer
Control of air pollution requires limiting the emission of air pollutants into the atmosphere. Six major air pollutants are:
Carbon monoxide Ozone - Osôn
Sulphur dioxide - Sylffwr deuocsid Nitrogen dioxide
Particulate matter and Lead (automobile emissions)
There are also air emission standards for friable asbestos during activities such as disposal of asbestos or its related materials.

## Slide 73: Air pollution continued
Pollution from the use and maintenance of motor vehicles and construction equipment must be controlled. Fumes from site vehicles must be controlled where possible.
Releases from stationary sources such as boilers, furnaces and the burning of waste should be controlled.
Smoke and fumes have a serious effect on people’s health and an overall detrimental effect on the environment - amgylchedd.

## Slide 74: Construction dust - Llwch adeiladu
Construction dust poses a serious health risk and can cause lung disease if not managed correctly, as covered in The Control of Substances Hazardous to Health Regulations 2002 (COSHH). Where the dust cannot be reduced it must be controlled through:
damping down with water - rhoi dŵr dros y llwch.
on-tool extraction
wearing Respiratory Protective Equipment (RPE)
limiting people near the area and rotating employees carrying it out
enclosing the work using sheeting or screens
using general mechanical ventilation.

## Slide 75: Noise control - Rheoli sŵn
Noise can be defined as unwanted sound.
A noise problem comprises of three interrelated problems:
Source - Ffynhonnell
Receiver - Derbynnydd
Transmission path between source and receiver.
The transmission path is usually the atmosphere.

## Slide 76: Noise safety - Diogelwch gyda sŵn
The safety guidelines to noise pollution are:
Procuring equipment with inbuilt noise control: Eradicate.
Moving the noise source away from the work area: Reduce.
Building sound absorbing total enclosure surrounding the noise source: Isolate.
Using silencers whenever possible: Control.
Using personal safety gear: PPE.
This is also known as ERIC P.

## Slide 77: Land contamination - Tir wedi’i halogi
There is very little difference between pollution and contamination, especially in environmental terms.
Pollution - Llygredd is something which is not welcomed in the environment.
Contamination - Halogiad refers to a substance which has been introduced to another substance, generally causing an adverse affect.
Pollution clean-up/remediation of soils or water would involve exactly the same actions as contamination clean-up.

## Slide 78: Health effects - Effeithiau iechyd
Chronic exposure to chromium, lead and other metals, petroleum, solvents, and many pesticide and herbicide formulations can be carcinogenic.
Chronic exposure to benzene at sufficient concentrations is known to be associated with higher incidence of leukemia.
Organophosphates and carbamates can induce a chain of responses leading to neuromuscular blockage.
Mercury - Mercwri is linked to higher incidences of kidney damage.

## Slide 79: Risk assessment on land or a site
The purpose of preliminary risk assessment is to develop an initial conceptual model of the site and establish whether or not there are potentially unacceptable risks.
Information collection may include:
desk study
site reconnaissance
additional desk study and exploratory site investigation.

## Slide 80
Any questions?
Unrhyw gwestiynau