## Slide 1: PowerPoint 2: Know the planning process
PowerPoint presentation
Unit 103: Introduction to the built environment life cycle

## Slide 2: Development control officer
Development control officers are employed by organisations like Cadw. Their main responsibilities include the following:
Asesu - Assessing planning applications and evaluating the outcomes.
Ymchwilio - Investigating developments, or proposed developments, checking that they comply fully with any restrictions.
Providing professional advice to colleagues, elected members, etc.
Cynghori - Advising outside experts, i.e. National Trust, Cadw on regulations and recommendations for conservation and developments.
Working within a team preparing schemes for the conservation of historic buildings and the countryside.

## Slide 3: Building heritage conservation officer
Building conservation officers are normally employed by the local council. Their role is to help to protect and conserve a diverse range of buildings including houses, church, windmills, lighthouses and even factories. Their main duties include:
Archwilio - Inspecting and surveying buildings and writing reports on their condition.
Recommending buildings for conservation - cadwraeth.
Producing schedules of conservation work.
Sourcing suppliers of traditional materials and suitable craftspeople - chrefftwyr.
Giving advice to owners, architects, heritage groups etc. on building conservation.

## Slide 4: Swyddog rheoli adeiladau - Building control officer
Building control is the minimum standard for design, construction and alteration to a building. A building control office will visit a site at set points to ensure that all work carried out meets the relevant regulations. Typical times to conduct an inspection are: before the concrete is poured into a foundation trench, when DPC height has been reached, when the roof is going on and when construction is finished.
Only when they are satisfied that all work has been carried out correctly will they sign off the project as complete. They can be either employed by the local authority or be an independent approved inspector.

## Slide 5: Consent or approval
The main types of consent or approval are:
Caniatâd cynllunio - Planning permissions (outline, reserved matters, full, discharge/variation of conditions)
Cymeradwyaeth rheoliadau adeiladu - Building Regulations approval
Listed building consent
Conservation area consent
Scheduled monument consent
Breaching legislation and regulations can result in enforcement, prosecution or demolition.

## Slide 6: Caniatâd cynllunio - Planning permission
Before any building work commences you need to know if planning approval is required to construct or demolish a building.
Cynllunio amlinellol - Outline planning is normally the first stage, where a brief description and drawings showing the planned position, size, layout and intended use are submitted. If the local authority approve in principle, full planning permission can then be submitted. This is advisable before commissioning architects etc. to produce detailed drawings and other documents.
Cynllun llawn - Full planning requires all the necessary plans and drawings relating to the proposed development including all supporting documentation to be submitted along with a completed application form and relevant fees.
Further information on consent types can be found at Consent types - Planning Portal - Wales

## Slide 7: Planning permission (continued)
Where outline permission has been granted, you may, within three years of the outline approval, make an application for the outstanding reserved matters, i.e. the information excluded from the initial outline planning application. This will typically include information about the layout, access, scale and appearance of the development - datblygiad.

## Slide 8: Permitted development rights
You can make certain types of minor changes to your house without the need to apply for planning permission. These are called ‘permitted development rights’ and can vary from one local authority to another and are not applicable in conservation areas or national parks. Examples are small extensions, garages, outbuildings, and conversion of a garage or roof space - ofod to.

## Slide 9: Retrospective planning permissions
Any building or structure that has been built without the proper planning approval in place is known as a planning breach and may require the submission of a retrospective planning application.
If planning has already been rejected the council can issue an enforcement notice requiring the building to be demolished or returned to its original form.
Failure to comply with an enforcement notice can lead to prosecution - erlyniad with fines up to £20,000

## Slide 10: Rheoliadau adeiladu - Building regulations
All new build and any adaptions to existing buildings, including listed buildings, must meet the current building regulations. These are made up several approved documents, each covering a specific area.
The building regulations are intended to protect people’s safety, health and welfare in and around buildings. The regulations are also designed to improve the conservation of fuel and power, protect and enhance the environment and promote sustainable development.

## Slide 11: Building regulations (continued)
Approved document | Document title
Part A | Structural safety
Part B | Fire safety
Part C | Resistance to contaminant and moisture
Part D | Toxic substances
Part E | Resistance to the passage of sound
Part F | Ventilation
Part G | Sanitation, hot water safety and water efficiency
Part H | Drainage and waste disposal
Part J | Heat producing appliances
Part K | Protection from falling, collision and impact
Part L | Conservation of fuel and power
Part M | Access to and use of buildings
Part N | Glazing safety
Part P | Electrical safety
Part Q | Security
Part R | Physical infrastructure for high speed electronic communications networks
 | Workmanship and material
Approved document | Document title
Part A | Structural safety
Part B | Fire safety
Part C | Resistance to contaminant and moisture
Part D | Toxic substances
Part E | Resistance to the passage of sound
Part F | Ventilation
Part G | Sanitation, hot water safety and water efficiency
Part H | Drainage and waste disposal
Part J | Heat producing appliances
Part K | Protection from falling, collision and impact
Part L | Conservation of fuel and power
Part M | Access to and use of buildings
Part N | Glazing safety
Part P | Electrical safety
Part Q | Security
Part R | Physical infrastructure for high-speed electronic communications networks
Approved document 7 | Workmanship and material

## Slide 12: Gwarchod treftadaeth - Heritage protection
Types of heritage protection for buildings and structures include:
listed building (Grade I, II* and II)
scheduled monument
conservation area
Safle Treftadaeth y Byd - World Heritage Site
rhestrau lleol - local listing
Ecclesiastical Exemption.
A Grade II listed building: Watchtower Bay in Barry, built in the 1860s as a coastguard station.

## Slide 13: Adeiladau treftadaeth - Heritage buildings
A heritage building is any building that has a historical and cultural importance to the community. These are often listed buildings. Some examples of heritage buildings in Wales are shown below.
Yr Hen Gapel, Llwynrhydown
    Glashirfyn a 450-year-old timber framed building in Llansilin
Notes: http://www.welshchapels.org/wp-content/uploads/2019/02/Finished-300x300.jpg
Visit Home (welshchapels.wales) to find out more.

## Slide 14: Listed building grades
Gradd I - Grade I: buildings of exceptional interest, of the highest significance.
Grade II: buildings of special interest, warranting every effort to preserve them.
Grade II*: particularly important buildings of more than special interest.
Ddeddfwriaeth - Legislation covering listed buildings and conservation areas include the Listed Buildings and Conservation Areas Act 1990.
https://www.legislation.gov.uk/ukpga/1990/9/contents
Any breaches to legislation or damage caused can lead to a fine and/or a court order stipulating that all work is undone and the building returned to its original state.

## Slide 15: Listed buildings in Wales as of August 2020
Blaenau Gwent (53) Bridgend (375) Caerphilly (377) Cardiff (861)
Carmarthenshire (1,843) Ceredigion (1,890) Conwy (1,744)
Denbighshire (1,808) Flintshire (1,027) Gwynedd (4,167)
Isle of Anglesey (1,123) Merthyr Tydfil (234) Monmouthshire (2,425)
Neath Port Talbot (396) Newport (437) Pembrokeshire (2,876)
Powys (5,484) Rhondda, Cynon, Taff (370) Swansea (521)
Torfaen (259) Vale of Glamorgan (739) Wrexham (1,051)

## Slide 16: Ardal gadwraeth - Conservation area
If you live in a conservation area you will need ‘conservation area consent’ before carrying out a range of work.
Dymchwel - Demolish a building with a volume of more than 115 m3 .
Demolish a gate, fence or railing more than 1m high next to a highway or more that 2m anywhere else.
Newid - Replace windows or change the appearance of a building.
Full details can be found on the link to the planning portal below: https://www.planningportal.co.uk/wales_en/info/5/applications/58/consent_types/5

## Slide 17: Schedule monument consent
Scheduling identifies monuments which are considered to be of national importance to Wales. This means that they have importance not just locally but for the wider cultural heritage of Wales. They range in date from prehistoric caves occupied over a quarter of a million years ago to industrial and military structures built during the twentieth century. (https://cadw.gov.wales/)
It is a criminal offence - drosedd to carry out any works that would disturb a scheduled monument or the ground within a scheduled monument without first obtaining scheduled monument consent. The main purpose of scheduling is to protect and preserve scheduled monuments. These are manged by Cadw in Wales. There are over 4,000 scheduled monuments in Wales.
Link to all scheduled monuments in the UK: https://ancientmonuments.uk/map#.Xyg2si2ZNhE

## Slide 18: Safle Treftadaeth y Byd - World heritage site
Wales currently has three world heritage sites:
The castle and town walls of Edward I at Caernarfon, Conway, Beaumaris and Harlech in North West Wales.
Blaenavon Industrial Landscape in South East Wales.
Pontcysyllte Aqueduct and canal in North East Wales.
All planning enquires that might affect a world heritage site must be directed to Cadw.

## Slide 19: Local listings and Ecclesiastical Exemption
When a building does not meet the national criteria but is of special local interest - diddordeb lleol it can be given the status of a local listing.
Under Ecclesiastical Exemptions (Listed Buildings and Conservation Areas) (Wales) Order 2018, some religious denominations are not required to obtain listed building consent from the local planning authority to carry out work to their listed place of worship.
Further information can be found at: http://www.legislation.gov.uk/wsi/2018/1087/contents/made

## Slide 20
Unrhyw gwestiynau?
Any questions?

## Slide 21: PowerPoint 3: Understanding the stages of construction and the installation of services
PowerPoint presentation
Unit 103: Introduction to the built environment life cycle

## Slide 22: Strwythur adeilad - Building structure
A building is split into three distinct parts:
Is-strwythur - Substructure: Anything below ground level is classed as been part of the substructure.
Uwchstrwythur - Superstructure: Everything structural above ground level is classed as been part of the superstructure.
Cydrannau mewnol - Internal components: Everything that goes into a building that is nonstructural is classed as an internal component.

## Slide 23: Parts of the substructure: Foundations - Sylfeini
The type of foundation used will depend on the type of building and the ground conditions. The most common types are:
Brick pillar
Pad foundation
Steel column
Traditional strip foundation
Pad foundation -
Pad foundation with bolts
Sylfaen pad

## Slide 24: Parts of the substructure: Foundations (continued)
The type of foundation used will depend on the type of building and the ground conditions. The most common types are:
Hardcore
Foundation concrete
Raft foundation
A cylindrical pile foundation
Sylfaen rafft -
Sylfaen pentwr silindr

## Slide 25: Examples of a typical domestic building's substructure

## Slide 26: Parts of the superstructure
The superstructure is best described as any part of the building above ground level that bears a live load. This includes:
Waliau allanol - External walls: These are constructed using either brick, block or stone outer leave with lintels and cills forming openings, an inner leave of brick, block or timber frame is secured using brick ties, the cavity between these is filled with insulation.
Decorative finish
Floor
Inner leaf
Wall tie
Insulation
Outer leaf

## Slide 27: Bondiau brics cyffredin - Common brick bonds
Stretcher brick bond is the most common bond. It is easy to lay with little waste and is made up of stretcher set in rows, with each course been offset by half a brick.
English brick bond is made up of alternating courses of stretchers and headers.
Flemish brick bond is an alternating layer of heads and stretchers on a single course, with the next course laid with the header in the centre of the stretcher.

## Slide 28: Load-bearing internal walls
Any internal wall that supports the overall structure is known as a load-bearing wall; they normally carry the ends of the upper floor joists. They are normally constructed using block work; however, bricks and timber framed construction are also used.
Head
Sole plate -
Noggins
Studs
Head plate
Timber stud wall -
Puncheon
Wal stydiau pren
Pen
Plât unigol
Stydiau

## Slide 29: Lloriau gwaelod solet - Solid ground floors
Types of floors include: solid ground, block and beam, suspended timber ground, upper timber.
Early solid ground floors built in the 1930s to the 1950s had issues with rising damp as many did not have any damp proof membranes fitted. Modern solid floors include a damp proof membrane and a layer of insulation.
Screed
Insulation
Concrete DPM
Sand blinding
Hardcore
Concrete floor

## Slide 30: Lloriau pren crog - Suspended timber floors
The principle has remained the same: timber joists span the width of the building with intermediate supports (honeycombed dwarf walls) ever 1.2m, allowing for small timber section sizes to be used.
Suspended timber floor construction has only changed slightly over the years with the introduction of proprietary fixings and modern insulation and ventilation regulations.
Honeycombed sleeper wall
Joist supported on hangers
Slab on hardcore or blinding
DPC min 150mm
above ground level
Suspended wood floor -
Llawr pren crog

## Slide 31: Lloriau uchaf pren - Timber upper floors
Timber upper floors need to span the full distance of the room below without any intermediate support, the timber sections need to be able to span this distance and take any loads without failing so are usually a much thicker section size (the building regulations give the sizes to be used).
More modern methods include I beams and metal web (posi- joists); these are lightweight engineered alternatives.
Posi-joist
I-beam - Trawst I

## Slide 32: Toeau - Roofs
Roofs can be either traditionally cut and erected using sections of timber or constructed using prefabricated trusses. There are various types of roof design and coverings from the simple to the complex, each serving the purpose of providing protection from the elements and providing insulation - Insiwleiddiad
Collar roof
Loads imposed are spread to preventing collapse

## Slide 33: Cydrannau to torri traddodiadol -Traditional cut roof components
LEVEL 2 DIPLOMA IN SITE CARPENTRY AND BENCH JOINERY
305
Gable end
Gable end
Eaves
Eaves
Jack rafter
Wall plate Crown rafter
Hipped end
Hip rafter
Purlin
Verge
Valley rafter
Cripple jack rafter
Ridge board
Common rafter

## Slide 34: Toeau cypledig - Truss roofs
Trusses are available in many formats to suit the end user, the span and the loads imposed.
Fan
Attic
Mono
Girder
King post
Fink

## Slide 35: Truss roofs (continued)
The safest way to erect a roof. These are constructed at ground level and craned into place.
Crane
Spreader bar
Slinging from joists
Manually lifting trusses -
Mechanically lifting trusses -
Codi’r cyplau â llaw
Codi’r cyplau yn fecanyddol

## Slide 36: Gorchuddion to - Roof coverings
Roof covers are available in a wide range of material. Traditional locally available materials were used in the past, but today many man-made materials are used, such as clay tiles, slate, concrete tiles, thatch, interlocking metal sheets, fiberglass, and so on.
Slate
Cement fibre slate
Roof tiles
Llechi
Teils to

## Slide 37: Grisiau - Stairs
Stairs are designed to allow access between floors. They come in different styles and layouts to fit available space. However, all types must be compliant with Building regulation K.

## Slide 38: Llinyn grisiau - Stair strings
Each flight of stairs has two strings in the image:
the right-hand string has been cut to follow the treads and risers; this is known as a cut string
the left-hand string has an equal width down the full length that encloses the treads and risers; this is known as a closed string.
The stair string or stringer is the section of timber that is housed to accommodate the treads and risers.

## Slide 39: Cydrannau mewnol - Internal components
Any component that can be removed without affecting the integrity of the structure is classed as an internal component. These include:
non-load-bearing partition wall
plasterboards and plaster
second fix carpentry: doors, windows, frames, mouldings, fitted units (kitchen, bedroom)
second fix sanitary ware: toilets, baths, showers, basins, sinks and drainage
decorative finishes: paint and wall coverings.

## Slide 40: Uwchstrwythur - Superstructure
External walls: brick bonds, stone, block, lintels (traditional, modern), cills, insulation, brick ties.
Deunyddiau cladin - Cladding materials : timber, metal, plastic.
Lloriau - Floors: solid ground floor, suspended timber floors, upper timber floors, block and beam.
Roofs: flat, gable, hips and valleys, traditional and trussed, roof coverings.
Straight flight and with turns stairs: quarter-turn, half-turn, winders, closed and cut string.

## Slide 41: Cydrannau mewnol - Internal components
Internal components are applied or fitted after completion of the superstructure these can be classed as either first or second fix
First fix is anything prior to plastering, i.e. partition walls, door frames and linings, plumbing and electrical runs.
Second fix is everything after plastering, i.e. hanging doors, decorative mouldings, sanitary fittings and drainage, fitting units and kitchens, electrical sockets and appliances.
Final finishing includes tiling, painting and decorating.

## Slide 42: Trefn y gwaith - Sequencing of works
Before building work can commence, you need to plan the work activities to ensure work is completed to the client’s requirements and within the timescale agreed. Planning any construction or building services project starts well before any personnel arrives on site, and includes:
writing the of Programme of Works
writing method statements
cynnal asesiadau risg - carrying out risk assessments
planning site layout
organising suppliers, sub contractors, welfare facilities plant and equipment hire etc.

## Slide 43: Sequencing of works (continued)
Remember the 6 Ps:
Proper Planning and Preparation Prevents Poor Performance

## Slide 44: Critical path analysis
Critical path analysis (CPA) is a method used to sequence the tasks required to complete a project. It shows what must be completed in an orderly sequence and what can be completed simultaneously to achieve the planned outcome in a timely manner.

## Slide 45: Siart Gantt - Gantt chart
A Gantt chart (named after its inventor Henry Gantt) lists all the tasks needed on the vertical axis and the time intervals on the horizontal axis in hours, days or weeks (dependent on the size of the project).
Labour plant and equipment can also be shown, allowing for effective planning and ordering of materials.
Designated time for each task is added during the planning process and the actual times taken during the construction process can be added later. This allows for the necessary actions to be implemented at the right time and any changes can be mitigated to diminish the impact of any delays on the overall project.

## Slide 46: Example of a basic Gantt chart
Green planned time
Red actual time

## Slide 47: Cyfathrebu ar y safle - Site communication
What is communication and how is it achieved?
Communication is the process or tool which people use to exchange or pass on information.
How do we exchange or pass on information?
There are many ways to communicate.

## Slide 48: Importance of communication
Good communication is important, as it can help to:
increase work productivity and so time management
ensure smooth day-to-day running of the site
reduce unseen costs – storage, damage, returned deliveries, slow work progress
enhance morale and working relationships between all team members
encourage quick and accurate relaying of information between members of the workforce.
ensure a safe working environment is maintained.

## Slide 49: Communication methods
There are many ways to communicate.
Verbal or oral communication (talking) is an example. This includes:
group discussions
meetings, lectures etc
wyneb yn wyneb, un i un - face-to-face, one-on-one
telephone conversations, video links.

## Slide 50: Verbal communication
Verbal communication is the quickest and most common method of communicating.
We use speech in two ways:
Anffurfiol - Informally – general conversations with your friends and family etc; chatting to people.
Ffurfiol - Formally – at work, during interviews, on the telephone to customers.

## Slide 51: Cyfathrebu’n ysgrifenedig - Written communication
Letters – personal and official.
Memos and notes – short and precise.
Timesheets – various forms.
Invoices – used to bill customers.
Drawings and sketches.
Specifications.
Schedules – lists of building components.
Graphs and charts – used to display data.

## Slide 52: Electronic communication
Involves using electronic equipment, including:
telephone and video calling equipment
fax machines
television and radio
cyfrifiadur – e-bost a’r rhyngrwyd - computers – email and the internet.

## Slide 53: Arwyddion a hysbysiadau - Signs and notices
Signs and notices are designed to communicate information in a visual format.
They can cross language barriers through the use of symbols.
RAG rated.
Show safe exit and escape routes.
Are placed in prominent positions and are usually associated with specific H&S issues.

## Slide 54: Communication channels: Examples
From | To | Method
Architect - Pensaer | Directors / Clerk of works / Site managers | verbal, electronic, written
Directors / Clerk of works | Site managers | verbal, electronic, written
Site managers | Trade personal | verbal, electronic
Site managers | Builders merchants | verbal, electronic, written
Trade personal - Masnachol | Operatives | verbal, electronic
Operatives | Trade personal | verbal, electronic

## Slide 55: Other forms of communication
Iaith y corff - Body language: A non-verbal method that can show an individual’s mood and feelings.
Iaith arwyddion ac ystumiau - Sign language and gestures: Another non-verbal method of communicating often used to communicate between drivers and banks persons.

## Slide 56
Any questions?
Unrhyw gwestiynau?