## Slide 1: PowerPoint 1: Trosolwg iechyd a diogelwch - Health and safety overview
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Trosolwg iechyd a diogelwch - Health and safety overview
Health and safety within the construction industry – and in everyday life – should be at the top of everyone's priority list.
Ensuring the safe welfare, wellbeing, condition and physical performance of everyone is of paramount importance to employers and employees.
Managing health and safety in the workplace can be a challenge.
There can be struggles with staff adapting to rules, machinery failures, material failures and poorly maintained mechanisation, which can all have an effect on the planning of construction projects.

## Slide 3: Health and safety guidance
Mae iechyd a diogelwch yn y gweithle - Health and safety in the workplace are governed by law and legislation.
The legislation and regulations are in place primarily to protect people. These rules are created and must be followed to ensure that nobody comes into contact with harmful substances and that, as far as is reasonably practicable, the welfare of workers and the public is protected.

## Slide 4: Why is legislation necessary?
Legislation is necessary because some individuals and organisations may not otherwise adopt safe practice. Failure to comply with legislation (the law) may result in criminal proceedings - achosion troseddol.
Health and safety legislation in construction covers a whole host of different pathways for specific material or hazards.
Each specific piece of legislation or regulation is designed to give guidance on that entire topic.

## Slide 5: Deddfwriaeth iechyd a diogelwch - Health and safety legislation
Health and Safety
at Work Act
1974 HSWA
The Provision and
Use of Work Equipment
Regulations
(PUWER) 1998
The Construction
(Health, Safety & Welfare)
Regulations
(HSW) 1996
The Management of
Health and Safety
At Work Regulations
(MHSW) 1999
The Personal
Protective Equipment
at Work Regulations
(PPEW) 1992
The Reporting of Injuries,
Diseases and Dangerous
Occurrences Regulations
(RIDDOR) 2013
The Control of Substances
Hazardous to Health
Regulations
(COSHH) 2002
Manual Handling
Regulations 1992
Control of Noise
at Work Regulations 2005
Construction Design
Management regulations
(CDM) 2015
Working at Height Regulations 2005
Electricity at Work Regulations 1989
Lifting Operations and
Lifting Equipment
Regulations
(LOLER)

## Slide 6: Health and Safety at Work Act
The HASAWA oversees all other legislation and regulations. It is a single Act to enable and enforce with the intent to create simple rules and adequate, enforceable law. It has four main objectives:
  To secure – sicrhau the health, safety and welfare of all persons at work.
  To protect the general public from risk to health and safety arising out of work activities.
  To control the use, handling, storage and transportation of explosives and highly flammable substances.
  To control - rheoli the release of noxious or offensive substances into the atmosphere – atmosffer.

## Slide 7: Health and Safety at Work Act
Creates duties for:
  Employers - Cyflogwyr
  Employees - Gweithwyr
  Others - Eraill
This makes it everyone‘s responsibility.

## Slide 8: The Management of Health and Safety at Work Regulations 1999 (MHSW)
The Management of Health and Safety at Work Regulations (MHSW) came into force on 29 December 1999 and cover the following:
  risk assessments - asesiadau risg
  planning, organising and control of health and safety arrangements Health surveillance
  appointment of competent persons
  appropriate procedures for imminent danger
  contacts with emergency services
  Cont’d…

## Slide 9: The Management of Health and Safety at Work Regulations 1999 (MHSW)
Cont’d…
  providing information for employees
  cooperation and coordination with fire - tân procedures
  temporary workers - gweithwyr dros dro
  new or expectant mothers
  protection of young people.

## Slide 10: The Construction (Health, Safety and Welfare) Regulations 1996 (HSW)
What the Regulations are about - Beth sydd yn y Rheoliadau:
‘Impose requirements with respect to the health, safety and welfare of persons at work carrying out "construction work" and of others who may be affected by that work.’

## Slide 11: The Construction (Health, Safety and Welfare) Regulations 1996 (HSW)
The Regulations impose requirements on:
  employers, the self-employed and others who control the way in which construction work is carried out
  employees in respect of their own actions
  every person at work as regards cooperation with others and the reporting of danger.

## Slide 12: The Provision and Use of Work Equipment Regulations 1998 (PUWER)
The Regulations impose requirements on:
  employers, the self-employed and others who control the way in which construction work is carried out
  employees in respect of their own actions
  every person at work as regards co-operation with others and the reporting of danger – berygl.

## Slide 13: The Provision and Use of Work Equipment Regulations 1998 (PUWER)
These regulations apply to all work equipment. PUWER sets the standard for the provision and use of work equipment in the workplace.
The primary objective is to provide safe equipment and ensure it is safe to use. The range of equipment covered by the regulations includes:
  dumper trucks
  cranes - craeniau
  scaffolding - sgaffaldiau
  mobile access platforms
  wood working machines.
  Hammers - morthwylion
  portable drills
  drill bits
  shovels - rhawiau
  wheelbarrows - berfâu

## Slide 14: The Provision and Use of Work Equipment Regulations 1998 (PUWER)
Employers must train staff in the safe use of work equipment.
Training must be adequate and include:
  users - defnyddwyr
  supervisors - goruchwylwyr
  managers - rheolwyr
The training must include safe work methods, possible risks and the precautions to be taken while using work equipment.

## Slide 15: Toolbox talks - Sgyrsiau blwch offer
A ‘toolbox talk’ is a short presentation to the workforce on a single aspect of health and safety.
These toolbox talks can take place at any time during site activities.
A toolbox talk may include current issues, new trends, ideas on how to make deliveries safer, dealing with compliance, filling skips safely or any other safety-related matter.
It is designed to deliver safety messages to everyone.

## Slide 16: Site inductions - Sesiynau cynefino ar safleoedd
Site inductions are a mandatory requirement on all construction sites. They are designed to ensure that everyone who is working on the site has been briefed on the dangers and their own responsibilities within the workplace.
Site inductions can often involve a test of some description to check that the person entering the site is competent and is aware of the site dangers.

## Slide 17: Safe access and egress
Safe access and egress is a compulsory requirement on a construction site - safle adeiladu.
Entering a site in a safe manner and exiting the site in a safe manner is what all employers plan for.
When planning the site layout, it is important for everyone to be able to move around the site with no hazards or problems to be encountered while they are working.
Planning the site layout involves careful consideration and a lot of thought. Disability access must also be considered.

## Slide 18
Any questions?
Unrhyw gwestiynau?

## Slide 19: PowerPoint 2: Health and safety regulations - Rheoliadau iechyd a diogelwch.
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 20: Session aims - Nod y sesiwn
In this session you will gain an understanding of the different safety rules and regulations. These will include:
The Health and Safety at Work Act (HASAWA)
Reporting Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Control of Substances Hazardous to Health (COSHH)
Provision and use of Work Equipment Regulations (PUWER)
Manual Handling Regulations - Rheoliadau Codi a Chario
Personal Protective Equipment (PPE) at Work Regulations

## Slide 21: Session aims cont…..
Work at Height Regulations - Rheoliadau Gweithio ar Uchder
Control of Noise at Work Regulations
Control of Vibration at Work Regulations
Electricity at Work Regulations - Rheoliadau Trydan yn y Gweithle
Lifting Operations and Lifting Equipment Regulations (LOLER)
Construction (Design and Management) Regulations (CDM)
Approved Code of Practice (ACOP)
HSE information.

## Slide 22: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
The RIDDOR Regulations are all about reporting accidents. They cover:
    deaths and major injuries - marwolaethau ac anafiadau mawr
    incapacity to work for more than 3 days
    specified diseases
    dangerous occurrences or near misses.
  Any of the above occurrences must be reported to the HSE using the prescribed form.
  This is also available on the web at www.riddor.gov.uk

## Slide 23: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
It is vital that accurate records are kept of any incident. For example, records may be kept by:
  keeping copies of report forms in a filing system
  cofnodi - recording the details on a computer
  cadw - keeping a written log in a notebook.

## Slide 24: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
If you choose to report the incident by telephone or through the website, the Incident Contact Centre will post you back a copy of the record held.
You will be able to make amendments to the record if you feel the report is not fully accurate - hollol gywir.

## Slide 25: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
The RIDDOR Regulations include the following personnel:
    employers
    employees
    self-employed
    trainees - hyfforddeion
    other people injured on employers’ premises, such as visitors.

## Slide 26: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of major injuries include:
    any fracture, other than to the fingers, thumbs or toes
    amputation of any limb
    dislocation of the shoulder, hip, knee or spine
    loss of sight or penetrating eye injury – anaf.

## Slide 27: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of serious conditions include:
  certain eye injuries – anafiadau.
  electric shock requiring attention
  unconsciousness through lack of oxygen – ocsigen.
  decompression sickness
  poisoning
  acute illness due to exposure of certain materials
  hospitalisation for more than more than 24 hours.
Notes: Title
The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of serious conditions include:
certain eye injuries;
electric shock requiring attention;
unconsciousness through lack of oxygen;
decompression sickness;
poisoning;
acute illness due to exposure of certain materials;
hospitalisation for more than more than 24 hours.

## Slide 28: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of reportable diseases include:
  certain poisonings - gwenwynau
  some skin diseases such as occupational dermatitis and skin cancer - canser y croen.
  lung diseases including occupational asthma, farmer's lung, pneumoconiosis, asbestosis
  infections such as: hepatitis, tuberculosis, anthrax, legionellosis and tetanus
  other conditions such as: occupational cancer, decompression illness and hand-arm vibration syndrome.

## Slide 29: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of reportable occurrences include:
  structural collapses such as buildings or scaffolds
  fires and explosions - ffrwydradau
  releases of gasses or other dangerous substances
  failure of breathing apparatus while in use
  incidents with dangerous substances in transit
  contact with or arcing of overhead cables.

## Slide 30: RIDDOR – Summary
The RIDDOR Regulations cover:
  deaths, major injuries and incapacity to work for more than 3 days
  specified diseases - clefydau penodedig
  dangerous occurrences or near misses.
And finally….
  keep records of all reports - adroddiadau
  remember RIDDOR involves everyone at work.

## Slide 31: Control of Substances Hazardous to Health
These regulations are usually referred to as COSHH and they contain responsibilities for:
  employers
  employees
  self employed
  subcontractors.
The regulations are aimed at protecting people when they are working with substances hazardous to their health - beryglus i’w hiechyd.

## Slide 32: Control of Substances Hazardous to Health - Rheoli Sylweddau Peryglus i Iechyd
The regulations state what employers must do.
  Assess risks to health caused by substances. used at work;
  Prevent or control exposure.
  Ensure use of control methods.
  Monitor the work environment.
  Carry out necessary health surveillance.
  Provide information, instruction and training as necessary.
  Provide suitable storage for hazardous substances.

## Slide 33: Control of Substances Hazardous to Health
The regulations also state what employees must do.
  Co-operate with the employer - Cydweithredu â’r cyflogwr.
  Make correct use of control measures (safe systems, safety equipment).
  Report all defects (plant, machinery and safety equipment and other control measures).
  Attend medical examinations when required – angen.
  Provide health information to medical advisers when necessary.

## Slide 34: Control of Substances Hazardous to Health
Hazardous substances can be:
  specified by law
  recognised from experience
  recognised with common sense.
Examples of hazardous substances include:
cement | plaster | wood - pren
paint | MDF | paints
thinners | solvents | bitumen
oil - olew | grease - saim | dust - llwch
fumes - mwg |  | 

## Slide 35: Control of Substances Hazardous to Health - Rheoli Sylweddau Peryglus i Iechyd
Alternatively, hazardous substances may exist all around our working and living environment.
For example, there may be toxic substances already on site such as:
  in the soil from a previous use of the site
  silica contained in masonry and mortars
  accumulations of bird droppings
  substances left by others
  spillage of hazardous liquids.

## Slide 36: Control of Substances Hazardous to Health
COSHH does not apply to work with:
  asbestos
  lead - plwm
  radioactive materials.
These substances have their own specific legislation as they present a much greater hazard. Specialist training is required to be able to work with these substances.

## Slide 37: Control of Substances Hazardous to Health
solid materials | liquid - hylif
gas - nwy | micro-organisms.
breathed in | absorbed through the skin
swallowed. | 
Harmful substances may be in the form of:
Hazardous substances can be:
Effects vary between individuals but some may be instant and result in long-term illness or even death.

## Slide 38: COSHH – things to remember - pethau i’w cofio
Where am I working?
What are the hazards?
What are the rules? (safe systems, safety equipment)
Who else is involved? Can I endanger them? Can they endanger me?
How do I plan the work?
Does everything work correctly?
Do not use unsafe equipment: report all defects – diffyg.

## Slide 39: Control of Substances Hazardous to Health
Look out for these signs:
Toxic or very toxic
Flammable / risk of fire
Harmful/Irritant
Corrosive -
Cyrydol

## Slide 40: Manual Handling Regulations - Rheoliadau Codi a Chario
The Manual Handling Operations Regulations (often abbreviated to MHOR) are health and safety legislation that affects both employers and employees.
It passed into law in 1992, and was amended in 2002.

## Slide 41: Manual Handling Regulations continued
MHOR 1992 set out a clear ranking of measures for dealing with risks from manual handling. These are:
first: avoid hazardous manual handling operations so far as is reasonably practicable
second: assess any hazardous manual handling operations that cannot be avoided, and
third: reduce the risk of injury so far as is reasonably practicable - ymarferol.

## Slide 42: PPE at Work Regulations
Employers have duties concerning the provision and use of personal protective equipment (PPE) at work – gwaith.
PPE is equipment that will protect the user against health or safety risks at work.
It can include items such as safety helmets, gloves, eye protection, high-visibility clothing, safety footwear and safety harnesses. It also includes respiratory protective equipment (RPE).
Session 9 gives an in-depth look at the PPE regs.

## Slide 43: Work at Height Regulations
The purpose of The Work at Height Regulations 2005 is to prevent death and injury caused by a fall from height. If you are an employer or you control work at height (for example, facilities managers or building owners who may contract others to work at height), the Regulations apply to you.
Employers and those in control of any work at height activity must make sure work is properly planned, supervised and carried out by competent people. This includes using the correct type of equipment for working at height. Low-risk, relatively straightforward tasks will require less effort when it comes to planning.
Session 12 gives an in-depth look at access equipment and working at height.

## Slide 44: Control of Noise at Work Regulations - Rheoliadau Rheoli Sŵn yn y Gwaith
The Control of Noise at Work Regulations 2005 (the Noise Regulations) came into force for all industry sectors in Great Britain on 6 April 2006 (except for the music and entertainment sectors where they came into force on 6 April 2008).
The aim of the Noise Regulations is to ensure that workers' hearing is protected from excessive noise at their place of work, which could cause them to lose their hearing and/or to suffer from tinnitus (permanent ringing in the ears).
The Control of Noise at Work Regulations 2005 replace the Noise at Work Regulations 1989

## Slide 45: Control of Vibration at Work Regulations
The Control of Vibration at Work Regulations 2005 (the Vibration Regulations), came into force on 6 July 2005 and aim to protect workers from risks to health from vibration.
The regulations introduce action and limit values for hand-arm and whole-body vibration – dirgrynu.

## Slide 46: Electricity at Work Regulations
The purpose of this guidance is to highlight what can be done by duty holders to achieve electrical safety compliance with the duties imposed by the Regulations.
It is relevant to all work activities and premises except certain offshore installations and particular ships. Of particular relevance to duty holders, it will also be of interest and practical help primarily to engineers (including those involved in design, construction, operation or maintenance of electrical systems and equipment), technicians and their managers.
The Electricity at Work Regulations 1989 (SI 1989/635) (as amended) (the Regulations) came into force on 1 April 1990. The purpose of the Regulations is to require precautions to be taken against the risk of death or personal injury from electricity in work activities - tasgau gwaith.

## Slide 47: Lifting Operations and Lifting Equipment Regulations
These Regulations (often abbreviated to LOLER) place duties on people and companies who own, operate or have control over lifting equipment. This includes all businesses and organisations whose employees use lifting equipment, whether owned by them or not.
In most cases, lifting equipment is also work equipment so the Provision and Use of Work Equipment Regulations (PUWER) will also apply (including inspection and maintenance). All lifting operations involving lifting equipment must be properly planned by a competent person, appropriately supervised and carried out in a safe manner.

## Slide 48: LOLER continued
LOLER also requires that all equipment used for lifting is fit for purpose, appropriate for the task, suitably marked and, in many cases, subject to statutory periodic 'thorough examination'. Records must be kept of all thorough examinations and any defects found must be reported to both the person responsible for the equipment and the relevant enforcing authority – awdurdod.

## Slide 49: Construction (Design and Management) Regulations
Whatever your role in construction, CDM aims to improve health and safety in the industry by helping you to:
sensibly plan the work so the risks involved are managed from start to finish – diwedd.
have the right people for the right job at the right time.

## Slide 50: CDM Regulations continued
CDM also helps you to:
cooperate and coordinate your work with others
have the right information about the risks and how they are being managed
communicate this information effectively to those who need to know
consult and engage with workers about the risks and how they are being managed.

## Slide 51: Approved Code of Practice
Each ACOP is approved by the Health and Safety Executive, with the consent of the Secretary of State. It gives practical advice on how to comply with the law. If you follow the advice, you will be doing enough to comply with the law in respect of those specific matters on which the Code gives advice. You may use alternative methods to those set out in the Code in order to comply with the law.
However, the Code has a special legal status. If you are prosecuted for breach of health and safety law and it is proved that you did not follow the relevant provisions of the Code, you will need to show that you have complied with the law in some other way, or a court will find you at fault.

## Slide 52
Any questions?
Unrhyw gwestiynau?