## Slide 1: PowerPoint 5: Emerging technologies and materials 1 - Technolegau a deunyddiau newydd 1
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 2: Emerging technologies and materials in construction
      How many of these new technologies in construction have you heard of?
Long-lasting LEDs
Impermeable paint - Paent anhydraidd
Corrosion-proof steel
Interactive panels
Spray-on solar panels
Self-healing concrete
Robotic construction - Robotic construction
Super wood, translucent wood
Perspiring polymer
Germ-repellent materials
3D printed buildings
Rice buildings - Adeiladau reis
Light generating concrete
Pollution absorbing bricks - Brics sy’n amsugno llygredd

## Slide 3: 3D printing - Argraffu 3D
Photo by Tom Claes on Unsplash
      3D printing is the computer-controlled sequential layering of materials to create 3D shapes. The process is sometimes called Additive Manufacturing (AM) or Autonomous Robotic Construction System (ARCS).
      3D printers can use a huge range of materials, such as plastics, thermoplastic polyurethane filaments, nylon, wood filaments with cork dust and polylactic acid, and metal powder.
      Photo by ZMorph Multitool 3D Printer on Unsplash
      Uses for printing in metal can be applied to repairs of historical components or replicas.

## Slide 4: 3D printing in construction
      Examples of components printed for construction:
      guttering (metal) - cafnau (metel)
      historical replicas (metal)
      replacement columns (concrete). -colofnau newydd (concrit).
      Source: MX3D
https://youtu.be/1r_Azsa4nqU
MX3D’s ambitious, fully functional 3D printed stainless steel construction bridge was designed by the Joris Larmaan lab. Using specially designed MX3D software and multi-axis industrial robots, it took these four machines six months of printing to complete the full span of the metal bridge. Measuring 12.5m in length and 6.3m in width, the design currently weighs 4,500kg and uses over 1,100km of wire. The next phase of development is testing, where its structural integrity will be verified.
      Source:

## Slide 5: 3D printing in construction - Argraffu 3D ym maes adeiladu
      The main 3D printing methods used at a construction scale are:
      extrusion (concrete/cement, wax, foam, polymers)
powder bonding (polymer bond, reactive bond, sintering).
      The three stages to 3D concrete print are:
      data preparation: using 3D scanning technology (e.g. Trimble pulse, Matterport and CAD or CAM software)
      concrete preparation: mixing and placing the concrete into the container, which is then pumped through a nozzle, layer by layer
      component printing: using specialist design software and construction hardware 3D printing technology (gantry crane or robotic arm).

## Slide 6: 3D printing in construction
      Highest rated 3D printers of 2020:
      Dyma'r argraffwyr 3D a ddaeth i’r brig yn 2020:
        5. Crane WASP https://www.3dwasp.com/en/3d-printing...
        4. Apis Cor https://www.apis-cor.com/
        3. COBOD https://cobod.com/
        2. Hadrian X https://www.fbr.com.au/
        1. Icon Vulcan II https://www.iconbuild.com/
        Source: Tech Machine channel on YouTube: https://youtu.be/69HrqNnrfh4

## Slide 7: The limitations of 3D printing buildings
        3D printing currently only prints walls (vertical elements). Horizontal, flat planes such as roof and floor are assembled on-site.
        Specialist hardware and software, for operations, limits accessibility to mainstream.
        Technology needs to be developed to be in line with architect’s and designer's software.
        Development of the hardware to produce high-rise built assets needs further development.
        Uncertainty as to how 3D printed elements will integrate with other building components or how they will incorporate services to standard.
        To stimulate mainstream adoption, particularly in the UK, development of a solution for restricted city centre sites is required.
        The investment required to bring 3D printing to mainstream would be phenomenal.
        Number of manual workers required will reduce, meaning less jobs.
Arachne 3D Printed Building Façade,
design by Lei Yu / Yuexiu Group27 Oct 2018
                Source:https://www.e-architect.co.uk/china/arachne-3d-printed-building-facade-building-façade
                https://www.designingbuildings.co.uk/wiki/File:3dprinting.jpg#filelinks

## Slide 8: The benefits of 3D printing buildings - Manteision argraffu adeiladau 3D
        On-site and off-site printing is possible, of building components (cladding and structural panels and columns).
        The process allows it to be undertaken in harsh or dangerous environments not suitable for a human workforce, such as in space for example.
        These new capabilities are more efficient and take less time.
        Sustainable capabilities (use of local materials).
        The process produces less waste, even zero waste in some cases.
        Reduction of manual labour used on site, leading to cost savings.
        Reduced logistics/transport costs.
        Reduced storage required.
        No double handling of materials on-site.
        A 3D printer can work 24 hours a day, 7 days a week.
        The design possibilities are endless.

## Slide 9: 3D printing case studies - Astudiaethau achos argraffu 3D
      Hadrian X: robotic construction
Technological advancements led to the development of FBR's revolutionary bricklaying robot, Hadrian X.
This construction robot is mounted into a classic cab over-engine truck or other base to easily transport it to and from a location for on-site building.
Find out more at Hadrian X® | Outdoor Construction & Bricklaying Robot from FBR

## Slide 10: 3D printing case studies
The unique control system uses CAD to create a 3D model of the building design, which is then used to calculate the materials list and tell Hadrian X what to build.
The Fastbrick Wall System uses uniquely designed blocks and adhesive for continuous construction. Blocks are 12 times bigger than standard house bricks and are lighter, stronger and designed to minimise waste – gwastraff.
The special adhesive bonds in just 45 minutes, holds stronger and results in greater thermal and acoustic properties than traditional mortar. No more lost days waiting for mortar to dry - morter i sychu.
                Source:https://cobod.com/

## Slide 11: 3D printing case studies - Astudiaethau achos argraffu 3D
        Earth House GAIA
        Project: Gaia , 6–7 October 2018
        3D printer: Crane WASP
        Materials: Raw earth, straw, rice husk and lime
        Construction time: 100 hours
        Location: Via Castelletto 104, Massa Lombarda (RA)
        Design: WASP in collaboration with RiceHouse
        Floor area: 20m2
        Printed building envelope: 30m2
Source:https://www.3dwasp.com/en/3d-printed-house-gaia/. Case study on the Wasp website

## Slide 12: 3D printing case studies
      Largest printed building by Apis Cor
Foundation - Sylfaen : Conventional construction by general contractor
Walls - Waliau : 3D printed by Apis Cor
3D printing material: Gypsum-based mixture developed by Apis Cor
Reinforcement: 3D printed formwork columns, manually filled with rebar and heavy concrete
Slabs - Slabiau : precast
Roof, windows, insulation: Conventional by general contractor
      Source: https://www.apis-cor.com/dubai-project

## Slide 13: 3D printing case studies
      COBOD (Construction of Buildings on Command), European developments
In 2017, COBOD 3D printed the first building in Europe. It took two months from start to finish.
Explanation and insights - Esboniad a dealltwriaeth – 3D printing the BOD building a second time, in 2019, took 3 days.
                Source:https://cobod.com/

## Slide 14
Unrhyw gwestiynau?
Any questions?

## Slide 15: PowerPoint 6: Emerging technologies and materials 2 - Technolegau a deunyddiau newydd 2
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 16: Immersive technologies - Technolegau Ymgolli
      What is an immersive experience? - Beth yw profiad ymgolli?
      It’s when you engage in an experience that blurs the lines between reality and the virtual world. An immersive experience often uses one or more technologies linked together.
        Immersive experiences include:
  Virtual Reality - Rhith Realiti
  Augmented Reality
  Mixed Reality - Realiti Cymysg
  Digital twins
  360º content
  3D simulations and visualisations.

## Slide 17: Immersive technologies: Virtual Reality (VR)
VR is a digital simulation that you can interact with. VR technologies, when used with the BIM models, make it possible to ‘walk around’ the building.
Combining VR with laser scanning (also known as LIDAR or point cloud survey) the site makes it the most accurate. When you combine laser scanning technology with drones you can create highly detailed models for VR. This allows the client to see that their brief is understood by the designers and the contractors.
                Source: Trimble technologies How Mixed Reality is Transforming the Construction Industry
The benefits of using VR in a project:
save time and money - arbed amser ac arian
improve training safety
improve collaboration
improve/shorten timescale
improved quality - gwell ansawdd
                Source: Trimble technologies How Mixed Reality is Transforming the Construction Industry

## Slide 18: Immersive technologies: Augmented Reality (AR) Technolegau ymgolli: Realiti Estynedig (AR)
        AR is a computer-simulated ‘enhancement’ of real life. Augmented Reality is the overlaying of digitally-created content on top of the real world. It can be offered through a headset or a screen in a 2D display.

## Slide 19: Immersive technologies: Augmented Reality (AR)
Superimposing BIM is possible at all stages of construction:
Before work begins - Cyn i’r gwaith ddechrau: similar to a VR experience, the difference is that you can see the real world around you.
During the course of building - Yn ystod y cyfnod adeiladu: workers can use AR to see if everything is going according to plan and prevent mistakes by double-checking the work on site.
After the project is finished - Ar ôl i’r prosiect ddod i ben: to make sure that all the components were laid down as designed and that the project’s requirements were met.

## Slide 20: Immersive technologies: Augmented Reality (AR)
The benefits of using AR in a project:
Less rework and downtime cost
Improve training safety - Gwella diogelwch hyfforddiant
Better project management and collaboration
Improved/shorter timescale
Improved quality - Gwell ansawdd
Accurate space and measurement projection
The limitations of using AR in a project:
Expensive, although software is becoming cheaper, especially with the availability of mobile apps
Safety issues – not all AR headset allow for hard hats to be worn
The distraction factor can affect health and safety, for example, failure to see a hole or a crane
Poor internet connections - Cysylltiadau rhyngrwyd gwael.

## Slide 21: Immersive technologies: Mixed Reality (MR) - Technoleg Realiti Cymysg.
Mixed reality (MR) combines both Virtual and Augmented Reality.
      You're wearing a headset device again. In this case, however, you're being immersed in the digital content, still aware of your physical surroundings so that you can interact with both physical and digital objects at the same time. All those different technologies can be applied to communicate and collaborate around the construction site.
      Watch the video to find out how Trimble Buildings uses Mixed Reality Technology - Technoleg Realiti Cymysg.

## Slide 22: Immersive technologies: digital twins
Digital twins are near-exact virtual models of real-life objects, processes or systems. Digital replicas of real-world objects can help construction companies mitigate risk and deliver more with fewer resources.
Using this technology means that the various pieces of a structure can be produced in an off-site factory and then assembled on site: meaning buildings can be disassembled and reused to support a circular economy - economi gylchol.
      Watch the video to find out more about digital twins.

## Slide 23
Unrhyw gwestiynau?
Any questions?

## Slide 24: PowerPoint 7: Emerging technologies and materials 3 Technolegau a deunyddiau newydd 3
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 25: Emerging technologies and materials in construction
      Some examples of evolving materials are:
        graphene
        surface coverings - gorchuddion arwyneb
        ventilated building materials
        liquid roof - to hylif
        transparent aluminum
        self-healing concrete.
                Source https://www.letsbuild.com/blog/10-innovative-construction-materials infographic

## Slide 26: Evolving materials: Graphene - Deunyddiau esblygol: Graffin
        Graphene was isolated in 2004 by two researchers at the University of Manchester, Professor Andre Geim and Professor Kostya Novoselov. They won the Nobel Prize in Physics for their pioneering work extracting the graphene from graphite.
        Graphene is revolutionising scientific fields due to its unique properties. It has a tensile strength 200 times stronger than steel and an electrical mobility (that is how quick the electron moves) two to three times that of silicon.
Potential applications in architecture include small-scale products such as coatings, solar cells and electronics, long-lasting LEDs, impermeable paint, corrosion-proof steel, interactive panels, spray-on solar panels and self-cleaning concrete.

## Slide 27: Evolving materials: Graphene
        Graphene composites are:
        Stronger than steel -
        Yn gryfach na dur
        1 million times thinner than a human hair
        More conductive than copper
        Stretchable, transparent and flexible - hyblyg
        Multidisciplinary, world’s first two dimensional material
https://www.graphene.manchester.ac.uk/learn/applications/composites-and-coatings/Composites_1748x2480.jpg

## Slide 28: Evolving materials: surface coverings - Deunyddiau esblygol: gorchuddion arwyneb
        3D-printed bioplastics
        Waste is a major problem in the construction industry. Dutch firm Aectual believe 3D printing floors and stairs from a renewable bioplastic source will make a difference to the environment.
        Source: https://www.engineering.com/BIM/ArticleID/17639/Aectual-3D-Prints-Everything-from-Floors-to-Walls.aspx

## Slide 29: Evolving materials: Alusion panels
The material - Y deunydd : architectural stabilised aluminium foam is claimed to be uniquely versatile, suitable for covering buildings, doors, floors and more.
This Toronto-based business discovered a way of injecting air into molten aluminium that forms bubbles due to the dispersion of ceramic particles in the mix. Benefits include noise reduction, 100% recyclable, strong and non-combustible.
Cymat Technologies
https://www.alusion.com/files/Brochure_AlusionTM_Feb2020.pdf

## Slide 30: Evolving materials: ventilated building materials
        Ventilation – Awyru refers to the process of 'clean' air (normally outdoor) being supplied to a space, while stale air is removed.
        Ventilated façade system (rain screens): Cladding materials include panels made of fibre cement, ceramics, steel, aluminium. high-pressure laminate (HPL) and aluminium.
        A ventilated façade is two layers of façade separated by an air cavity. This separation creates an open cavity, allowing exchange of the air contained between the wall and the outer cladding.
        Using a ventilated façade has thermal, acoustic and structural benefits.
        Source: https://innowood.com/concealed-fixing/

## Slide 31: Evolving materials: ventilated building materials
        Breathing walls - Waliau anadlu : The design of porous materials for heat exchange and decentralised ventilation
        This study demonstrated how to design pores in building materials so that incoming fresh air can be efficiently tempered with low-grade heat while conduction losses are kept to a minimum. Any material can be used in principle, so long as it can be manufactured with millimeter-scale air channels.
        Source: https://reader.elsevier.com/reader/sd/pii/S0378778817300476?token=C8A5BFBB37535EFCB07423266E08B649B8C6C9ABAD35EA81726D0985E0B987EC2E87B4CE26229EC9F68B3A2C86B1A8C9

## Slide 32: Evolving materials: breathing walls - Deunyddiau esblygol: waliau anadlu
This is a pneumatic façade, that is a breathable façade. Covered in pore-like holes to allow the air to flow through.
This biomimetic project was led by Stuttgart University student Tobias Becker.
Source: https://youtu.be/a67brMDgiW4
FUTURISM CREATIVEJUNE 22ND 2016 WEBSITE: http://futurism.com

## Slide 33: Evolving materials: building façade - Deunyddiau esblygol: ffasâd adeiladu
Decker Yeadon developed a breathable façade that mimics the design of organic skins. The system works using two glass panels that are sandwiched together called ‘muscles’. Inside the sandwich is a flexible engineered ribbon made of polymer materials that can be polarised. These muscles contract or expand according to pressure differences.
This façade controls the flow of light, matter and temperature between the inside and outside. The technology can then be adjusted, making it similar to an air conditioning unit. Imagine a curtain, AC unit and a window all in one system without electricity.
Homeostatic Building Facade (internationalfacade.com)
Material transformations: Martina Decker at TEDxNJIT – YouTube

## Slide 34: Evolving materials: liquid roof
        A liquid roof coating is a single piece roof membrane with elastic properties. When applied it becomes the top layer of the roof system. Liquid roofs have existed since the early 1800s, when natural bitumen was combined with jute, straw, rag felt and other man-made materials.
        Modern liquid roofs - Toeau hylif modern:
        Are applied cold by roller or brush
        Are high performance, rapid curing
        Can be applied to flat or pitched roofs, made of asbestos, felt, asphalt, concrete, metal, bitumen, wood or metal
        Can be applied onto wet or dry surfaces
        Can be used on building components such as tiles, down pipes, chimneys, roof lights, up stands and parapet walls
        Can provide anti-skid finish for designated walkways and balconies.

## Slide 35: Evolving materials: transparent aluminium - alwminiwm tryloyw
        Aluminum oxynitride (known commercially as ALON), is a transparent ceramic made of aluminum, oxygen and nitrogen. It is commonly referred to as transparent aluminium.
        Although this material is still very expensive, it has the potential to create large glass structures such as aquariums, windows and façades. It will not fracture like silica glass and can be used for harsh environmental conditions.
        Watch this video to find out more about this material:
                /

## Slide 36: Evolving materials: self-healing concrete - Deunyddiau esblygol: concrit hunan-drwsio
Concrete is a popular choice for large-scale structures, such as bridges, tunnels, roads and buildings, but is not without problems. Every year billions of pounds are spent maintaining, fixing and restoring concrete structures, damaged by vehicle vibration ground movement.
Cardiff University Research team Materials for Life (M4L) looked into the development of healing agents. Research is continuing under (RM4L) Resilient Materials for Life. Watch the video to find out about RM4L.
                Home - M4L (rm4l.com)

## Slide 37: Evolving materials: self-healing concrete - Deunyddiau esblygol: concrit hunan-drwsio
Watch the video to find out about RM4L.

## Slide 38
Unrhyw gwestiynau?
Any questions?