## Slide 1: PowerPoint 1: Construction trades
PowerPoint presentation
Unit 102: Introduction to the trades in the construction and built environment sector

## Slide 2: Construction and building services engineering trades
There are often a wide range of trades, both construction and building services engineering (BSE), involved on a single construction project.
Crefftau adeiladu a pheirianneg gwasanaethau adeiladu

## Slide 3: Construction trades
The activities associated with each of the main trades in the construction industry are explored in the following slides.
Construction trades
Trowel occupations
Wood occupations
Plastering
Decorative finishing/ industrial painting
Roofing occupations
Construction/civil engineering occupations
Crefftau adeiladu

## Slide 4: Trowel occupations
Galwedigaethau trywel - Trowel occupations: A generic term given to anyone who works with bricks, blocks, stone and associated aggregates.
Brics a blociau - Bricks and block: The majority of new buildings built in Wales require builders skilled in brick or blockwork. However, bricklayers’ skills are also needed to repair old brick buildings.
Brickwork at Hampton Court Palace
Galwedigaethau trywel

## Slide 5: Trowel occupations (continued)
Gwaith maen - Stone masonry: Stone masonry is a diverse trade and includes banker masons, fixer masons, monumental masons and stone masons who work on rubble or dressed stone work. The majority of masons in Wales work on wall repair using rubble or semi-dressed stone.
A gargoyle on the side of Llandaff Cathedral
Dry stone wall traditional construction, The Gower Peninsula, South Wales

## Slide 6: Trowel occupations (continued)
The laying of bricks, blocks or stone is usually undertaken by setting the block in a mortar and then filling the gaps. The finished surface is then either pointed or rendered with a similar mortar.
Morter - Mortar = Bulk material or Aggregate + Binder
A bulk material or aggregate can include sand, gravel, earth or materials with more insulative properties, such as cork or hemp.
A binder can be cement or lime.

## Slide 7: Galwedigaethau gwaith coed Wood occupations
Any tradesperson that works with timber or timber-based products works in a ‘wood occupation’. The range of specialisms in wood occupations is large and includes on-site and off-site work.
Site carpenters typically work on a construction site undertaking structural carcassing (first fix) and internal fitting out, such as hanging doors and fitting skirting boards (second fix). Timber framers are involved in the repair of historic roof trusses and timber-framed buildings – this is an on-site wood occupations specialism.
Gable and wooden roof trusses to a timber frame house under construction
Carpenter working on site
Saer coed -

## Slide 8: Wood occupations (continued)
Architectural or bench joiners usually work in a workshop making standard and bespoke joinery components. Shop fittings and sash window repair would be undertaken in a workshop and the final product would then be installed on-site.
Repairing and restoring a sash window frame
Atgyweirio ac adfer ffrâm ffenestr ddalennog

## Slide 9: Plastering
Plastrwyr - Plasterers are responsible for creating finished surfaces internally and externally.
Solid plastering can involve working with a range of materials including plasterboard, gypsum plaster, lime plaster and a range of cement and lime external renders.
Plasterers are also often responsible for laying and screeding solid concrete or limecrete floors.
Plastro -

## Slide 10: Plastering (continued)
Gwaith plastr ffibrog - Fibrous plasterwork involves the creation and repair of decorative mouldings and cornices. It often uses plaster of Paris in its creation and can involve creating bench moulds or undertaking repairs ‘in-situ’.
Ceiling roses
Rhosynnau nenfwd -
Notes: https://lh3.googleusercontent.com/proxy/kmc2sztjr1o8E0cVIIH7KFCmmmFXLXDlkt47s25iZfdaGPVJAHGng8iswrz0RzcvKGvB_QdspLNwjVKL_swyUvNP67V2IQrTiyE0szxui4HcST11USSHG8iIPDEkrILW1eXWRqpQ64fXCPTa61E5YeLpndhcmaeu8PQEAZV_9tKWJ53Uxr0
Traditional ceiling in situ running mold repair – Copyright -Philip Gaches – Gaches Traditional Plasterers Ltd

## Slide 11: Decorative finishing and industrial painting occupations
Paentwyr domestig - Domestic painters: Painting is the application of liquid-based coverings such as emulsions and oil paints. Decorators apply paper-based decorative finishes, such as vinyl and embossed papers.
Paentwyr diwydiannol - Industrial painters: Work on larger commercial or civil projects and often use spray guns to apply a protective coating to steel structures, such as bridges etc., as well as to factory walls and floors.
Notes: https://encrypted-tbn0.gstatic.com/images?q=tbn%3AANd9GcTcLfd4TyT0ccEuMXZd59yNTGjYcFOCzJdtdkdjlTAnk-Dh7yWi&usqp=CAU
https://grantpainters.com.au/wp-content/uploads/2016/08/HARBOUR.jpg

## Slide 12: Galwedigaethau toi - Roofing occupations
Towyr - Roofers cover pitched or flat roofs with waterproof material.
This could include the application of felts, bitumen and breathable membranes as a layer, under a more durable material such as slate, tiles or metal. Lead or a similarly flexible alternative are usually used for sealing junctions between roofs and around chimneys. Roofers typically work with a broad range of materials.

## Slide 13: Roofing occupations (continued)
Traditionally a roofer would cover a pitched roof with locally available material such as llechi - slate, stone or thatch. The use of lead was rare and traditional gullies show great skill in keeping water out without using any waterproof membranes.
Traditional roofs © Tywi Centre
Notes: Visit https://www.tywicentre.org.uk/ for more information

## Slide 14: Roofing occupations (continued)
A modern roofer’s role increasingly involves installing solar collectors to new and existing roofs.
Installing solar panels
Gosod paneli solar -

## Slide 15: Construction and civil engineering operations
The range of specialisms within civil engineering operations is very broad. They include ground works; laying drainage; laying kerbstones and paths; fixing steel and undertaking reinforcing work; pouring and finishing concrete; erecting steel framework; erecting scaffolding; and operating heavy plant/machinery.
Specialisation in areas such as operating machinery and erecting scaffolding requires specific training.
Scaffolding
Sgaffaldiau -

## Slide 16: Construction and civil engineering operations (continued)
Cyflogaeth - Employment in construction and civil engineering operations offers opportunities to work on a diverse range of projects, ranging from smaller house building projects to large infrastructure projects such as roads, airports, railways, bridges, dams, power plants and water treatment systems.

## Slide 17
Any questions?
Unrhyw gwestiwn?

## Slide 18: PowerPoint 2: Building services engineering trades
PowerPoint presentation
Unit 102: Introduction to the trades in the construction and built environment sector

## Slide 19: Building services trades
This diagram shows the activities associated with each of the main trades in the building services industry.
Building services trades
Electro-technical
Plumbing
Gas installation engineering
Heating and ventilation
Mae’r diagram hwn yn dangos y gweithgareddau sy’n gysylltiedig â phob un o’r prif grefftau yn y diwydiant gwasanaethau adeiladu.

## Slide 20: Building services trades: Electrotechnical
Electrotechnical: electricians can be divided mainly into two categories:
Trydanwyr gosod - Installation electricians who test and install wiring systems (lighting, security, fire) and equipment. They work in homes, building sites, office blocks and industrial sites.
Trydanwyr cynnal - Maintenance electricians who test and maintain electrical equipment and often work in commerce or heavy industry.

## Slide 21: Building services trades: Electrotechnical (continued)
Your duties will depend on which area you decide to work in. You could be re-wiring a home, laying cables on a building site, testing systems in a factory or installing a CCTV system in an office – there’s a variety of potential jobs awaiting you.

## Slide 22: Building services trades: Electrotechnical (continued)
Below are some examples of electrical equipment that you may encounter.
Double socket outlet
Fused spur unit
1 way lighting switch
Allfa soced ddwbl
Uned cainc â ffiws
Swits goleuadau 1 ffordd

## Slide 23: Building services trades: Electrotechnical (continued)
Below are some examples of cables used in electrical work.
PVC/PVC
Flex
Steel wire armoured
Fire resistant
Fflecs -
Gwrthsefyll tân -
- Gwifren ddur haengaled

## Slide 24: Building services trades: Electrotechnical (continued)
Y sgiliau sydd eu hangen i fod yn drydanwr -
Skills needed to be an electrician
To become a successful electrician, you will require the following attributes:
good practical skills
good at following detailed instructions
adaptable
good with both heights and confined spaces
careful and precise.

## Slide 25: Building services trades: Plumbing
Plymwr - Plumber: A plumber is someone who installs and maintains pipes in homes and businesses. These pipes need to be installed and maintained for potable water, drainage, irrigation and sewage, as well as other uses.
Plumbers can be involved in hands-on work or may work in a design capacity, drafting blueprints and helping make the installation process more efficient. This is a profession with an extensive number of possible career paths.

## Slide 26: Building services trades: Plumbing (continued)
Plumber duties and responsibilities
Plumbers must be able to perform the following tasks:
Gosod - Install pipes and plumbing fixtures.
Clear obstructions from sink drains and toilets.
Visually inspect equipment and operate test equipment such as pressure and vacuum gauges to determine the cause and location of issues.
Troubleshoot problems and decide how to fix them.
Trwsio - Repair pipes and plumbing fixtures.
Estimate costs of installations and repairs.

## Slide 27: Building services trades: Plumbing (continued)
Examples of plumbing installations
Pibellwaith - Pipework
Cawod - Showers
Tapiau- Taps
Ystafelloedd ymolchi - Bathrooms

## Slide 28: Building services trades: Plumbing (continued)
Examples of plumbing equipment
Plastic pipes
Pibellau copr a hyblyg -
Copper and flexible pipes
Various fittings - Gwahanol osodion
Valves - Falfiau
Pibellau plastig -

## Slide 29: Building services trades: Heating and ventilation
Peiriannydd gwresogi ac awyru - Heating and ventilation engineer: Heating and ventilation engineers install and maintain the heating and air conditioning systems found in larger buildings – from offices and schools to shops and sports centres.

## Slide 30: Building services trades: Heating and ventilation (continued)
Heating and ventilation engineer responsibilities
There are a variety of roles in the industry, for example:
Heating installers fit heating equipment and pipework systems in buildings such as office blocks, hospitals and schools.
Ductwork installers put in ductwork and ventilation systems in large buildings such as sports stadia, airport terminals and shopping centres.
Domestic heating installers fit central heating systems in homes and ensure they work properly.

## Slide 31: Building services trades: Heating and ventilation (continued)
Heating and ventilation engineer responsibilities (continued)
Peirianwyr gwasanaeth - Service engineers plan and carry out regular maintenance and repairs on all systems to make sure they are working safely and efficiently.
Peirianwyr comisiynu - Commissioning engineers make sure systems meet their original design specification by testing and checking carefully that they do what the customer needs them to do.
Peirianwyr rheoli - Control engineers design and install the control panels that operate and adjust heating systems.

## Slide 32: Building services trades: Heating and ventilation (continued)
Heating and ventilation engineer responsibilities (continued)
Energy efficiency is extremely important, and part of your job would be to make sure systems work as efficiently as possible. This is to reduce fossil fuel consumption, carbon emissions and help people save energy - ynni.
You would also work with renewable energy heating systems such as ground source heat pumps, which take the heat from underground and pump it to the surface and then into buildings to supply warm air.

## Slide 33: Building services trades: Heating and ventilation (continued)
Air conditioning systems
Air conditioning and
heating systems
Heating, ventilation and air conditioning systems
Examples of heating and ventilation installations
Systemau aerdymheru -

## Slide 34: Building services trades: Heating and ventilation (continued)
Fans
Room ventilation systems
Ducting
Examples of heating and ventilation equipment
Gwyntyllau -
Dwythellau -

## Slide 35: Building service trades: Refrigeration and air conditioning engineer
Refrigeration/air conditioning (AC) engineer
AC engineers install, maintain and repair AC systems used to keep spaces cool in summer and warm in colder months.
Most AC engineers tend to work in commercial buildings, but AC systems are also becoming more widely available for domestic applications.
Any AC engineer working with and handling the refrigerant gasses inside an AC system should be registered and hold an F Gas Certificate.

## Slide 36: Building service trades: Refrigeration and air conditioning (continued)
Refrigeration/air conditioning engineer
Refrigeration is the design, installation and maintenance of cooling rooms. Examples include walk-in fridges in restaurant kitchens, hospitals, mortuaries and supermarkets, as well as food processing plants and factories where a low temperature needs to be maintained.

## Slide 37: Building services trades: Gas installation engineering
Nwy - Gas installation engineer
A gas installation engineer specialises in the installation, service, repair and maintenance of gas-fired appliances in commercial and domestic settings. In a domestic setting engineers would work on hobs, ovens, boilers, fires and heaters, as well as static ovens and tumble dryers in a commercial environment. Gas installation engineers normally start out as a Level 2 plumber and specialise in gas at Level 3.

## Slide 38
Unrhyw gwestiwn?
Any questions?