## Slide 1: PowerPoint 1: Know the design of buildings and structures
PowerPoint presentation
Unit 103: Introduction to the built environment life cycle

## Slide 2: Pwrpas tirfesur - The purpose of surveying
Before any project can start, the land needs to be surveyed to determine the topography of the area including:
pellter - distances between set points
lefelau - levels and features of the existing ground.

## Slide 3: The purpose of surveying (continued)
everything is in the correct position
draeniau - drains fall at the correct angle
ffyrdd - roads and pavements are in the right position with camber
buildings are positioned at the right angle and height.
During the construction process a surveyor will set out roads, drains, foundation heights and positions of buildings or structures. Surveying ensures:

## Slide 4: Mesur tir â chadwynfeydd - Chain surveying
To transfer levels and datums for a range of tasks using various methods and points.
Chain surveying is a simple traditional method used to survey measurements when the area is fairly level and is small and free from obstacles. It uses a network of triangles to plot positions using a chain.
A metric chain has links every 200mm with tallies positioned at every 10 links (2m); a brass ring is fitted in between each tally at five links, denoting every 1m. Example: Ring 1m, tally 2m, ring 3m, tally 4, two links = 4.4m

## Slide 5: Mesur tir â chwmpawd - Compass surveying
When an area is too large for chain surveying, compass surveying is used. However, it can not be used if the area contains iron ore or power lines as these can affect the compass - cwmpawd readings.
While a chain uses triangulation to measure, a compass uses traversing. This is where directions of survey lines are determined with a compass and the length of the lines are measured with a chain or tape.

## Slide 6: Meincnodau - Benchmarks
Meincnodau arolwg - Ordnance survey benchmarks: these can be found across the country, etched into buildings. They can all be referenced back to the mean sea level from Newlyn in Cornwall and are used to transfer levels locally.
Meincnodau dros dro - Temporary benchmarks: a fixed point on site that is referenced from the ordnance benchmark. All other heights and positions are referenced from this across site to calculate heights of foundation, floors, openings in buildings, and so on.

## Slide 7: Cyfarpar tirfesur modern - Modern surveying equipment
Theodolitau - Theodolites
Theodolites have been used since the mid-1700s. They are used for measuring angles both vertically and horizontally. Modern theodolites are often electronic (digital) and measure very precisely.

## Slide 8: Lefelau awtomatig - Automatic levels
An automatic level uses a swinging prism that hangs. This will self level if positioned close to level on a tripod. They have an inbuilt telescope that enables accurate readings to be taken from a staff when transferring levels or measuring datum points.

## Slide 9: Lefelau laser - Laser levels
Rotary laser levels are available for precise setting out on sites. By using a staff and detector they can be used as a traditional automatic level.
Smaller non-rotating levels are often used by a range of tradespersons on site to set out partitions, transfer datum - datwm point for suspended ceilings, check for plum when fitting door frames and windows - ffenestri, check for level when fitting kitchens, hanging wall papers, and so on.

## Slide 10: Cyfarpar mesur digidol - Digital measuring equipment
Digidol - Digital measuring tools can accurately measure lengths, widths and heights, they can calculate square and cubic meterage at a push of a button.
Some devices can also calculate the hypotenuse by using the run (length) and rise (height) measurements - mesuriadau.

## Slide 11: Sganwyr laser - Laser scanners
Laser scanners are available in both 2D and 3D, with 3D scanners most often used in construction. Laser scanners work by combining two sets of information from different cameras trained on an object. Readings taken from a laser are then collated on a computer and a three-dimensional model can be generated which allows for virtual walkthroughs.

## Slide 12: Llygredd a gynhyrchir drwy adeiladu - Pollution generated through construction
During the construction process, care must be taken to reduce any pollutants contaminating the surrounding area. The main sources of pollution from a building site include:
spillages of chemicals used
contaminated water running off-site into water sources
dust and other airborne particles
fumes from construction machines and fires.
To mitigate against these, it is important that each company has a set of precautionary and preventive measures in place.

## Slide 13: Mesurau rhagofalus - Precautionary measures
Precautionary measures can include the following:
Cyflwyno - Implementing a training / induction programme in environmental protection and emergency implementation actions for all site personnel.
Sicrhau - Ensuring chemical storage safety requirements are strictly followed.
Solid site boundary fencing to reduce wind-blown debris leaving the site.

## Slide 14: Precautionary measures (continued)
All demolition - dymchwel undertaken must have a minimal impact on the environment.
No burning of waste on-site - ar y safle.
.
Recycle and reuse construction waste on site; i.e. bricks can be used as hardcore/ ballast.
Site housekeeping, road sweeping etc.

## Slide 15: Ystyriaethau ecolegol - Ecological considerations
Gorlifdiroedd - Flood plains: building on flood plains has a knock-on effect of either flooding the properties situated there or having run-off water diverted into watercourses causing flooding and erosion downstream. By carefully planning (houses designed to be raised on stilts or elevated plots) and through water management, flood plains can still be built on if water holding ponds etc. are incorporated into the design.
Any new development or adaptation to existing property has the potential to impact on the environment in a variety of ways.

## Slide 16: Polisi ‘y llygrwr sy’n talu’ - Polluter pays policy
The Environmental Damage (Prevention and Remediation) Regulations 2009 manages and enforces the ‘polluter pays’ policy within Wales.
The principles behind this regulation is to ensure that those that produce pollution should bear the costs of managing it to prevent damage to the environment or to human health; it covers any pollutants that are released into the air, water or on land.
To avoid prosecution or heavy fines, responsible companies adopt a series of procedures of ‘precaution’ and ‘preventive’ measures and have a ‘rectifying at source’ emergency procedure that stops any spills, accidental discharges etc. impacting on the environment.

## Slide 17: Egwyddorion cynaliadwyedd - Principles of sustainability
Within the developed world greater responsibility is now focused on reducing waste, protecting natural resources and reducing the carbon footprint of and the release of greenhouse gases from new and existing developments.
To reduce the use of fossil fuels and the damage their extraction causes to the natural environment (such as impact on local ecosystem, impact on plants and animals within the effected ecosystems), along with the carbon and toxic waste produced from burning fossil fuels, renewable energy sources and better insulation are being used. These help to reduce the energy used and wasted.

## Slide 18: Cadwraeth ecosystemau - Conservation of ecosystems
Legislation is in place to protect the natural environment from development.
Areas containing rare and endangered species of fauna and flora are exempt from development. Any breaches will result in prosecution.
Trees, shrubs and hedgerows are not allowed to be removed during the breeding season as nesting birds will be disturbed. Roosting, feeding and migration routes are also protected.
Land that might have any protected species living on it must be surveyed before any groundwork commences, and precautions implemented so as not to disturb them.

## Slide 19: Rywogaethau gwarchodedig - Protected species
Mamaliaid - Mammals: bats, badgers, water voles and dormice.
Ymlusgiaid - Reptiles: smooth snake, grass snake, adder, common lizard, sand lizard and slowworm.
Amffibiaid - Amphibians: great crested newt and pond frog.
Adar - Birds: most species
Planhigion - Plants: Snowdon lily, Black mountain hawkweed, Riddelsdell’s hawkweed.

## Slide 20: Renewable/sustainable energy sources (continued)
Solar: solar panels work by absorbing sunlight with photovoltaic cells that generate direct current electricity that is converted to alternating current to be used in the home.
Gwynt - Wind: wind turbines work by harnessing the energy from the wind turning the turbines blades; these are connected to a generator that produces electricity.
Hydro: a hydro turbine works in a similar way to a wind turbine, but the energy is taken from moving water rather than wind.

## Slide 21: Renewable/sustainable energy sources (continued)
Ffynhonnell aer - Air source: air source heat pumps work by absorbing heat from the air in a fluid and running it through a compressor, which increases the temperature of the water which can then be used to heat the home or as hot water.
Ffynhonnell y ddaear - Ground source: these work the same as air source heat pumps, but in this case the heat is taken from pipes sank into the ground.

## Slide 22: Inswleiddio - Insulation
Ynni - Energy use is significantly reduced through the use of insulation lofts, brick cavities, ground floors, with slab or roll insulation and widows and doors with double/ triple glazing, K glass and draught excluders. All these help to save natural resources and money.

## Slide 23: Arbed dŵr - Water conservation
Most modern appliances are water efficient by design. But water use can be reduced in several ways.
Casglu dŵr glaw - Grey water harvesting: rainwater is collected and stored. This is used to flush toilets, so it does not have to be drinking quality.
Dŵr glân - Clean water that is used for washing and food preparation is collected as grey water and used to top up harvested water or as irrigation watering for the garden.

## Slide 24: Rheoli dŵr gwastraff - Wastewater management
Pre-1920 properties had a mixed drainage system. Post-1920 properties have a split system with surface water going directly to a local water source and foul water been taken to the local treatment plant.
It is illegal - anghyfreithlon to deliberately mix foul with surface as it will pollute the local stream or rivers with human waste or chemicals.
Notes: Redraw

## Slide 25: Optimising site potential and building space
By careful and considerate planning, new developments can maximise the number of properties on a single plot by reducing the footprint of each home via building them closer together and designing overall structures/ rooms that make use of commercially available sizes of materials.

## Slide 26: Designing waste out of projects
Brics, blociau, pren - Bricks, blocks, timber and sheet material all come in standard sizes. To save waste, houses are often designed so that the outside walls are equally dividable by the length of a brick.
Ceiling heights match the length of plasterboards and partitions are built to accommodate the width of plasterboards. Timber is commercially available in increments of 300mm from 2.1m, so lengths can be ordered that reduces the amount of waste.

## Slide 27: Deunyddiau cynaliadwy - Sustainable materials
Conventional building materials | Green building materials
Structural Bricks, concrete and steel | Structural Timber frame, stone and straw bale, fly ash bricks, glass
Insulation Foam boards and Therma-wrap | Insulation Sheep's wool, cellulose insulation ( made from recycled newspapers)
Flooring Concrete, wood-based laminates and tiles | Flooring Stone, bamboo, corkwood and timber from a sustainable source

## Slide 28: Danfon a storio - Delivery and storage
Planning when materials are required and estimating how much is required allows the ordering of materials in a phased delivery, which saves on storage and avoids potential damage and waste. The correct storage of materials also reduces the likelihood of materials being damaged. Using FIFO (First In First Out) with perishable materials such as plaster, cement etc. again will reduce waste.

## Slide 29: The hierarchy of waste and sustainability
There are many factors that need to be considered when selecting materials used in the construction process, including the whole life cycle of the materials and the impact this has on the natural environment.

## Slide 30: Site waste management plan (SWMP)
What are the waste actions that the SWMP covers? The waste hierarchy consists of four main methods of handling waste:
Ailddefnyddio - Reuse – in other projects, or in another phase of the same project.
Ailgylchu - Recycle – such as turning the results of demolition into recycled aggregate for use in roads.
Adfer - Recover – for example, recovery of mercury and other non-ferrous metals from end-of-life industrial sites, or the cleaning and re-selling of bricks during demolition.
Gwaredu - Dispose – to landfill, the final and least preferred option within any waste management hierarchy.

## Slide 31: Gwaredu gwastraff - Waste disposal
Timber should be placed in a timber-only skip where it can go to be recycled into sheet materials or, if unsuitable for repurposing, pulped to use as fuel in a biomass plant.
Metal should again go into a metal-only skip so it can easily be sorted and recycled. Separating waste will reduce the amount going to landfill, saving money and landfill taxes.

## Slide 32: Waste disposal
Plasterboard needs to be disposed of separately, as if it is mixed with organic material and added to landfill it gives of hydrogen sulphide (H2S). This is a colourless gas that smells like rotten eggs and is extremely poisonous, corrosive and flammable - fflamadwy.

## Slide 33: Plans and documents used in construction
Types of drawings and scales:
Scale | Use
1:1 | Full size (used for rods)
1:2 1:5 1:10 | Building details
1:20 1:50 1:100 1:200 | Plans, elevations and sections
1:200 1:500 1:1250 | Site plans
1:1250 1:2500 | Location plans
Mathau o luniadau a graddfeydd:

## Slide 34: Cynllun bloc/cynllun lleoliad - Block plan/location plan
Block plan/ location plans identify the proposed site in relation to the surrounding area. These are usually drawn at a scale of 1:2500 or 1:1250.

## Slide 35: Cynllun o’r safle - Site plan
Site plans show more detail than a block plan and normally include boundaries of the plot, the position and dimensions of buildings within the plot, position of existing and new trees, position of manholes and drain runs and other services. These are usually drawn at a scale of 1:500 or 1:200.

## Slide 36: Cynlluniau llawr - Floor plans
Floor plans show the layout, size and position of rooms from above, showing the location of fitted units etc. and the position and opening of doors.

## Slide 37: Lluniadau manwl - Detailed drawings
Detailed drawings provide a pictorial view of how components join together, scales range from 1:10 to 1:20 with 1:1 being the recognised scale for setting out details.
Jamb
Head
Meeting stiles
Cill

## Slide 38: Range drawings
Range drawings give a pictorial view of the available items or components available within a specific range. The most common examples are doors, windows, kitchen units and ironmongery - drysau, ffenestri, unedau cegin a gwaith haearn.

## Slide 39: Projection types
There are a number of projection types used for drawing production. These are:
Orthograffig - Orthographic
Acsonometrig - Axonometric
Isometrig - Isometric
Persbectif - Perspective

## Slide 40: Tafluniad orthograffig - Orthographic projection
This 3D image shows how each 2D elevation is drawn in an orthographic projection.
E
F
End elevation
Front elevation
Plan view
First angle orthographic

## Slide 41: Orthographic projection (continued)
Orthographic projection is a drawing where the front elevation of a structure has the plan view directly below it.
Side or end elevations are shown directly next to each side of the front elevation.
Elevation ‘A’
C
A
B
‘X’
Elevation ‘B’ ‘X’
Plan
Elevation ‘C’
Section ‘X–X’
Orthographic projection

## Slide 42: Perspective, isometric and axonometric projections
Persbectif - Perspective are where the lines converge to a vanishing point with the detail at the rear of the drawing often difficult to see.
Isometrig - Isometric is a 3D projection technique. Lines are drawn at 30º.
Acsonometrig - Axonometric is a 3D projection technique. Lines are drawn at 45o.

## Slide 43: Tafluniad isometrig - Isometric projection
In isometric projection, one corner of the structure is represented as closer to the viewer, providing a more ‘realistic’ view.
90°
30°
Base line
Isometric projection
Notes: Check with author

## Slide 44: Diagramau weirio - Wiring diagrams
Used by electricians - trydanwyr, these are are simple visual representations of the layout of an electrical system. They show how wires are interconnected and where fixtures and components are connected within the system.
25 mm2 tails
16 mm2 earthing conductor
10 mm2 main protective bonding
20 A radial
2.5 mm2 6242Y
20 A radial
2.5 mm2 6242Y
32 A ring ﬁnal
2.5 mm2 6242Y
32 A cooker 6 mm2 6242Y
6 A lighting 1.5 mm2 6242Y
6243Y
Spur
Branch
Typical wiring drawing

## Slide 45: Hatchings, symbols and abbreviations
All plans and drawings show hatchings, symbols and abbreviations. These provide additional detail and information to the drawing, while keeping the plan clear and legible.
Hatchings are used to show the different materials used in a specific location.
Symbols represent a specific item.
Abbreviations are shortened versions of the full name of an item.
Croeslinellau, symbolau a byrfoddau

## Slide 46: Abbreviations
Item | Abbreviation | Item | Abbreviation
Air brick | AB | Air conditioning | AC
Brickwork | BWK | Blockwork | BLK
Concrete | CONC | Cupboard | CPD
Damp proof course | DPC | Damp proof membrane | DPM
External | EXT | Expanded polystyrene | EPS
Foundation | FDN | Finished floor level | FFL
Hardwood | HWD | Hardcore | HC
Internal | INT | Insulation | INSU
Plasterboard | PBD | Polyvinyl chloride | PVC
Rainwater pipe | RWP | Softwood | SWD
Stainless steel | SS | Tongue and groove | T&G
Byrfoddau -

## Slide 47: Hatchings and symbols
Sawn timber (unwrot) - Pren wedi’i lifio (heb ei weithio) | Concrete - Concrid
Stonework - Gwaith cerrig | Earth (subsoil) - Pridd (is-bridd)
Top Bottom Side Hinging position of windows | Stairs up Stairs down Stairs up and down

## Slide 48: Hatchings and symbols
Insulation - Inswleiddiad | Brickwork - Gwaith brics
Cement screed -Ffyn lefelu sment - | Damp proof course/ membrane
Timber – softwood. Machined all round (wrot) | Timber – hardwood. Machined all round (wrot)

## Slide 49: Hatchings and symbols (continued)
Sink | Sinktop | Wash basin - Basn ymolchi | Bath | Shower tray - Llawr cawod
WC - Toiled | Window | Door - Drws | Radiator - Gwresogydd | Lamp
Switch | Socket | North symbol |  | 

## Slide 50: Rhestr - Schedule
A schedule shows repetitive information (e.g. covering all the information for different doors etc.). When used alongside a floor plan it shows all the information required to select the correct component to be fitted.
Example of a door schedule
Master Internal Door Schedule |  |  |  |  |  |  | 
Ref: | Door size | S.O. width | S.O. height | Lintel type | FD30 | Self closing | Floor level
D1 | 838 ×1981 | 900 | 2040 | BOX | Yes | Yes | GROUND FLOOR
D2 | 838 ×1981 | 900 | 2040 | BOX | Yes | Yes | GROUND FLOOR
D3 | 762 ×1981 | 824 | 2040 | BOX | No | No | GROUND FLOOR
D4 | 838 ×1981 | 900 | 2040 | N/A | Yes | No | GROUND FLOOR
D5 | 838 ×1981 | 900 | 2040 | BOX | Yes | Yes | GROUND FLOOR
D6 | 762 ×1981 | 824 | 2040 | BOX | Yes | Yes | FIRST FLOOR
D7 | 762 ×1981 | 824 | 2040 | BOX | Yes | Yes | FIRST FLOOR
D8 | 762 ×1981 | 824 | 2040 | N/A | Yes | No | FIRST FLOOR
D9 | 762 ×1981 | 824 | 2040 | BOX | Yes | Yes | FIRST FLOOR
D10 | 762 ×1981 | 824 | 2040 | N/A | No | No | FIRST FLOOR
D11 | 686 ×1981 | 748 | 2040 | N/A | Yes | No | SECOND FLOOR
D12 | 762 ×1981 | 824 | 2040 | BOX | Yes | Yes | SECOND FLOOR
D13 | 762 ×1981 | 824 | 2040 | 100 HD BOX | Yes | Yes | SECOND FLOOR
D14 | 686 ×1981 | 748 | 2040 | N/A | No | No | SECOND FLOOR

## Slide 51: Manyleb - Specifications
A specification is a written document that specifies certain details of the product being produced or assembled that can not be shown via a drawing. Examples include:
the species of timber to be used
the grade of timber to be used
fire rating
the type of glass that will be used
the finish that is to be applied
the quality of the workmanship.

## Slide 52
Any questions?