## Slide 1: PowerPoint 8: Off-site construction 1 - Adeiladu oddi ar y safle 1
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 2: Introduction to off-site construction
Off-site construction means that products are manufactured in
a factory and then transported and assembled and installed on-site.
Off-site construction products include:
Components - Cydrannau
Subassemblies - Is-osodiadau
Panels - Paneli
Pods - Podiau

## Slide 3: Introduction to off-site construction - Cyflwyniad i adeiladu oddi ar y safle
Off-site construction is a Modern Method of Construction (MMC) that aims to optimise the construction process. It is also known as OSM (Off Site Manufacture) or prefabrication.
Learn more about off-site construction from the videos below:
https://www.youtube.com/channel/UCw8NH6SuOs77wOo1YCL5Vmw
https://youtu.be/Hgq14W6v2vU

## Slide 4: Benefits of off-site construction - Manteision adeiladu oddi ar y safle
The benefits of off-site construction are:
a controlled production environment
consistent production process
production is not impacted by weather conditions, as on-site
quicker production process
less waste.

## Slide 5: Benefits of off-site construction - Manteision adeiladu oddi ar y safle
Sustainability - Cynaliadwyedd
The factory environment provides a cleaner and safer place of work. The production is controlled, making it easier to achieve environmental performance criteria.
Economic: achieved by the speed of production.
Social: achieved by the reduced risk to construction personnel than on-site.
Environmental: achieved with the higher quality products and resulting performance (e.g. insulation) .
                Off-site fundamentals Slides by Dr Mila Duncheva and Carola Calcagno, Edinburgh Napier University

## Slide 6: Benefits of off-site construction
                Offsite fundamentals Slides by Dr Mila Duncheva and Carola Calcagno, Edinburgh Napier University
Value - Gwerth
The factory environment guarantees higher quality, more predictable product behaviour, better performance and little defects, with consequent higher customer satisfaction.
Technical: the factory environment guarantees higher quality, more predictable product behaviour.
Quality: quality control is achieved by the regularised and dry environment, producing components with predictable better performance and fewer defects.
Customer satisfaction: a consequence of improved quality within an efficient process.

## Slide 7: Benefits of off-site construction
Efficiency - Effeithlonrwydd
The factory environment provides greater efficiency.
Time: savings can be made, carrying out site operations at the same time as manufacturing off-site components.
Waste: reduction in the production of waste can be achieved when mass producing components accurately with fewer defects.
Flexibility: a consequence of improved quality, within an efficient (possibly automated) process.
                Offsite fundamentals Slides by Dr Mila Duncheva and Carola Calcagno, Edinburgh Napier University

## Slide 8: Materials used in off-site construction: timber
                Offsite fundamentals Slides by Dr Mila Duncheva and Carola Calcagno,
                Edinburgh Napier University
Timber products are available in the form of:
sub-assemblies - is-osodiadau
panels
engineered timber products
volumetric units - unedau cyfeintiol
Benefits | Challenges
High environmental credentials (e.g. carbon capture) | Special attention needs to be taken when designing with timber, because of its natural properties, which can result in differential movement due to changes in its moisture content
Good thermal performance and air-tightness | Fire regulations prescribing the use of non-combustible materials can be a barrier

## Slide 9: Materials used in off-site construction: concrete
                Offsite fundamentals Slides by Dr Mila Duncheva and Carola Calcagno,
                Edinburgh Napier University
Concrete is available in pre-cast
components
sub-assemblies - is-osodiadau
panels
volumetric units.
Benefits | Challenges
Removes the need for ‘wet’ construction with associated curing times | Components are heavy: associated health and safety risks
Opportunity for buildings with special security and durability requirements (prisons, infrastructures, etc) | Usually includes only the concrete structure; the remaining work needs to be arranged and synchronised on site
 | Transportation issues; remote locations can become a barrier

## Slide 10: Materials used in offsite construction: steel
                Offsite fundamentals Slides by Dr Mila Duncheva and Carola Calcagno, Edinburgh Napier University
Steel is available in:
components - cydrannau
many shapes and forms; due to its structural performance.
Benefits | Challenges
Particularly suitable for large-scale projects where large spans need to be covered | Transportation can become a challenge
‘Dry’ method: results in a clean work environment and a quick onsite assembly | Components cannot be easily modified
 | Steel has a high thermal conductivity: detail design and insulation installation need to be particularly accurate to avoid thermal bridging
 | Corrosion is a risk

## Slide 11
Unrhyw gwestiynau?
Any questions?

## Slide 12: PowerPoint 9: Off-site construction 2 - Adeiladu oddi ar y safle 2
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 13
Types of off-site construction: sub-assemblies
Sub-assemblies are a combination of components that are manufactured off-site. They may form panelised or volumetric systems and require delivery, storage and skilled assembly as part of the construction programme.
I-joists
Steel elements - Elfennau dur
Roof systems
Floor systems
Stairs - Grisiau
Doors
Windows - Ffenestri

## Slide 14
Types of off-site construction: components
Components are constituent parts of a building made as independent units. They are usually self-contained and sourced from one supplier.
The term is used for:
fasteners and fixings – caewyr a gosodiadau
metal, meshwork and seals
adhesives - gludiau
vapour barriers
breather membranes - pilenni anadlu
cladding
curtain walling panels.

## Slide 15
Types of off-site construction: panelised system - Mathau o adeiladu oddi ar y safle: system banel
      Open system - System agored
      Made with structural elements only, non-insulated, occasionally one side is sheeted.
      Closed system - System gaeedig
      Insulated, sheeting on both sides and a service zone.
      SIPs (Structural Insulated Panels)
      Variation of closed panels; solid insulation ‘sandwiched’ with two layers of oriented strand board (OSB) .

## Slide 16
Types of off-site construction: volumetric units - Mathau o adeiladu oddi ar y safle: unedau cyfeintiol
Volumetric units are three-dimensional units that enclose usable space.
Typically, they are fully finished internally and can also be finished externally.
They can also be non-structural – pods: used for bathrooms, plant rooms and roof-top services.

## Slide 17
Types of off-site construction: volumetric units
Panel assembly - Creu paneli. Before the assembly of the volumetric unit, the panels are manufactured in a similar way to a closed panel factory.
Unit assembly - Cydosod yr uned. The panels are placed to form floor, walls and roof of the volumetric unit. At this stage, some additional operations are completed, such as the installation of insulation.
Windows and doors - Ffenestri a drysau. The building envelope is completed with the installation of windows and doors.
MEP systems installation - Gosod systemau MEP. MEP stands for mechanical, electrical and plumbing. These systems are installed by a skilled worker.

## Slide 18
                Source:
Types of off-site construction: volumetric units
Internal finishes - Gorffeniad mewnol. The volumetric units are completed internally with wall linings, such as plasterboard and tiles, and with flooring systems, such as parquet. In some cases, furniture and electric appliances are also installed.
External finishes – Gorffeniad allanol. The volumetric elements may need to be completed with a breather membrane and then clad.

## Slide 19
These are combinations of more than one system, using a mixture of sub-assemblies, panelised and/or volumetric systems.
Types of off-site construction: hybrid systems - Mathau o adeiladu oddi ar y safle: systemau hybrid

## Slide 20
Unrhyw gwestiynau?
Any questions?

## Slide 21: PowerPoint 10: Off-site construction 3 - Adeiladu oddi ar y safle 3
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 22: Off-site construction case study: Wernick Buildings -
The ‘Y Twyni’ building is a modular teaching block at Swansea University’s Bay campus designed and built by Wernick Buildings Ltd.
The following information is reproduced with kind permission from Wernick Buildings. For more information visit Modular Building Manufacturer UK | Wernick
Astudiaeth achos adeiladu oddi ar y safle: Wernick Buildings

## Slide 23
2500–3000m² flexible lecture theatre
Relocatable solution required for the building – adeilad.
Big open plan spaces to accommodate up to 500 persons per room
Tall ceilings with exposed services and AV
Aesthetically pleasing building which blends into surroundings
Low energy and easily upgradable to positive energy – ynni.
Firmly fixed deadline of November 2019
Simple and speedy procurement process
The client’s brief – established November 2018

## Slide 24: Modular system - System Fodiwlaidd
To get the most from a modular solution, engage early with your modular contractor and bring them into the team at RIBA stage 1 or 2.
This allows the building to be designed around the modular system, maximising design, manufacture and construction efficiencies and leading to a hugely reduced programme when compared to traditional construction as well as improved value for money - gwerth am arian.
                Source: Wernick

## Slide 25
Is modular or offsite construction an option?
Appoint design team, including modular manufacturer
Design team work with modular manufacturer to maximise the benefits of offsite
Design team oversee manufacture both on and offsite
The full benefits of modular construction are realised
Early engagement – the key to modular success

## Slide 26: Key benefits of Wernick modular buildings - Prif fanteision adeiladau modiwlaidd Wernick
Up to 50% shorter build times than traditional construction
Lower overall project cost compared to traditional construction
Programme certainty due to offsite manufacture and concurrent working
Factory conditions improve health and safety, accuracy and quality
Design for Manufacture and Assembly (DfMA) with near zero waste for modular production
Less noise, waste and disruption to site
Fully non-combustible wall panel system
Higher thermal mass compared to traditional light gauge steel modular

## Slide 27: Wernick module design - Dyluniad modiwlau Wernick
Module lengths from 6m to 15m long
Maximised internal ceiling heights
Up to 3300mm to underside of structure
Max. 3600mm to underside of soffit
Multi-storey clear internal spans to 12m
External wall panels
Low U- values (thermal transmittance) and fully non-combustible systems available
High performance floors
Concrete and more sustainable cross-laminated timber (CLT) floors
6-storey capability

## Slide 28: Programme - Rhaglen
Enquiry received – November 2018
Planning permission submitted – December 2018
Order placed – March 2019
Start on site – June 2019
Module delivery – July 2019
Handover – November 2019

## Slide 29: Building energy - Ynni adeilad
Low U-values, best practice air tightness
The system is warm frame and virtually all repeating thermal bridges have been removed, helping to produce a low energy solution.

## Slide 30: BREEAM Excellent proven system
The system meant that near-zero waste was generated in the module manufacture. The 60 modules of the Swansea project weighed around 8 tons each, making the overall modular structure of the building approximately 480 tons - tunnell.
The manufacture of the 60 modules generated only 650kg of waste, around 0.15% total waste. Figures for traditional construction are often quoted as high as 10%.

## Slide 31: BREEAM Excellent proven system
BREEAM Excellent target 19kg/m2
Wickford Head Office: 1,000sqm two storey office
Module manufacture: 262 kg = 0.262 kg/m2
Factory module fit out: 4,071 kg = 4.071 kg/m2
Site fit out: 11,080 kg = 11.08 kg/m2
Total waste generated - Cyfanswm y gwastraff a gynhyrchwyd = 15.151 kg/m2
Percentage of waste recycled and diverted from landfill = 98%

## Slide 32: Module delivery - Darparu'r modiwlau
Using a modular solution allowed concurrent working. So, while the site was being prepared and foundations laid, the 60 modules were being manufactured 10 miles away at the Wernick factory.
Site work took place during building manufacture
Modules manufactured at specialist manufacturing plant

## Slide 33: Off-site construction case study: Wernick
Delivery of the modules took place over five days. They were craned into place and sealed up prior to the start of the fit out.
The system can accommodate a temporary roof protection system, meaning that the building did not need scaffolding, again saving time and money.

## Slide 34: Completed project - Y prosiect wedi’i gwblhau
360 virtual tour - Swansea University ‘Y Twyni’ Building • Wernick

## Slide 35
Unrhyw gwestiynau?
Any questions?