## Slide 1: PowerPoint 1: Introduction to the unit - Cyflwyniad i’r uned
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 2: Introduction
By the end of this unit you will:
  know the use of Building Information Modelling (BIM) within construction and the built environment
  know about emerging technologies and materials
  know about offsite construction - adeiladu oddi ar y safle.

## Slide 3: How does construction need to change?
In Imagining construction’s digital future McKinsey & Company identified five trends that will shape construction and capital projects going forward:
Higher-definition surveying and geolocation Rapid digital mapping and estimating
Next-generation 5D building information modelling Design platform for the future
Digital collaboration and mobility Moving to paperless projects, from the office to the workforce
The Internet of Things and advanced analytics Intelligent asset management and decision making
Future-proof design and construction Designing with materials and methods of the future - dulliau’r dyfodol.
Imagining-constructions-digital-future.pdf (mckinsey.com)

## Slide 4: Building Information Modelling: What is it?
    Building Information Modelling (BIM) is a 3D model-based process that allows design and construction teams to collaborate efficiently. Watch the video below to find out more about the BIM model.

## Slide 5: What is the BIM process?
      Plan - Cynllunio
        Capture real world data of environments
      Design - Dylunio
        Use the 3D captured data to inform design
      Build - Adeiladu
        The BIM specification and logistic data is shared with trades and contractors
      Operate - Gweithredu
        BIM data is used for operation and maintenance of finished assets
                Source https://www.rmjm.com/building-information-modelling-an-introduction-to-bim

## Slide 6: BIM levels - Lefelau BIM
Different projects use different ‘levels of maturity’. Each level has its own criteria. Levels go up to 4D, 5D and 6D.
Level 0 BIM: No collaboration, using 2D CAD and working with drawings.
Level 1 BIM: Using 2D CAD for drafting production information.
Level 2 BIM: All parties use 3D CAD models and share information through a common file format.
Level 3 BIM: All parties use one shared 3D model, easily accessible to all.

## Slide 7: Key terminology - Termau allweddol
  Digital Plan of Work - Cynllun Gwaith Digidol
  Common Data Environment (CDE)
  Soft landings - Glaniadau meddal
  Project Information Modelling (PIM)
  Asset Information Modelling (AIM)
  Construction Operations Building Information Exchange (COBie)
  Employer’s Information Requirements (EIR)
  BIM Execution Plan (BEP) - Cynllun Gweithredu BIM (BEP)
  BIM Protocol
  Employer within the supply chain

## Slide 8: Emerging technologies and materials in construction
      Immersive technologies - Technolegau Ymgolli
        (VR) Virtual Reality
        (MR) Mixed Reality
        (AR) Augmented Reality

## Slide 9: Emerging technologies and materials in construction
      3D printing of buildings
        For example, using concrete
      Argraffu adeiladau mewn 3D
        Er enghraifft, defnyddio concrit

## Slide 10: Emerging technologies and materials in construction
      Evolving materials include:
        Graphene
        Surface coverings
        Ventilated building materials
        Liquid roof - To hylif
        Transparent aluminum
        Self-healing concrete
Notes: What do we mean by emerging technologies?
Task: internet search on the headings.

## Slide 11: Off-site construction - Adeiladu oddi ar y safle
      The pre-assembly of elements, components or modules in a factory, before installation on-site. Also known as prefabrication or off-site manufacturing, it is an element of modern method of construction (MMC).
Notes: Off-site is a construction method that adds substantial value to a product via the manufacture and pre-assembly of components, elements or modules in a factory, before installation into their final location.

## Slide 12: The benefits of off-site construction
                Offsite fundamentals by Dr Mila Duncheva and Carola Calcagno, Edinburgh Napier University
Dr Mila Duncheva and Carola Calcagno, Edinburgh Napier University, have identified the following benefits of off-site construction:
Value:
Technical
Quality
Customer satisfaction
Efficiency:
Time
Waste
Flexibility
Sustainability:
Social
Economic
Environmental
Cynaliadwyedd:
Cymdeithasol
Economaidd
Amgylcheddol
Effeithlonrwydd:
Amser
Gwastraff
Hyblygrwydd
Gwerth:
Technegol
Ansawdd
Bodlonrwydd cwsmeriaid
Notes: Off-site is a construction method that adds substantial value to a product via the manufacture and pre-assembly of components, elements or modules in a factory, before installation into their final location. Off-site can be also referred to as OSM, short for Off-Site Manufacture. Off-site construction is considered a way to achieve MMC, however implementing offsite construction does not guarantee the achievement of MMC process efficiencies. Off-site systems can have different levels of enhancement in the factory, or valued added in the factory environment. According to Miles and Whitehouse, for example, a project can be considered off-site if less than 40% of its value is added on-site.
Authors: Dr Mila Duncheva, Carola Calcagno, and Victor Henquel, Centre for Offsite Construction + Innovative Structures, Edinburgh Napier University, Edinburgh
Offsite Construction

## Slide 13: Types of off-site construction - Mathau o adeiladu oddi ar y safle
      Components or sub-assemblies
      Panelised systems
      Volumetric systems
      Hybrid systems
Notes: Authors: Dr Mila Duncheva, Carola Calcagno, and Victor Henquel, Centre for Offsite Construction + Innovative
Structures, Edinburgh Napier University, Edinburgh
Components/sub assembles
Pre-manufactured elements that don’t fall in the previous categories
Stairs
Doors
Windows
I-joists
Steel elements
Panelised
Planar unit which may or may not have a structural function
Open: usually when non-insulated with only the structural elements and if applicable sheeting on one side
Closed: include insulation, sheeting on both sides and a service zone; can be furtherly enhanced with the addition of internal lining, external cladding, windows and doors and services
SIPs (Structural Insulated Panels): variation of closed panels; solid insulation ‘sandwiched’ with two layers of OSB.
Volumetric
They represent three-dimensional units that enclose usable space.
Typically are fully finished internally and can also be finished externally
Can also be non-structural – pods: used for bathrooms, plant rooms and roof-top services
Hybrid
Generic term covering a wide variety of construction techniques, particularly where different systems and/or materials are used in combination to fulfil a specific function

## Slide 14
Any questions?
https://www.offsiteready.com/training-materials/digital-design
Watch the video below to find out about various digital design tools that can be used in offsite construction.

## Slide 15
Unrhyw gwestiynau?
Any questions?

## Slide 16: PowerPoint 2: Building Information Modelling 1 - Modelu Gwybodaeth Adeiladu 1
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 17: Building Information Modelling: what is it?
      Building Information Modeling (BIM) is an intelligent 3D model-based process that gives architecture and construction staff the insight and tools to more efficiently plan, design, construct and manage buildings and infrastructure projects.
    https://images.unsplash.com/photo-1568952433726-3896e3881c65?

## Slide 18: What is the BIM process? - Beth yw'r broses BIM?
      Plan - Cynllunio
        Capture real world data of environments
      Design - Dylunio
        Use the 3D captured data to inform design
      Build - Adeiladu
        The BIM specification and logistic data is shared with trades and contractors
      Operate - Gweithredu
        BIM data is used for operation and maintenance of finished assets
                Source https://www.rmjm.com/building-information-modelling-an-introduction-to-bim

## Slide 19: When do we use BIM? - Pryd fyddwn ni’n defnyddio BIM?
Within a project timeline it’s key to have regular exchange of data at strategic points using a common data environment (CDE).
In April 2016, it was made a mandatory requirement for all publicly tendered projects in the UK to operate a level 2 BIM.

## Slide 20: When do we use BIM?
      We use BIM throughout the life cycle of a building:
        programming/inception
        conceptual design
        detailed design - dylunio manwl
        analysis
        Documentation - dogfennau
        fabrication
        construction
        logistics
        operation and maintenance
        demolition - dymchwel
        renovation.

## Slide 21: How to ensure BIM is implemented
It was made a mandatory requirement for all publicly tendered projects in the UK to operate a level 2 BIM.
Commitment to the process must be demonstrated by all those involved.
The project partners and their respective team members must have the digital tools and technology (hardware) and data infrastructure (software) platforms to design, analyse, construct and operate the building asset. When used together, these are called the BIM workflow.
In many cases, extra training may be needed for each person utilising and modifying the model - addasu’r model.

## Slide 22: Benefits of the BIM process - Manteision proses BIM
      Plan: Capturing real world data of environments ensures accurate coordination and collaboration.
      Design: Using the 3D captured data to inform design gives quicker and higher levels of customisation and flexibility, and optimisation of schedule and cost.
      Build: The BIM specification and logistic data allows for quick conflict detection and risk mitigation.
        Operate: Using the BIM data makes schedules for maintaining the asset for its lifecycle easier.
                Source https://www.rmjm.com/building-information-modelling-an-introduction-to-bim
Notes: https://www.rmjm.com/building-information-modelling-an-introduction-to-bim
Better design: building proposals can be rigorously analysed, simulations performed quickly and performance benchmarked, enabling improved and innovative solutions.
Controlled whole-life costs and environmental data: environmental performance is more predictable, and lifecycle costs are better understood.
Better production quality: documentation output is flexible and exploits automation.
Automated assembly: digital product data can be exploited in downstream processes and used for manufacturing and assembly of structural systems.
Better customer service: proposals are better understood through accurate visualisation.
Lifecycle data: requirements, design, construction and operational information can be used in facilities management.

## Slide 23: Definition of BIM levels - Diffinio lefelau BIM
Different projects use different ‘levels of maturity’. Each level has its own criteria:
2
1
0
3
Level 3 BIM: All parties use one shared 3D model, easily accessible to all.
Level 2 BIM: All parties use 3D CAD models and share information through a common file format.
Level 1 BIM: Using 2D CAD for drafting production information.
Level 0 BIM: No collaboration, using 2D CAD and working with drawings.
Notes: Level 0 BIM
Level 0 refers to no collaboration whatsoever. This level is generally in operation when using 2D CAD and working with drawings/digital prints.
Level 1 BIM
Level 1 usually means that 3D CAD is being used for concept work, while 2D CAD is used for drafting production information. A large number of firms are at level 1, which doesn’t tend to involve much collaboration, with each stakeholder publishing and managing their own data.
Level 2 BIM
In April 2016, it was made a mandatory requirement for all publicly tendered projects in the UK to operate a level 2 BIM. At level 2, all parties involved utilise 3D CAD models, and the way stakeholders exchange their data varies from other levels.
Information is shared through a common file format, and all firms involved combine this with their own data. This saves time and costs, and reduces the need for rework.
Level 3 BIM
Level 3 means that everyone on the project uses one, shared project model instead of working on their own 3D model independently. This makes it the most collaborative level among the first four. This ‘open BIM’ approach exists in a central environment, making it easily accessible and editable by everyone.

## Slide 24
Any questions?
Unrhyw gwestiynau?

## Slide 25: PowerPoint 3: Building Information Modelling 2 – Modelu Gwybodaeth Adeiladu 2
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 26: BIM dimensions – to get a fuller understanding of a project
BIM dimensions 4D, 5D and 6D can all occur within a BIM level 2 workflow.
4D (construction sequencing)
      Scheduling data-time related information linked to the visual model - model gweledol.
      This helps with planning, designing and constructing, ensuring a safely, logically and efficiently sequenced project.
      Creating a mockup of the assets in a model for feedback from the design team and client avoids costly mistakes made later, on-site.

## Slide 27: BIM dimensions – to get a fuller understanding of a project
BIM dimensions 4D, 5D and 6D can all occur within in a BIM level 2 workflow.
2. 5D (cost)
      Costs are linked to the graphic model. Allowing an easily trackable predicted spend.
3. 6D BIM (project lifecycle information)
      Information to support facilities management and operation – gweithredu.
BIM DIMENSIONS

## Slide 28: Key terminology: Common Data Environment (CDE)
  This is the single source used to collect and manage information, documentation: the graphical model and non-graphical data gathered by the whole project team. CDE is a collaborative environment where all project team members can communicate. This helps avoid mistakes and duplication.
  Below are the five current leaders in open source CDE software:
        https://www.autodesk.com/bim-360/
        https://connect.trimble.com/
        https://www.bentley.com/en/products/brands/projectwise
        http://www.procore.com/
        https://www.bimplus.net/en/
        For more information on CDEs view this video:
Notes: The common data environment (CDE), is the single source of information used to collect, manage and disseminate documentation, the graphical model and non-graphical data for the whole project team (i.e. all project information whether created in a BIM environment or in a conventional data format
https://www.designingbuildings.co.uk/wiki/Common_data_environment_CDE
https://www.planbim.io/blog/2020/04/07/the-top-5-common-data-environments-cde-for-bim/
Software examples on cloud

## Slide 29: Key terminology: soft landings
Soft landings brings together best practice at all stages of a project - prosiect.
Soft landings is a process for a gradual handover of a new building, where a period of professional aftercare by the project team is a contractual client requirement - cytundebol y cleient.
It is planned for and carried through from project inception, through design development and review, pre handover, initial aftercare and for up to three years post-completion.

## Slide 30: Key terminology: digital plan of work
Employers are responsible for defining what is required at each stage of a construction project in the form of a digital plan of work (DPoW).
This plan covers the entire project timeline, from developing a strategy to managing the built asset - ased adeiledig.
Tasks must be carried out sequentially to ensure effective collaborative working, using standardised processes and agreed standards and methods such as the RIBA (The Royal Institute of British Architects) Plan of Work or using the BIM toolkit developed by the NBS (National Building Specification) to help develop a digital plan of work.
  style for sources.

## Slide 31: Key terminology: Project Information Model (PIM)
  PIM is a subtype of Information Model developed during the design, production and construction (or renovation) phases of a project.
  At handover to the client, the Project Information Model (PIM) is the basis for the Asset Information Model (AIM) and so must be an accurate representation of what has been built and installed, and not only what the original designers intended.

## Slide 32
Any questions?
Unrhyw gwestiynau?

## Slide 33: PowerPoint 4: Building Information Modelling 3 – Modelu Gwybodaeth Adeiladu 3
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 34: What is an Asset Information Model (AIM)?
      An AIM is a model that can provide graphical and non-graphical data and information as well as metadata and documents describing procedures for the operational phase of the built asset.
      It may have been created from the existing PIM or from new information.
      It may describe the original design intent of the asset.
      It may include 3D models – modelau.
      It may link to information regarding ownership, surveys or rights and restrictions - hawliau a chyfyngiadau.
      It should include operation and performance information.
      It will be managed within the Common Data Environment (CDE).

## Slide 35: Construction Operations Building Information Exchange (COBie)
  ‘Construction Operations Building Information Exchange (COBie) is a non-proprietary data format for the publication of a subset of building information models (BIM) focused on delivering asset data as distinct from geometric information - gwybodaeth geometrig.
What is COBie? 29 October 2018 | by Dr Stephen Hamil

## Slide 36: Key terminology - Termau allweddol
  COBie holds the data for facility asset information delivery.
  Two types of assets are included in COBie: equipment and spaces.
  rum/.

## Slide 37: Employer’s Information Requirements (EIR)
The information required by the employer from their own team and suppliers.
Technical - Technegol
Details of software platforms
Data exchange format
Definitions of levels of detail
Standard methods and procedures, training
Management - Rheoli
Standards
Roles and responsibilities
Planning the work and data segregation
Clash detection process
Collaboration process
Model review process
Health and safety, Construction (Design and Management) Regulations 2015
System performance constraints
Compliance plan
Delivery strategy for asset Information
Commercial - Masnachol
Timing of data drops
Client’s strategic purpose
Defined BIM project deliverables
BIM – specific competence assessment

## Slide 38: BIM Execution Plan (BEP)
  The pre-contract BIM execution plan is a document prepared by potential suppliers outlining their proposals for meeting the Employer’s Information Requirements.
  The post-contract BIM execution plan is developed from the pre-contract BEP by the successful contracted suppliers, setting out how the Employer’s Information Requirements will be met, in full detail.

## Slide 39: BIM protocol
  The BIM protocol is a standardised legal agreement that can be included within construction contracts.
  Key objectives - Amcanion allweddol:
  To enable the production of the Building Information Model to be defined at agreed stages of the project.
  Supports collaborative working using common standards or working practices.
  Requires the appointment of an Information Manager.
  Download a copy of the 2nd Edition BIM Protocol at: bim-protocol-2nd-edition-2.pdf (cic.org.uk)
  style for sources.

## Slide 40
Unrhyw gwestiynau?
Any questions?