## Slide 1: Environmental Considerations
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 301: Understanding construction practice in Wales

## Slide 2: Environmental Considerations
Contaminated Sites
It is a statutory requirement for premises holding dangerous or toxic substance to be licensed.
In addition, the company must complete a risk assessment identifying the risks of the chemicals that they use, and the precautions required to minimize the risk.

## Slide 3: Contaminated Sites
The building regulations Approved Document C also details contaminants of land which may be naturally occurring or the results of previous land or building use.
Special precautions may be needed to treat these hazards and monitor potential long-term problems.
Some landfill sites produce large quantities of methane gas which should be adequately vented to the atmosphere in a suitable way to prevent explosion.

## Slide 4: Contaminated Sites
Radon gas created in grounds such as granite can permeate into buildings, and special precautions may be required to prevent this if development is anticipated on ground where this occurs.
The geology of the area should be familiar when dealing with this latter case and monitoring of gas discharges should be undertaken, if possible, over long periods.
Sites where the ground to be covered by the building is likely to contain contaminants may be identified at an early stage from planning records or from local knowledge of previous uses.

## Slide 5
POSSIBLE CONTAMINANTS AND ACTIONS |  | 
Signs of possible contaminants | Possible contaminant | Relevant action
Poor growth or absence of vegetation | Metals, metal compounds | None
 | Organic compounds, gases | Removal
Unusual colours and contours may Indicate wastes and residues | Metals, metal compounds | None
 | Oil and tarry wastes | Removal, filling or sealing
 | Asbestos (loose) | Filling or sealing
 | Other mineral fibres | None
 | Organic compounds including phenols | Removal or filling
 | Combustible materials including coal and coke dust | Removal or filling
 | Refuse and waste | Total removal
Fumes and odours | Flammable explosive and asphyxiating gases including methane and carbon dioxide | Removal
 | Corrosive liquids | Removal, filling or sealing
 | Faecal animal and vegetable matter | Removal or filling
Drums and containers | Various | Removal with all contaminated ground