## Slide 1: PowerPoint 3: Know the changes in construction pressures and materials over time.
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 301: Understanding construction practice in Wales

## Slide 2: Know the changing construction industry
Factors influencing pre-1919 construction
Factors influencing post-1919 to modern construction
Factors influencing twenty first century construction

## Slide 3: Factors influencing pre-1919 construction
Learners to research binders and mortars used pre-1919 and types of lime used (quick lime, hot lime) and how it was produced and slaked.
Binders are minerals which bind fibres when mixed with other minerals and water, which then harden, chemically or physically, for protection or decoration.
They are organic (bitumen) or inorganic (lime, cement, gypsum).
Mortars are typically paste mixtures of sand and cement (and water) which harden. Mortars can bond e.g., bricks together for structural strength or be laid on internal walls for decoration or external walls for protection and decoration. Pre-1919 construction used lime mortars (sand & lime (and water)) which have excellent properties, including being breathable. Restoration of pre-1919 buildings need lime mortars allowing ventilation with traditions (Cadw).
Aggregates are medium-to-course grained sand, gravel & crushed stone used to add strength to all surfaces for protection and/or decoration.

## Slide 4: Factors influencing pre-1919 construction
Learners research why pre-1919 construction resources were sourced locally
Due to transport and infrastructure constraints, this affected the type and look of buildings e.g., local quarries produced different types of aggregate across regions
Learners to understand the uses of stone, slate, timber and earth
Local resources would be used to build and therefore techniques would differ
Natural and cut-blocks stone would be used to build walls of buildings for strength, protection from the elements and decoration.
Slate would be used for roofs and sometimes walls for the same reasons.
Timber would be used for buildings for all aspects, walls, floors and roofs. This could be quicker but not as resilient as stone or slate, for the same reasons.
Earth could be used for walls, floors and roof coverings eg "clom" - earth, straw and animal manure or "wattle & daub" - timber strips and earth/clay.

## Slide 5: Factors influencing post 1919 to modern construction
Learners to know how transport systems were developed, pre & post 1919
Ancient Britons (pre-Welsh) made the first basic tracks (ley lines), the Romans repaired and built new (15,000km). These fell into disrepair and so towns became responsible for their section, with tolls, called turnpikes. 1760 saw the industrial revolution and an insufficient road network, therefore railways and canals were built. Some road networks were built post 1919 which allowed better movement of construction materials. 1936 saw major trunk road development and 1958 the first motorway, offering better movement.

## Slide 6: Factors influencing post 1919 to modern construction
Learners to know cost impact, good and bad, of more widely available materials
Economies of scale mean the larger the amount, the cheaper it becomes, making materials cheaper for builders. The more businesses providing these materials, the more competitive their prices must be, lowering profits and in turn, losing staff.
Learners to discuss post-1919 to modern construction methods
The cavity wall was the biggest change to post-1919. Non-traditional builds post WW11 saw pre-fabricated quick builds with no insulation or ventilation. The 1960's saw the high-rise era and then normal service resumed from the 1980's with cavities, insulation, ventilation and more modern techniques, to present day.

## Slide 7: Factors influencing post 1919 to modern construction
Learners to know churches and government buildings would cost more.
This is due to more expensive materials, better quality of workmanship and scale.
Know that buildings post-1919 have DPC, DPM, steel, glass & are quicker builds
Damp-Proof-Course is a 150mm wide roll of waterproof polythene which covers a course of bricks, then ties-in with a damp proof membrane (DPM) which lays beneath the floor (or roof). Steel can be used for house frames, panels, roofs, stud partition, lintels, RSJ's and re-bar. Glass is used more in properties due to improvements in U-values and off-site construction. All materials and techniques decrease build times.

## Slide 8: Factors influencing post 1919 to modern construction
Learners to know modern BSE materials and uses, such as plastic and copper.
Copper and plastic (PVCu & polybutylene) pipes have replaced cast iron, lead, galvanised steel and clay for water supply (hot and cold), heating, soil & waste & guttering. More recent jointing techniques include copper push-fit & press-fit and PEX.

## Slide 9: Factors influencing twenty first century construction
Learners to know sustainable construction for modern construction projects.
Use renewable (natural – wood, straw) and recyclable materials
Reduce a material's "embodied" energy (carbon release) during its life cycle
extraction, manufacturing, construction, maintenance, and disposal
Reduce the energy consumption of a building
Reuse on-site waste
Protect natural habitats during the construction life cycle.
Know the Well-being of Future Generations (Wales) Act 2015 for the industry
Improving the social, economic, environmental and cultural well-being of Wales.

## Slide 10
Any questions?