## Slide 1: New Technology Methods
PowerPoint presentation 1.1
Unit 101: Introduction to the Built Environment
Unit 301: Understanding construction practice in Wales

## Slide 2: New Technology and Methods Used in Construction
As industry advances with new technology, the design of buildings changes accordingly.
Many buildings are constructed for a specific purpose.
This will determine their shape, size and style and will also affect the quality and the eventual cost of the building.
The actual structure of the building is termed the external envelope, it protects the internal environment from all outside elements.

## Slide 3: Structural Forms
There are many structural forms in present day use, each being modified from time to time, in order to take the best possible benefit from new materials and developing new techniques.
The basic forms of structure used in the construction of buildings are:
● Solid structure
● Framed structure

## Slide 4: Solid Structure
The walls of this type of construction support the loads, protect the internal environment and also enclose the space.
The walls are therefore loadbearing, transferring the loads from the building down to the foundations.
The characteristic of this particular form is the thickness of the wall, due to the materials and the manner in which they are used.

## Slide 5: Solid Structure
Solid construction, in the form of brick, stone and concrete, is an easily erected structure. It is built up from small units gradually block by block.
When concrete is used some form of mould has to be provided to support the wet concrete until it has hardened.
There are two main types of solid wall construction:
● Cellular
● Cross wall

## Slide 6: Cellular Structure
This structure consists of walls, each connected to form the rooms of the building.
The result is a very rigid, loadbearing structure.
The external walls form the external envelope, and the internal walls divide and build up the rooms.

## Slide 7: Cross Wall Structure
Cross wall construction is the second method, it consists of a series of walls parallel to each other and at right angles to the front of the building.
Parallel walls

## Slide 8: Framed Structures
A framed structure is a network of beams and columns connected together to form the skeletal frame of the building.
The interconnecting members also have a supporting function, and they transfer the loads to the foundations.
Protection is provided by either cladding fixed over the framework, or infill panels fixed between the members.

## Slide 9: Framed Structures
Framed construction is suitable for a very wide range of buildings from low rise to high rise and is easily erected from pre-made members.
The members are simply connected together in a certain sequence to form the structural framework.
Concrete and steel are the two main materials used, with a small number of low-rise buildings having a timber framed structure.

## Slide 10: Framed Structures
The rectangular framed structure is the most common type and consists of a series of upright and horizontal members.
The resulting frame provides the bearing for the floors, walls and roof.
The structure can be cladded with brick when the building has been made watertight.